YTNC is a "backend" for the G8BPQ switch.

It works in a similar manner to, and has the same command line
arguments as the G8BPQ supplied equivalent BPQHTNC2.

YTNC <number of COM ports> <first COM port> <first BPQ host port>

Examples:

YTNC 25 1 1
Create 25 COM ports numbered COM1 through COM25, using the first 25 host ports.

YTNC 3 12 19
Create 3 COM ports numbered COM12 through COM14, using host ports 19 - 21.


YTNC does not support unproto or monitoring, and has a minimal command set:

 CONVerse      -  Change stream to Converse mode.
 Trans	       -  Change stream to Transparent mode.
 ^C	       -  Change stream to Command mode. (send break does same)

 Connect       -  Return stream connect status.
 Connect CALL  -  Connect application to callsign.
 Disconne      -  Disconnect application from switch.
 K	       -  Connect application to switch.

 APPLFlag      -  Set application flags.
 APPL	       -  Set application mask.
 BText	       -  Set beacon text.
 CONOk	       -  ON/OFF - Allow/disallow connects from users.
 CPactime      -  ON/OFF - Enable packetize-on-inactivity timer for CONV mode.
 CR	       -  ON/OFF - SENDP character included/not included in packet.
 Paclen        -  Set packet size.
 SEndp	       -  Character that will force tx of packet.

YTNC resets PACLEN to the node default at disconnect.


On the COM port side, YTNC supports the normal DOS functions 1-7,
plus some G8BPQ node specific function 30 subfunctions:

1  - Return node software version.
2  - Returns connect status of stream.
3  - Returns # unacked frames.
4  - Returns user to node.
5  - Disconnects user.