Page 1

    Class DOSThread: a base class for multithreaded DOS programs.
    ---------------------------------------------------------------------

      Author: John English (je@unix.brighton.ac.uk)
              Department of Computing
              University of Brighton
              Brighton BN2 4GJ, England.

      Copyright (c) J.English 1993.

      Permission is granted to use copy and distribute the
      information contained in this file provided that this
      copyright notice is retained intact and that any software
      or other document incorporating this file or parts thereof
      makes the source code for the library of which this file
      is a part freely available.


    1. Introduction.
    ----------------
    Class DOSThread provides a framework for writing DOS applications
    which consist of multiple (pseudo-)parallel "threads" of execution.
    DOS was not designed as a multithreading operating system (in fact,
    it actively hinders multithreading by being non-reentrant) but this
    class allows you to create multithreaded DOS applications without
    worrying about such problems (although you should read section 11
    for some important caveats concerning direct calls to the BIOS).

    To create a thread using this class, you must derive a class from
    it which contains the code you want to be executed in a member
    function called "main".  All you have to do then is declare an
    instance of your derived class and then call the member function
    "run" to start it running.  Each thread will be executed in bursts
    of 1 clock tick (55ms) at a time before being suspended to allow
    the other threads a chance to execute.  The length of the timeslice
    can be changed if necessary using the member function "timeslice".
    If required, timeslicing can be disabled entirely, in which case
    it is up to each thread to relinquish the use of the processor at
    regular intervals so that the other threads get a chance to run.

    Threads can delay themselves for a given number of clock ticks by
    using the member function "delay", they can relinquish the use of
    the processor to allow other threads to execute by using the member
    function "pause", and they can terminate themselves or each other
    by using the member function "terminate".  It is also possible to
    inspect the current state of any thread (ready-to-run, terminated,
    delayed and so on) by using the member function "status" and to
    wait for a thread to terminate by using the member function "wait".

    Two additional classes (DOSMonitor and DOSMonitorQueue) allow you
    to derive monitor classes of your own to facilitate communication
    between threads.  A monitor will normally contain data structures
    which can be accessed by several threads.  You can guarantee that
    only one thread at a time is executing a monitor member function
    which accesses the data by calling the member function "lock" at
    the start of the monitor function.  If any other thread is already
    executing a monitor function guarded by a call to "lock", the
    current thread will wait until it is safe to proceed.  At the end



                                                                Page 2

    of the monitor function, you should call "unlock" to allow any
    waiting threads to proceed.  Monitors can also contain instances
    of DOSMonitorQueue which allow threads to suspend themselves in a
    monitor function until some condition has been fulfilled (e.g.
    that a buffer isn't empty).  Some other thread executing within
    the monitor can resume any suspended threads when the condition
    is fulfilled (e.g. after a data item has been put into an empty
    buffer).  A template class which implements a bounded buffer is
    included in this distribution.  This is probably the commonest
    use of monitors in most applications, so it may well not be
    necessary to define any other monitor classes of your own.

    If you find this class useful or have any suggestions as to how it
    can be enhanced, please contact the author at one of the addresses
    given above.  E-mail and postcards will both be welcome!


    2. Deriving a new thread "MyThread" from class DOSThread.
    ---------------------------------------------------------
    Every thread is created by deriving a new class from the base class
    DOSThread.  Each derived thread class must provide a definition of
    a member function called "main" which contains the code which the
    thread will execute.  "Main" is declared like this:

        void MyThread::main ()
        {
            // code to be executed by your thread
        }

    The constructor for your derived class "MyThread" will invoke the
    constructor for DOSThread.  The constructor for DOSThread requires
    a single unsigned integer parameter which specifies the size of the
    stack to be allocated for the thread.  However, a default of 2048
    bytes is assumed, and if this is sufficient you need not explicitly
    call the DOSThread constructor at all.

    Having created a derived thread class, you can then declare instances
    of this class in your program, as for example:

        MyThread thread1;           // a thread called "thread1"
        MyThread threads [5];       // five identical threads

    The threads you declare will not be executed until you call the member
    function "run", as follows:

        thread1.run ();

    "Run" returns a result to the calling program which is TRUE (1)
    if the thread was started successfully, and FALSE (0) if it could
    not be started (either because there was insufficient memory to
    create the necessary data structures or because it has already
    been started).  Note that you cannot call "run" from your thread
    constructor since the virtual function "main" is not accessible
    until you have finished executing the constructor.

    Once a thread has been started successfully, it will be executed
    in parallel with the main program.  The main program effectively
    becomes another thread (although it has no name, and it can only



                                                                Page 3

    make use of the static functions "pause" and "delay" described
    below).

    The default is for each thread to be granted a "timeslice" of one
    clock tick (55ms).  If a thread is still running when its timeslice
    expires, it is moved to the back of the queue of ready-to-run threads
    and execution of the next thread in the queue is then resumed.  The
    static member function "timeslice" can be used to change the length
    of the timeslices used.  "Timeslice" requires an unsigned integer
    parameter specifying the desired timeslice length in clock ticks,
    as for example:

        DOSThread::timeslice (18);    // timeslice once a second (18 x 55ms)

    If the parameter is zero, timeslicing is disabled.  In this case
    it is up to individual threads to relinquish control to each other
    by calling a member function which will cause another thread to be
    scheduled.  A member function "pause" is provided for just this
    purpose, and is described below.

    "Timeslice" must be called before any threads are declared; as soon
    as the first thread has been declared, calls to "timeslice" will be
    ignored.  This means you cannot dynamically change the length of the
    timeslice during execution of the program.


    3. Writing the member function "main".
    --------------------------------------
    "MyThread::main" (the main function of your derived class) will be
    executed in parallel with the rest of the program once it has been
    started by calling "run" as described above.  While "MyThread::main"
    can be written in exactly the same way as any other function, it is
    important to remember that it is sharing the processor with a number
    of other threads and that if it has nothing useful to do, it should
    allow some other thread to run.  The member function "pause" lets you
    temporarily release the processor to another thread:

        pause ();                   // schedule another thread

    This is a static member function, so is can be called from any
    point in a program as "DOSThread::pause".  Even if you are using
    timeslicing, it is a good idea to call "pause" if your thread is
    temporarily unable to proceed (e.g. it is waiting for a key to
    be pressed), as otherwise it will do nothing useful for several
    milliseconds until its timeslice expires and another thread gets
    a chance to run.

    You can also make your thread wait for a fixed time by using the
    static member function "delay", specifying the delay period as
    a number of 55ms clock ticks:

        delay (18);                 // delay for 1 second (18 x 55ms)

    Note that "pause" and "delay" are both static member functions
    which always affect the current thread.  This means that you are
    not able to "pause" or "delay" any other thread.  It also means
    that you can call these functions from the main program if you
    need to.



                                                                Page 4

    When "MyThread::main" returns, the thread terminates.  You can also
    terminate a thread explicitly using the member function "terminate".
    If another thread (or the main program) wants to terminate "thread1",
    it can do it like this:

        thread1.terminate ();

    This is potentially problematical, as you have no idea what "thread1"
    is doing at the time.  A thread can also terminate itself:

        terminate ();

    which has the same effect as returning from the main function of
    the thread.


    4. Initialisation and finalisation.
    -----------------------------------
    When a thread is declared by the main program or by another thread
    the constructor for class DOSThread is called to create the thread
    and any constructor defined by your derived thread class is then
    called to complete the initialisation.  Note that a thread is not
    completely constructed until this sequence is complete, and in
    particular this means that you cannot call "run" from inside your
    derived class constructor to start the thread running immediately.

    When you reach the end of a block in which a thread was declared,
    the destructor for the thread will be called.  Any destructor you
    provide in your derived class is called first (while the thread
    could still be running), and the standard DOSThread destructor is
    then called to wait for the thread to terminate before tidying up.
    This means that your destructor should not do anything which might
    cause the thread to fail.  The member function "wait" allows you to
    wait for the thread to terminate, and your destructor should call
    this function before doing anything that might cause the thread to
    fail.  In other words, your destructor should be written like this:

        MyThread::~MyThread ()
        {
            wait ();            // wait for thread to terminate
            ...                 // do any class-specific tidying up
        }


    5. Handling "control-break" and critical errors.
    ------------------------------------------------
    Class DOSThread provides a simple mechanism for dealing with events
    reported by DOS.  The first such event is the "control-break" key
    being pressed to abort a program.  Class DOSThread intercepts these
    events and sets an internal flag.  Individual threads (or the main
    program) can call the static member function "userbreak" to test
    if control-break has been pressed:

        if (DOSThread::userbreak ()) ...

    The flag will remain set so that other threads can also inspect it.
    Alternatively, you can use the static function "cancelbreak", which
    is identical to "userbreak" except that it also resets the internal



                                                                Page 5

    flag.  This allows an individual thread to deal with a control-break
    event without any other threads being able to deal with the same event
    as well as providing a means for resetting the flag.  If threads do
    not use either of these functions, control-breaks will be ignored
    completely.

    Critical errors (the familiar "Abort, Retry, Fail?" errors) can be
    generated by DOS if a disk is write protected or a printer is offline.
    Classes derived from DOSThread can provide a virtual function "error"
    to deal with any critical errors they may generate.  Threads provide
    their own critical error handlers on an individual basis; the default
    handler just fails the operation.  To provide a critical error handler
    for a thread class, define a member function "DOSerror" as follows:

        DOSThread::Error DOSerror (int N);

    The parameter N is the DOS code defining the cause of the error.
    "DOSerror" should return a result of "DOSThread::IGNORE" to ignore
    the error, "DOSThread::RETRY" to retry the operation that caused the
    error, or "DOSThread::FAIL" to fail the operation.  Note that during
    critical-error handling, the only DOS services that you can use are
    functions 00 to 0C.  Class DOSThread will intercept and ignore any
    other functions, as they would otherwise cause DOS to crash.

    The function "DOSerror" should never be called directly; it will be
    called automatically if an error occurs during execution of a thread.


    6. Inspecting the status of threads.
    ------------------------------------
    The member function "status" allows you to determine what the
    status of a thread is at any time.  It can be called as follows:

        state = thread1.status ();

    The result is a value of type DOSThread::State, which will be one
    of the following values:

        DOSThread::CREATED      -- the thread is newly created and can
                                   be started by calling "run".
        DOSThread::READY        -- the thread is ready to run (or is
                                   currently running).
        DOSThread::DELAYED      -- the thread has delayed itself by
                                   calling "delay".
        DOSThread::WAITING      -- the thread is waiting to enter a
                                   monitor function guarded by "lock".
        DOSThread::QUEUED       -- the thread is inside a monitor and is
                                   suspended on a monitor queue.
        DOSThread::TERMINATED   -- the thread has terminated.


    7. Using monitors for interthread communication.
    ----------------------------------------------
    One of the problems with multithreaded programs is communicating
    between threads.  Since you do not know when a thread will be
    rescheduled, it is unsafe to modify shared global variables as
    it is perfectly possible for you to be interrupted during the
    process of updating them.  If another thread performs a similar



                                                                Page 6

    update, you may well complete your update using out-of-date
    values when your thread resumes, which means that the global
    variables end up in an inconsistent and incorrect state.

    The base class DOSMonitor provides a basis for developing classes
    which allow safe interthread communication.  All you have to do is
    to derive a class from DOSMonitor which encapsulates any data which
    will be updated by more than one thread and which provides access
    functions to access the data.  Each access function should begin
    by calling the member function "lock" and end by calling "unlock".
    This will guarantee that only one thread at a time is executing an
    access function in any individual monitor.  The general structure
    of a monitor access function is therefore as follows:

        void MyMonitor::access ( /* parameter list */ )
        {
            lock ();
            ...         // access shared data as required
            unlock ();
        }

    Classes derived from DOSMonitor can also contain instances of
    class DOSMonitorQueue.  Within an access function, you can call
    the member function "suspend" with a DOSMonitorQueue as its
    parameter to suspend the thread executing the access function
    until some condition is satisfied.  This will allow other
    threads to execute access functions within that monitor.  The
    other access functions can resume any threads suspended on a
    particular queue by calling the member function "resume"
    with the queue as a parameter.  This will reawaken the threads
    suspended in that queue.

    Note that suspend should be called from within a loop; since
    "resume" will restart all the threads in the specified queue,
    it is not guaranteed that the condition for which the thread
    is waiting will still be true at the time the thread actually
    resumes execution.  Thus to suspend a thread until a counter
    is non-zero, code such as the following should be used:

        while (counter != 0)
            suspend (some_queue);

    As an example, consider a monitor to provide a 20-character
    buffer to transfer data from one thread to another.  It might
    look something like this:

        class Buffer : public DOSMonitor
        {
            char data[20];          // the buffer itself
            int count;              // no. of chars in buffer
            int in;                 // where to put next char
            int out;                // where to get next char from
            DOSMonitorQueue full;
            DOSMonitorQueue empty;
        public:
            Buffer ()               { count = in = out = 0; }
            void get (char& c);     // get a char from the buffer
            void put (char& c);     // put a char in the buffer
        };



                                                                Page 7

    The class constructor initialises "count" to zero to indicate an
    empty buffer and sets "in" and "out" to point to the start of the
    buffer.  Threads must then call "get" and "put" in order to access
    the contents of the buffer.   Two DOSMonitorQueue instances are
    used; "full" is used to suspend threads which call "put" when the
    buffer is full, and "empty" is used to suspend threads which call
    "get" when the buffer is empty.  The code for "get" would be like
    this:

        void Buffer::get (char& c)
        {
            //--- lock the monitor against re-entry
            lock ();

            //--- suspend until the buffer isn't empty
            while (count == 0)
                suspend (empty);

            //--- get next character from the buffer
            c = data [out++];
            out %= 20;

            //--- resume any threads waiting until buffer isn't full
            resume (full);

            //--- unlock the monitor to let other threads in
            unlock ();
        }
     
       
    9. The class "BoundedBuffer".
    -----------------------------
    The class "BoundedBuffer" included in this distribution is a template
    class derived from DOSMonitor which implements a bounded buffer like
    the example above.  You can create a 20-character buffer using this
    class as follows:

        BoundedBuffer<char> buffer(20);

    The type given in angle brackets <...> is the type of item that you
    want to store in the buffer, and the parameter value is the maximum
    number of items the buffer can hold.  The following member functions
    are provided:

        get (item)      -- Get the next item from the buffer and store
                           it in "item".  The function returns 1 (TRUE)
                           if it is successful and 0 (FALSE) if the buffer
                           has been closed (see below).
        put (item)      -- Put a copy of "item" into the buffer.  This
                           function returns 1 (TRUE) if it is successful
                           and 0 (FALSE) if the buffer has been closed
                           (see below).
        items ()        -- Return the number of items in the buffer.
        close ()        -- Close the buffer to prevent further accesses.
                           If you do not close buffers when you have
                           finished using them, you run the risk of your
                           program never terminating -- a thread may be
                           suspended waiting for a character that will
                           never arrive, which means that its destructor
                           will wait forever for it to terminate.



                                                                Page 8

    10. Error handling in monitors.
    -------------------------------
    Monitors derived from class DOSMonitor should provide a virtual
    function called "error" which will be called if any errors are
    detected in a monitor.  "Error" should be declared as follows:

        void error (DOSMonitor::ErrorCode);

    The parameter to "error" is a code for the error which has been
    detected.  This can take any of the following values:

        DOSMonitor::NEW_FAIL        -- there was insufficient memory
                                       to create the necessary data
                                       structures for the monitor.
        DOSMonitor::NO_THREAD       -- a monitor has been called when
                                       there are no threads running.
        DOSMonitor::LOCK_FAIL       -- the current thread is calling
                                       "lock" when it has already
                                       locked the monitor.
        DOSMonitor::UNLOCK_FAIL     -- the current thread has called
                                       "unlock" without having locked
                                       the monitor.
        DOSMonitor::SUSPEND_FAIL    -- the current thread has called
                                       "suspend" without having locked
                                       the monitor.
        DOSMonitor::RESUME_FAIL     -- the current thread has called
                                       "resume" without having locked
                                       the monitor.

    The last five of these indicate a bug in the monitor code which
    should be corrected.  The default action if a monitor does not
    provide a definition for "error" is to exit the program with an
    exit status in the range -1 to -6 (-1 for NEW_FAIL through to -6
    for RESUME_FAIL).


    11. Potential problem areas.
    ----------------------------
    Class DOSTask uses an internal monitor to guard against re-entrant
    calls to DOS, as these are certain to crash your machine.  Direct
    calls to BIOS functions are not protected in the same way.  While
    BIOS calls are generally safer (they use the caller's stack), they
    still manipulate a global shared data area.  It is therefore not
    advisable to call BIOS functions directly, as this can lead to
    hard-to-identify bugs resulting from an inconsistent internal
    state.  However, C++ library functions normally use DOS services
    rather than calling BIOS functions, so most of the functions in
    the standard library are safe to use.  The major exceptions to
    this are the functions defined in <bios.h> and the functions
    "int86" and "int86x".

    If you do need to use BIOS functions directly, the best approach
    to adopt is to localise all BIOS calls in a single monitor so that
    only one task at a time can call a BIOS function; however, since
    DOS services will perform their functions by making BIOS calls,
    you must also use the monitor to encapsulate all DOS calls to
    guarantee that only one task at a time is making a BIOS call.
    This may not be a terribly practical solution.



                                                                Page 9

    Another point worth noting is that screen output is best done
    using "fputs" rather than "cout", "printf" or "puts".  Each of
    these generates several DOS calls to generate their output, and
    it is therefore possible for another thread to interleave some
    other output with it.  In particular, if you use "cout" it is
    possible for the same output to appear twice if the thread is
    interrupted after the output has been displayed but before the
    internal buffer has been cleared.  The next thread which uses
    "cout" will have its output appended to the existing contents
    of the buffer which will then be displayed in its entirety.

    A more serious problem (which I have been completely unable to
    resolve) is that programs which use direct BIOS calls can crash
    the system if high memory is being used.  If your program needs
    to use direct BIOS calls, you should only do this if you are
    NOT using an upper memory manager such as EMM386 or QEMM.  There
    is obviously some memory management context information which
    needs to be saved on a thread context switch, but without any
    knowledge of the internal workings of upper memory managers I
    do not know how to proceed on this (and if anyone can help me
    here, I will be eternally grateful!).


    12. A plea for feedback.
    ------------------------
    If you use this class, please contact the author via the addresses
    at the beginning; if you don't have e-mail access please send me a
    postcard (I like postcards!) just to let me know you've looked at
    it.  Feel free to suggest enhancements, find bugs or (better still)
    fix them and send me patches.  Happy hacking!