DRVTEST

        DRVTEST tests SCSI disk drives in a PC compatible system. In
        order to function correctly on a system, an ASPI (Advanced SCSI
        Programming Interface) driver must be available and installed on
        the system. DRVTEST communicates with the SCSI drive though the
        ASPI driver. Many manufacturers provide ASPI drivers for their
        controllers. LOMAS DATA PRODUCTS, Inc. provides ASPI drivers for
        their line of advanced caching/mirroring controllers for AT bus
        systems. This program was developed and tested on the LDP CACHE
        II PLUS controller and its ASPI driver and has been tested on the
        world's fastest AT bus caching controller, the LDP CACHE IV.

        It is assumed that the person using this test is familiar with
        SCSI peripherals and error conditions and codes. Using this
        utility, the SCSI disk drive can be rigorously tested and any bad
        sectors found can be remapped using the SCSI REASSIGN BLOCK
        command.

        ERROR REPORTING

        When an error is found, an error message is printed on the screen
        that identifies the ASPI MANAGER error code along with the
        information provided by a SCSI SENSE command. This information
        will identify the error that occurred along with the record that
        caused the error. In order to properly respond to error
        conditions, you should have a list of the error codes your drive
        may provide. A basic list of SENSE KEYs codes are provided at the
        end of this document. If your drive did not come with a manual
        defining what SENSE KEYs and EXTENDED SENSE CODES, the drive
        provides in error circumstances, you may use these codes as a
        guide. It is unlikely that any error with a SENSE KEY other than
        '3' will benefit from having the record remapped.

        An example of the error report follows:

                ASPI error reading id 1, error code 4
                          Error code = 70
                           Sense key = 03
                 Extended sense code = 11
                        Block number = 34565
                Should the failing block be reassigned?(y/n)

        STARTING DRVTEST

        DRVTEST requires one parameter, the SCSI device id of the drive
        to be tested, and may accept one additional parameter which
        defines how DRVTEST responds to error conditions.
        The test is begun as follows:

                DRVTEST SCSI_DEVICE_ID <nN,rR>

        n,N is an optional non destructive specifier.
        r,R automatically reassigns bad blocks when encountered during
            testing


        The following are examples of acceptable command lines:

                DRVTEST 1

                Tests the drive attached at SCSI address 1. Any
                read/write testing will destroy data on the  drive
                and users are prompted before reassigning a bad
                record.

                DRVTEST 1 R

                Test the drive attached at SCSI address 1.
                Read/write tests will destroy any existing data on
                the drive. Any blocks found to be failing will be
                automatically reassigned.

                DRVTEST 1 N

                Tests the drive attached at SCSI device 1.
                Nondestructive testing will be performed. Data on
                the drive will be preserved by saving the data
                before testing the records under tests and restoring
                them when the test is complete. The user will be
                prompted before any bad records are reassigned.

                DRVTEST 1 NR

                Tests the drive attached at SCSI device 1. Non
                destructive testing will be performed. Any failing
                records will be automatically reassigned.


        The test will verify that the device is a random access device
        before proceeding.

        The following menu will then be displayed:

                1. READ TEST
                2. SIMPLE READ/WRITE TEST
                3. EXHAUSTIVE READ/WRITE TEST
                4. RANDOM READ TEST (SEEK TEST)
                5. LOW LEVEL FORMAT THE SCSI DRIVE
                6. EXIT

        READ TEST:

        Read test will read all the records on the drive and if an error
        occurs, it will be reported to the user. If the option 'R' was
        specified, the bad record will automatically be reassigned.
        Otherwise, the user will have the option of remapping the failing
        sector if appropriate. The test will continue unless aborted by
        the user. The test may be aborted at any time by typing ESC.

        SIMPLE READ/WRITE TEST

        Each record will have a '11100110' test pattern written to it
        with a write-verify command. If the option 'R' was specified, any
        bad records will automatically be reassigned otherwise the user
        will have the option of remapping the failing sector if
        appropriate. If the 'N' option is specified on the command line,

        the test is done non-destructively. The test may be aborted at
        any time by typing ESC.

        EXHAUSTIVE READ/WRITE TEST
        Each record will have several patterns written to it and
        verified. The test patterns used will be:

                00000000
                11111111
                01010101
                10101010
                11001100

        If the option 'R' was specified, the bad record will
        automatically be reassigned otherwise the user will have the
        option of remapping the failing sector if appropriate. If the 'N'
        option is specified on the command line, the test is done non-
        destructively. The test may be aborted at any time by typing ESC.

        RANDOM READ TEST

        The random read test will randomly read sectors from the harddisk
        drive specified. An error count will be kept and reported to the
        user. No attempt will be made to reassign errors encountered. The
        user will be prompted for how many read operations should be done.
        Each read will consist of 1 sector only. This test is designed to
        exercise the drive head positioning mechanism.

        LOW LEVEL FORMAT THE SCSI DRIVE

        This menu option will perform a low level format on the specified
        drive. This option uses the SCSI FORMAT UNIT command to perform
        the format and no additional testing is performed. This low level
        format will format the drive in a manner that will remove any
        records reassigned by any of the previous operations. After
        performing this format, the drive should be tested with the
        EXHAUSTIVE READ/WRITE TEST before being used.

        SCSI ERROR CODES

        SENSE KEY       Description

        0h              NO SENSE: Indicates that there is no specific
                        sense key information to be reported for the
                        designated unit.

        1h              RECOVERY ERROR: Indicates that the last command
                        was successfully completed, with some recovery
                        action performed by the drive. Details can be
                        determined by examining the additional sense
                        bytes in the information bytes.

        2h              NOT READY: Indicates that the drive cannot be
                        accessed. Operator intervention may be required
                        to correct this condition.


        3h              MEDIUM ERROR: Indicates that the command
                        terminated with a non-recovered error condition
                        which was probably caused by a flaw in the
                        medium, or an error in the recorded data.

        4h              HARDWARE ERROR: Indicates that the drive detected
                        a non-recoverable hardware failure while
                        performing the command, or during the self test.
        5h              ILLEGAL REQUEST: Indicates that there was an
                        illegal parameter in the command descriptor block
                        or in the additional parameters suplied as data
                        for some commands.

        6h              UNIT ATTENTION: Indicates that reset occured
                        since the last selection by the initiator.

        7h              DATA PROTECTION: Indicates the drive cannot be
                        written because it has been write protected.

        8h thru Fh      For DRVTEST these codes have no meaning.