þ frequently asked questions and the appropriate answers
______________________________________________________________________

þ Section A : Who helps, if not this text ?                          þ

  Questions and  suggestions,  equal  whether  you  are  owner  of a
  license for use or not,  are  welcome  in  the  author's  mailbox.
  Please  understand,  that  we do not answer questions for which an
  answer could be found in this documentation, and which do not need
  a deep knowledge of serial communications in detail.

  A very important entreaty  :  please  remove all comment text from
  configuration files, if you send them to the author together  with
  a request for help.

  Use  e-mail  or the BBS system of the author for asking questions.
  Fax  or  snail  mail  is  answered  only  if  you  give  an e-mail
  destination for the answer, for cost reasons.

  The author will set up a mailing list server, to send mails  about
  ZuTSR news (new versions, etc) to all users who request to receive
  this information.  Interested users, please ask for it.

  Registered users, who

  - know  about  the  basic  principles  of  PCs,  MS-DOS,  resident
    programs, mailers and ZuTSR, and who
  - like to trial, test,
  - who show creativity while searching for possible errors and bugs
    and while inventing new features
  - who are reachable via e-mail in the international networks by
    the author (see list below)

  will  be  of  great  help for the further development of ZuTSR.  A
  special form  has  not  to  be  filled  out.   The  access  to the
  so-called  "ZuTSR  test  file  area"  in  the  author's   mailbox,
  containing alpha- and beta- releases, will be given on request.

  You might reach the author as follows : (subject to change)

    Kolja Waschk                FidoNet  :            2:240/5814
    Oevelgoenne 23              ZyXELNet :           16:100/2215
    22605 Hamburg               UniNet   :           127:100/906
    Germany                     UseNet   : kawk@zerebrm.hanse.de

    Phone   (11:00 - 22:00 GMT+1 resp. GMT+2 in summer (CET/CEST)),
    BBS     (7:15 - 1:15, requests 24h except 02:30-03:30 GMT)
    Fax :
                 +49-40-8804056

--
> Important ! Commercial enquiries,  product orders, etc. must not   <
  be  sent  through systems of the above listed electronic networks,
  as these nets are meant  only for private, non-commercial mailing.
  Please send those mails always direct, as a "crashmail",  fax,  or
  as a normal letter !

  You  may  request  the  most recent public version of ZuTSR in the
  author's BBS at any time, using the magic name

  ZUTSR    - (ca.  60k) program & english documentation
  ZUTSRG   - (ca.  40k) german documentation, without program

  ZUTSBETA - small updates without complete documentation, mostly
             prereleases

______________________________________________________________________

þ Section B : frequently asked questions                             þ


--
> After ZuTSR  is  loaded,  the  mailer  does  not  answer any call. <
  Instead the message "NO CARRIER" appears a few seconds  after  the
  first ring signal.

  This  happens,  because ZuTSR might try to send commands faster to
  the modem than that is able  to receive them.  Increase the values
  for "CommandDelay", "CharDelay", and/or insert delays in  critical
  modem commands (~D, ~P, ~p).  To start, set

  CommandDelay 200
  CharDelay 20

  Please read the following notice also.

--
> If  the  option  'Debug' is enabled, everything works wonderfully. <
  But as soon as  it  is  taken  from  the config, messages won't be
  replayed anymore and other.

  This points to a timing problem also.  Try to find  out  which  is
  the  last  command  sent to the modem before the error occurs, and
  then add a leading or trailing delay in the command (~P, ~p, ~D)

--
> After ZuTSR detects a  human  call,  an external program should be <
  executed to handle the voice call.  The external program  actually
  starts  up,  but  before  it does anything, something hangs up the
  line...

  First, determine where the line gets  hung up.  There are at least
  four different possibilities:

  (a) ZuTSR itself hangs up (see next question & answer)
  (b) The mailer hangs up, before it  shells  out  to  the  external
      program.   Normally, this means that your mailer is configured
      to "drop DTR", or,  more  generally,  to initialize the modem,
      before it executes the external program.  Please refer to  the
      documentation of your mailer to solve this problem.
  (c) Somewhere  in  your  batch file (if used)  the connection gets
      terminated.  Check your batch program.
  (d) The   external  program   generally  terminates  any  possibly
      existing connection before starting up.  Look  for  a  command
      line  switch  or  anything  similar for starting the software,
      that would disable this behaviour.

  Whether you have problems with  (a)/(b) or (c)/(d) could be simply
  tested; just replace the execution of the external  program  by  a
  small delay or anything similar.

--
> ZuTSR immediately hangs up after handling an incoming call, and no <
  connect  message  is  simulated; instead, I get "NO CARRIER" in my
  mailer's log file.

  Make sure that you have the script command "S" as the last command
  of the appropriate script.   This  is  NOT  the case in the sample
  script included with the sample configuration files.  Please refer
  to the samples in INSTALL.DOC and the informations in REFER.DOC to
  learn about the meaning of the script commands.

--
> ZuTSR does NOT hang up the modem after handling a  call;  instead, <
  the  mailer  just waits for the next call on a line which is still
  switched off hook.

  When simulating a connect  message,  ZuTSR  does not actually make
  the modem go on hook, to enable external programs to take  control
  over  the  call.   Either  disable  the  simulation of the connect
  message (remove  the  script  command  "S"  from  the  end  of the
  appropriate script, or replace it by "H"), or  let  some  external
  program  do the hang up (for example, by using ECHO ATH > COM1, if
  your modem is connected to Com1)

--
> Voice calls are passed correctly to an external program, but ZuTSR <
  gets restarted by the  external  program  and  tries to handle the
  call again (as from the beginning) ?

  If you've configured the external program to use the Fossil driver
  for data transfer to the modem, all data will pass ZuTSR also.  To
  avoid ZuTSR from reacting on another "ATA", sent by  the  external
  program for example to establish a data connection, simply disable
  ZuTSR  before  executing  the  external  program  (ZUTSR  /D)  and
  re-enable  it  afterwards  (ZUTSR /E).  Another option would be to
  configure the external program  not  to  use the Fossil driver, if
  available.

--
> Voice files cannot be replayed using ZFax; there's only noise.     <
  Also, converting the files to another file format using  VCNVT  or
  similar does not work.

  Probably you've set the parameter "Compression" to 6,7 or 8. Using
  this setting, ZuTSR will generate voice files, which are not fully
  compatible  to  the  file format used by ZFax.  Files of this type
  can be replayed only with  few  other programs than ZuTSR.  Please
  see also the informations about file formats in REFER.DOC.

  Other reasons for noise might be slow hardware, or a locked serial
  speed below 38400 bps.  Often, you might experience  this  problem
  when  running ZuTSR in (pseudo-) multitasking environments like MS
  Windows, or under OS/2,  where  data gets lost easily.  Hopefully,
  the option "WindowsBlock" might help you in the latter situation.

--
> Sometimes, when a single beep tone should be generated, TWO beeps  <
  can be heard; sometimes,  ZuTSR  seems  to  halt  completely,  and
  sometimes, a beep tone does not stop anymore at all...

  This  behaviour  is  a bug in many modems equipped with a Rockwell
  chipset, using old firmware.  The only  thing  to do for you is to
  look for a newer firmware or to replace the beep tone by a  signal
  tone sampled as a voice file.

--
> ZuTSR halts while doing the script command "Q".                    <

  To  implement  this action on Rockwell based modems as on other IS
  101 compatible modems, ZuTSR  uses  a  method that requires a very
  stable and well-programmed firmware in the modem, that is able  to
  switch  between  recording  and  replaying  mode  very quickly and
  reliable.  Some modems show their limits to you here.

--
> I'm using a ZyXEL modem, but cannot utilize the compression modes  <
  4 and 8.

  1. 4bits/Sample  Z-ADPCM  is  available  starting  with  6.22;  no
     earlier firmware version is capable of this.

  2. The serial link  speed between modem and computer has to be  at
     least  set  to 57600 bps (a Fossil driver setting).  This speed
     will definitely  cause  problems  on  slow  systems, ie.  those
     which are not equipped with a 16550 chip, or similar.

  Yet, simply use another compression mode.

--
> Regardless whether I'm using the  script  commands  "r"  and  "P", <
  ZuTSR always will store the data in "Destination A".

  This  is  a  limitation  of  the  unregistered  version.   If this
  behaviour remains even after you've  inserted  a valid key code in
  your configuration, please contact the author.

--
> What can I  do  to  force  ZuTSR  to  hang  up  immediately  while <
  answering  a  call,  to  take over using my phone connected at the
  rear of the modem or parallel to it ?

  Press the <Esc> key  on  the  keyboard  of  the  PC where ZuTSR is
  running on.

--
> I'm using a ZyXEL modem, and therefore cannot make ZuTSR to detect <
  automatically when I've taken the phone set connected to  it.   It
  will  not interrupt the call handling, and I have to stand up from
  bed and make many steps to  reach  the PC, to press the <Esc> key,
  before I can talk in the phone...

  Use a micro switch located under the phone hand set,  and  connect
  it  to  some  unused digital input at your PC (for example, to the
  game port instead of a  joystick  button, or to the printer port).
  Then, the configuration verb "HardBreak" can be used to make ZuTSR
  react on a release of this micro switch similar to the pressing of
  the <Esc> key on the keyboard.  Hint: Use a switch that is  opened
  normally,  and closed when you lift up the phone; otherwise, ZuTSR
  will  not  operate  properly  when  the  switch  is  not connected
  temporarily.

--
> After a call has been assumed to be  a  human  call,  ZuTSR  shall <
  record  a  message.  It does so, but the recording will be stopped
  too early, interrupting the caller while speaking.

  ZuTSR is very sensitive  even  for  very short periods of silence.
  To avoid this, please read the answer on the next topic.  The fact
  that ZuTSR obviously stops the  recording  even  if  there  is  no
  silence,  but  while  the caller is actually talking, is caused by
  another  problem.   ZuTSR's  internal  audio  signal  analyzer  is
  optimized to distinguish between  human  and machine calls, not to
  handle human calls.  If tends to be a real  problem,  disable  the
  internal  analyzer  (remove "IntAnalyze" from your configuration),
  or use external programs for the voice call handling.

--
> I want  to  change  the  silence detection interval (configuration <
  verb "Silence") between first and following recordings.

  Only if you're NOT using "IntAnalyze", you may do this by using  a
  simple  trick: Just let a modem command, which is used only before
  starting another recording, change the silence detection interval.
  For example, add the setting's  change  to the "Beep" command, and
  let ZuTSR send it to the modem before  recording  (script  command
  "B").

--
> Are there any other programs to utilize the voice mode, except for <
  ZuTSR ?

  Beside  some  programs,  that  can  be  bought  only directly from
  commercial distributors, there are some  very good (if not better)
  programs available as Shareware or in the  Public  Domain,  to  be
  obtained  from  many  public  BBS  systems,  as  from the author's
  system.

  The following lists only a few of them:

  ZUtil - written by the same author as ZuTSR

    ZUtil is a program to be used on the DOS command line, or within
    batch programs.  It enables you  to record voice, send voice, to
    send commands to the modem and await its  responses,  and  more.
    Using  this  program,  and having little knowledge of using DOS'
    batch program language,  you'll  be  able  to  build up your own
    powerful voice  call  handling  system  to  answer  calls,  make
    outgoing calls, and more.

    The  current version of ZUtil is quite old, and can be used with
    ZyXEL modems only yet.  Planned  for the future is a combination
    of ZuTSR and ZUtil, which will work with other  modem  types  as
    well.

  VoiceConnect - by Thomas Haukap, Haukap Kommunikationstechnik

    VoiceConnect  obviously  is  the  most  powerful  voice  program
    available  on  the  shareware market yet; beside many voice call
    handling  options  it   features   an   internal  fax  receiver,
    transmitter and viewer.  Also available are features to  provide
    fax  documents  on demand, or to be polled with any fax machine.
    It is a very big  program, nevertheless it's running more stable
    than many other commercial programs.  Not to forget, it is  able
    to  utilize  a  SoundBlaster(tm) compatible sound card to replay
    and  record  voice  files,  and  to  listen  to  incoming calls.
    VoiceConnect can be used with almost any modem that has a  voice
    mode,  ZyXEL  modems,  Rockwell  based  modems, and other IS 101
    compatible modems.  Currently, VoiceConnect  is the only program
    beside ZuTSR which is able to record and  replay  files  in  the
    enhanced  ZFax  file  format,  to  store  Rockwell  data  and/or
    Resync-data.

    A port to MS Windows will be available in the late summer of '94.

    VoiceConnect can be copied from Thomas Haukap's BBS, the
    Intuition : +49-40-8705378.

  VCNVTA - by Thomas Haukap, Haukap Kommunikationstechnik

    VCNVTA is a little utility to  convert voice files from one file
    format (ZyXEL CELP, Z-ADPCM, R-ADPCM) to Creative Lab's VOC file
    format, and vice versa.  VCNVTA is also  capable  of  converting
    files recorded with ZuTSR in the compression modes 6,7 and 8.

    VCNVTA can be copied from Thomas Haukap's BBS, the
    Intuition : +49-40-8705378.