**************************************************************
        *                                                            *
        *                                                            *
        *                   **   ** ******* *******                  *
        *                   ***  **  **   *  **   *                  *
        *                   **** **  ** *    ** *                    *
        *                   ** ****  ****    ****                    *
        *                   **  ***  ** *    ** *                    *
        *                   **   **  **   *  **                      *
        *                   **   ** ******* ****                     *
        *                                                            *
        *                                                            *
        *                        Version 2.00                        *
        *                                                            *
        *     File Distribution for BinkleyTerm(*) Style Systems     *
        *                                                            *
        *                                                            *
        **************************************************************
        *                                                            *
        *       (C) Copyright 1991-1994  by  Alberto Pasquale        *
        *                                                            *
        *           A L L   R I G H T S   R E S E R V E D            *
        *                                                            *
        **************************************************************
        
        
        (*) "BinkleyTerm" is trademark of Bit Bucket Software, Co.
        
        
        
        




                  NEF 2.00 User's Manual, by Alberto Pasquale
        
        
        
                                  INTRODUCTION
        
        
        -> For licensing information, please see License.Doc.
        
        Thanks for evaluating NEF: a "New Echo Files" distribution
        system. Main characteristics:
        
        - It works on systems with a Binkley(*) Style outbound and
          *.MSG or Squish(**) message base.
        
        - File Import/Forward/Hatch via the standard .TIC system,
          initially implemented by Tick(***).
        
        - File "Areafix", to automatically link/unlink file areas via
          netmail messages. Wildcards can be used to make multiple
          link/unlink requests easier.
        
        - Flexible file announcements via echo or netmail messages.
          Wildcards in file area tags allow easy configuration of
          multiple announcement areas for different groups of file
          areas.
        
        - Full multitasking support. File sharing problems are handled
          wherever necessary.
        
        - Full 4D operation; no direct support for ancient pointnet
          addressing method. However points addressed via pointnet can
          obviously be seen with their pointnet adress.
        
        - Very flexible MultiAka support. You can use different
          addresses in different areas, different addresses for
          different downlinks in the same area, etc.
        
        - Long Description ("LDESC" keyword) support.
        
        - Automatic creation of new areas from authorized uplinks.
        
        - Automatic linking of specified downlinks to selected new
          areas when they are automatically created.
        
        - Check on imported description strings, to avoid trojan horses
          using certain control characters.
        
        - Clean and compact link configuration file.




        
        - Easy addition (on area TAG basis) of text strings at the head
          of imported descriptions, to allow inclusion of flags and
          download counters in selected areas.
        
        - Easy partial/total area split/merge: you can forward
          certain files to a new area TAG.
        
        
        
        (*)   "BinkleyTerm" is trademark of Bit Bucket Software, Co.
        
        (**)  This program uses the "MsgAPI" version 2 code by Scott J.
              Dudley. "Squish" is a trademark of Scott J. Dudley.
        
        (***) "Tick" is Copyright by Barry Geller
        
        




                               OVERALL OPERATION
        
        
        When invoked, first of all NEF looks into the netmail area(s)
        for netmail messages to the Link Robot (Areafix like) and
        executes the commands required; then it looks for new .TIC files
        in the netfile area(s) and forwards them.
        
        The ingoing files are moved to their destination directory and
        the description (the long one if available) is appended to the
        files.bbs (after being truncated in order to respect the 256
        character limit of files.bbs entries). A careful check is
        operated on the text of the description, to avoid trojan horses
        that use special control characters.
        
        If the Replace command is present in the ingoing .TIC, the
        pertinent file is erased and its description removed from the
        files.bbs; otherwise the files.bbs is scanned for the presence
        of the name of the new file and, if found, its description is
        removed. This avoids multiple entries for files that are
        periodically distributed with the same name and with no Replace
        command in the accompanying .TIC.
        
        The .BSY support avoids conflicts in the outbound, while
        possible conflicts in the access to files.bbs are minimized by
        waiting about 10s before giving up.
        
        Finally, NEF writes the announcements of the received files;
        each message is limited to a maximum of less than 8KB to avoid
        problems with old mail processors.
        
        Conflicts on the message base should be handled by the Squish
        MsgAPI. Unfortunately, there is a bug in the MsgAPI code that
        could cause base corruption in certain cases. To minimize the
        hazard, it is recommended not to use message editors while mail
        processing is in operation.
        




                                  INSTALLATION
        
        
        1) Edit Nef.Cfg.
           You can find useful information both in Nef.Cfg itself and in
           the "CFG REFERENCE" section of this documentation.
        
        2) Edit your batch file in order to call NEF whenever you would
           like to test for the presence of .TIC files in your inbounds
           and process them.
           If you do not pass a different pathname as a command line
           parameter, Nef.Cfg must reside in the current directory.
        
        3) (OS/2): Make sure you have the MSGAPI32.DLL in a directory
           contained in your LIBPATH. MSGAPI32.DLL can be found in the
           Squish 1.10 archive.
        
        
                             COMMAND LINE SWITCHES
        
        
        To get help about the command line syntax, use the "-h" or "-?"
        command line switch: type "NEF -h" or "NEF -?".
        
        
        a) NEF [-c<cfg>]
        b) NEF [-c<cfg>] HATCH|MATCH
        c) NEF [-c<cfg>] HATCH|MATCH <name>[,<replace>] <TAG> <desc>
        
        
        -c<cfg>
                This command line switch allows to use a configuration
                file different from the default "Nef.Cfg".
                Example: "Nef -ce:\cfg\nef2.cfg"
        
        HATCH
        MATCH
                If you specify HATCH or MATCH, NEF will not process
                inbound .TIC files; instead it will send the specified
                files to your links.
                Examples: "Nef Hatch"
                          "Nef Match"
        
                The b) type of command line needs your interaction with
                the program: you will be requested the filename
                specification (Dos or OS/2 wildcards allowed) and, for
                each matching file, the optional "replace" name, the
                area TAG, the description and the optional "Long
                Description".




        
                HATCH sends the specified files without moving them: if
                they are in the directory that belongs to the specified
                <TAG>, the specified description is appended to the
                files.bbs.
        
                MATCH moves the specified files to the directory that
                belongs to the specified <TAG>, then it does a normal
                HATCH.
        
                If you use the c) type of command line, then you must
                specify all the requested fields and you cannot give a
                "Long Description".
        
        <name>
                It's the full pathname of the files you want to Hatch or
                Match. You need to specify the full path even if you are
                hatching files that reside in the directory belonging to
                <TAG>.
        
        <replace>
                It's the optional name of the file to be replaced: if
                the receiving system has this feature enabled, a file
                named <replace> in the <TAG> area will be deleted while
                importing the new file.
        
        <TAG>
                It's the tag used for distributing an echo-file area.
        
        <desc>
                It's the file description and must begin with the quotes
                character '"'. It's not necessary to terminate the
                description with a matching '"'. If you need to include
                the '"' character in the description, precede it with a
                backslash escape character: '\"'.
        
        
        Examples:
        
                NEF Hatch d:\p\prg12.rar,prg11.rar COMMS "New comm prg
        
                d:\p\prg12.rar is hatched but NOT moved; prg11.rar will
                be deleted on receiving systems.
        
                NEF Match d:\p\prg12.rar COMMS "New comm prg
        
                d:\p\prg12.rar is moved to the directory belonging to
                the COMMS file area, it is hatched to the COMMS area,
                no replace information is put in the outgoing .TICs.




        
        
        
                                        ERRORLEVELS
        
        
          0 - File areas modified: Match or .TIC processed.
          1 - File areas not modified: Hatch or NO .TIC processed.
          2 - Help requested.
          3 - Abnormal termination
          4 - Configuration file not found.
          5 - Invalid parameter on command line.
          6 - No Outbound defined in cfg file.
          7 - Disk Full.
          8 - Out of Memory.
          9 - Can't open Log file.
         10 - Prefix or Suffix too long.
         11 - User Input Error (interactive hatch/match).
         12 - TimeOut waiting for concurrent NEF process to finish.
         13 - Error while accessing .SAV file.
        250 - MsgApi Init Error.
        251 - MsgApi Area Open Error.
        252 - MsgApi Area Lock Error.
        253 - MsgApi Area Close Error.
        




                                 CONFIGURATION
        
        
        Before analyzing the cfg keywords in detail, let's introduce the
        overall mechanism that is at the basis of NEF's file forwarding
        capabilities.
        
        Each area (defined via the FileArea keyword) can be
        mono-directional or bi-directional.
        
        In bidirectional areas every link can send files to us and we
        forward to everyone, unless those with a "receive-from"
        override.
        
        Monodirectional areas can be "receive from everyone" or "send to
        everyone". Obviously, at least one link must have an override in
        the opposite direction, unless we are the destination or
        origination of all the files.
        
        NEF uses the three flags 'I' (Input: we accept from), 'O'
        (Output: we send to) and '*' (bidirectional) to define the
        direction of an area or link.
        
        Each area has a direction, that can be overridden on a per-node
        basis by a global (in the FileLink statement) or local (in the
        FileArea statement, before the pertinent link address) direction
        override.
        
        In other words: each link has a direction that is defined in
        order of priority (from lowest to highest) by the area direction
        (I|O|* in FileArea), the global link override (in the FileLink
        statement), the local link override (before link address in the
        FileArea statement).
        
        It is recommended not to use the global link override when not
        really useful, so that the area definition statements remain
        clearly readable without the need to keep one eye on the
        FileLink statements.
        
        Usually the global link override is useful when you have an
        uplink for many areas. For example: if one day the uplink and
        one of the downlinks switch their role, you have to move the 'I'
        flag from one FileLink statement to the other with no need to
        change all the area definitions.
        
        The area direction definition is very useful to allow automatic
        linking via the Link Robot both to normal "Uplink to Downlinks"
        areas and to reverse "Downlinks to Uplink" areas (mostly used
        for "pre" areas to collect files and send them to the




        coordinator).
        
        As a matter of fact, in response to a link request, the Link
        Robot only adds the requesting address (with no flags) to the
        FileArea statement. So the real characteristics of the link
        depend on the Area direction and on the link flags (FileLink
        statement).
        
        
        
                                 CFG REFERENCE
        
        
        
        - Items between square brackets (e.g. [<item>]) are optional.
        
        - Items separated by '|' are mutually exclusive (e.g. I|O|*).
        
        - The names of the various Keywords are NOT case sensitive.
        
        - The area TAGs are NOT case sensitive and must be legal DOS
          names: they are limited to a maximum of 8 characters.
        
        - <WTAG> is a "Wild TAG" specification: it can be a normal area
          TAG or a partial TAG followed by the '*' wildcard.
        
        - When a directory path is required, the trailing backslash '\'
          is optional.
        
        - The ';' character starts comments: any character following the
          ';' is ignored. Please note that configuration text strings
          (e.g. Subject, Origin) cannot contain the ';' character.
        
        - The maximum length of configuration lines (including FileArea
          definitions) is 510 characters.
        
        - Unless differently specified, addresses are standard 4D and
          MUST begin with the zone number.
        
        Please, note that the order of the configuration statements
        follows some logical rule. In order not to create confusion in
        the .cfg file and not to break some _necessary_ order relation,
        please follow the scheme proposed in the example NEF.CFG file
        and in this reference documentation.
        
        
        
                                     SYSTEM
        




        
        RegKey <RegKey>
        
                Registered Users only: <RegKey> is the registration key
                and it is NOT case sensitive.
        
            Example:
        
                RegKey dfhyuwru6274623
        
        
        Address <Address>
        
                You can use as many Address statements as you need for
                all of your AKAs. The first one specifies the "primary"
                address. <Address> is a standard 4D address
                specification.
        
            Example:
        
                Address 2:332/504.0   ; Primary Address
                Address 2:332/524.0   ; Second line aka
                Address 2:332/500.0   ; Hub aka
                Address 9:999/999.9   ; one more aka
        
        
        StatusLog <LogFile>
        
                <LogFile> is the name of the file where all the
                operations performed by NEF will be logged, following
                the "Binkley Style".
        
                In multitasking environments, please be sure to use a
                file that cannot be used by other processes at the same
                time. For example: if (in your system) NEF can be
                executed while Binkley is running, please use different
                log files.
        
                Multiple NEF processes using the same config file
                (and therefore the same <LogFile>) will have no problem
                since NEF does not begin operations until the previous
                launched instance (if it uses the same .cfg file) has
                finished.
        
                Should you not want the log file, you can comment this
                keyword out.
        
            Example:
        




                StatusLog c:\max\nef.log
        
        
        NetFile <InboundDir>
        
                You can specify as many NetFile statements as you need,
                one for each inbound directory where NEF must look for
                new .TIC files.
                <InboundDir> is the pathname of the inbound directory.
        
            Example:
        
                NetFile c:\file\net
        
        
        OutBound <RootPath> [<Zone>]
        
                The outbound directories are specified with the same
                method as in squish.cfg.
                <RootPath> should not have an extension.
        
                The first OutBound statement does not have the <Zone>
                field and specifies the directory where NEF will build
                file attaches for the zone of the primary address.
        
                Subsequent OutBound statements must have the <Zone>
                field (Decimal). File attaches for the specified <Zone>
                are built in <RootPath>.<###>, where <###> is a 3 digit
                extension representing the zone number (hexadecimal).
        
                File attaches for zones different from the primary one
                and not matching any <Zone> of the OutBound statements
                are built in <RootPath>.<###>, where <RootPath> is the
                one specified in the first OutBound statement and <###>
                is a 3 digit extension representing the hexadecimal
                zone number.
        
            Example:
        
                OutBound c:\out\fidonet
                OutBound c:\out\amiganet 39
                OutBound c:\out\amiganet 40
        
                FileAttaches will be built in:
                Primary zone -> c:\out\fidonet
                zone 39      -> c:\out\amiganet.027
                zone 40      -> c:\out\amiganet.028
                other zones  -> c:\out\fidonet.<###>
                                where <###> is the 3 digit hexadecimal




                                representation of the zone number
        
        
        TicHold <TicDir>
        
                This specifies the directory that holds all the .TIC
                files addressed to downlinks until they are sent and
                erased.
        
            Example:
        
                TicHold c:\file\tichold
        
        
        BusyFlags
        
                This enables the Binkley-Style .BSY support.
        
                When attaching a file to a node, the presence of an
                appropriate .BSY file is checked; if it is present, some
                other process may be working on the same node, so NEF
                saves the attach info to a private <config>.SAV file
                (i.e. NEF.SAV when NEF.CFG is the config file). On
                subsequent runs, NEF will look for a <config>.SAV file
                and use the information in it to attempt again the
                creation of the file attaches.
                If the .BSY file is not found, it is created, the file
                attach is built, then the .BSY is erased.
                The name of the .BSY file is the same as a file attach
                to the same node: only the extension changes.
        
            Warning: The .BSY method has a nasty drawback: if the
                process that has created a .BSY file hangs or is
                shutdown abruptly, the .BSY file remains in its outbound
                directory, so that no other process will gain access to
                that node until somebody erases the .BSY file.
                It is advisable to delete *.BSY from the most used
                outbound directories at startup (in autoexec.bat (Dos)
                or startup.cmd (OS/2)).
        
        
        TicAreaCfg <filename>
        
                This defines the name of the file that contains all the
                file area definitions. See the "FileArea" keyword below
                for a description of the syntax.
        
                This keyword is optional: if you omit it, you can define
                your file areas directly in the .cfg file, provided you




                put all the FileArea statements _after_ the FileLink
                statements, at the end of the .cfg file.
        
                For systems with few areas the one-file configuration is
                handy, for systems with many areas and links, the
                separate file solution is recommended.
        
                Please note that the TicAreaCfg file can contain
                FileArea statements and comments ONLY.
        
            Example:
        
                TicAreaCfg c:\max\ticarea.cfg
        
        
        
                                 TIC Processing
        
        
        KeepSeenby
        
                If it is commented out, the outgoing .TIC will contain
                the SeenBy of the two systems directly involved only,
                thus saving a lot of bytes.
        
                The SeenBys are not really useful since the tree
                structure of file distribution should prevent circular
                paths that could cause files to flow through the loop
                again and again.
        
                At present, NEF does not use SeenBys for internal
                processing. Anyway it will keep all the SeenBys in
                outgoing .TICs if the KeepSeenby statement is used.
        
        
        CheckCRC
        
                This enables the CRC check of ingoing .TICs.
                If an ingoing .TIC has the CRC keyword, the specified
                CRC is checked against that of the relative file and an
                error is reported in case of mismatch.
                Outgoing .TICs will have the CRC only if it is present
                in the ingoing one.
                TICs originated by NEF (Hatch or Match) will always have
                the CRC keyword.
        
        
        Touch
        




                Ingoing files are "touched" while being moved to their
                destination directory (i.e. their timestamps are set to
                NOW, so that they will be seen as new files by all the
                utilities that use the file date-time to compute the age
                of files).
        
            Warning: The original file timestamp is lost and the
                downlinks will receive the forwarded files with the new
                timestamps.
        
        
        NewAreasPath <rootdir>
        NewAreasFrom <address> [#<aka>]
        
                <rootdir> is the base directory for new file areas
                automatically created by NEF on reception of .TICs with
                unknown area TAGs.
        
                <address> is a 4D address that must be enabled to
                automatically create new areas.
        
                <aka> is the optional from-address to be used by NEF in
                outgoing .TICs for the areas automatically created by
                <address>.
        
                Any number of NewAreasFrom statements can be used.
        
                While adding new areas, NEF will NOT re-order the
                existing ones, anyway it will respect an existing
                alphabetical order while adding the new entries.
        
            Example:
        
                NewAreasPath c:\file
                NewAreasFrom 2:331/110
                NewAreasFrom 9:1/1 #9:999/999.9
        
                Let's suppose we have received a .TIC for area NEWAREA,
                which is not currently defined:
                - if it is coming from an address different from
                  2:331/110 and 9:1/1 -> an error is reported.
                - if it is coming from 2:331/110 -> a new area is
                  created with path c:\file\NEWAREA.
                - if it is coming from 9:1/1 -> a new area is created
                  with path c:\file\NEWAREA and it is configured so that
                  NEF will use 9:999/999.9 (which must be an aka
                  previously defined in an Address statement) as the
                  from-address for outgoing .TICs.
        




        
        TagFwd <OrgTag> <FwdTag> <FileSpec> [<FileSpec> ...]
        
                This allows to forward files from an area to another.
        
                <OrgTag> and <FwdTag> are area TAGs.
                <FileSpec> is a file specification that accepts the OS/2
                style wildcards (?,*).
        
                All ingoing files of area <OrgTag> which match one of
                the <FileSpec> are forwarded to area <FwdTag>.
                This way you can split or merge areas.
        
            Example:
        
                TagFwd 1-Comm Bbs AC*n prova.*
                TagFwd 1-Data bbs *
                TagFwd 1-DITO BBS *
                TagFwd 1-Comm BBO *
                TagFwd ISNMAIN POINTLST ptlist.* ptdoc.*
        
                Files AC*n and prova.* coming from area 1-Comm and all
                the files coming from 1-Data and 1-DITO are forwarded to
                area BBS.
        
                All the files from 1-COMM are also forwarded to area
                BBO.
        
                Files ptlist.* and ptdoc.* from area ISNMAIN are
                forwarded to area POINTLST.
        
        
        BefDesc <WTAG> [<WTAG> ...] "<string>"
        
                This allows to add <string> at the head of files.bbs
                descriptions while tossing files from area TAGs that
                match one of the <WTAG> specifications.
        
                This statement is useful for people using download
                counters and/or maximus flags for free download.
        
            Example:
        
                BefDesc 1* 2* "/bt [00] "
        
                This adds "/bt [00] " at the head of files.bbs
                descriptions while tossing files from areas whose TAG
                begins with '1' or '2'.
        




        
        
                               TIC Announcements
        
        
        Each announcement area is defined by a dedicated group of
        statements. Many of these statements can be used before the
        first announcement area definition to establish defaults to be
        used in all subsequent area definitions, thus avoiding the need
        to unnecessarily repeat common statements.
        
        === Statements that can be used before area definitions to set
        === defaults (please note that all these statements can be
        === overridden in each area definition).
        
        
        FromNode <address>
        
                This specifies the 4D address to be used as the
                from-address in the announcement messages: it is used in
                the header, in the Origin and in the MSGID. Usually, it
                should be your primary address.
        
            Example:
        
                FromNode     2:332/504.0
        
        
        ToNode <address>
        
                This specifies the 4D address to be used as the
                to-address in the announcement messages: it is used in
                the header. Usually, for echo area announcements, it
                should be the same as in FromNode.
        
            Example:
        
                ToNode       2:332/504.0
        
        
        From <name>
        
                This specifies the name to be used as the from-name in
                the announcement messages. Usually it should be the
                SysOp name.
        
            Example:
        
                From         Alberto Pasquale




        
        
        To <name>
        
                This specifies the name to be used as the to-name in the
                announcement messages. Usually it should be "All".
        
            Example:
        
                To           All
        
        
        Subj <subject>
        
                This specifies the string to be used as the subject in
                the announcement messages.
        
            Example:
        
                Subj         New Echo Files
        
        
        Attr [P][K][C|H|D|N|O]
        
                This specifies the attributes to be used in the
                announcement messages. Usually no special attribute is
                necessary, except for private announcements in the
                netmail area.
        
                The available attributes are:
                P -> Private
                K -> Kill/Sent
                C -> Crash
                H -> Hold
                D -> Direct (equivalent to "CH")
                N -> Normal (default)
                O -> Normal (default)
        
                The required attributes can be listed in any order and
                are not case sensitive.
        
            Examples:
        
                Attr            ; no attributes
                Attr N          ; no attributes (Normal flavour)
                Attr PK         ; Private and Kill/Sent
                Attr PC         ; Private and Crash
                Attr PDK        ; Private, Direct, and Kill/Sent
        




        
        Prefix <filename>
        
                This specifies the file containing the prefix text for
                announcement messages: it is put by NEF at the head of
                the message body, just before the real announcement
                lines. It should usually contain something like "New
                Echo Files Received:".
        
            Example:
        
                Prefix       c:\max\PREFIX.NEF
        
        
        Suffix <filename>
        
                This specifies the file containing the suffix text for
                announcement messages: it is put by NEF at the end of
                the message body, just before the tear-line and the
                Origin. It should usually contain something like "File
                Request open to everybody between 06:00 and 23:00 GMT".
        
            Example:
        
                Suffix       c:\max\SUFFIX.NEF
        
        
        Origin <origin>
        
                This specifies the text to be used as the Origin in
                announcement messages. NEF will add the required " * "
                at the head and the address at the end, truncating
                <origin> if necessary to fit the 79 character maximum
                length.
                To disable the Origin (e.g. in netmail area) use an
                empty origin string.
        
            Examples:
        
                Origin       <VIDEL BBS Modena Italy><Tel.+39-59-450643>
                Origin       ; empty origin to disable origin generation
        
        
        === End of statements that can be used before area definitions
        === to set defaults. All the preceding statements can be used
        === both before announcement area definitions (to set defaults)
        === and inside each of these definitions to override the
        === defaults.
        




        
        AreaPath <path> [-$]
        
                This starts the definition of an announcement area.
                <path> is the directory for the *.MSG format or the
                full filename (no extension) for the Squish format.
                The optional -$ specifies the use of the Squish format.
        
                Any of the statements described above in this "TIC
                announcements" section can be used after the AreaPath
                statement to override the defaults for this announcement
                area only.
        
                Please note that you can use different AreaPath
                definitions with the same message area path, in order to
                announce different file areas in different messages but
                in the same message area.
        
            Examples:
        
                AreaPath     d:\msg\swn     ; path for *.MSG
                AreaPath     d:\msg\swn -$  ; files d:\msg\swn.* for
                                            ; Squish format
        
        
        Announce <WTAG> [<WTAG> ...]
        NoAnnounce <WTAG> [<WTAG> ...]
        
                This defines the list of file areas to be announced in
                the current announcement message area (the one defined
                by the last AreaPath statement).
        
                All the TAGs that match one of the <WTAG> in "Announce"
                and do not match any of the <WTAG> in "NoAnnounce" are
                announced in the area defined by the previous AreaPath.
                Obviously you can omit the "NoAnnounce" statement if you
                do not need to exclude areas that have been included via
                the "Announce" statement.
        
                There are two special TAGS that can be used in the
                "Announce" statement: "<BAD>" and "<DEF>".
        
                "<BAD>" is used to announce all the TICs that have been
                processed with some error.
        
                "<DEF>" is used to announce all the files that have not
                been announced elsewhere. A separate announcement is
                generated after all other announcements have been
                completed, even if "<DEF>" is listed together with other




                TAGs.
        
            Examples:
        
                Announce UTILNET SOFTDIST SDS*
                NoAnnounce SDSOTH
        
                This announces the file areas with tag "UTILNET",
                "SOFTDIST" and all those whose TAG starts with "SDS" but
                "SDSOTH".
        
                Announce PRIVFILE <BAD> <DEF>
        
                This announces area "PRIVFILE" and all the TICs that
                have been processed with errors; at the end, in a
                separate message, it announces the files that have not
                been announced elsewhere.
        
            Complete example of the announcement definition section:
        
          ; Defaults definition
        
            FromNode     2:332/504.0
            ToNode       2:332/504.0
            From         Alberto Pasquale
            To           All
            Subj         New Echo Files
            Attr
            Prefix       PREFIX.NEF
            Origin       <VIDEL BBS Modena><Tel.+39-59-450643>
            Suffix       SUFFIX.NEF
        
          ; Announcement areas: each statement is local to the preceding
          ; AreaPath and overrides the default one.
        
            AreaPath     d:\msg\swn
            Announce     UTILNET
            Subj         UTILNET file news
        
            AreaPath     d:\msg\msd_news -$
            Announce     UTILNET
            Subj         UTILNET file news
        
            AreaPath     d:\msg\swn
            Announce     FIDONEWS SDS* ECHO-* FTSC NEWSLETR SOFTDIST
            NoAnnounce   ECHO-R*
            Subj         SDS/NEWS file news
        
            AreaPath     d:\msg\swn




            Announce     SDN* 1-*
            Subj         SDN file news
        
            AreaPath     d:\msg\net     ; Netmail to the SysOp
            Announce     NODE* POINTLST <BAD> <DEF>
            Origin                       ; No Origin for netmail !
            Subj         Reserved file news
            Attr         PK      ; This must be private and kill/sent
            From         NEF
            To           Alberto Pasquale
            ToNode       2:332/504.1
        
        
        
                                   Link Robot
        
        
        It's the traditional "Raid" or "TicFix" function: it allows
        downlinks (but also special uplinks) to link/unlink file areas
        via a netmail message.
        
        The message should have the agreed password as the subject,
        possibly followed by the "-L" and/or "-Q" switches.
        The required password is that defined in the "FileLink"
        statement described below.
        
        The -L switch requests a "help file" that will be sent in the
        answer message and that usually contains information about the
        available areas and/or details about commands available for the
        Link Robot.
        
        The -Q switch requests a list of available area TAGS. The reply
        informs about the areas linked and the type of link available
        for linked and linkable areas.
        
        The body of the message contains the link/unlink commands.
        There can be several commands on a single line provided they are
        separated by blanks.
        
        The available commands are:
            [+]<WTAG>
                Adds all the areas whose TAG matches <WTAG>.
                The '+' character is optional but it is essential when
                <WTAG> starts with the '-' character.
            -<WTAG>
                Deletes all the areas whose TAG matches <WTAG>.
        
        
        Example:




        
                From: John Doe of 2:332/580.0
                To:   Raid     of 2:332/504.0
                Subj: Secret -Q -L
                -----------------------------
                1* -1-COMM
                +2*
                -2-WINDOW
                ---
        
                Adds all areas whose tag begins with '1', deletes area
                "1-COMM", adds all areas whose tag begins with '2',
                deletes area "2-WINDOW"
        
        Notes:  The actual order of command execution is based on the
                area definition order. NEF scans the defined areas from
                the first one to the last one only once, applying for
                each area all the pertinent commands.
        
                If a link in a FileArea statement is not properly
                defined in a FileLink statement, it is removed when the
                Link Robot re-writes that FileArea statement in
                execution of an Add or Delete command.
        
                While re-writing areas, the Link Robot will NOT re-order
                the links. However it will respect an existing order
                while adding new links.
        
        
        AutoLink <name>
        
                The robot will answer to the messages addressed to one
                of the addresses defined in the "system" section and to
                one of the names defined in the AutoLink statements.
                You can use as many AutoLink statements as you need to
                define all the akas you like.
                If no AutoLink statement is used, then the Link Robot is
                disabled.
        
            Example:
        
                AutoLink NEF
                AutoLink Raid
                AutoLink TicFix
        
        
        NetMail <path> [-$]
        
                This defines a netmail area to be searched for messages




                addressed to the robot. You can use as many NetMail
                statements as you need, one for each of your "physical"
                netmail message areas (if you have two or more "logical"
                netmail areas pointing to the same path, you can use a
                unique NetMail statement).
        
                The optional -$ indicates a Squish format area.
        
                No "primary address" specification is needed, since NEF
                always uses the destination address of the message
                addressed to the robot as the from-address for replies.
        
            Example:
        
                NetMail d:\msg\fidonet -$  ; Fidonet netmail area
                NetMail d:\msg\amiganet -$ ; Amiganet netmail area
        
        
        KillReceived
        
                This keyword instructs NEF to kill messages addressed to
                the Link Robot after the execution of the contained
                commands. When commented out, the messages are marked as
                received instead of being erased.
        
        
        AreaList <filename>
        
                This keyword defines the file to be put into the Link
                Robot's answer in reply to the "-L" switch that can be
                used in the subject of the message to the Link Robot.
                Usually this file contains information about the
                available areas and/or instructions for using the Link
                Robot.
        
            Example:
        
                AreaList c:\max\ticarea.lst
        
        
        ProtArea <WTAG> <level>[/<keys>]
        
                This keyword allows to selectively protect areas from
                automatic linking. Unlinking is always possible.
        
                The protection scheme is based on the traditional
                combination of level and keys.
        
                <WTAG>  specifies the TAG or group of TAGs to be




                        protected.
                <level> is an integer number in the range 0-65535.
                <keys>  is a subset of the following 32 element set:
                        {12345678ABCDEFGHIJKLMNOPQRSTUVWX}
                        These keys are case insensitive.
        
                When processing an area TAG, NEF scans the ProtArea
                statements from the first one to the last one: the first
                matching <WTAG> determines the protection level and
                keys. If no match is found, <level> is assumed to be the
                maximum and <keys> the full set of available keys, so
                that the area gains maximum protection.
        
                Usually it's convenient to override the default maximum
                protection so that you can list only a few special areas
                with their protection level and keys while letting all
                the others get a default NULL protection (automatic
                linking for everybody). To accomplish this result, you
                can use a "ProtArea * 0" as the last ProtArea statement.
        
                Please, note that the order of the ProtArea statements is
                _essential_, since they area scanned from the first one
                to the last one in search for a match between the TAG in
                examination and the <WTAG> of the ProtArea statements.
        
            Example:
                ProtArea PRIVATE  1000/12ABC  ; Protected private area
        
                ProtArea 1*       100/P       ; Areas starting with '1'
                                              ; are not for everybody.
        
                ProtArea *        0           ; The remaining areas are
                                              ; for everybody.
        
        
        FileLink <address> <password> [#<address>] <flags>
                 [<attr> [<level>[/<keys>] [<WTAG> ...]]]
        
                The parameters of this keyword have been represented on
                two lines because of space, but they MUST be listed on a
                unique line in the .cfg file.
        
                This keyword defines a file link; you must use a
                FileLink statement for each of your links (both
                downlinks and uplinks).
        
                <address>  is the 4D address of the link.
        
                <password> is the case insensitive password to be used




                           for all TIC exchanges and for the Link Robot
                           function. NEF has no limit for the password
                           length, anyway you should be aware that other
                           similar programs could have limits, so check
                           with your downlink/uplink before choosing a
                           long password (8 characters should be OK for
                           everyone).
        
                #<address> This optional field indicates a 4D address to
                           be used as the primary address for the .TICs
                           sent to this link (overrides the global
                           primary address and, if present, the local
                           area override (see FileArea)).
        
                <flags>    This field is a (case insensitive) set of
                           characters:
        
                           <H|C|D|N|F>[<S|T>][<I|O|*>].
        
                           It can be 1 to 3 characters long:
        
                         - The first flag is mandatory; it defines the
                           flavour of the file-attaches that NEF will
                           create for .TIC and associated files.
        
                           Please note that this flag can be overridden
                           on a per-area basis by prefixing the link
                           address with a new flavour-flag in the
                           FileArea statement.
        
                           The available choices for this flag and the
                           consequent file-attach extension follow:
        
                           H -> .HLO (Hold)
                           C -> .CLO (Crash)
                           D -> .DLO (Direct)
                           F -> .FLO (Normal)
                           N -> .FLO (Normal)
        
                           The 'N' flag is provided for "compatibility",
                           but it's the same as 'F'.
        
                         - The second flag is optional: it defines
                           whether NEF must send a .TIC together with
                           the file or not.
        
                           S -> .TIC sent (default).
                           T -> .TIC not sent.
        




                           Usually the default is used (this flag can be
                           omitted), but sometimes points like not
                           receiving the .TIC file.
        
                           Please note that this flag can be overridden
                           on a per-area basis by prefixing the link
                           address with a new flag in the FileArea
                           statement.
        
                         - The third flag is optional. It is provided
                           for completeness and it is sometimes very
                           handy, but it is recommended not to use it
                           too often since its use could unnecessarily
                           complicate the interpretation of the
                           configuration.
        
                           It defines whether this link has
                           bidirectional access to file areas or not.
        
                           This is an override to the "area direction"
                           field of each FileArea definition.
        
                           Please note that this flag can be overridden
                           on a per-area basis by prefixing the link
                           address with a new flag in the FileArea
                           statement.
        
                           I -> Only Input is allowed from this link.
                                NEF will not send files.
                           O -> Only output is allowed to this link.
                                NEF will not accept files.
                           * -> Bidirectional link.
        
                <attr>     These are the (case insensitive) attributes
                           for the Link Robot's netmail replies:
        
                           K -> Kill/Sent
                           C -> Crash
                           H -> Hold
                           D -> Direct (equivalent to "CH")
                           N -> Normal (default)
                           O -> Normal (default)
        
                           The Private attribute is always implied.
        
                           ATTENTION: you should usually use the 'H'
                           attribute for file links that are not netmail
                           links too. Otherwise the "Normal" flavoured
                           netmail replies will be routed as per your




                           routing configuration instead of being holded
                           for the file link.
        
                <level>    This is an integer number in the range
                           0-65535 and represents the access level to
                           the Link Robot for this node. Defaults to 0.
        
                           If it is greater or equal to the protection
                           level of a certain file area, then this node
                           can link the area via the Link Robot,
                           provided it has the necessary keys.
        
                <keys>     is a subset of the following 32 element set:
                           {12345678ABCDEFGHIJKLMNOPQRSTUVWX}
                           and represents the (case insensitive) access
                           keys to the Link Robot for this node.
        
                           If <keys> contains all the keys that protect
                           a certain area, then the node can link the
                           area via the Link Robot, provided it has a
                           sufficient access level.
        
                <WTAG>     The optional list of <WTAG>s specifies the
                           area TAGs that must be automatically linked
                           to this node when they are automatically
                           created by NEF.
        
                           NEF can create new areas when unknown TAGs
                           are found in ingoing .TICs (see NewAreasFrom
                           above in this reference). With the <WTAG>
                           list in the FileLink statement, you can make
                           NEF automatically link some nodes to areas
                           whose TAGs begin with certain strings.
            Examples:
        
              - FileLink 2:332/593 pwd593 IN
        
                Node 2:332/593 has password "pwd503", is enabled to send
                .TICs to us ('I') and the file attaches addressed to it
                (if any) will be normal flavoured ('N').
        
                Note that file attaches to this node will only be
                possible if a local area override will be used, since
                the 'I' flag instructs NEF to accept files from the node
                but not to send to it.
        
                Nothing is specified about the Link Robot's reply flags
                and access level and keys, so this node will be able to
                link only areas with protection level 0 and no keys; the




                Robot's reply will be normal flavoured.
        
              - FileLink 2:331/196 pwd196 H NK 300/ab
        
                Node 2:331/196 has password "pwd196", nothing is
                specified about link direction (it will depend on the
                "area direction" and local overrides), the file attaches
                will be Hold flavoured ('H'), the reply netmails will be
                normal flavoured ('N') and kill/sent ('K'), the access
                level is 300 and the access keys are a,b.
        
              - FileLink 2:332/504.1 pwd1 #2:332/504 H N 900/ab MI* FW*
        
                Node 2:332/504.1 has password "pwd1", all the TICs sent
                to this node will use the primary address 2:332/504
                (even in areas with a different local override), the
                file attaches will be Hold flavoured ('H'), the netmail
                replies will be normal flavoured ('N'), the access level
                is 900 and the access keys a,b.
        
                New areas whose TAG begins with "MI" or "FW" will be
                automatically linked when they are automatically created
                by NEF.
        
        
        FileArea <TAG> <path> I|O|* [#<address>] [[<flags>]<link> ...]
        
                This keyword defines an echo file area.
        
                If you have a small system, you can put the area
                definitions in the main configuration file (e.g.
                NEF.CFG). For systems with a large number of areas and
                links, it is recommended to use a separate file for the
                area definitions: see the "TicAreaCfg" keyword, formerly
                discussed in this documentation.
        
                ATTENTION: when using the "TicAreaCfg" separated file,
                you must put ALL the FileArea statements in that file.
                You are not allowed to put area definitions both in the
                main .cfg file and in the dedicated TicAreaCfg file at
                the same time !
        
                Please note that all the FileArea statements, if
                included in the main .cfg file, MUST be defined _after_
                the FileLink statements.
        
                <TAG> is the area TAG.
        
                <path> is the directory for the file area.




        
                I|O|*  is the (case insensitive) "area direction" and
                       defines the default direction for the area:
        
                    'I': we accept files from the listed nodes but do
                         not send to them, unless an override flag is
                         present before the <link> or in the pertinent
                         "FileLink" definition.
        
                         This should usually be used for "pre" areas, in
                         which files must be collected from downlinks
                         and sent to the area coordinator via the
                         uplink, which will need a local 'O' override.
        
                    'O': we send files to the listed nodes but do not
                         accept from them, unless an override flag is
                         present before the <link> or in the pertinent
                         "FileLink" definition.
        
                         This should usually be used for areas that must
                         be distributed to downlinks. The uplink will
                         need a local 'I' override before its <link>
                         field or a global one in its FileLink
                         definition.
        
                    '*': the area is bidirectional, so we both send and
                         accept files to/from the listed nodes, unless
                         an override flag is present before the <link>
                         or in the pertinent "FileLink" definition.
        
                         This should be used for bidirectional areas, in
                         which everybody is allowed to "hatch" files.
        
                #<address>: defines the primary address to be used for
                         this area. If a node has a private address
                         override in its "FileLink" definition, that one
                         will be used in spite of this "area-level"
                         override.
        
                The list of linked nodes follows; each node can have
                some <flags> attached before the node address. The
                available flags are the same as for the <flags> field in
                the "FileLink" statement.
        
                <flags>    This is an optional (case insensitive) field
                           made up of 1 to 3 characters:
                           [H|C|D|N|F][S|T][I|O|*].
        
                         - The first flag defines the flavour of the




                           file-attaches that NEF will create for .TIC
                           and associated files.
        
                           Please note that this flag overrides that in
                           the pertinent "FileLink" statement.
        
                           The available choices for this flag and the
                           consequent file-attach extension follow:
        
                           H -> .HLO (Hold)
                           C -> .CLO (Crash)
                           D -> .DLO (Direct)
                           F -> .FLO (Normal)
                           N -> .FLO (Normal)
        
                           The 'N' flag is provided for "compatibility",
                           but it's the same as 'F'.
        
                         - The second flag defines whether NEF must send
                           a .TIC together with the file or not.
        
                           S -> .TIC sent.
                           T -> .TIC not sent.
        
                           Please note that this flag overrides that in
                           the pertinent "FileLink" statement.
        
                         - The third flag defines the direction of the
                           link.
        
                           Please note that this flag overrides that in
                           the pertinent "FileLink" statement, which in
                           turn overrides the "area direction".
        
                           I -> Only Input is allowed from this link.
                                NEF will not send files.
                           O -> Only output is allowed to this link.
                                NEF will not accept files.
                           * -> Bidirectional link.
        
                <link>     This is a 4D address, that can be abbreviated
                           whenever the preceding address has the same
                           zone, zone:net or zone:net/node.
        
                           For the first <link>, if incomplete, the
                           primary address for the area is used; anyway
                           NEF always writes the first address in
                           complete form when rewriting the area due to
                           a Link Robot command.




        
            Examples:
        
            Please note that the situation could be a little different
            from what explained below, since the FileLink definitions
            could have some overriding flags.
        
            FileArea area1 d:\file\area1 O #2:332/500 I2:332/596 C555
        
            Area "area1" in path "d:\file\area1" is a normal "up-link to
            down-links" area ('O'); we use 2:332/500 as the default
            primary address; we accept files from 2:332/596 and forward
            to 2:332/555 with a crash flavoured file attach.
        
            FileArea AREA2 d:\file\area2 O S2:332/504.1 10:10/0 *100/1
        
            Area "AREA2" in path "d:\file\area2" is a normal "up-link to
            down-links" area ('O'); 10:100/1 is the only node enabled to
            send to us (bidirectional override '*'); we forward to
            2:332/504.1 and 10:10/0. If we hatch files, we send to
            10:100/1 too, since it is bidirectional. We send the .TIC
            accompanying files to 2:332/504.1 ('S') even if it had a 'T'
            flag in its FileLink definition.
            
            FileArea Area3 d:\file\area3 I O2:5/1 3/1 332/504.2 .3
        
            Area "Area3" in path "d:\file\area3" is a reverse
            "down-links to up-link" area ('I'), we accept files from
            2:3/1, 2:332/504.2 and 2:332/504.3 and send them to 2:5/1
            ('O'). 
        
        
                                T H E   E N D