Resident Alarm Clock - ACLOCK v.1.2
                 (c) 1993 by MarkoTech, A. Danileiko
    e-mail: danileiko@vtcc1.cc.vt.edu, adanil@g386bsd.first.gmd.de

ACLOCK is a small TSR program (784 bytes in memory) that shows real time
in display upper right corner, beeps every hour and plays music at the
selected time.

                          Usage:

ACLOCK /option -color alarm_time

Possible options are:
                      U to unload the program;
                      D to disable displayed time.

COLOR is hexadecimal attribute number. Default one is 1F.

ALARM_TIME is time in form hour:minute to be set as alarm time.


It is possible to operate with the program via INT 2F:

====================== INT 2F =======================

Loading check:

Input: AX = 9200h

If ACLOCK is leaded then

Output: AX = 1234h
        ES = program CS

-----------------------------------------------------
Set attribute & disable flag:

Input: AX = 9201h
       BH = attribute
       BL = 1 to disable displaying or 0 to enable it
Output: None

-----------------------------------------------------
Set alarm time:

Input AX = 9202h
      CH = hour
      CL = minute
Output: None

-----------------------------------------------------