HOW TO CONFIGURE THE BOOKIE JOINT FOR VARIOUS COM PORT SETUPS

    The Bookie Joint now supports DigiBoard and other intelligent serial
    communications boards as well as fossil drivers.

    DIGIBOARDS
    ----------
    DigiBoards contain 4 or 8 serial ports along with their own on-board
    processor to control the ports.  These boards are actually a single-board
    computer dedicated to handling serial port I/O.

    By moving the serial I/O functions from the Host Computer to the
    DigiBoard, the IRQ and Interrupt Latency bottleneck that plagues
    Multi-Tasking users is eliminated. 

    Bookie Joint supports the DigiBoard in two ways:

    Direct Programming and INT14/EBIOS calls.

    Direct Programming is the fastest because it eliminates the need
    for costly software interrupt calls to a slower BIOS. In addition
    it does not require the presence of a Device Driver which basically
    performs the same functions as the Direct Programming method.

    INT14/EBIOS requires that a Device Driver be loaded (this driver
    is supplied by DigiBoard). Serial Port I/O is performed by issuing
    software interrupts (Interrupt 14). 

    Whether or not to use the Direct Interface or the INT14/EBIOS
    Interface depends on the BBS which will be running the Bookie Joint
    program. If the BBS is utilizing the Device Driver, then that is
    how a Bookie Joint program must be configured. If the BBS is a GAP system
    and the Sysop is using the Direct Interface, then the Bookie Joint program
    must be configred the same.

    The two interfaces can not be intermixed since the Direct Interface will
    essentially put the Device Driver to sleep.

    When using the INT14/EBIOS interface and the DigiBoard supplied Device
    Driver, it is not necessary to turn on the "Character Waiting" flags
    for each of the ports. Bookie Joint does not use these flags as they basically
    defeat the purpose of using a multi-port board in a multi-tasking
    system. To use these flags an IRQ must be dedicated to the DigiBoard.
    If the flags are not used, the IRQ need not be set.

    Imagine running 8 ports under a Multi-Tasker where all 8 ports
    are in use. As characters are received by each of the 8 ports, an
    interrupt is generated. The Device Driver must service the
    interrupt request and since the driver runs on the Host Computer,
    it will be spending a lot of precious time figuring out which of
    the ports generated the interrupt and updating its "Character
    Waiting" flag for that port.

    By disabling the "Character Waiting" flags and not utilizing the
    IRQ, the Host Computer will not know it has 8 serial ports running
    at high speed at the same time.

    If, however, the Sysop has the IRQ and Character Waiting flags enabled,
    no harm is done. Bookie Joint simply will not utilize the flags.

    The Character Waiting flags are provided because making Interrupt
    14 calls takes longer than simply checking a memory address (which,
    by the way, is what the Direct Programming interface does).


    Here are the various config file setups.

    Line 5 - The COM Port Interface to use:

               NONE      = Regular Communications Port Interface.  Use this
                           if you run COM 1 or COM 2 with standard IRQ.
                           Lines 6 thru 10 will be ignored and need not be
                           defined.

             STANDARD    = Regular Communications Port Interface. This
                           is what you would use if you run a standard
                           serial board but with non-standard IRQ or BASE
                           ADDRESS.

             DIGIBOARD   = Direct DigiBoard Programming Interface. Must
                           be used in conjunction with a program called
                           RESETDIG.EXE. If you don't have this program
                           but have a DigiBoard, then use the INT14
                           option below.

               INT14     = Indirect DigiBoard Support via a Device Driver.
                           All Communications to the DigiBoard (or any
                           board that supports INT14/EBIOS) are performed
                           via a Software Interrupt that the Device Driver
                           handles.

                 FOSSIL  = Supports most fossil drivers. (X00 is recommended)

    NOTE :  Lines 6 and above are not needed for standard and fossil setups.

    Line 6 - This is the port IRQ if NOT using the DIGIBOARD or INT14
             interface.  This line is for systems that run standard serial
             boards but with ports other than 1 or 2 or non-standard IRQ.
             If you use DIGIBOARD or INT14 then set this line to 0.

    Line 7 - This is the port base address if NOT using the DIGIBOARD or
             INT14 interface.  This line is for systems that run standard
             serial boards but with ports other than 1 or 2.
             If you use DIGIBOARD or INT14 then set this line to 0.

    Line 8 - This is the DigiBoard Memory Window, or the address the
             card uses as a communications area between the card and
             the Host Computer. Only needed if using an Interface set
             to DIGIBOARD. If using STANDARD or INT14/EBIOS, this can
             be set to 0. This address must be entered in Hexadecimal.

             Valid entries are: C000, C800, D000, and D800

    Line 9 - This is the DigiBoard I/O Port address that the Board is
             attached to. Only needed if using an Interface set to
             DIGIBOARD. If using STANDARD or INT14/EBIOS, can be set
             to 0. This address must be entered in Hexadecimal.

             Valid entries are: 100, 110, 120, 200, 220, 300 and 320

   Line 10 - This is the DigiBoard Channel Number for the port this
             program will be utilizing. This is REQUIRED for DIGIBOARD
             and INT14/EBIOS Interfaces. This is 1 - 8 for the
             DIGIBOARD Interface and usually 4 - 11 for the INT14/EBIOS
             Interface. This number tells the program which of the 
             Com Ports on the DigiBoard it should use.

    The new configuration file for a Bookie Joint that will be using a
    DigiBoard Serial port would look like the following:

    BOOKIE.CFG w/Interrupt 14 interface
    -----------------------------------
    C:\GAP
    No Anchovies PC
    GAP
    0000
    INT14
    4
    03F8
    D000
    320
    4

    Lines 6 and 7 are ignored by the program and can be set to 0. 
    Because this is an INT14/EBIOS interface, lines 8 and 9 are also
    ignored. Line 10 is the Channel Number and in this case, it is the
    first serial port on the DigiBoard (Channel Numbers 1 - 4 are
    generally reserved for COM 1 - COM 4 on the Host Computer, although
    this is up to the Sysop and how he/she configured the Device Driver).


    To use the Direct Programming Interface, the configuration file
    would look something like:

    BOOKIE.CFG w/DigiBoard direct interface
    ---------------------------------------
    C:\GAP
    No Anchovies PC
    GAP
    0000
    DIGIBOARD
    4
    03F8
    D000
    320
    1

    Lines 6 and 7 are ignored by the program and can be set to 0. 
    Line 8 is the Memory Window that the DigiBoard and the program
    use to communicate with each other. Line 9 is the I/O port that
    the board uses. Line 10 is the Channel Number which, in this case,
    is the first serial port on the DigiBoard.


    To use the Standard COM Port Interface with ports other than 1 or 2
    or with non-standard IRQs, the configuration file would look something
    like:

    BOOKIE.CFG w/standard interface
    -------------------------------
    C:\GAP
    The Crow's Nest BBS
    GAP
    0000
    STANDARD
    4
    03F8
    0
    0
    0

    Line 6 is the port number and  Line 7 is the IRQ. Line 5 tells the program
    to use its own internal interrupt handler. Lines 8-10 are not used and
    can be set to 0.  Note that even if the DigiBoard specific options are
    not used or needed they must still be present in the Configration File.


    To use the Standard Com Port Interface with ports 1 or 2 and standard
    IRQ, the configuration file would look something like:

    BOOKIE.CFG w/Normal setup
    -------------------------
    C:\GAP
    No Anchovies PC
    GAP
    0000
    NONE


    To use a fossil driver with the Bookie Joint the configuration file
    would look like this:

    BOOKIE.CFG w/fossil support
    ---------------------------
    C:\GAP
    No Anchovies PC
    GAP
    0000
    FOSSIL