VERSAMAP (version 1.51)
                                 15 November 1995
        
                    Copyright 1991-1995 by Charles H. Culberson
                                   8 Ritter Lane
                              Newark, Delaware  19711
                                      U.S.A.
        
        
                          Phone: 302-731-0694
                       Internet: 70511.3134@compuserve.com
                     CompuServe: 70511,3134
        
        
                 CONTENTS                                           PAGE
        
         1.      Introduction                                         2
         1.1.    Computer Requirements for Running VERSAMAP           3
         1.2.    Disclaimer                                           3
         1.3.    Registration                                         3
         1.4.    Plotting the Default World Map                       4
         1.5.    Finding your Way with Latitude and Longitude         5
         1.6.    Keys with Special Functions in VERSAMAP              6
         1.6.3.  Exit the program                                     6
        
         2.      Running VERSAMAP                                     9
         3.      Projection menu                                     10
         4.      Map Design menu                                     16
         5.      Input/Output menu                                   32
         6.      Run menu                                            41
        
         7.      Sources of Digital Map Data for use with VERSAMAP   42
         7.1.    World Data Bank II                                  42
         7.2.    Micro World Data Bank II                            46
         7.3.    VERSAMAP Micro World Database                       47
         7.4.    USGS Digital Line Graph Data                        47
         7.7.    Importing Your Own Data into VERSAMAP               52
        
         8.      Use of VERSAMAP with Graphing Programs              55
        
         9.      Program Compatibility with Software and Hardware    56
         9.1.    Running VERSAMAP under Windows                      56
        
        10.      Installing VERSAMAP                                 57
        11.      VERSAMAP Order Form                                 58
        12.      Acknowledgements                                    61
        13.      Glossary                                            62
        14.      References                                          65
        15.      Index                                               66
        
        
        
        


        VMAP.DOC version 1.51                                    Page  1 






        1.        Introduction
        
        Welcome to VERSAMAP, a versatile mapping program for drawing outline
        maps on 14 different map projections.  Maps can be printed on dot
        matrix or laser printers; and exported as PCX, CGM, DXF, PIC, or
        ASCII files, for use with paint programs, word processors, and
        presentation or technical graphics programs.  VERSAMAP is supplied
        with Courier and Helvetica fonts which allow text to be added to
        maps displayed on the screen.
        
        The shareware version of VERSAMAP contains the following files:
        
           VMAPREAD.ME  --  how to get started
              VMAP.EXE  --  the mapping program
             VMAP4.MAP  --  digital map of the world (16,000 points)
              VMAP.DOC  --  instruction manual
          REGISTER.DOC  --  order form
        
          VMTAIWAN.PKV  --  sample map of Taiwan from World Data Bank II
            VMOAHU.GRV  --  sample map of Oahu from USGS DLG database
          VMAPUSER.PRN  --  ASCII file containing latitude, longitude data,
                            study this file to learn how to plot your own
                            data with VERSAMAP
          VMAPUSER.UTM  --  ASCII file containing coordinates in meters,
                            study this file to learn how to plot your own
                            UTM data with VERSAMAP
        
            VM_FIX.MPS  --  utility file used to concatenate World
                            Digitized binary map files
            VM_FIX.MP1  --  utility file used to concatenate World
                            Digitized ASCII map files.
        
          VMVENDOR.DOC  --  information for shareware vendors
          VENDINFO.DIZ  --  information for shareware vendors
           FILE_ID.DIZ  --  information for BBS operators
        
          COUR_EGA.FON  --  fixed-space Courier font for EGA
          COUR_VGA.FON  --  fixed-space Courier font for VGA
        
        
        The following additional files are supplied with the registered
        version of VERSAMAP:
        
          HELV_EGA.FON  --  proportional Helvetica font for EGA
          HELV_VGA.FON  --  proportional Helvetica font for VGA
        
             VMAP3.MAP  --  digital map of the world (31,000 points)
             VMAP5.MAP  --  digital map of the world  (6,000 points)
        
            VMCITY.PRN  --  ASCII file that can be plotted from VERSAMAP
                            containing positions and names of 606 world
                            cities
        


        VMAP.DOC version 1.51                                    Page  2 






        Additional, more detailed maps are also available; see Section 7 for
        details.  Please make backup copies of the VERSAMAP distribution
        disks before running the program.
        
        
        1.1.      Computer Requirements for Running VERSAMAP
        
             MS-DOS 3.0 or higher;
             EGA or VGA;
             640K memory;
             hard disk.
        
        A math coprocessor is not required to run VERSAMAP but the program
        will run 3-4 times faster if one is installed.
        
        VERSAMAP will not change your AUTOEXEC.BAT or CONFIG.SYS files, it
        will not alter your keyboard settings, and it will not write any
        files to disk without your permission.
        
        Instructions for installing VERSAMAP are given in the file
        VMAPREAD.ME on the VERSAMAP distribution disk.
        
        
        1.2.      Disclaimer
        
        Users of VERSAMAP must accept this disclaimer of warranty:
        
        "VERSAMAP is supplied as is.  The author disclaims all warranties,
        expressed or implied, including, without limitation, the warranties
        of merchantability and of fitness for any purpose.  The author
        assumes no liability for damages, direct or consequential, which may
        result from the use of VERSAMAP."
        
        Do not use this program for navigation!  Use the proper aeronautical
        or nautical charts for navigation.
        
        
        1.3.      Registration
        
        Shareware distribution gives users a chance to try software before
        buying it.  VERSAMAP is a "shareware program" and is provided at no
        charge to the user for evaluation.  If you find this program useful
        and find that you continue to use VERSAMAP after a reasonable trial
        period, you must register the program.  The registration fee will
        license one copy for use on any one computer at any one time.  You
        must treat this software just like a book.  An example is that this
        software may be used by any number of people and may be freely moved
        from one computer location to another, so long as there is no
        possibility of it being used at one location while it's being used
        at another.  Just as a book cannot be read by two different persons
        at the same time.
        
        


        VMAP.DOC version 1.51                                    Page  3 






        Registration of the program is $15 for which you will receive a copy
        of the most recent version of the program; Helvetica fonts for EGA
        and VGA; the additional digital map files VMAP3.MAP (31,000 points)
        and VMAP5.MAP (6,000 points); and a gazetteer, VMCITY.PRN,
        containing the names and positions of 606 major world cities. 
        Registration entitles you to support by mail, telephone, and
        electronic mail, concerning problems you encounter with VERSAMAP. 
        An order form is included in the file REGISTER.DOC, and in Section
        11 of this manual.
        
        You are encouraged to share a copy of VERSAMAP with your friends for
        evaluation.  Please encourage them to register their copy if they
        find it useful.
        
        This program is produced by a member of the Association of Shareware
        Professionals (ASP).  ASP wants to make sure that the shareware
        principle works for you.  If you are unable to resolve a
        shareware-related problem with an ASP member by contacting the
        member directly, ASP may be able to help.  The ASP Ombudsman can
        help you resolve a dispute or problem with an ASP member, but does
        not provide technical support for members' products.  Please write
        to the ASP Ombudsman at 545 Grover Road, Muskegon, MI 49442-9427,
        USA; FAX 616-788-2765; or send a CompuServe message via CompuServe
        Mail to ASP Ombudsman 70007,3536.
        
        
        1.4.      Plotting the Default World Map
        
        Before reading the rest of the manual, let's plot a map of the
        world.  This will familiarize you with the operation of VERSAMAP. 
        The rest of the manual should make more sense once you have actually
        used VERSAMAP.
        
        VERSAMAP has built in defaults which plot a world map, from 90 N to
        90 S latitude, and from 180 W to 180 E longitude, on an
        Equirectangular projection.  The default settings will not print any
        files to disk.
        
        To run VERSAMAP with the default settings:
        
         1.  change to the drive and directory containing VERSAMAP;
         2.  type VMAP;
         3.  press the Enter key.
        
        A screen with a menu bar across the top will appear once the program
        has loaded.  The pull-down menus are selected by pressing the Alt
        key, followed by the highlighted letter of the desired menu; or by
        pointing and clicking the left mouse button.
        
        To plot the world map:
        
         1.  press the Alt key, to access the menus
         2.  press R, to select the Run menu
         3.  press Enter, to select the Size 100% option and begin the plot.

        VMAP.DOC version 1.51                                    Page  4 






        When the map begins plotting, the top line of the screen will
             display (1) a reminder that pressing the Esc key will terminate
             plotting and return you to the menu bar; (2) the name of the map
             input file being read, VMAP4.MAP in this case; and (3) the number of
             points which have been read from the input file, VMAP4.MAP.
        
        The menu bar will reappear when the map is finished plotting.  The
        default map takes 11 seconds to plot on a 33 MHz 486 computer.
        
        To exit the program and return to DOS:
        
         1.  press the Esc key, to halt plotting;
         2.  press the Alt key, to access the menus;
         3.  press P, to select the Projection menu;
         4.  press X from the Projection menu to exit the program.
        
        Pressing the Esc key halts program execution and returns you to the
        menu bar.  Pressing Esc will not exit the program.
        
        Please read the rest of the instruction manual before attempting to
        plot maps which do not use the default parameters.
        
        
        1.5.      Finding your Way with Latitude and Longitude
        
        To use this program you should be familiar with the concepts of
        latitude and longitude.
        
        Latitude is the angular distance (in degrees) of a point on the
        earth's surface north or south of the equator.  The maximum values
        of latitude are 90 N (north pole) and 90 S (south pole).  The
        equator is 0 N/S latitude.
        
        Longitude is the angular distance (in degrees) of a point on the
        earth's surface east or west of the meridian that passes through
        Greenwich, England.  The maximum values of longitude are 180 W and
        180 E (the international date line).  The meridian passing through
        Greenwich is 0 E/W longitude.
        
        Latitude and longitude values in VERSAMAP are entered as degrees,
        minutes, seconds.  There are 60 seconds in 1 minute, and 60 minutes
        in 1 degree.  One degree of latitude is equal to 60 nautical miles
        (1 nautical mile = 6080 feet = 1.8532 kilometers = 1.1515 statute
        miles).  One minute of latitude is equal to 1 nautical mile.  One
        second of latitude is equal to 101 feet (31 meters).
        
        For example, the position for Rio de Janeiro, Brazil, written as
        degrees, minutes, and seconds (22 degrees, 53 minutes, 43 seconds
        south latitude; 43 degrees, 13 minutes, 22 seconds west longitude)
        is,
        
        
        


        VMAP.DOC version 1.51                                    Page  5 






                                           Deg Min Sec
        
                             latitude   =   22  53  43  S
                             longitude  =   43  13  22  W
        
        
        The position for Paris, France (48 degrees, 50 minutes, 14 seconds
        north latitude; 2 degrees, 20 minutes, 14 seconds east longitude)
        is,
        
                                           Deg Min Sec
        
                             latitude   =   48  50  14  N
                             longitude  =   02  20  14  E
        
        
        If you are unfamiliar with the use of latitude and longitude to
        locate points on the surface of the earth, please consult an
        encyclopedia or an atlas.
        
        
        1.6.      Keys with Special Functions in VERSAMAP
        
        
        1.6.1.    Esc
        
        Pressing the Esc key halts program execution and returns you to the
        menu bar.  Pressing Esc will not exit the program.
        
        If you are in the process of plotting or printing a map, the program
        checks the Esc key each time the record number or point, shown in
        the upper right corner of the screen, is updated.  Consequently, the
        program may take several seconds to respond after Esc is pressed.
        
        
        1.6.2.    Alt
        
        Pull-down menus are selected by pressing the Alt key, followed by
        the highlighted letter of the desired menu.  Individual menu items
        are selected by pressing the highlighted letter of each item; by
        moving through the menu with the up or down cursor keys, and then
        pressing Enter to select the item; or by moving the mouse cursor
        over the desired item and pressing the left mouse button.
        
        
        1.6.3.    Exit the program
        
        To exit the program and return to DOS:
        
         1.  press the Esc key, several times if necessary, to halt plotting
             or erase the current window(s);
         2.  press the Alt key, to access the menus;
         3.  press P, to select the Projection menu;
         4.  press X from the Projection menu to exit the program.

        VMAP.DOC version 1.51                                    Page  6 






        If a window is on the screen or a map is in the process of being
             drawn, you must press Esc before you can access the menus and exit
             the program.
        
        
        1.6.4.    Letter B
        
        Pressing the letter B erases the menu bar and changes the background
        color of the menu bar to the background color of the map.  This
        feature is useful if you use a screen-capture program to save maps
        displayed on the screen.  You must press B a second time, or press
        Esc, to redisplay the menu bar and reactivate the pull-down menus.
        
        
        1.6.5.    Letter T
        
        Pressing the letter T toggles the menu bar on and off; and replaces
        it with the name of the current projection, and the time taken to
        draw the current map.  You must press T a second time, or press Esc,
        to redisplay the menu bar and reactivate the pull-down menus.
        
        
        1.6.6.    Using a mouse
        
        Most VERSAMAP features can be accessed by pointing and clicking the
        left mouse button.  Windows and pull-down menus can be closed by
        clicking the left mouse button when the mouse cursor is outside the
        window or menu box.
        
        
        1.6.7.    Moving around windows
        
        The windows which pop up when menu selections are made contain
        several types of items: (1) input fields; (2) vertical list boxes;
        and (3) pushbuttons.
        
        Input fields allow numeric and alphabetic input into the program. 
        An example of a window with numeric input fields is the LATITUDE AND
        LONGITUDE LIMITS window displayed after selecting the Map Boundaries
        option in the Map Design menu.  You can move within an input field
        with the right, left, Home, and End cursor keys.  To enter data into
        an input field, type the correct characters from the keyboard, and
        press Enter.  Use the Tab key to move between lines in this window.
        
        Vertical list boxes allow one or more items in a list to be chosen. 
        An example of a window with a vertical list box is the SELECT MICRO
        WORLD DATA BANK II FEATURES window displayed after selecting the
        Geographic Features option in the Map Design menu.  Move through the
        list with the up and down cursor keys, and select the correct
        item(s) by pressing the Space Bar or Enter.  The item(s) selected
        will be highlighted or indicated with a checkmark.
        
        


        VMAP.DOC version 1.51                                    Page  7 






        If the number of items in the list is too large to fit inside the
        box, a scroll bar will appear along the right side of the box,
        allowing all items to be viewed.
        
        Pushbuttons, indicated by text inside brackets, such as < ok >,
        allow the user to control program execution.  An example of a window
        with a pushbutton is the LATITUDE AND LONGITUDE LIMITS window
        displayed after selecting the Map Boundaries option in the Map
        Design menu.  The text inside the brackets indicates the action to
        be taken when the pushbutton is selected.  The brackets of the
        currently active pushbutton are highlighted, and its text is shown
        in all capital letters.  To select a pushbutton, tab to that button
        and press Enter.
        
        Use the Tab key to move between items when more than one list box or
        pushbutton occur in a window.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  8 






        2.        Running VERSAMAP
        
        Each map projection in VERSAMAP has built in latitude/longitude
        defaults which are active the first time you access the projection
        during each session with VERSAMAP.  These defaults allow you to plot
        maps using each map projection without getting error messages.  The
        defaults are only active the first time you access a particular map
        projection.  For instance, if you access the Mercator projection,
        then the Equirectangular projection, and then return to the Mercator
        projection, the latitude limits of the grid will be those of the
        previous Equirectangular projection, 90 N/S, and you will get an
        error message if you attempt to plot a Mercator projection without
        changing the grid.
        
        Sections 3 through 6 provide a detailed discussion of each VERSAMAP
        pull-down menu.  For your first experience with VERSAMAP you should
        run the program with its default settings (see Section 1.4).
        
        When VERSAMAP is started, the following menu bar appears at the top
        of the screen.
        
        -----------------------------------------------------------------
          Projection      Map Design      Input/Output      Run
        -----------------------------------------------------------------
        
        
        When you begin plotting a map, by selecting an option in the Run
        menu, the menu bar is replaced by the following line.  This line is
        not a menu bar, it is for your information only.
        
        
        -----------------------------------------------------------------
         Esc: goto menu         Input file:             Reading record:
        -----------------------------------------------------------------
        
        
        While a map is plotting, the top line of the screen displays (1) a
        reminder that pressing the Esc key will terminate plotting and
        return you to the menu bar; (2) the name of the current map input
        file;  and (3) the number of points which have been read from the
        input file.
        
        Once the map is completed, the menu bar reappears on the top line.
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  9 






        3.        Projection menu
        
        -----------------------------------------------------------------
          Projection      Map Design      Input/Output      Run
        +----------------------------------------------------------------
        | Mercator                  |
        | Equirectangular           |
        | Hammer equal-area         |
        | Robinson                  |
        |---------------------------|
        | Equidistant conic         |
        | Conformal conic           |
        | Albers equal-area         |
        |---------------------------|
        | Gnomonic                  |
        | Stereographic             |
        | Orthographic              |
        | Vertical Perspective      |
        | Azimuthal equidistant     |
        | Azimuthal equal-area      |
        |---------------------------|
        | UTM                       |
        |---------------------------|
        | Exit                      |
        +---------------------------+
        
        This menu lists the map projections on which you can plot your map. 
        VERSAMAP assumes that the earth is a sphere of radius 6,371 km for
        all projections except the Universal Transverse Mercator (UTM).  The
        UTM projection assumes that the earth is an ellipsoid.
        
        Maps can be classified by the type of projection (azimuthal, conic,
        cylindrical) used in their construction; or by their common
        properties (azimuthal, conformal, equal-area, and equidistant).
        
        On azimuthal projections, the direction from the central point of
        the map to any other point is correct, and the scale of the map is
        constant along any circle centered on the map center.
        
        On conformal projections, the map scale is the same in all
        directions at a given point.
        
        On equal-area projections, the relative areas of all regions on the
        map are correct.  However, shapes of particular areas may be greatly
        distorted.
        
        On equidistant projections, the scale is constant along all great
        circles from one or two points.
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  10 






        3.1.      Mercator
        
        A conformal projection on which meridians and parallels are parallel
        lines perpendicular to each other.  Meridians are equally spaced,
        parallels are unequally spaced.  The north and south poles cannot be
        plotted because they project to infinity.
        
        The scale is true along the equator, or along two parallels
        equidistant from the equator.  Since the scale increases rapidly
        away from the equator, the areas of polar regions are greatly
        exaggerated compared to those of equatorial regions.
        
        The Mercator projection is commonly used for maps of the world, and
        is designed so that straight lines on the map are rhumb lines (lines
        of constant compass bearing).  This is a useful property in
        navigation and many nautical charts use the Mercator projection.
        
        
        3.2.      Equirectangular
        
        Meridians and parallels are equally spaced parallel lines
        perpendicular to each other.  The scale is true along the two
        standard parallels and along all meridians.  The scale along
        parallels is too small between the equator and the standard
        parallels, and too large between the standard parallels and the
        poles.
        
        The map can be visualized as projected on a cylinder which
        intersects the globe at two standard parallels equidistant from the
        equator.  VERSAMAP allows the user to select the latitude of the
        standard parallels.
        
        The fact that meridians and parallels are equally spaced makes
        interpolation easy.  The projection is useful for maps of small
        regions, since distortion is not large if one of the standard
        parallels is chosen to bisect the region under consideration.
        
        
        3.3.      Hammer Equal-Area
        
        An equal-area projection useful for maps of the entire world.
        
        The central meridian is a straight line.  Other meridians are curves
        concave to the central meridian and intersecting at the poles.  The
        equator is a straight line; other parallels are arcs concave toward
        the nearest pole.
        
        The scale of the projection is only correct along the equator and
        the central meridian.
        
        
        
        


        VMAP.DOC version 1.51                                    Page  11 






        3.4.      Robinson
        
        This projection is useful for general purpose world maps with a
        pleasing visual appearance.  The National Geographic Society uses
        the Robinson projection for world maps.
        
        The central meridian and all parallels are straight lines.  Other
        meridians are curves concave to the central meridian.  The map scale
        is true along 38 N and 38 S latitudes.
        
        
        3.5.      Equidistant Conic
        
        An equidistant conic projection on which meridians are equally
        spaced lines converging at a point beyond one of the poles. 
        Parallels are equally spaced circular arcs centered on the point
        where the meridians converge.  The poles are circular arcs of
        infinite scale.  Distortion on the projection is intermediate
        between that of equal-area and conformal conic projections.
        
        The scale is true along meridians and along two standard parallels. 
        VERSAMAP allows the user to select the latitudes of the standard
        parallels.
        
        
        3.6.      Conformal Conic
        
        A conformal conic projection on which meridians are equally spaced
        lines converging at a point, which is one of the poles.  Parallels
        are unequally spaced circular arcs centered on the point where the
        meridians converge.  The pole opposite the point of convergence
        cannot be shown.
        
        The scale is true along two standard parallels, which VERSAMAP
        allows the user to select.
        
        
        3.7.      Albers Equal-Area Conic
        
        An equal-area conic projection on which meridians are equally spaced
        lines converging at a point beyond one of the poles.  Parallels are
        unequally spaced circular arcs centered on the point where the
        meridians converge.  The poles are shown as circular arcs of
        infinite scale.  This projection is commonly used to maps of the 48
        conterminous United States.
        
        The scale is true along two standard parallels, which VERSAMAP
        allows the user to select.  Since the projection is equal area, the
        scale at any point on a meridian is the reciprocal of the scale
        along a parallel at that point.
        
        
        


        VMAP.DOC version 1.51                                    Page  12 






        3.8.      Gnomonic
        
        An azimuthal projection with the characteristic that great circles
        plot as straight lines.  This projection is commonly used for long
        distance navigation, since the shortest distance between two points
        on the projection is the straight line connecting them.
        
        The range of the Gnomonic projection must be less than 90 degrees,
        relative to the center of the map.  The scale of the projection is
        only correct at the map center, and distortion increases rapidly
        away from the center.
        
        
        3.9.      Stereographic
        
        A conformal azimuthal projection.  The polar aspect of this
        projection is commonly used for maps of polar regions.
        
        The range of the projection cannot be more than 90 degrees, relative
        to the center of the map.
        
        
        3.10.     Orthographic
        
        An azimuthal projection which has the appearance of a globe, and
        which resembles the earth as seen from a great distance in space.
        
        The range of the projection cannot be more than 90 degrees, relative
        to the center of the map.  Map scale is only true at the center of
        the map.
        
        
        3.11.     Vertical Perspective
        
        An azimuthal projection which shows the earth as it appears from any
        point above the earth's surface.  The projection provides views of
        the earth resembling those seen from space.
        
        The area of the earth's surface that can be displayed by this
        projection is less than 1 hemisphere.  VERSAMAP allows the user to
        select the distance above the surface from which the earth is
        viewed.  The default distance is 35,840 km (the distance of
        geosynchronous communication and weather satellites above the
        equator).
        
        
        3.12.     Azimuthal Equidistant
        
        An azimuthal projection on which the distance between the map center
        and any other point on the map is true.  By centering the map at the
        location of interest, you can determine the distance from that point
        to any other place on the earth.
        


        VMAP.DOC version 1.51                                    Page  13 






        This projection can show the entire globe.  The scale of the map is
        true along any straight line radiating from the center of the
        projection.
        
        
        3.13.     Azimuthal Equal-Area
        
        An equal-area azimuthal projection which is recommended for maps of
        nearly circular regions of the globe.
        
        The projection can show the entire globe.  The scale of the
        projection is only correct at the center of the map.
        
        
        3.14.     UTM - Universal Transverse Mercator
        
        The Transverse Mercator projection is a normal Mercator projection
        which has been rotated 90 degrees so that the projection is tangent
        to the earth along a central meridian, rather than along the
        equator.  If the scale along the central meridian is made slightly
        less than 1, the projection becomes tangent to the earth along 2
        small circles equidistant from the central meridian.  The scale
        factor of the central meridian is often set equal to 0.9996. In this
        case, lines of true scale (scale 1.0000) occur 180 km (97 nautical
        miles) on either side of the central meridian.  Because scale errors
        on the Transverse Mercator are small near the central meridian, this
        projection is commonly used to map areas near the central meridian. 
        The projection is not used to map large regions.
        
        When applied to an ellipsoidal earth, the Transverse Mercator is
        also called the Gauss-Kruger projection.  The UTM is a special case
        of the Gauss-Kruger projection.
        
        The UTM projection differs from the other projections in VERSAMAP in
        several respects.
        
         1.  It assumes that the earth is an ellipsoid, not a sphere. 
             Although this assumption complicates the mathematics, it is
             necessary for accurate mapping of small areas.  All other
             projections used by VERSAMAP assume that the earth is a sphere
             of radius 6,371 km.
        
         2.  Positions are expressed in meters, not as degrees of latitude
             or longitude.
        
         3.  Positions can be located more precisely on the UTM than on the
             other projections used by VERSAMAP.  Positions on the UTM can
             be located to fractions of a meter; whereas positions on the
             other projections, which are rounded to the nearest second of
             latitude and longitude, are precise to about 30 meters.
        
        
        


        VMAP.DOC version 1.51                                    Page  14 






        The UTM was adopted by the U.S. Army in 1947 for large scale maps of
        the world.  For use with the UTM, the earth is divided into 60
        longitudinal zones, each 6  wide, running east from 180 W.  The
        first zone is centered on 177 W longitude; the 30th zone on 3 W; the
        31st zone on 3 E; and the 60th zone is centered on 177 E. 
        Latitudinal bounds for the UTM extend from 84 N to 80 S.  The
        Universal Polar Stereographic (UPS) projection is used for maps of
        the polar regions extending north of 84 N or south of 80 S.
        
        The UTM projection in VERSAMAP can also be used to plot maps on the
        Gauss-Kruger projections used for various national grids.  The user
        may select the ellipsoid; the scale factor of the central meridian;
        the longitude of the central meridian; the latitude of the map
        origin; the false easting; and the false northing.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  15 






        4.        Map Design menu
        
        -----------------------------------------------------------------
          Projection      Map Design      Input/Output      Run
        -----------------------------------------------------------------
                        | Map Boundaries        |
                        | Standard Parallels    |
                        | Great Circle          |
                        | Grid Type             |
                        | Geographic Features   | 
                        |-----------------------|
                        | Add Text to Map       |
                        | Select Font           |
                        | Display Previous Text |
                        |-----------------------|
                        | Labels                |
                        |-----------------------|
                        | Background Color      |
                        | Grid Color            |
                        |-----------------------|
                        | Save Map Design       |
                        | Recall Map Design     |
                        +-----------------------+
        
        This menu allows you to modify the design of your map.  You may
        change the boundaries of the map (ZOOM in or out); select the
        standard parallels, if any; define a Great Circle to be plotted;
        define the type of grid superimposed upon the map; select the
        geographic features that you wish to plot; add text to the map;
        display labels associated with map points; change the background and
        grid colors of the map; and save your selected map parameters for
        recall at a later time.
        
        
        4.1.      Map Boundaries
        
        This option allows you to increase or decrease (ZOOM in or out) the
        area covered by a map.  After selecting this item, one or more
        windows appear in which the boundaries of the map projection are
        entered.  Data entered define the area to be plotted, and the
        spacing of grid marks on the finished map.
        
        
        4.1.1.    Non-azimuthal projections
        
        The following items are displayed in the LATITUDE AND LONGITUDE
        LIMITS window for non-azimuthal projections (Mercator,
        Equirectangular, Hammer equal-area, Robinson, Equidistant conic,
        Conformal conic, Albers equal-area).
        
        
        
        


        VMAP.DOC version 1.51                                    Page  16 






                       Northernmost latitude of the map?
                       Southernmost latitude of the map?
                 Degrees of latitude between grid marks?
        
                       Westernmost longitude of the map?
                       Easternmost longitude of the map?
                Degrees of longitude between grid marks?
        
        
        For the non-azimuthal projections, you define the map boundaries by
        specifying the northern and southern latitudes, and western and
        eastern longitudes of the map.
        
        VERSAMAP requires that the grid spacing you select for non-azimuthal
        projections yield equally spaced divisions between the northern- and
        southernmost latitudes, and between the western- and easternmost
        longitudes.  You will get an error message, requiring you to edit
        the data, if the degrees between grid marks that you have chosen do
        not yield equally spaced divisions along the axes.  For example, the
        northernmost latitude of the default Equirectangular projection is
        90 N and the southernmost latitude is 90 S.  The difference between
        the northernmost and southernmost latitudes is 180 degrees of
        latitude.  The Degrees of latitude between grid marks for the
        default Equirectangular projection is 30 degrees, which divides
        evenly into the distance between the northernmost and southernmost
        latitudes (180/30 = 6.00).  However, you would get an error message
        if you tried to set the Degrees of latitude between grid marks to 19
        degrees, since 19 does not divide evenly into 180 (180/19 = 9.47)!
        
        Once you have entered the items in the LATITUDE AND LONGITUDE LIMITS
        window and pressed the < ok > button, the program checks for errors
        in the latitude/longitude limits of your map projection, and for
        errors in grid spacing.  If the program detects an error, it prints
        an error message on the screen telling you to correct the mistake.
        
        For instance, the program will not allow a Mercator projection to be
        plotted if the Northernmost latitude is 90 N (north pole) or if the
        Southernmost latitude is 90 S (south pole).  Try entering 90 N as
        the Northernmost latitude limit for a Mercator projection.  In this
        case, an error message will appear, forcing you to edit the data.
        
        Pressing the < cancel > button allows you to exit the window and
        ignore any changes made to the latitude and longitude limits of the
        map.  Pressing < cancel > restores the latitude and longitude limits
        in use when the window was opened.
        
        
        4.1.2.    Azimuthal projections
        
        For azimuthal projections (Gnomonic, Stereographic, Orthographic,
        Vertical Perspective, Azimuthal equidistant, Azimuthal equal-area)
        the following items are displayed in the LATITUDE AND LONGITUDE
        LIMITS window.


        VMAP.DOC version 1.51                                    Page  17 






                            Central latitude of the map?
                 Degrees of latitude between grid marks?
        
                           Central longitude of the map?
                Degrees of longitude between grid marks?
        
                                Range of map in degrees?
        
        
        The map boundaries of azimuthal projections are defined by
        specifying the position at the center of the map (central latitude,
        central longitude), and the range of the map.  The range of the map
        is the arc distance, in degrees, from the center of the map to the
        edge of the map.  Note, that in VERSAMAP, all azimuthal map
        projections plot with a circular shape.  Since the central meridian
        of the azimuthal projections is a straight vertical line, the Range
        of map in degrees is best thought of as the distance in latitude,
        along the central meridian, from the center of the map to the top
        edge of the map.
        
        For azimuthal projections, VERSAMAP requires that the Degrees of
        latitude between grid marks that you select, yield equally spaced
        divisions when divided into 180 degrees; and that the Degrees of
        longitude between grid marks that you select, yield equally spaced
        divisions when divided into 360 degrees.  You will get an error
        message, requiring you to edit the data, if the degrees between grid
        marks that you have chosen do not yield equally spaced divisions
        when divided into 180 or 360 degrees.  For example, the Degrees of
        latitude between grid marks for the default Stereographic projection
        is 30 degrees, which divides evenly into 180 degrees (180/30 =
        6.00). However, you would get an error message if you tried to set
        the Degrees of latitude between grid marks to 25 degrees, since 25
        does not divide evenly into 180 (180/25 = 7.20)!
        
        For the Vertical Perspective projection (satellite view), the item
        Range of map in degrees is replaced by Distance above surface in
        kilometers.  As the distance from the earth's surface increases, the
        area (range) of the Vertical Perspective projection increases.  The
        default distance, 35840 km, is the distance of geosynchronous
        communications and weather satellites above the equator.
        
        
        4.1.3.    UTM projection
        
        Three windows are used to define the parameters needed to plot a map
        on the UTM projection.
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  18 






        4.1.3.1.  UTM spheroid
        
        The first window, SELECT UTM SPHEROID, allows the user to select 1
        of 9 ellipsoids that define the earth's shape.  The following table
        lists spheroids used for particular regions of the earth.
        
        
             Spheroids used to map different regions of the earth in the UTM
             and the Gauss-Kruger projections.
        
             Spheroid               Scale       Region
                                    Factor
        
                         Spheroids for the UTM Projection
        
             Clarke (1866)          0.9996      North America, Philippines
             Clarke (1880)                      France, most of Africa
             Everest (1830)                     India, Burma, Pakistan,
                                                Afghanistan, Thailand
             Bessel (1841)                      Most of Central Europe,
                                                Chile, China, Indonesia
             International (1924)               Remainder of world
        
                      Spheroids for Gauss-Kruger Projections
        
             Airy (1830)            0.9996      Britain, Ireland
             Krasovsky (1940)       1.0000      Soviet Union, Warsaw Pact
        
        
        Once a spheroid has been selected, the parameters defining its shape
        (equatorial radius and flattening) are listed in the Map Parameter
        Report option of the Input/Output menu.
        
        
        4.1.3.2.  UTM parameters
        
        The second window, SELECTION OF UTM PARAMETERS, allows the user to
        select the following map parameters.  The default values shown below
        plot a map of Ireland.
        
        
                 Central longitude of UTM zone?  009 00 00 W
                        Latitude of map origin?   00 00 00 N
        
                                False  easting?   0500000
                                False northing?  00000000
        
             Scale factor of central longitude?  0.9996
        
        
        For the UTM projection, the only parameters which vary are the
        central longitude of the UTM zone and the false northing.  All other
        parameters are constant.


        VMAP.DOC version 1.51                                    Page  19 






        The central longitude of a given UTM zone is calculated as follows,
        
             Central longitude of UTM zone = -183 + 6 * (zone number)
        
        where negative values represent west longitude.  Ireland is in zone
        29, which runs from 12 W to 6 W.
        
        The false easting and false northing are added to the calculated x,y
        coordinates so that positions on the map are always positive.  On
        the UTM projection, the false northing is 0 for maps in the northern
        hemisphere, and 10,000,000 for maps south of the equator; the false
        easting is always 500,000.
        
        For the Gauss-Kruger projection, the above parameters may vary
        depending on the national grid chosen.  The following table gives
        values for Britain, Ireland, and countries of the former Warsaw
        Pact.
        
        
               Gauss-Kruger Projection Parameters for National Grids
        
                                  Britain     Ireland     Warsaw Pact
                                                                       
             Central longitude:   02 00'W      08 00'W      UTM zone
        Latitude of map origin:   49 00'N      53 30'N      00 00'N
        
                False  easting:   0400000      0200000      0500000
                False northing:  00100000     00250000     00000000
        
                  Scale factor:   0.9996       0.9996       1.0000
        
                      Spheroid:     Airy        Airy       Krasovsky
        
        
        The central longitude for the Warsaw Pact countries is the same as
        the equivalent UTM longitude.
        
        
        4.1.3.3.  UTM boundaries
        
        The third window, BOUNDARIES OF UTM PROJECTION, allows the user to
        define the map boundaries and grid spacing.  The default values
        shown below plot a map of Ireland.
        
        
           Northern boundary of map in meters?  06200000
           Southern boundary of map in meters?  05600000
        Meters between north/south grid marks?  00100000
        
            Western boundary of map in meters?   0300000
            Eastern boundary of map in meters?   0800000
          Meters between east/west grid marks?   0100000
        


        VMAP.DOC version 1.51                                    Page  20 






        The boundaries of the UTM projection are defined by specifying their
        coordinates in meters.  The x-axis runs from left to right; the
        y-axis from bottom to top.
        
        VERSAMAP requires that the grid spacing you select for the UTM
        projection yield equally spaced divisions between the northern and
        southern boundaries, and between the western and eastern boundaries. 
        You will get an error message, requiring you to edit the data, if
        the meters between grid marks that you have chosen do not yield
        equally spaced divisions along the axes.  In the above example, the
        northern boundary of the default UTM projection is 6,200,000 meters
        and the southern boundary is 5,600,000 meters.  The difference
        between the northern and southern boundaries is 600,000 meters.  The 
        Meters between north/south grid marks for the default UTM projection
        is 100,000 meters, which divides evenly into the distance between
        the northern and southern boundaries (600,000/100,000 = 6.00). 
        However, you would get an error message if you tried to set the
        Meters between north/south grid marks to 125,000 meters, since
        125,000 does not divide evenly into 600,000 (600,000/125,000 = 4.8)!
        
        
        4.1.3.4.  Estimation of UTM coordinates
        
        The conversion between geographic coordinates (latitude and
        longitude in degrees) and UTM coordinates (meters) is not obvious. 
        The following paragraphs show how to estimate the x,y coordinates of
        a UTM projection given the latitude and longitude limits of the map.
        
        Since 90 degrees of latitude is nearly equal to 10,000,000 meters,
        the y coordinate corresponding to a given latitude is approximately,
        
        
             y coordinate = false northing + (10,000,000/90)*latitude
                          = false northing + 111111*latitude
        
        
        For example, the y coordinate for a point at 50 N latitude is
        approximately 5,555,550 meters; for a point at 50 S the y coordinate
        is about 4,444,450 meters (10,000,000 - 111111*(-50)).
        
        To determine the x-axis limits of a UTM projection, first determine
        the central longitude of the UTM zone in which the map occurs,
        
        
             Central longitude of UTM zone = -183 + 6 * (zone number)
        
        
        Use the following criteria to check your calculated value for the
        central longitude: central longitude of UTM zone plus 3 must be
        evenly divisible by 6.  In equation form,
        
        
                  (Central longitude of UTM zone + 3)/6 = integer


        VMAP.DOC version 1.51                                    Page  21 






        Once you have determined the central longitude, set the Western
        boundary of map in meters to 0 meters, and the Eastern boundary of
        map in meters to 1,000,000 meters.  This will draw a map 1000 km
        wide, centered on the central longitude.  You can then gradually
        increase the western boundary and decrease the eastern boundary
        until the map covers the area of interest.
        
        
        4.2.      Standard Parallels
        
        After selecting this item, a window appears in which the latitudes
        of the standard parallels are entered.
        
        
        4.2.1.    Conic Map Projections
        
        The conic projections in this program (equidistant conic, conformal
        conic, Albers equal-area) require that you select 2 standard
        parallels of latitude.  The scale of the map is true along the
        standard parallels; the spacing of the parallels determines the
        angle between meridians on the map.
        
        There are 2 constraints on selection of the standard parallels:
        
         1.  they must lie between the northern- and southernmost latitudes
             of your grid; and
        
         2.  they cannot be symmetrical about the equator.  Standard
             parallels at 20 N and 20 S are not allowed, because this would
             turn the cone into a cylinder.
        
        The program places default values for the standard parallels at 1/6
        and 5/6 of the distance between the northern- and southernmost
        latitudes of the grid.
        
        When this screen appears, the cursor will be in the first position
        of the degrees column of the northernmost standard parallel.  If the
        default values are acceptable, tab to the < ok > button and press
        Enter to continue.
        
        To change the values, tab to the line to be edited, enter the new
        value in the field you wish to edit, and press Enter.  The cursor
        will skip to the next field.  Enter a new value if desired and press
        Enter.  Continue until you have edited the last field.  When done,
        tab to the < ok > button and press Enter.
        
        If you attempt to enter standard parallels which are equally spaced
        about the equator, the program will print an error message and force
        you to change the latitude of one or both parallels.
        
        Pressing the < cancel > button allows you to exit the window and
        ignore any changes made to the standard parallels.  Pressing
        < cancel > restores the standard parallels in use when the window
        was opened.

        VMAP.DOC version 1.51                                    Page  22 






        4.2.2.    Equirectangular Map Projection
        
        This projection requires 2 standard parallels at equal distances
        north and south of the equator.  You may only select the northern
        standard parallel.  The other parallel is automatically placed in
        the southern hemisphere at an equal distance from the equator.  
        
        The program places default values for the standard parallels at 1/2
        the distance between the northern- and southernmost latitudes of the
        grid if the northern- and southernmost latitudes lie in the same
        hemisphere.  If the northern- and southernmost latitudes of the grid
        lie in opposite hemispheres, then the standard parallels are placed
        at 1/2 the distance between the equator and whichever of the
        northern- or southernmost latitudes of the grid lies closer to a
        pole.
        
        When this screen appears, the cursor will be in the first position
        of the degrees column of the northernmost standard parallel.  If the
        default values are acceptable, tab to the < ok > button and press
        Enter to continue.
        
        To change the values, enter a new value in the field being edited
        and press Enter.  The cursor will skip to the next field.  Enter a
        new value if desired and press Enter.  Continue until you have
        edited the last field.  When done, tab to the < ok > button and
        press Enter.
        
        Pressing the < cancel > button allows you to exit the window and
        ignore any changes made to the standard parallels.  Pressing
        < cancel > restores the standard parallels in use when the window
        was opened.
        
        
        4.3.      Great Circle
        
        This option allows you to define the endpoints of a Great Circle,
        the shortest distance between 2 points on the earth's surface.  The
        default endpoints will plot the Great Circle between San Francisco
        and Kuwait.  The course and distance at selected waypoints along the
        Great Circle can be viewed by selecting the Great Circle Report
        option from the Input/Output menu.
        
        To plot a Great Circle, enter the starting and ending latitudes and
        longitudes, tab to the < ok > button, and press Enter.  Once you
        press < ok >, a second window titled SELECT GREAT CIRCLE COLOR will
        appear, allowing you to plot the Great Circle in any 1 of 16 colors. 
        
        The Great Circle will be displayed on the next map to be plotted,
        and will be shown on all successive maps.  To display a Great Circle
        you have defined, select one of the Size options from the Run menu.
        
        To stop plotting a Great Circle that you have previously defined,
        tab to the < cancel > button, and press Enter.


        VMAP.DOC version 1.51                                    Page  23 






        4.4.      Grid Type
        
        This window allows you to select the type of grid that you wish
        superimposed on your map.  You have several choices,
        
         1.  the outer boundary of the grid shown as a solid line and the
             interior grid points plotted as individual points (the
             default);
        
         2.  the outer boundary of the grid shown as a solid line and no
             interior grid points plotted;
        
         3.  all grid points connected by lines;
        
         4.  all grid points plotted as individual points with no lines
             connecting them; and
        
         5.  no grid (the map will be plotted without any latitude or
             longitude markings).
        
        
        To get a quick view of the appearance of the different grid choices,
        select a grid type, then enter a null string (i.e. no file name) for
        the map input filename, and finally plot the map.  In this case, the
        program will plot the grid, but no map, on the screen.
        
        In VERSAMAP, the azimuthal map projections (Gnomonic, Stereographic,
        Orthographic, Vertical Perspective, Azimuthal equidistant, Azimuthal
        equal-area) are truncated to fit a circular shape, and points that
        lie outside the bounding circle are not plotted.  Due to the complex
        shape of the grid for these projections, the outside boundary of the
        map may not be well marked when grid type 4 (all grid points plotted
        as individual points) is selected.  To indicate the edge of the map
        for azimuthal projections with grid type 4, VERSAMAP plots a
        bounding circle, composed of discrete points spaced 3 degrees apart.
        
        
        4.5.      Geographic Features
        
        After selecting this item, a window appears which contains a list of
        geographic features (coastlines, islands, lakes, rivers, countries,
        U.S. States, Canadian Provinces, Australian States) in Micro World
        Data Bank II (MWDB-II) files which can be plotted by VERSAMAP.  Move
        through the vertical list with the up and down cursor keys, and
        toggle the features on or off with the space bar.  Checkmarked
        features will be plotted.  The defaults plot all features.  Move to
        Proceed and press Enter to exit the window.
        
        You may select a different color for each geographic feature.  The
        color in which a geographic feature will be plotted is displayed to
        the left of the feature name.  As you move through the geographic
        feature list box, a second list box appears, allowing you to select
        the color of each geographic feature.


        VMAP.DOC version 1.51                                    Page  24 






        The map files supplied with VERSAMAP (file extension .MAP) are an
        enhanced version of MWDB-II and can be used to plot the different
        features.  Please note that the original MWDB-II files (file
        extensions .ALL, .CCI, .PNT) do not contain data for Canadian
        Provinces or Australian States.
        
        VERSAMAP has the ability to plot as many as 9 map files, one after
        the other, on a map.  These 9 map files represent different layers
        or features on your map.  Features selected by accessing the
        Geographic Features option in the Map Design menu only affect
        features plotted for the first map file (which will be the default
        map input file, VMAP4.MAP, until you enter a new filename in the Map
        Input Filenames option of the Input/Output menu).  When you enter a
        MWDB-II filename in the Map Input Filenames option, VERSAMAP
        automatically prompts you for the geographic features that you wish
        to plot for that particular file.
        
        In addition to MWDB-II, VERSAMAP allows geographic features to be
        plotted from 2 other digital map databases: (1) World Data Bank II
        (WDB-II), a digital map database covering the entire world, which
        contains 36 different geographic categories; and (2) U.S. Geological
        Survey Digital Line Graph (USGS DLG) data, a database covering the
        United States, containing 72 different geographic features.  These
        are the most detailed map databases that can be plotted with
        VERSAMAP; they are described in Sections 7.1 and 7.4.  Geographic
        features for WDB-II and USGS DLG map files are selected when you
        enter their filenames in the Map Input Filenames option of the
        Input/Output menu.
        
        
        4.6.      Add Text to Map
        
        You may chose the size, color, orientation, and content of text to
        be entered on the map.  When you select this option, a window
        appears containing 6 boxes labeled Text #, Size, Color, Angle, PIC
        Font, and Text.  The use of each box is described below.
        
        
        Text #:
        
        VERSAMAP allows you to store 100 text strings (and their associated
        size, color, angle, PIC font, and position) in memory to be recalled
        later.  The Text # box allows you to select the number of the text
        string to be entered.
        
        
        Size:
        
        This box allows you to select the point size of the text that will
        be written on the map.  The fixed-space Courier font has 3 possible
        sizes: 8, 10, 12 point.  The proportionally spaced Helvetica font
        has 6 sizes: 8, 10, 12, 14, 18, and 24 point.  The height of the
        font in inches is equal to the point size divided by 72.  A 24 point
        font has letters 1/3 inch high.

        VMAP.DOC version 1.51                                    Page  25 






        Color:
        
        You may print text in any 1 of 16 colors.
        
        
        Angle:
        
        You may print text in 1 of 4 orientations.  Selecting 0  prints the
        text horizontally from left to right; selecting 90  prints the text
        vertically with the first letter at the bottom; selecting 180 
        prints the text horizontally, upside down, from right to left;
        selecting 270  prints the text vertically with the first letter at
        the top.
        
        
        PIC Font:
        
        The PIC Font number has no effect on maps which are not exported as
        PIC files.
        
        The text that you enter on the map will be incorporated in any Lotus
        PIC graphics file that you export.  Text in PIC files can be printed
        in 1 or 2 fonts.  These Lotus fonts are not the same as the Courier
        and Helvetica fonts supplied with VERSAMAP.
        
        The PIC Font box allows you to select the font number, 1 or 2, with
        which you want the text string to be printed when you print your PIC
        file.  For instance, the PrintGraph utility from Lotus 1-2-3 version
        2.2 allows you to chose 2 fonts from a list of 11 possible fonts
        (block1, block2, bold, forum, italic1, italic2, Lotus, Roman1,
        Roman2, script1, script2).
        
        If you plan to export maps as PIC files, I recommend that you
        prepare a test map annotated with both the Courier and Helvetica
        fonts in all possible point sizes.  Export this test map from
        VERSAMAP as a PIC file, import the file into your graphics program,
        and print the PIC file from within your graphics program.  This will
        give you an idea of the appearance of each font in its various
        sizes.
        
        
        Text:
        
        Type the text that you want printed on the map in the Text box, and
        press Enter to store the string.  You must press Enter to save the
        text string!
        
        Text strings can have a maximum length of 56 characters.  With 12
        point or larger text, you may not be able to fit 56 characters
        across the map.
        
        
        


        VMAP.DOC version 1.51                                    Page  26 






        The following table lists the keystrokes necessary to print a degree
        sign,  , in applications running under DOS or Windows.  To print a
        degree sign for all output options except Save as DXF, hold down the
        Alt key and type the number 176 or 248 on the numeric keypad.
        
        
                  Output Option         DOS          Windows
        
                   Screen             Alt-248        Alt-248
                   Print Map          Alt-248        Alt-248
                   Save as PCX        Alt-248        Alt-248
                   Save as CGM        Alt-248        Alt-176
                   Save as PIC        Alt-176        Alt-176
                   Save as DXF          %%d            %%d
        
        
        The keystrokes Alt-176 will be displayed as a stippled block,  , and
        an underline character, _, in VERSAMAP, but will print a degree sign
        when the output file is printed.
        
        To incorporate a degree sign in a DXF file, type the 3 character
        sequence, %%d.  These 3 characters will be displayed as a degree
        sign when the DXF file is imported into AutoCAD.  If %%d does not
        display a degree sign in your application, try Alt-176 or Alt-248.
        
        
        4.6.1.    Positioning text on the map
        
        After selecting the text parameters, tab to the < ok > button, and
        press Enter.  The window will disappear, and the text string
        previously entered in the Text box will be printed in the upper left
        corner of the map.  The mouse or the cursor keys are used to place
        the text string in the desired position on the map.  The horizontal
        and vertical pixel position of the cursor is continuously updated in
        the upper right corner of the screen.
        
        The menu bar is erased when you press the < ok > button.  It is
        replaced by a reminder that pressing Esc will restore the menus.  To
        access the menus again you must press Esc or click the left mouse
        button on the top line of the screen.  This will terminate text
        addition, and reactivate the menus.
        
        If you have a mouse, move the mouse cursor to the position at which
        you want the text to appear, then press the left mouse button.  The
        mouse cursor represents the lower, left corner of the text string. 
        The text string will appear in the new position.  Pressing the left
        mouse button toggles the text string on and off.  The program will
        beep if the position you have chosen is too near the edge of the map
        to print the full text string.
        
        
        
        


        VMAP.DOC version 1.51                                    Page  27 






        You can use the up, down, right, and left cursor keys to position
        the text string if you do not have a mouse.  The cursor position is
        represented by a plus sign, +.  The plus sign is not visible until
        you press one of the cursor keys.  The distance the cursor moves is
        controlled by pressing the numbers 3, 2, or 1.  Pressing the number
        3, causes the cursor to move 50 pixels each time a cursor key is
        pressed; pressing the number 2, causes the cursor to move 10 pixels
        each time a cursor key is pressed; and pressing the number 1, causes
        the cursor to move 1 pixel each time a cursor key is pressed.  Once
        the cursor is in the correct position, press Enter.  The center of
        the + represents the lower, left corner of the text string. 
        Pressing Enter, toggles the text string on and off.  The program
        will beep if the position you have chosen is too near the edge of
        the map to print the full text string.
        
        Once you have placed the text in the correct location, press Esc (or
        click the left mouse button on the top line of the screen) to
        terminate text addition, and reactivate the menus.
        
        
        4.6.2.    Adding additional text to the map
        
        To enter a second text string on the map, press Esc to activate the
        menus and select the Add Text to Map option in the Map Design menu. 
        Place the highlight bar over the number 2 in the Text # box, and
        press Enter.  Then proceed to modify the text parameters as
        necessary.  The second text string will print in the upper left
        corner of the screen when the < OK > button is pressed; this string
        will overprint any text already present in the upper left corner. 
        However, the original text will be restored when you move the second
        text string to a new location on the screen.
        
        Text that you enter on the map will be incorporated into maps that
        you print or save using the Print Map or Save as PCX, CGM, DXF, or
        PIC options in the Input/Output menu.  Text entered on maps is not
        incorporated into maps saved with the Save as ASCII option, since
        most technical and business graphing programs have the ability to
        annotate imported graphs.
        
        
        4.7.      Select Font
        
        This option allows you to select the font used to print text on the
        screen.  You may select a fixed-space Courier font or a
        proportionally spaced Helvetica font.
        
        The fonts used by VERSAMAP are stored in 4 files with the file
        extension .FON:
        
                            COUR_EGA.FON, COUR_VGA.FON
                            HELV_EGA.FON, HELV_VGA.FON
        
        


        VMAP.DOC version 1.51                                    Page  28 






        The program will select the correct font for your video adapter. 
        Fonts labeled _EGA are for EGA adapters, and those labeled _VGA for
        VGA adapters.  After making backup copies, you may delete the
        unnecessary font files to save disk space.  The Helvetica fonts are
        only included in the registered version of VERSAMAP.
        
        The font files must be in the same directory as the VERSAMAP
        program, VMAP.EXE.
        
        After selecting this option a window titled SELECT FONT appears. 
        The default font is fixed-space Courier.  If this is acceptable,
        press Enter.  To select the Helvetica font, highlight Helvetica with
        the down arrow key, and press Enter.
        
        You may add text in both fonts to the same map.  However, using both
        fonts on the same map is not recommended.  The length of a text
        string depends on the font and point size; text which fits on a map
        in one font and point size may not fit on the map in the second
        font.  Use only one font per map if you plan to export a map as a
        CGM, DXF, or PIC vector graphics file.  The vector graphics files
        exported by VERSAMAP allow only 1 font to be specified, that font
        will be the last font selected before exporting the file.
        
        
        4.8.      Display Previous Text
        
        This option allows you to redisplay, on the screen, all previously
        defined text strings.  Once text is redisplayed it can only be
        erased by redrawing the map.
        
        
        4.9.      Labels
        
        This option allows you to import text that will be displayed next to
        points plotted by VERSAMAP.  The PRN and UTM ASCII file formats
        supported by VERSAMAP allow you to include a text string that can be
        printed next to the latitude, longitude or x,y coordinates of the
        point.  The file structure of the PRN and UTM files is discussed in
        Section 7.7, Importing Your Own Data into VERSAMAP.
        
        You may select one of the following items in the Labels option,
        
                       Do Not Display Labels
                       Display Labels
                       Convert Labels to Text
                       Erase Labels Converted to Text
        
        
        The default setting, Do Not Display Labels, ignores labels contained
        in a PRN or UTM file.
        
        
        


        VMAP.DOC version 1.51                                    Page  29 






        Selecting Display Labels causes VERSAMAP to display labels contained
        in a PRN or UTM file when the next map is drawn.  Labels are
        displayed to the lower right of their associated point.  Labels
        which would extend off the right side of the screen are displayed to
        the lower left of the point.  Labels displayed by selecting Display
        Labels are incorporated in maps saved with the Print Map and Save as
        PCX options of the Input/Output menu; they are not incorporated into
        maps saved as vector graphics files with the Save as CGM, DXF, PIC,
        or ASCII options.
        
        The Convert Labels to Text item converts labels displayed on the
        screen into text objects that can be edited from within VERSAMAP. 
        When you select this option, labels which were previously imported
        into VERSAMAP using the Display Labels item are converted into text
        strings that can be edited using the Add Text to Map option.  Labels
        which have been converted to text are added to the end of the list
        of text strings in the Add Text to Map option.  Labels converted to
        text can be edited and repositioned using the Add Text to Map
        option.  In addition, labels which have been converted to text are
        included in maps saved as CGM, DXF, and PIC vector graphics files.
        
        To convert labels to text, perform the following steps,
        
         1.  Select Display Labels
         2.  Replot your map to display the labels
         3.  Select Convert Labels to Text
        
        If you now access the Add Text to Map option in the Map Design menu,
        and page down through the list of text strings, you will see that
        the labels have been converted to text strings and occur at the end
        of the list.
        
        The last menu item, Erase Labels Converted to Text, deletes any
        labels, that you have previously converted to text, from the text
        strings in the Add Text to Map option.
        
        A detailed example showing how to display labels is given in Section
        7.7, Importing Your Own Data into VERSAMAP.
        
        
        4.10.     Background Color, Grid Color
        
        These options allow you to change the background or grid color of
        the map, to any 1 of 16 colors.  The new color that you select will
        be displayed when the next map is plotted.  If you plan to export
        maps as PCX or CGM files, and to print them as black on white,
        change the background color to white and the grid color to black.
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  30 






        4.11.     Save Map Design
        
        This option allows you to save the map parameters you have selected
        in a configuration file for recall at a later time.  After selecting
        this item, a window titled ENTER FILENAME FOR CONFIGURATION FILE
        appears.  Type in the filename and press Enter to select the
        filename.  Press Enter on the < ok > button to save the
        configuration file to disk.  Your configuration file will be written
        to disk immediately after you press the < ok > button.
        
        
        4.12.     Recall Map Design
        
        This option allows you to recall a previously defined configuration
        file.  After selecting this item, a window titled RECALL MAP DESIGN
        appears.  This window contains a vertical box, listing all
        configuration files (file extension .CNF) in the current directory. 
        Move to the desired file and press Enter to load the file into
        VERSAMAP.  The configuration file will be loaded immediately after
        you press Enter.
        
        VERSAMAP does not automatically display a new map when a
        configuration file is loaded into the program.  To display the new
        map, you must manually plot the map by selecting the checkmarked
        option in the Run menu.  If the new map includes text, you must also
        redisplay the text using the Display Previous Text option in the Map
        Design menu, once you have redrawn the map.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  31 






        5.        Input/Output menu
        
        -----------------------------------------------------------------
          Projection      Map Design      Input/Output      Run
        -----------------------------------------------------------------
                                        | Map Input Filenames   |
                                        | Map Parameter Report  |
                                        | Great Circle Report   |
                                        | View Disk Directory   |
                                        |-----------------------|
                                        | Print Map             |
                                        | Select Printer        |
                                        |-----------------------|
                                        | Save as PCX           |
                                        | Save as PIC           |
                                        | Save as CGM           |
                                        | Save as DXF           |
                                        | Save as ASCII         |
                                        | Save Great Circle     |
                                        +-----------------------+
        
        This menu allows you to enter filenames for input and output files;
        to display a report describing the currently selected map; to
        display a report listing course and distance at waypoints along a
        Great Circle; to view the contents of any disk directory; to print
        the map on dot matrix and laser printers; and to save maps as disk
        files.
        
        You may export maps produced by VERSAMAP: (1) by copying the screen
        directly to your printer; (2) as bit-mapped PCX graphics files; (3)
        as vector graphics CGM, DXF, or Lotus PIC files; and (4) as vector
        based ASCII files.
        
        Maps exported by options 1 and 2 are limited by the resolution of
        your monitor.  Even with a VGA monitor, the screen resolution (640
        pixels horizontally, 480 pixels vertically) is fairly coarse.  Maps
        exported as CGM, DXF, or PIC files (option 3) are independent of
        monitor type and have much greater resolution (3200 dots
        horizontally, 2311 dots vertically) than PCX files.  If you have a
        choice, export your maps as CGM, DXF, or PIC files.  This is
        particularly true if you have an EGA monitor.  The most detailed
        maps produced by VERSAMAP are those produced by saving them as ASCII
        files (option 4).  The resolution of these vector based ASCII files
        is limited only by the resolution of the input map boundary files. 
        However, the use of ASCII files produced by option 4 requires a
        technical graphing program that can import large data sets.
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  32 






        5.1.      Map Input Filenames
        
        This option allows you to select the digital map file(s) that you
        wish to plot, and to define the symbols and colors used to plot
        them.  After selecting this item, a window appears in which the
        names of the digital map files you wish to plot are entered.  Up to
        9 filenames may be entered.  You can think of these 9 input files as
        representing different layers or features on your map.
        
        The default file name for the first input file is VMAP4.MAP in the
        current directory.  VMAP4.MAP is the world map included on the
        VERSAMAP disk.  The default file names of the remaining 8 map input
        files are null strings (i.e. no file name).  The program displays
        the current path, but no filename, for input files which have not
        been defined.
        
        When the window is first displayed, the cursor is located at the end
        of the first input file name.  Type in the correct path name and
        press Enter to accept the path name.
        
        
        Symbol Type and Size:
        
        Once you enter a filename, a second window will appear which allows
        you to specify the symbol used to plot the points in that file.
        
        The symbol type determines whether your data is plotted as lines,
        points, crosses, squares, diamonds, triangles, or circles.  If you
        select the symbol type Line, all points on a particular polyline
        will be connected by straight lines.  This is the default symbol
        type for all files.
        
        The other symbol types (Point, Cross, Square, Diamond, Triangle,
        Circle) allow you to superimpose individual latitude/longitude
        points on a map created from a digital map database.
        
        In addition, you may chose the size of the symbols used to plot your
        data.  The size that you enter is the radius of the symbol in
        pixels.  The maximum size is 99 pixels.  Size has no effect on the
        Line and Point symbol types, these two types are always 1 pixel
        wide.
        
        NOTE:     File types (DAT, MP1, MPS, PNT, PRN, UTM) without multiple
                  geographic features allow you to select the color with
                  which to plot the file from this window. 
        
        Once you have entered the symbol type, size, and color (if any) for
        the first input file, tab to the < ok > button and press Enter.
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  33 






        Label Size and Color:
        
        ASCII files with file extensions PRN or UTM may contain text labels. 
        For these 2 file types, a window titled SELECT LABEL SIZE & COLOR
        allows you to select the point size and color of labels you wish
        printed on the map.
        
        
        Geographic Features:
        
        For file types (ALL, CCI, MAP, PKV, PKD, GRV, GRF) which contain
        multiple geographic features, the program will prompt you to enter
        the geographic features to be plotted.
        
        You may select a different color for each geographic feature.  The
        color in which a geographic feature will be plotted is displayed to
        the left of the feature name.  As you move through the geographic
        feature list box, a second list box appears, allowing you to select
        the color of each geographic feature.
        
        Once you select Proceed on the Geographic Features list box, the
        window disappears, and you are prompted for the name of the second
        map input file (if any).  If you wish to input a second map boundary
        file, type its name and press Enter.  Continue until you have
        entered all of your map input files.
        
        Once you have entered the last map input file that you wish plotted,
        tab to the < ok > button in the ENTER FILENAMES FOR MAP INPUT FILES
        window, and press Enter.
        
        The program does not require any input map boundary files.  If you
        do not wish to input data, erase the default filename (up to the
        rightmost backslash) of the first input file; press Enter; then tab
        to the < ok > button; and press Enter.  In this case, only the map
        grid (if any) will be plotted on the screen.
        
        VERSAMAP will accept map boundary input files from the following
        digital map databases: World Data Bank I, World Data Bank II, Micro
        World Data Bank II, The World Digitized, and U.S. Geological Survey
        Digital Line Graph Data.  In addition, VERSAMAP will accept input in
        an ASCII text format.  Section 7 contains a detailed discussion of
        the various map databases that VERSAMAP recognizes.
        
        VERSAMAP recognizes the various databases by their file name
        extensions.  The file names that you enter on this screen must have
        one of the extensions given in Section 7.  However, the names that
        you enter can have different extensions.  For instance, your first
        file could be from Micro World Data Bank II with the extension .ALL,
        your second file could be from the U.S. Geological Survey Digital
        Line Graph database with the extension .GRF, and your third file
        could be from World Data Bank II, with the extension, .PKV.
        
        


        VMAP.DOC version 1.51                                    Page  34 






        5.2.      Map Parameter Report
        
        The Versamap parameter report lists various information about the
        map: the projection type; the grid type; the latitude/longitude
        limits of the map; the maximum/minimum values of the transformed x,y
        map coordinates; scale and area errors at selected points on the
        map; and the names of the map input files.
        
        The X-axis Length and Y-axis Length, listed under Relative Length of
        Axes, are used to scale maps exported as ASCII file(s) to technical
        and business graphics programs.  The use of these two parameters is
        described in Section 8.
        
        Use the up, down, Home, and End keys to scroll through the report. 
        Press F1 to print the report.  Press Esc to exit the report and
        return to menu bar.
        
        
        5.3.      Great Circle Report
        
        Selecting this option displays a report listing the course and
        distance at selected waypoints along a Great Circle previously
        defined in the Great Circle option of the Map Design menu.
        
        The column labeled Course gives the initial course in degrees from
        the current waypoint to the next waypoint.  A course of 0  or 360 
        represents due north; 180  represents due south.  The last 2
        columns, list the cumulative distance in nautical miles (nm) or
        kilometers (km) from the initial point of the Great Circle to the
        given waypoint.
        
        Use the up, down, Home, and End keys to scroll through the report. 
        Press F1 to print the report.  Press Esc to exit the report and
        return to menu bar.
        
        
        5.4.      View Disk Directory
        
        This window allows you to view the contents of any disk and
        directory.  Disk drives are indicated by the letters <drive> to the
        right of the drive letter.  To select a disk drive, move the
        highlight bar over the drive letter and press Enter.  Directories
        are indicated by the letters <dir> to the right of the directory
        name.  To select a directory, move the highlight bar over the
        directory and press Enter.  The path which has been selected is
        displayed immediately above the vertical list box.
        
        The files in the directory are listed after the last directory
        listing.
        
        
        
        


        VMAP.DOC version 1.51                                    Page  35 






        5.5.      Print Map
        
        Maps displayed on the screen may be printed on dot matrix or laser
        printers.  When you select this item, a window titled MAP PLACEMENT
        ON PAGE IN INCHES appears, which allows you to define the dimensions
        and page placement of the printed map.
        
        This option copies the entire screen, except the menu bar, to the
        printer.  The default settings place the map in the center of the
        page, and set the width (the entire screen width) at 6 inches.  The
        width and height of the printed map are dependent.  Adjusting the
        width automatically fixes the height.  Any text displayed on the map
        will be printed.  The grid spacing, and other information about the
        printed map that you need to annotate it, can be obtained from the
        Map Parameter Report option in the Input/Output menu.
        
        Use the Tab key to move between items.  To print the map, tab to the
        < ok > button and press Enter.  The map will begin printing
        immediately after you press the < ok > button.  The Print Map option
        is slow!  On an Epson LQ-800, 24-pin, dot matrix printer, the
        default map takes 1.2 minutes to print from a 33 MHz 486 computer.
        
        Press Esc to exit a map that is currently being printed.
        
        
        5.6.      Select Printer
        
        Before you print a map, you must select the type of printer which
        will print the map.  When you select this item, a window titled
        SELECT PRINTER TYPE AND PORT appears.  You may select one of three
        printer types: Epson 9- or 24-pin dot matrix, or Hewlett-Packard
        LaserJet II.  If your printer is not compatible with one of these
        printers, select None.
        
        You may also select the printer port.  Lpt1 is the default.
        
        
        5.7.      Save as PCX
        
        Before saving the map as a bit-mapped PCX paint file, you must
        specify the filename and path of the file.  After selecting this
        item, a window titled ENTER .PCX FILENAME appears.  Type in the
        correct filename and press Enter to select the filename, then tab to
        the < ok > button and press Enter.  Since the PCX file will be
        written to disk immediately after you press Enter on the < ok >
        button, the map you wish to save must be displayed on the screen. 
        The menu bar is not saved as part of the file.
        
        Maps saved as PCX files are exported exactly as they are displayed
        on the VERSAMAP screen.  If you plan to edit your map in an another
        program, and then to print it as black on white, you can use the
        Background Color and Grid Color options in the Map Design menu to
        plot your map as black on white before exporting it from VERSAMAP.


        VMAP.DOC version 1.51                                    Page  36 






        Any text displayed on the screen (except the menu bar) will be
        included in the PCX file.  If you do not want text to be included in
        the PCX file, redraw the map.
        
        The grid spacing, latitude/longitude limits, and other information
        that you may need to annotate the map, can be obtained from the Map
        Parameter Report option in the Input/Output menu.
        
        
        5.8.      Save as PIC, Save as CGM, Save as DXF
        
        Before saving a map as a CGM, DXF, or PIC vector graphics file, you
        must specify the filename and path of the file.  After selecting one
        of these items, a window titled ENTER FILENAME appears.  Type in the
        correct filename and press Enter to select the filename, then tab to
        the < ok > button and press Enter.  Once you have specified the
        filename, redisplay the map using the Size 100% or Size 70% options
        in the Run menu.  The file will be written to disk as the map is
        drawn.  The menu bar is not saved as part of the file.
        
        NOTE:     Since the CGM, DXF, or PIC file is written to disk as the
                  map is being plotted on the screen, you must enter the
                  filename, and then immediately redraw the map with the
                  Size 100% or Size 70% option.
        
        Any text strings which have been defined with the Add Text to Map
        option in the Map Design menu will be included in the CGM, DXF, or
        PIC file, even if the text strings are not displayed on the screen. 
        If you do not want text to be included in the exported file, erase
        any previously defined text strings.
        
        To include text in a CGM, DXF, or PIC file, perform the following
        steps:
        
         1.  draw the map on the screen,
         2.  annotate the map using the Add Text to Map option,
         3.  select a name for the file using the Save as PIC, Save as CGM,
             or Save as DXF option, and
         4.  redraw the map using the same size option (Size 100% or Size
             70%) that was used in step 1.
        
        
        The file will be written to disk as the map is drawn on the screen
        in step 4.  Text added to the map in step 2 is not redisplayed on
        the screen when the map is redrawn in step 4; however, it is
        included in the CGM, DXF, or PIC file.  Select the Display Previous
        Text option in the Map Design menu to redisplay text previously
        added to a map.
        
        The grid spacing, latitude/longitude limits, and other information
        that you may need to annotate the map, can be obtained from the Map
        Parameter Report option in the Input/Output menu.
        


        VMAP.DOC version 1.51                                    Page  37 






        Maps printed on black and white printers may be difficult to
        interpret because of the many geographic features shown on the map. 
        For instance, due to the many lines on a map, it may be difficult to
        distinguish roads from railroads, or political boundaries from
        rivers.  This difficulty can be alleviated by using VERSAMAP to
        export each geographic feature as a separate CGM, DXF, or PIC file;
        and then importing the CGM, DXF, or PIC files into a graphics
        program, such as CorelDRAW!, which has the ability to import vector
        graphics files as layers of a drawing.  The line width and type
        (solid, dashed, dotted) of each geographic feature (layer) can then
        be modified to distinguished it from other features on the map.
        
        NOTE:     Due to their ASCII format, DXF files produced by VERSAMAP
                  are exceptionally large!  The default Equirectangular map
                  occupies 797,293 bytes of disk space when exported in DXF
                  format.
        
        
        5.9.      Save as ASCII
        
        This option allows your map to be exported to technical or business
        graphing programs for the production of publication quality maps
        (see Section 8, Use of VERSAMAP with Graphing Programs).
        
        After selecting this option, a window titled ENTER FILENAMES FOR
        ASCII OUTPUT FILES appears.  The input fields in this window allow
        you to name the various grid and map files to be exported.  You may
        choose any path names for these files.
        
        To enter a filename, tab to the name to be edited, type in the
        filename and press Enter.  The cursor will then move to the next
        filename (if there is one), or to the < ok > button.
        
        The window contains lines for 1 or 2 grid filenames, depending on
        the grid type selected in the Grid Type option of the Map Design
        menu.  In most cases, the window will contain space for a single
        grid file.  The only exception, the OUTSIDE BOUNDARY CONNECTED BY
        LINES, INTERIOR GRID POINTS SHOWN grid type (the default), contains
        space for two files: the first file contains the interior points,
        the second the outside boundary.
        
        The window contains lines for up to 9 map filenames, one for each of
        the map input files selected in the Map Input Filenames option of
        the Input/Output menu.  Each map output file corresponds to the
        corresponding map input file.  For instance, if you have 5 map input
        files, the fifth map output file will contain the transformed
        latitude/longitude coordinates from the fifth map input file.
        
        Data records in the ASCII grid and map output files have the
        following format.
        
           x coordinate | space (ASCII 32) | y coordinate |
           carriage return (ASCII 13) | line feed (ASCII 10)


        VMAP.DOC version 1.51                                    Page  38 






        Data in most digital map databases is organized as polylines; each
        polyline corresponds to a series of points which can be connected by
        straight lines.  In the ASCII output files, the beginning of each
        new polyline is indicated by a dummy point in which the x and y
        coordinates are both equal to 5.000000 (5 times the maximum x
        coordinate of 1.000000).  In an ASCII output file, any point with an
        x coordinate of 5.000000 is a dummy point which indicates the
        beginning of a new polyline, and which will plot outside the
        boundaries of the map.
        
        To output your map as a series of ASCII files, perform the following
        steps:
        
         1.  draw the map on the screen using one of the Size options in the
             Run menu;
         2.  select the Save as ASCII option in the Input/Output menu;
         3.  enter a name for each of the grid files listed under Grid
             filename;
         4.  enter a name for each of the map files listed under Map
             filename;
         5.  tab to the < ok > button and press Enter;
         6.  redraw the map using the same size option (Size 100% or Size
             70%) that was used in step 1.
        
        
        The file(s) will be written to disk as the map is drawn on the
        screen in step 6.  The Save as ASCII option does not export text
        defined with the Add Text to Map option.  Text displayed on the
        screen is ignored when the map data is written to disk.
        
        
        5.9.1.    Converting exported ASCII x,y coordinates back to
                  latitude, longitude in degrees
        
        Many users have asked how to convert ASCII x,y coordinates exported
        from VERSAMAP back into latitude, longitude values for use in other
        applications.  This can be done by using the Equirectangular map
        projection to export the data.  The x-axis of the Equirectangular
        projection is directly proportional to longitude; the y-axis is
        directly proportional to latitude.
        
        For an Equirectangular projection, the longitude in degrees
        corresponding a given x coordinate is,
        
        
               longitude =  (longitude range of map)*(x coordinate) +
                            (minimum longitude of map)
        
        
        If the calculated longitude is greater than 180 degrees, subtract
        360 degrees from the calculated value.
        
        


        VMAP.DOC version 1.51                                    Page  39 






        The latitude in degrees corresponding a given y coordinate is,
        
        
           latitude =  (latitude range of map)*(y coordinate)/(relative
                       length of y-axis) + (minimum latitude of map)
        
        
        The relative length of the y-axis used in the above equation is
        given in the Map Parameter Report option of the Input/Output menu,
        under Relative Length of Axes.  The relative length of the x-axis is
        always 1.000000, corresponding to the maximum possible value of the
        x coordinate.  The relative length of the y-axis may be greater than
        or less than unity, depending on the shape of the map.  In your
        calculations, ignore any points with x > 1; these points represent
        polyline breaks.
        
        
        5.10.     Save Great Circle
        
        This option allows the currently defined Great Circle to be written
        to disk for later recall.  The Great Circle is stored in the ASCII
        PRN file format that can be read by VERSAMAP (see Section 7.7,
        Importing Your Own Data into VERSAMAP).  The purpose of saving Great
        Circles to disk is to allow more than one Great Circle to be plotted
        on a map.  To plot more than one Great Circle on a map, export the
        Great Circles as ASCII PRN files, and then import them back into
        VERSAMAP using the Map Input Filenames option of the Input/Output
        menu.
        
        After selecting this option, a window titled ENTER GREAT CIRCLE
        FILENAME appears.  Type in the correct filename and press Enter to
        select the filename.  The cursor will then jump to the < ok >
        button.  Press Enter on the < ok > button to write the file to disk.
        
        The ASCII PRN file contains the same latitude/longitude waypoints
        listed in the Great Circle Report option of the Input/Output menu.
        
        Please note that before saving a Great Circle to disk, you must
        define its endpoints with the Great Circle option of the Map Design
        menu.
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  40 






        6.        Run menu
        
        -----------------------------------------------------------------
          Projection      Map Design      Input/Output      Run
        -----------------------------------------------------------------
                                                          | Size 100% |
                                                          | Size  70% |
                                                          +-----------+
        
        This menu contains 2 items.  Selecting Size 100% will plot the
        largest possible map on the screen.  Selecting Size 70% will plot a
        smaller map with margins around all sides.  The Size 70% option
        allows you to add text in the margins of the map without writing
        over the map itself.
        
        Your map will begin plotting immediately after either item is
        selected.  The program will cease plotting and return to the menu
        bar if Esc is pressed while the map is being drawn.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  41 






        7. Sources of Digital Map Data for use with VERSAMAP
        
        VERSAMAP will generate maps from the following databases, available
        commercially, as shareware, or in the public domain.  In addition,
        the program will accept input in a simple ASCII format.  VERSAMAP
        recognizes the various databases by their file extensions.  The most
        complete databases are (1) the Central Intelligence Agency's World
        Data Bank II (WDB-II), a detailed world map; (2) Micro World Data
        Bank II (MWDB-II), a smaller database derived from World Data Bank
        II; and (3) the U.S. Geological Survey's Digital Line Graph Data
        (USGS DLG), which contains detailed maps of all 50 states.
        
        Which digital map database you use depends on the size of the area
        you wish to map.  For world maps, MWDB-II is the best choice. 
        Although WDB-II can be used to draw world maps, it contains so many
        points that it plots very slowly when used to plot such a large
        area.  WDB-II is best used for maps of continental size or smaller. 
        The USGS DLG data is the best digital map database for plotting maps
        at the state or county level in the United States.
        
        
        7.1.      World Data Bank II (WDB-II)
                  File extensions PKV, PKD
        
        A database, developed by the Central Intelligence Agency, covering
        the entire world.  Latitude and longitude are given to the nearest
        second.  The original database is divided into 13 files containing
        data for Asia, Europe-Africa, North America, and South
        America-Antarctica.  The complete set of 13 files contains 6
        million, 20 character ASCII records, which require 120 million bytes
        of disk space.  WDB-II was last updated in January 1987.
        
        WDB-II was digitized using all available source information.  Maps
        used ranged in scale from 1:750,000 to 1:4,000,000.  Nominal scale
        was 1:3,000,000.  At 1:3,000,000 scale, 1 inch equals 47 statute
        miles (1 cm equals 30 km).  Successive points in the  database are
        never more than 127 seconds (approximately 2 miles or 3 km) of
        latitude or longitude apart.
        
        To make WDB-II easier to use on microcomputers, Micro Doc (3108
        Jackson Street, Bellevue, NE  68005) has reformatted WDB-II in a
        binary format (.PKD file extension).  The binary format reduces
        storage requirements by a factor of 10 (to 12 million bytes), and
        vastly reduces the time required to draw maps.  VERSAMAP can plot
        maps using the binary form of WDB-II (.PKD file extension), and from
        an enhanced version of Micro Doc's .PKD files (.PKV file extension),
        developed specifically for VERSAMAP.
        
        VERSAMAP can plot the following geographic features from World Data
        Bank II in the .PKV or .PKD file formats.
        
        
        


        VMAP.DOC version 1.51                                    Page  42 






                     Geographic Features in World Data Bank II
        
                Rank       Feature Name
              PKV   PKD
        
              Major Category: International Boundaries or Limits of
                              Sovereignty
        
               1     1     International Boundaries
               2     2     Indefinite or in dispute
               3     3     Separation line, land
               4     4     Separation line, sea
               5     5     Separation line, islands
               6     6     Continental Shelf, Persian Gulf
               7     7     Demilitarized zone, Israel
               8     8     No defined boundary
          
              Major Category: Coastlines, Islands, and Lakes
        
               9     1     Coastlines, Islands, Lakes
              10     2     Islands and lakes, large
              11     3     Islands and lakes, medium
              12     4     Islands and lakes, small
              14     6     Intermittent lakes, large
              15     7     Intermittent lakes, small
              16     8     Reefs
              17     9     Salt pans, large
              18    10     Salt pans, small
              21    13     Ice shelves, large
              22    14     Ice shelves, small
              23    15     Glaciers
        
              Major Category: Rivers
        
              24     1     Rivers
              25     2     Rivers, large
              26     3     Rivers, medium
              27     4     Rivers, small
              28     5     Rivers, double lined
              29     6     Intermittent rivers, large
              30     7     Intermittent rivers, medium
              31     8     Intermittent rivers, small
              33    10     Canals
              34    11     Canals, small
              36    13     Canals, irrigation
        
              Major Category: Internal Political Boundaries
        
              37     1     U.S. States
              38     1     Canadian Provinces
              39     3     Boundaries in Great Lakes
              40           Australian States  (not available in)
              41           Scotland and Wales (     .PKD format)


        VMAP.DOC version 1.51                                    Page  43 






        The WDB-II .PKV files, developed specifically for VERSAMAP, differ
        from Micro Doc's .PKD files in 2 respects.
        
        First, .PKV files contain political boundaries for the new countries
        which have formed from the Soviet Union and from Yugoslavia, for
        Slovakia and Eritrea, for Australian States, and for Scotland and
        Wales.  These borders are not included in Micro Doc's .PKD files,
        nor in the original ASCII version of WDB-II.
        
        Second, inspection of the above table shows that the ranks, of
        individual geographic features in Micro Doc's .PKD files, are not
        unique to a single major category (International Boundaries,
        Coastlines, Rivers, or Internal Boundaries).  The duplication of
        ranks between major geographic categories means that .PKD files
        cannot be concatenated into a single large file without losing
        information about which category a particular rank corresponds to. 
        To alleviate this problem, ranks in the specially modified .PKV
        files have been redefined so that they are unique for each
        geographical feature (see above table).  This modification allows
        .PKV files to be concatenated into a single large file for each
        continent.
        
        For use with VERSAMAP, the modified .PKV files were concatenated
        into 5 files, each file containing all geographic features for a
        particular region.  The 5 regions are (1) Africa, (2) Eurasia
        (Europe and Asia), (3) Oceania (Indonesia, Australia, New Zealand,
        and the Pacific Islands), (4) Latin America (including Antarctica),
        and (5) North America (Canada and the United States).  The .PKV
        files for individual regions or for the entire world are available
        on high density, floppy disks from the author.  See Section 11, the
        VERSAMAP Order Form, for details.
        
        As an example of the detail available in WDB-II, the file,
        VMTAIWAN.PKV, which contains all data from WDB-II for the island of
        Taiwan, is included on the VERSAMAP disk.  To plot the map of
        Taiwan,
        
         1.  Set the map boundaries at 26 N to 21 N latitude, and 119 E to 
             123 E longitude using the Map Boundaries option in the Map
             Design menu (use a grid spacing of 1 degree, i.e. 001 00 00).
        
         2.  Import the file VMTAIWAN.PKV into VERSAMAP using the Map Input 
             Filenames option in the Input/Output menu.  Toggle all
             geographic features on in the SELECT WORLD DATA BANK II
             FEATURES list box.
        
         3.  Plot the map using the Size 100% option in the Run menu.
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  44 






        When VERSAMAP plots maps using Micro Doc's packed .PKD files, it
        determines the major category of data being plotted from the third
        letter of the filename of the input file.  In Micro Doc's file
        naming scheme, this letter is unique for each of the 4 major
        geographic categories.  The third letter must be B for .PKD files
        containing International Boundaries or Limits of Sovereignty; it
        must be C for Coastlines, Islands, and Lakes; it must be R for
        Rivers; and it must be P for Internal Political Boundaries.  This
        restriction on filenames is not necessary when you use .PKV files,
        since geographic ranks in .PKV files are unique.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  45 






        7.2.      Micro World Data Bank II (MWDB-II)
                  File extensions PNT, ALL, CCI
        
        A database, covering the entire world, containing 178,000 latitude,
        longitude points.  Latitude and longitude are rounded to the nearest
        minute and stored as six byte binary records.  This database was
        derived from WDB-II by Micro Doc (3108 Jackson Street, Bellevue, NE 
        68005).  An enhanced version of MWDB-II, containing boundaries for
        the new countries which have formed from the Soviet Union and from
        Yugoslavia, for Slovakia and Eritrea, for Canadian Provinces, and
        for Australian States is available from the author.  See Section
        7.3, VERSAMAP Micro World Database, for details.
        
        VERSAMAP can plot the following geographic features from MWDB-II:
        coastlines, islands, lakes, rivers, countries, and U.S. States.
        
        MWDB-II contains several types of digital map files.  The first type
        (file extension .PNT) contains points from a single geographic
        feature at 5 levels of detail.  The second file type (file extension
        .ALL) contains points for all geographic features at a single level
        of detail.  A third MWDB-II file, MWDB5.CCI, contains only country,
        coastline, and island points at the lowest level of detail.  The
        .ALL and .CCI files are made from the .PNT files using the utility
        program, SELECT.EXE, supplied with MWDB-II.  SELECT.EXE allows the
        user to build customized map files containing any number of
        geographic features and levels of detail.  To save disk space,
        MWDB1.ALL and MWDB2.ALL, the 2 largest files, are not included in
        the MWDB-II package.  They are constructed by the user from the .PNT
        files and SELECT.EXE upon receiving MWDB-II.
        
        
                     Summary of Micro World Data Bank II Files
        
           Filename    Size(bytes)   # Points    Comment
        
           MWDB1.ALL    1,068,408     178,068    The entire database
           MWDB2.ALL      652,500     108,750
           MWDB3.ALL      157,176      26,196
           MWDB4.ALL       82,560      13,760
           MWDB5.ALL       27,180       4,530
           MWDB5.CCI       19,110       3,185
        
           COAST.PNT      449,802      74,967    Coastlines
          ISLAND.PNT      211,026      35,171    Islands
            LAKE.PNT       90,708      15,118    Lakes
           RIVER.PNT      169,164      28,194    Rivers
         COUNTRY.PNT      134,154      22,359    Country borders
           STATE.PNT       13,554       2,259    U.S. State borders
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  46 






        7.3.      VERSAMAP Micro World Database
                  File extension MAP
        
        A database containing 196,000 latitude, longitude points.  Latitude
        and longitude are rounded to the nearest minute and stored as six
        byte binary records.  This database is an enhanced version of
        MWDB-II described in Section 7.2.  Both map databases have the same
        file structure.  Enhancements incorporated in the VERSAMAP Micro
        World Database include (1) borders for the new countries which have
        formed from the Soviet Union; (2) borders for Eritrea, Slovakia, and
        the Yugoslav Republics, (3) borders for Canadian Provinces; (4)
        borders for Australian States; (5) more detail for U.S. State
        boundaries; (6) increased detail for the borders of Israel, Oman,
        the United Arab Emirates, and Yemen; and (7) removal of the borders
        between East and West Germany, and between the Yemen Arab Republic
        and the People's Democratic Republic of Yemen.
        
        VMAP1.MAP through VMAP5.MAP, the digital map files supplied with
        VERSAMAP Micro World Database, are enhanced versions of the
        equivalent .ALL files in MWDB-II.
        
        VERSAMAP can plot the following geographic features from VERSAMAP
        Micro World Database: coastlines, islands, lakes, rivers, countries,
        U.S. States, Canadian Provinces, and Australian States.
        
        
                        VERSAMAP Micro World Database Files
        
           Filename      Size      Number     Avg distance between points
                        (bytes)    Points        nautical miles    km
        
           VMAP1.MAP   1,174,788   195,798             4            7 
           VMAP2.MAP     719,670   119,946             6           11 
           VMAP3.MAP     187,122    31,187            19           35 
           VMAP4.MAP      98,490    16,415            33           61 
           VMAP5.MAP      34,944     5,824            72          133 
        
        The complete set of VERSAMAP Micro World Database .MAP files is
        available on floppy disk from the author.  See Section 11, the
        VERSAMAP Order Form, for details.
        
        
        7.4.      USGS Digital Line Graph Data (USGS DLG)
                  File extensions GRF, GRV
        
        A database developed by the U.S. Geological Survey containing
        detailed maps of all 50 states.  The database divides the United
        States into 21 sections.  The digital data for each section contains
        the following major categories: (1) streams and rivers, (2)
        coastlines and lakes, (3) roads, (4), railroads, (5) political
        boundaries, (6) administrative boundaries, (7) cultural features,
        and (8) hypsography.  Each major category contains numerous minor
        categories characterized by the size of the geographic feature.  The
        most recent data in the database dates from 1980.

        VMAP.DOC version 1.51                                    Page  47 






        Data in the USGS DLG database were derived by digitizing 1:2,000,000
        scale maps from the National Atlas of the United States at a
        resolution of 0.001 inch.  At 1:2,000,000 scale, 1 inch equals 32
        statute miles (1 cm equals 20 km).  Successive points in the 
        database are never more than 127 seconds (approximately 2 miles or
        3 km) of latitude or longitude apart.
        
        The database is available on CD-ROM (US GeoData - 1:2,000,000-Scale
        Digital Line Graph (DLG) Data) and can be ordered from the Earth
        Science Information Center, U.S. Geological Survey, 507 National
        Center, Reston, VA  22092.  Phone number: 1-800-USA-MAPS.
        
        VERSAMAP can plot maps using DLG data in the graphic file format
        (.GRF file extension) directly from the above CD-ROM.  These .GRF
        files consist of 20 character ASCII records, in which latitude and
        longitude are given to the nearest second.  The entire set of .GRF
        files, covering all 50 states, occupies 144 million bytes of space
        on the CD-ROM.
        
        To reduce storage requirements, and speed plotting, the ASCII .GRF
        files have been converted to the binary, packed WDB-II format
        mentioned above.  The .GRF files in packed WDB-II format have the
        file extension .GRV.  The packed .GRV files occupy 8 times less disk
        space (18 million bytes) and plot several times faster than the
        original ASCII .GRF files.  Packed .GRV files, for the 21 sections
        of the United States or for the entire country, are available on
        high density, floppy disks from the author.  See Section 11, the
        VERSAMAP Order Form, for details.
        
        As an example of the detail available in the USGS DLG data, the
        file, VMOAHU.GRV, which contains all data from the US GeoData CD-ROM
        for the island of Oahu in the Hawaiian Islands, is included on the
        VERSAMAP disk.  To plot the map of Oahu,
        
         1.  Set the map boundaries at 22 N to 21 N latitude, and 159 W to
             157 W longitude using the Map Boundaries option in the Map
             Design menu (use a grid spacing of 1 degree, i.e. 001 00 00).
        
         2.  Import the file VMOAHU.GRV into VERSAMAP using the Map Input
             Filenames option in the Input/Output menu.  Toggle all
             geographic features on in the SELECT USGS DIGITAL LINE GRAPH
             FEATURES list box.
        
         3.  Plot the map using the Size 100% option in the Run menu.
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  48 






        VERSAMAP can plot the following geographic features using DLG data
        in either .GRF or .GRV file formats.
        
        
                   Geographic Features Included in USGS DLG Data
        
                   #       Feature Name
        
                           Rivers and Streams
        
                   1       River, double line, shoreline
                   2       River, double line, centerline
                   3       River, perennial,        <30 km
                   4       River, perennial,       <100 km
                   5       River, perennial,       <350 km
                   6       River, perennial,      >=350 km
                   7       River, intermittent,     <30 km
                   8       River, intermittent,    <100 km
                   9       River, intermittent,    <350 km
                  10       River, intermittent,   >=350 km
                  11       River in lake, perenn.   <30 km
                  12       River in lake, perenn.   <80 km
                  13       River in lake, perenn.  >=80 km
                  14       River in lake, interm.   <30 km
                  15       River in lake, interm.  >=30 km
                  16       Braided stream
                  17       Canal, navigable,        <20 km
                  18       Canal, navigable,        <80 km
                  19       Canal, navigable,       >=80 km
                  20       Canal, other,            <20 km
                  21       Canal, other,            <80 km
                  22       Canal, other,           >=80 km
                  23       Ditch
                  24       Intercoastal waterway
        
                           Water Bodies
        
                  25       U.S. coastline and Great Lakes
                  26       Lake, island, perennial  <30 km
                  27       Lake, island, perennial  <80 km
                  28       Lake, island, perennial >=80 km
                  29       Lake, intermittent       <30 km
                  30       Lake, intermittent       <80 km
                  31       Lake, intermittent      >=80 km
                  32       Marsh, swamp,            <50 km
                  33       Marsh, swamp,           >=50 km
                  34       Dry lake, alkali flat
                  35       Glacier,                 <50 km
                  36       Glacier,                >=50 km
        
                           Roads and Trails
        
                  37       Interstate highway
                  38       Interstate, proposed

        VMAP.DOC version 1.51                                    Page  49 






                  39       Divided highway, limited access
                  40       Other hwy, limited access
                  41       Other hwy, non-limited access
                  42       Other hwy <10 km from major hwy
                  43       State secondary, all weather
                  44       Light duty, all weather
                  45       Unimproved, fair or dry weather
                  46       Highway, tunnel
                  47       Auto, ferry
        
                           Railroads
        
                  48       Railroad, main line
                  49       Railroad, branch line
                  50       Railroad, other
                  51       Railroad, tunnel
                  52       Railroad, ferry
        
                           Political Boundaries
        
                  53       International treaty line
                  54       National boundary, land
                  55       National boundary, water
                  56       State boundary, land
                  57       State boundary, water
                  58       County, large city, land
                  59       County, large city, water
                  60       City boundary,     >1.0 million
                  61       City boundary,     >0.5 million
                  62       City boundary,            small
        
                           Note that USGS DLG sections 3, 10, 11, and 15
                           through 21 do not contain city boundaries
                           (features 60, 61, 62).                   
        
                           Administrative Boundaries
        
                  63       National park            <20 km
                  64       National park           >=20 km
                  65       National park closure line
                  66       Indian reservation       <20 km
                  67       Indian reservation      >=20 km
                  68       Indian reservation closure line
                  69       Military reservation    <405 ha
                  70       Military reservation   >=405 ha
                  71       Mil. reservation closure line
        
                           Cultural Features
        
                  72       Alaska pipeline
        
        
        


        VMAP.DOC version 1.51                                    Page  50 






        7.5.      World Data Bank I
                  File extension DAT
        
        An obsolete database, covering the entire world, developed by the
        Central Intelligence Agency.  World Data Bank I contains 79,000
        points representing world coastlines.  Latitude and longitude are
        given to the nearest second.  Data are stored as 20 character ASCII
        records on 5, 5.25 inch, 360K disks, which can be ordered from the
        National Technical Information Service, United States Department of
        Commerce, 5285 Port Royal Road, Springfield, VA  22161.
        
        
        7.6.      The World Digitized
                  File extensions MPS, MP1
        
        An obsolete, shareware database containing 100,000 latitude,
        longitude points rounded to thousandths of a degree.  The database
        is available (in both binary and ASCII format) from shareware
        vendors.
        
        The World Digitized database is subdivided into directories, one
        directory for each continent.  Each of the World Digitized
        directories contains 2 or more map files.  To plot the entire World
        Digitized database from VERSAMAP, you will have to concatenate the
        individual .MPS (binary) or .MP1 (ASCII) files, since VERSAMAP will
        not accept more than 9 input files.  The VERSAMAP disks contain 2
        files, VM_FIX.MPS and VM_FIX.MP1, which must be used to concatenate
        World Digitized files for use with VERSAMAP.  These 2 files,
        VM_FIX.MPS and VM_FIX.MP1, force a line break at the end of each
        World Digitized file when it is concatenated.
        
        For example, to concatenate the World Digitized binary .MPS files in
        the Europe subdirectory for use with VERSAMAP, use the following
        form of the DOS copy command:
        
        
          COPY /B E0.MPS + VM_FIX.MPS + E1.MPS + VM_FIX.MPS + E2.MPS +
                                           VM_FIX.MPS + E3.MPS  EUROPE.MPS
        
        
        where EUROPE.MPS is the concatenated file.
        
        A similar procedure (without the binary /B switch) is used to
        concatenate the World Digitized ASCII .MP1 files for use with
        VERSAMAP:
        
        
          COPY E0.MP1 + VM_FIX.MP1 + E1.MP1 + VM_FIX.MP1 + E2.MP1 +
                                           VM_FIX.MP1 + E3.MP1  EUROPE.MP1
        
        
        Spurious diagonal lines will be plotted if you do not insert the
        VM_FIX.MPS or VM_FIX.MP1 files between the World Digitized files
        when they are concatenated for use with VERSAMAP.

        VMAP.DOC version 1.51                                    Page  51 






        7.7.      Importing Your Own Data into VERSAMAP
                  File extensions PRN or UTM
        
        In addition to the above file formats, VERSAMAP will also accept
        data in 2 ASCII formats.  These ASCII formats provide an easy way
        for users to plot their own data with VERSAMAP.  The file extension
        of these ASCII files must be PRN for coordinates in degrees, or UTM
        for coordinates in meters.  The PRN and UTM file formats are
        identical, except for the difference in coordinates.
        
        
        7.7.1.    Record Structure for PRN Files
        
        Coordinates are expressed as latitude and longitude in decimal
        degrees; negative values represent South latitude or West longitude. 
        Use the following formula to convert latitude and longitudes given
        as degrees, minutes, and seconds to decimal degrees:
        
             Decimal lat/lon = degrees + minutes/60 + seconds/3600
        
        For example, the decimal position for Rio de Janeiro, Brazil (22
        degrees, 53 minutes, 43 seconds south latitude; 43 degrees, 13
        minutes, 22 seconds west longitude) is:
        
             Decimal latitude  = -(22 + 53/60 + 43/3600) = -22.8953
             Decimal longitude = -(43 + 13/60 + 22/3600) = -43.2228
        
        The decimal position for Paris, France (48 degrees, 50 minutes, 14
        seconds north latitude; 2 degrees, 20 minutes, 14 seconds east
        longitude) is:
        
             Decimal latitude  = +(48 + 50/60 + 14/3600) = +48.8372
             Decimal longitude = +( 2 + 20/60 + 14/3600) = + 2.3372
        
        Decimal latitude and longitude, input into VERSAMAP, are rounded to
        the nearest second.  The program cannot distinguish between
        positions less than 101 feet (31 meters, 1 second of latitude)
        apart.
        
        
                                  PRN File Format
        
        field #1 - line header:  -1 for new polyline
                                  0 for point within polyline
               field separator:   one or more spaces (ASCII 32)
           field #2 - latitude:   decimal degrees, south latitude is
                                  negative
               field separator:   one or more spaces (ASCII 32)
          field #3 - longitude:   decimal degrees, west longitude is
                                  negative
                 end of record:   carriage return (ASCII 13),
                                  line feed (ASCII 10)
        


        VMAP.DOC version 1.51                                    Page  52 






        7.7.2.    Record Structure for UTM Files
        
        X,Y coordinates are expressed in meters.  Coordinates may contain
        decimal points, but they may not be negative.
        
        
                                  UTM File Format
        
        field #1 - line header:  -1 for new polyline
                                  0 for point within polyline
               field separator:   one or more spaces (ASCII 32)
        
        field #2 - x coordinate:  meters, value must be positive
                field separator:  one or more spaces (ASCII 32)
        
        field #3 - y coordinate:  meters, value must be positive
                  end of record:  carriage return (ASCII 13),
                                  line feed (ASCII 10)
        
        
        Records with these formats can be generated by most word processors,
        text editors, and spreadsheets.
        
        NOTE:     Several VERSAMAP users report getting INPUT PAST END OF
                  FILE error messages when plotting ASCII files.  This error
                  message usually indicates that the ASCII file contains
                  additional carriage returns (blank lines) after the last
                  coordinate in the file.  If you receive this error
                  message, delete any blank lines that occur at the end of
                  your file.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  53 






        7.7.3.    Plotting Sample ASCII Files
        
        The files VMAPUSER.PRN and VMAPUSER.UTM on the VERSAMAP disk are
        short files using the above ASCII formats.
        
        VMAPUSER.PRN contains the names and locations of 4 cities which plot
        as points; plus 5 points in the Indian Ocean which plot as a box
        when the points are connected by lines.
        
        VMAPUSER.UTM contains the names and locations of Belfast and Dublin
        which plot as points; plus 5 points in the center of Ireland which
        plot as a box when the points are connected by lines.
        
        Use these 2 files to study the appearance of the different symbols,
        fonts, and colors that VERSAMAP can plot.
        
        To plot the files,
        
         1.  Select the default Equirectangular projection for VMAPUSER.PRN,
             or the default UTM projection for VMAPUSER.UTM.
         2.  Select the Labels option of the Map Design menu, and choose the
             Display Labels item.
         3.  Select the Map Input Filenames option in the Input/Output menu.
         4.  Tab to filename #2, type VMAPUSER.PRN or VMAPUSER.UTM for the
             filename, and press Enter.
         5.  When the window titled ENTER SYMBOL TYPE, COLOR, & SIZE
             appears, select symbol type Solid square; the color Light
             Magenta; size 03 pixels; and press Enter on the < ok > button.
         6.  When the window titled SELECT LABEL SIZE & COLOR appears,
             select point size 10; label color Light Magenta; PIC font 1;
             and press Enter on the < ok > button.
         7.  When asked for the next filename, tab to the < ok > button and
             press Enter to end filename input.
         8.  To display the file, select the Size 100% option in the Run
             menu. 
        
        The screen will show the individual cities, marked by light magenta
        squares, with their names printed at the lower right corner of the
        square.
        
        The box plots as 4 individual points, because all symbol types,
        except Line, plot as points.  To plot the 4 individual points as a
        box, repeat the above steps, but choose symbol type Line.  In this
        case, the cities plot as light magenta dots, 1 pixel in size, which
        are hard to see; but the points of the box are connected by lines,
        and plot as a rectangle.
        
        To view the contents of VMAPUSER.PRN, type the following command at
        the DOS prompt and press Enter (the word TYPE is part of the
        command).
        
                                 TYPE VMAPUSER.PRN
        
        To view VMAPUSER.UTM, substitute VMAPUSER.UTM for VMAPUSER.PRN.

        VMAP.DOC version 1.51                                    Page  54 






        8.        Use of VERSAMAP with Graphing Programs
        
        VERSAMAP can be used to prepare publication quality maps in
        conjunction with suitable graphing programs.  To be useful in
        preparing maps, a graphing program should be able to:
        
         1.  handle large data sets;
         2.  use more than 1 data set per graph;
         3.  physically separate the X and Y axes, so that they do not show
             on the figure;
         4.  connect individual points on the graph with lines; and
         5.  exclude data which exceeds the X- and Y-axis limits.
        
        
        To print a map using a graphing program, import the map grid and the
        output map boundary files into the program.
        
        If there are two map grid files, the points in the first map grid
        file should be plotted as dots, and the points in the second map
        grid file should be connected by lines.  If there is only one map
        grid file, you can connect the grid points by lines or not,
        depending on how you want the grid to appear.
        
        The X- and Y-axes are scaled using the values of X-axis Length and
        Y-axis Length listed under Relative Length of Axes on the VERSAMAP
        Parameter Report.  The relative X-axis Length is defined as 1.000000
        for all maps; the relative Y-axis Length may be less than or greater
        than unity, depending on the projection and grid chosen.   Starting
        values of the X- and Y-axes should be set at 0.  The ending values
        of the X- and Y-axes will depend on your graphing program, but in
        general they will be one or both of the values listed under Relative
        Length of Axes on the VERSAMAP Parameter Report.
        
        You should configure the graphing program for data clipping (i.e.
        exclude points which lie outside the limits of the X- and Y-axes). 
        This will prevent the dummy points (X = 5.000000), which indicate
        new polylines (see Section 5.9, Save as ASCII), from being plotted.
        
        Map and grid output files produced by VERSAMAP have been
        successfully imported into the technical graphing programs, Grapher
        and SigmaPlot.  For use with SigmaPlot, dummy points (X,Y =
        5.000000) which indicate line breaks in map output files must be
        converted to dashes (X,Y = --------), indicating missing data,
        before the files are imported into SigmaPlot.  Changing the dummy
        points from 5.000000 to -------- can be done using the search and
        replace command in a word processor.
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  55 






        9.        Program Compatibility with Software and Hardware
        
        VERSAMAP has been tested successfully on computers running under DOS
        versions 4.01, 5.00, 6.00, and 6.20.  VERSAMAP should run on any
        computer with DOS 3.0 or higher.
        
        
        9.1.      Running VERSAMAP under Windows
        
        To run VERSAMAP as a DOS program under Microsoft Windows:
        
         1.  Choose the Run option from the File menu in the Program
             Manager.
        
         2.  Type C:\VERSAMAP\VMAP in the Command Line box.  Change the
             drive and path name if VERSAMAP is not stored in a directory
             named VERSAMAP.
        
         3.  Choose the OK button.
        
        
        Run VERSAMAP using the full screen.  Do not run VERSAMAP in a
        Window, since the mouse will not open VERSAMAP menus when the
        program is running in a Window.  If you must work in a Window, use
        the Alt key to open the VERSAMAP menus.
        
        
        9.2.      Memory Requirements
        
        The amount of conventional memory required to run VERSAMAP is
        increased when the Courier or Helvetica fonts are loaded in the
        program.  With no font loaded, VERSAMAP requires at least 443,000
        bytes of free conventional memory.  With the Courier VGA font
        loaded, the program requires 468,000 bytes of free memory.  With the
        Helvetica VGA font loaded, VERSAMAP requires 508,000 bytes of free
        conventional memory.
        
        
        9.3.      Program Overlays
        
        VERSAMAP uses program overlays to minimize conventional memory
        usage.  Overlays are stored in extended or expanded memory and
        loaded into conventional memory as needed.  On computers without
        extended or expanded memory, overlays are loaded from disk.
        
        Due to its use of program overlays, VERSAMAP runs fastest on
        computers equipped with extended or expanded memory.  If extended or
        expanded memory is not available, you will notice a delay, upon
        selecting menu items, as overlays are loaded into memory.  This
        delay is short for hard disks, but can be long when the program is
        run from a floppy disk.  
        
        


        VMAP.DOC version 1.51                                    Page  56 






        9.4. Video Compatibility
        
        VERSAMAP has been tested successfully on systems with EGA and VGA
        adapters and monitors.
        
        Several users have reported that VERSAMAP versions 1.20 and lower
        would not run on their systems because it did not recognize the type
        of video adapter (VGA or EGA) in their computer.  This version of
        VERSAMAP has been modified to allow users to force the program to
        run in a particular video mode.  This is done by adding an
        additional parameter after the word VMAP on the DOS command line
        when VERSAMAP is started.  VERSAMAP recognizes the following command
        line parameters:
        
        
        Command Line     Result
        
        VMAP             Run VERSAMAP, allow program to select video mode
        VMAP VIDEO       Display video monitor and adapter determined by
                           program
        VMAP HELP        Display list of valid command line parameters
        
        VMAP EGA         Force program to run in color EGA mode
        VMAP EGAMONO     Force program to run in monochrome EGA mode
        VMAP VGA         Force program to run in color or monochrome VGA
                           mode
        
        
        If VERSAMAP cannot recognize the video system in your computer, you
        will receive the error message "VERSAMAP 1.51 does not support your
        monitor and/or video display adapter!".  If you receive this error
        message, and you know the type of video adapter and monitor in your
        system, you can force VERSAMAP to run in that video mode by using
        one of the above commands.
        
        For instance, to force VERSAMAP to run in color EGA mode on a
        computer known to contain an EGA video adapter and a color EGA
        monitor, type the command VMAP EGA at the DOS prompt and then press
        Enter.
        
        
        10.       Installing VERSAMAP
        
        Installation of VERSAMAP is described in the file VMAPREAD.ME. 
        Please read VMAPREAD.ME for instructions on how to install the
        program on your hard drive.  Due to its size, VERSAMAP cannot be run
        from a low-density 5.25", 360K floppy disk.
        
        To run VERSAMAP, once it has been installed, change to the directory
        containing the VERSAMAP files, type VMAP at the DOS prompt, and then
        press the Enter key.
        
        


        VMAP.DOC version 1.51                                    Page  57 






        11.       VERSAMAP Order Form (version 1.51)              page 1/3
        
        
        Make checks payable to Charles Culberson.  Persons living outside
        the United States can register VERSAMAP by obtaining a Postal Money
        Order payable in U.S. dollars from their National Post Office; or by
        personal check in their local currency at the current exchange rate. 
        Send order form and comments to:
        
                                 Charles Culberson
                                 8 Ritter Lane
                                 Newark, DE  19711
                                 USA
        
        
        ------------------ Registration, version 1.51 ------------------
        
        Date: __________________________________________________________
        
        Where did you obtain VERSAMAP? _________________________________
        
        Your Name: _____________________________________________________
        
        E-mail Address: ________________________________________________
        
        Postal Address: ________________________________________________
        
        ________________________________________________________________
        
        ________________________________________________________________
        
        ________________________________________________________________
        
        
        Please mark the floppy disk size that you would like the VERSAMAP
        files supplied on.
        
                                 5.25" 1.2M                    3.5" 1.4M
        
        
        --------------------------- Comments ---------------------------
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  58 






        11.       VERSAMAP Order Form (version 1.51)              page 2/3
        
        
        Item                                                           Cost
        
        1.  VERSAMAP, registered copy , $15                          ______
        
        Most recent version of mapping program plus Helvetica
        fonts, maps VMAP3.MAP (31,000 points) and VMAP5.MAP
        (6,000 points), and gazetteer containing positions of
        over 600 world cities.
        
        
        2.  Printed Manual, $15                                      ______
        
        Printed copy of VERSAMAP instruction manual with clear
        plastic cover.  The text of the printed manual is
        identical to the text of the manual, VMAP.DOC, included
        on the VERSAMAP disk.
        
        
        3.  VERSAMAP Micro World Database, $15                       ______
        
        Complete set of 5 maps, VMAP1.MAP (196,000 points) to
        VMAP5.MAP (6,000 points).  See Section 7.3 of
        instruction manual for details.
        
        
        4.  World Data Bank II in VERSAMAP .PKV format.  See
            Section 7.1 of instruction manual for details.
        
        Region            Comments
        
        Africa            Suez Canal divides Africa and Eurasia
        Eurasia           includes Japan and Taiwan
        Latin America     Mexico to Chile, including Antarctica 
        North America     Canada, United States (Hawaii is in Oceania)
        Oceania           Indonesia, Philippines, Australia, New
                          Zealand, and Pacific Islands
        
        
        ------- Circle regions wanted -------
        
        Region            Number of      Cost
                            Disks
        
        Africa                2           $10
        Eurasia               5           $25
        North America         3           $15
        Latin America         2           $10
        Oceania               1           $ 5
        
                           Total cost of World Data Bank II files.   ______


        VMAP.DOC version 1.51                                    Page  59 






        11.       VERSAMAP Order Form (version 1.51)              page 3/3
        
        
        Item                                                           Cost
        
        5.  USGS Digital Line Graph data in VERSAMAP .GRV format.
            See Section 7.4 of instruction manual for details.
        
        
        -------------- Circle sections wanted --------------
        
          USGS         States on disk(s)                    Number of
        Sections                                                Disks
        
        01            CT, MA, ME, NY, VT, NH, RI                 1
        02            DE, MD, OH, NJ, PA, VA, WV                 1
        03, 04        FL, GA, NC, SC                             1
        05            AL, AR, LA, MS, TN                         2
        06            IA, IL, IN, KY, MO                         2
        07            MI, MN, WI                                 1
        08            TX     (TX in section 09 also)             1
        09            TX, OK (TX in section 08 also)             1
        10            CO, KS, NE                                 1
        11            MT, ND, SD, WY (MT in section 15 also)     1
        12            AZ, NM                                     1
        13, 14, 21    CA, HI, NV, UT                             1
        15            ID, MT, OR, WA (MT in section 11 also)     1
        16 thru 20    AK                                         5
        
        
                       Total cost of USGS Digital Line Graph files
                                    (number of disks x $5 per disk). ______
        
        
        6.  $5 charge for shipping to addresses outside the U.S.
                                                          or Canada. ______
        
        
        7.  $7 charge for checks drawn on foreign banks in foreign
            currency.  Except for Canadian banks, I cannot accept
            checks drawn on foreign banks in U.S. currency.  There
            is no charge for checks drawn on U.S. banks.             ______
        
        
        
        
            Minimum order is $15.  Total cost of items 1 through 7,
            or $15, whichever is greater.                            ______
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  60 






        12.       Acknowledgements
        
        
        VERSAMAP is written in Microsoft Visual Basic for MS-DOS.  VERSAMAP
        uses the font files COURB.FON, COURE.FON, HELVB.FON, and HELVE.FON
        supplied with Microsoft BASIC 7.0.  Portions(C) 1982-1989 Microsoft
        Corporation.  All rights reserved.
        
        VERSAMAP uses routines from the PCX Programmer's Toolkit, Copyright
        (c) Genus Microprogramming, Inc.  1988-1990.
        
        VERSAMAP uses the QuickWindows Advanced User Interface Library which
        is Copyrighted 1990 by Software Interphase, Inc.
        
        The boundary files, VMAP1.MAP through VMAP5.MAP, contain data from
        Micro World Data Bank II, a digital map database placed in the
        Public Domain by Fred Pospeschil and Antonio Riveria.
        
        The enhanced World Data Bank II files (.PKV file extension)
        distributed with VERSAMAP are derived from the packed, binary
        version of World Data Bank II (.PKD file extension) developed and
        placed in the Public Domain by Fred Pospeschil (Micro Doc, 3108
        Jackson Street, Bellevue, NE  68005, USA).
        
        AutoCAD is a registered trademark of Autodesk, Inc.  CorelDRAW is
        copyrighted by Corel Systems Corporation.  Epson is a registered
        trademark of Epson America, Inc.  Grapher is a trademark of Golden
        Software, Inc.  Hewlett-Packard is a registered trademark of
        Hewlett-Packard Company.  Lotus and 1-2-3 are registered trademarks
        of Lotus Development Corporation.  Microsoft is a registered
        trademark and Windows, Visual Basic, and MS-DOS are trademarks of
        the Microsoft Corporation.  SigmaPlot is a trademark of Jandel
        Corporation.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  61 






        13.       Glossary
        
        
        Aspect:   Conceptual placement of a projection in relation to the
           earth's axis (polar, equatorial, oblique).
        
        Azimuthal projection:   Projection on which the azimuth or direction
           from the central point to any other point is shown correctly.
           The scale of an azimuthal projection is constant along the
           circumference of any circle centered on the map center.
        
        Central meridian:   Meridian passing through the center of a
           projection, often a straight line about which the projection is
           symmetrical.
        
        Conformal projection:   Projection on which all angles at each point
           are preserved.  On a conformal projection the scale is the same
           in all directions at a given point.
        
        Conic projection:   Projection resulting from the conceptual
           projection of the earth onto a tangent or secant cone, which is
           then cut lengthwise and laid flat.
        
        Cylindrical projection:   Projection resulting from the conceptual
           projection of the earth onto a tangent or secant cylinder, which
           is then cut lengthwise and laid flat.
        
        Ellipsoid:   A solid geometric figure formed by rotating an ellipse
           about its shorter axis.
        
        Equal-area projection:   Projection on which the areas of all
           regions are shown in the same proportion to their true areas. 
           Shapes may be greatly distorted.
        
        Equatorial aspect:   Aspect of a projection on which the center of
           projection or the origin is some point along the Equator.
        
        Equidistant projection:   Projection that maintains constant scale
           along all great circles from one or two points.
        
        Great circle:   Any circle on the surface of the earth (assumed to
           be a sphere) formed by the intersection of the surface with a
           plane passing through the center of the earth.  It is the
           shortest distance between any two points on the circle and
           therefore important for navigation.  All meridians and the
           Equator are great circles.
        
        Grid:   Network of lines representing a selection of the earth's
           parallels and meridians.
        
        Kilometer:   Unit of length in the metric system.  1 km = 1000
           meters = 0.53961 nautical miles = 3280.8 feet.
        


        VMAP.DOC version 1.51                                    Page  62 






        Latitude:   Angle made by a perpendicular to a given point on the
           surface of the earth and the plane of the Equator, north or south
           to 90 degrees.  One of the two common geographic coordinates of
           a point on the earth.
        
        Longitude:   Angle made by the plane of a meridian passing through
           a given point on the earth's surface and the plane of the (prime)
           meridian passing through Greenwich, England, east or west to 180
           degrees.  One of the two common geographic coordinates of a point
           on the earth.
        
        Meridian:   Reference line on the earth's surface formed by the
           intersection of the surface with a plane passing through both
           poles and some third point on the surface.  This line is
           identified by its longitude.  On the earth, this line is half a
           great circle.
        
        Meter:   Basic unit of distance in the metric system.  Originally
           defined as 1/10,000,000 of the distance from the equator to the
           poles.  Consequently, 90 degrees of latitude is approximately
           equal 10,000,000 meters.  1 meter = 3.2808 feet.
        
        Nautical mile:   One minute of arc along a great circle.  For a
           spherical earth of radius 6371 km, 1 nautical mile = 1853.2
           meters = 6080 feet = 1 minute of arc.  Consequently, 1 degree
           of arc = 60 minutes of arc = 60 nautical miles.
        
        Oblique aspect:   Aspect of a projection on which the center of the
           projection or the origin is located at a point which is neither
           at a pole nor along the Equator.
        
        Parallel:  Small circle on the surface of the earth formed by the
           intersection of the surface with a plane parallel to the plane of
           the Equator.  This line is identified by its latitude.  The
           Equator (a great circle) is also treated as a parallel.
        
        Polar aspect:   Aspect of a projection on which the earth is viewed
           from the polar axis.
        
        Radius of the earth:   VERSAMAP assumes that the earth is a sphere
           of radius 6371 km for all projections except the Universal
           Transverse Mercator.
        
        Scale:  Ratio of the distance on a map to the corresponding distance
           on the earth; usually stated in the form 1:5,000,000, for
           example.
        
        Secant cone, cylinder:   A secant cone or cylinder intersects the
           earth's surface along two separate lines.
        
        Small circle:   Circle formed by the intersection of the earth's
           surface and a plane that does not pass through the center of the
           earth.  Parallels of latitude, other than the Equator, are small
           circles.

        VMAP.DOC version 1.51                                    Page  63 






        Spheroid:   A solid geometric figure formed by rotating an ellipse
           about its shorter axis.
        
        Standard parallel:   A parallel of latitude along which the scale of
           the map is correct.  There are one or two standard parallels on
           most cylindrical and conic map projections.
        
        Statute mile:   Unit of distance on land.  1 statute mile = 5280
           feet = 1.60934 km = 0.86842 nautical miles.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  64 






        14.       References
        
        
        When plotting maps with VERSAMAP it is useful to have an atlas handy
        to determine the latitude/longitude coordinates of the area you wish
        to plot.  An easy to use, up-to-date, and reasonably priced atlas is
        the:
        
             Quick Reference World Atlas.  1995.  Rand McNally & Company,
             Chicago.  58 pages.  $5.95.  ISBN 0-528-83733-8.
        
        
        A easily understandable book on the theory of map projections is:
        
             Porter W. McDonnell.  1991.  Introduction to Map Projections. 
             Second edition.  Landmark Enterprises, 10324 Newton Way, Rancho
             Cordova, California  95670.  198 pages.  ISBN 0-8247-6830.
        
        
        The map projections and equations used in this program, along with
        most of the definitions in the Glossary are taken from:
        
             John P. Snyder.  1987.  Map Projections - A Working Manual. 
             U.S. Geological Survey Professional Paper 1395.  U.S.
             Government Printing Office.  383 pages.
        
             John P. Snyder and Philip M. Voxland.  1989.  An Album of Map
             Projections.  U.S. Geological Survey Professional Paper 1453. 
             U.S. Government Printing Office.  249 pages.
        
        
        A detailed, technical book on map projections is:
        
             D. H. Maling.  1992.  Coordinate Systems and Map Projections. 
             Second edition.  Pergamon Press, Oxford.  476 pages.
             ISBN 0-08-037234-1.
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        
        


        VMAP.DOC version 1.51                                    Page  65 






        15.       Index
        
        
        Acknowledgements . . . . . . . . . . . . . . . . . . . . . . 1, 61
        Add Text to Map. . . . . . . . . . . . . . .16, 25, 28, 30, 37, 39
        Administrative boundaries. . . . . . . . . . . . . . . . . .47, 50
        Afghanistan. . . . . . . . . . . . . . . . . . . . . . . . . . .19
        Africa . . . . . . . . . . . . . . . . . . . . . . .19, 42, 44, 59
        Airy . . . . . . . . . . . . . . . . . . . . . . . . . . . .19, 20
        Alaska pipeline. . . . . . . . . . . . . . . . . . . . . . . . .50
        Albers equal-area. . . . . . . . . . . . . . . . . .10, 12, 16, 22
        ALL. . . . . . . . . . . . . . . . . . . . . . . . .25, 34, 46, 47
        Alt. . . . . . . . . . . . . . . . . . . . . . . . . . 4-6, 27, 56
        Antarctica . . . . . . . . . . . . . . . . . . . . . . .42, 44, 59
        ASCII. . . . . . . .2, 28-30, 32, 34, 35, 38-40, 42, 44, 48, 51-55
        Aspect . . . . . . . . . . . . . . . . . . . . . . . . .13, 62, 63
        Association of Shareware Professionals . . . . . . . . . . . . . 4
        Australia. . . . . . . . . . . . . . . . . . . . . . . . . .44, 59
        Australian states. . . . . . . . . . . . . .24, 25, 43, 44, 46, 47
        AutoCAD. . . . . . . . . . . . . . . . . . . . . . . . . . .27, 61
        Azimuthal. . . . . . . . . . . . . . . . 10, 13, 14, 16-18, 24, 62
        Azimuthal equal-area . . . . . . . . . . . . . . . .10, 14, 17, 24
        Azimuthal equidistant. . . . . . . . . . . . . . . .10, 13, 17, 24
        Background color . . . . . . . . . . . . . . . . . . 7, 16, 30, 36
        Bessel . . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
        Boundary file. . . . . . . . . . . . . . . . . . . . . . . . . .34
        Britain. . . . . . . . . . . . . . . . . . . . . . . . . . .19, 20
        Burma. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
        Canada . . . . . . . . . . . . . . . . . . . . . . . . .44, 59, 60
        Canadian provinces . . . . . . . . . . . . . . .24, 25, 43, 46, 47
        CCI. . . . . . . . . . . . . . . . . . . . . . . . . . .25, 34, 46
        Central latitude of the map. . . . . . . . . . . . . . . . . . .18
        Central longitude of the map . . . . . . . . . . . . . . . . . .18
        CGM. . . . . . . . . . . . . . . . . . . . . .2, 27-30, 32, 37, 38
        Chile. . . . . . . . . . . . . . . . . . . . . . . . . . . .19, 59
        China. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
        Clarke . . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
        CNF. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .31
        Coastlines . . . . . . . . . . . . . . . . . . . . . 24, 43-47, 51
        Color. . . . . . . . . . . . .7, 16, 23-26, 30, 33, 34, 36, 54, 57
        Command line . . . . . . . . . . . . . . . . . . . . . . . .56, 57
        Compatibility. . . . . . . . . . . . . . . . . . . . . . 1, 56, 57
        Configuration file . . . . . . . . . . . . . . . . . . . . . . .31
        Conformal. . . . . . . . . . . . . . . . . . . . 10-13, 16, 22, 62
        Conformal conic. . . . . . . . . . . . . . . . . . .10, 12, 16, 22
        Conic. . . . . . . . . . . . . . . . . . . .10, 12, 16, 22, 62, 64
        CorelDRAW. . . . . . . . . . . . . . . . . . . . . . . . . .38, 61
        Countries. . . . . . . . . . . . . . . . . . . .20, 24, 44, 46, 47
        COUR_EGA.FON . . . . . . . . . . . . . . . . . . . . . . . . 2, 28
        COUR_VGA.FON . . . . . . . . . . . . . . . . . . . . . . . . 2, 28
        Courier. . . . . . . . . . . . . . . . . . . 2, 25, 26, 28, 29, 56
        Cylindrical. . . . . . . . . . . . . . . . . . . . . . .10, 62, 64
        DAT. . . . . . . . . . . . . . . . . . . . . . . . . . . . .33, 51
        Data clipping. . . . . . . . . . . . . . . . . . . . . . . . . .55

        VMAP.DOC version 1.51                                    Page  66 






        Default. . . . . . . 1, 4, 5, 9, 13, 17-25, 29, 33, 34, 36, 38, 54
        Degree sign. . . . . . . . . . . . . . . . . . . . . . . . . . .27
        Degrees of latitude between grid marks . . . . . . . . . . .17, 18
        Degrees of longitude between grid marks. . . . . . . . . . .17, 18
        Digital Line Graph . . . . . . . . . . . 1, 25, 34, 42, 47, 48, 60
        Digital map. . . . . . . . 1, 2, 4, 25, 33, 34, 39, 42, 46, 47, 61
        Directory. . . . . . . . . . . . . . .4, 29, 31-33, 35, 51, 56, 57
        Disclaimer . . . . . . . . . . . . . . . . . . . . . . . . . .1, 3
        Disk directory . . . . . . . . . . . . . . . . . . . . . . .32, 35
        Display Previous Text. . . . . . . . . . . . . . . .16, 29, 31, 37
        Distance above surface in kilometers . . . . . . . . . . . . . .18
        DOS. . . . . . . . . . . . . . . . 3, 5, 6, 27, 51, 54, 56, 57, 61
        Dot matrix . . . . . . . . . . . . . . . . . . . . . . . 2, 32, 36
        DXF. . . . . . . . . . . . . . . . . . . . . .2, 27-30, 32, 37, 38
        Easternmost longitude of the map . . . . . . . . . . . . . . . .17
        Easting. . . . . . . . . . . . . . . . . . . . . . . . .15, 19, 20
        EGA. . . . . . . . . . . . . . . . . . . . . . 2-4, 28, 29, 32, 57
        Ellipsoid. . . . . . . . . . . . . . . . . . . . . .10, 14, 15, 62
        Equal-area . . . . . . . . . . . . . 10-12, 14, 16, 17, 22, 24, 62
        Equatorial . . . . . . . . . . . . . . . . . . . . . . .11, 19, 62
        Equidistant. . . . . . . . . . . . . . . 10-14, 16, 17, 22, 24, 62
        Equidistant conic. . . . . . . . . . . . . . . . . .10, 12, 16, 22
        Equirectangular. . . . . . . . . . 4, 9-11, 16, 17, 23, 38, 39, 54
        Eritrea. . . . . . . . . . . . . . . . . . . . . . . . .44, 46, 47
        Error message. . . . . . . . . . . . . . 9, 17, 18, 21, 22, 53, 57
        Esc. . . . . . . . . . . . . . . . . . .5-7, 9, 27, 28, 35, 36, 41
        Eurasia. . . . . . . . . . . . . . . . . . . . . . . . . . .44, 59
        Europe . . . . . . . . . . . . . . . . . . . . . . .19, 42, 44, 51
        Everest. . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
        Exit . . . . . . . . . . . . . . . . 1, 5-7, 10, 17, 22-24, 35, 36
        Export . . . . . . . . . . . . . . . . . . . 26, 29, 30, 32, 38-40
        F1 . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .35
        Filename . . . . . . . . . . .24, 25, 31, 33, 34, 36-40, 45-47, 54
        FON. . . . . . . . . . . . . . . . . . . . . . . . . . . 2, 28, 61
        Font . . . . . . . . . . . . . . 2, 16, 25, 26, 28, 29, 54, 56, 61
        Format . . . . . . . . . . . 34, 38, 40, 42, 43, 48, 51-53, 59, 60
        France . . . . . . . . . . . . . . . . . . . . . . . . . 6, 19, 52
        Gauss-Kruger . . . . . . . . . . . . . . . . . . . .14, 15, 19, 20
        Geographic Feature . . . . . . . . . . . . . . .24, 34, 38, 46, 47
        Geological Survey. . . . . . . . . . . . . .25, 34, 42, 47, 48, 65
        Germany. . . . . . . . . . . . . . . . . . . . . . . . . . . . .47
        Gnomonic . . . . . . . . . . . . . . . . . . . . . .10, 13, 17, 24
        Grapher. . . . . . . . . . . . . . . . . . . . . . . . . . .55, 61
        Graphing program . . . . . . . . . . . . . . . . . . . . . .32, 55
        Great Circle . . . . . . . . . . . . . .16, 23, 32, 35, 40, 62, 63
        Great Circle Report. . . . . . . . . . . . . . . . .23, 32, 35, 40
        GRF. . . . . . . . . . . . . . . . . . . . . . . . . . . 34, 47-49
        Grid color . . . . . . . . . . . . . . . . . . . . . . .16, 30, 36
        Grid file. . . . . . . . . . . . . . . . . . . . . . . . . .38, 55
        Grid type. . . . . . . . . . . . . . . . . . . . . .16, 24, 35, 38
        GRV. . . . . . . . . . . . . . . . . . . . . . . .2, 34, 47-49, 60
        Hammer equal-area. . . . . . . . . . . . . . . . . . . .10, 11, 16
        Hawaii . . . . . . . . . . . . . . . . . . . . . . . . . . . . .59
        HELV_EGA.FON . . . . . . . . . . . . . . . . . . . . . . . . 2, 28

        VMAP.DOC version 1.51                                    Page  67 






        HELV_VGA.FON . . . . . . . . . . . . . . . . . . . . . . . . 2, 28
        Helvetica. . . . . . . . . . . . . . .2, 4, 25, 26, 28, 29, 56, 59
        Import . . . . . . . . . . . . . . .26, 29, 32, 38, 40, 44, 48, 55
        Index. . . . . . . . . . . . . . . . . . . . . . . . . . . . 1, 66
        India. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
        Indonesia. . . . . . . . . . . . . . . . . . . . . . . .19, 44, 59
        Input field. . . . . . . . . . . . . . . . . . . . . . . . . . . 7
        Input file . . . . . . . . . . . . . . . .5, 9, 25, 33, 34, 38, 45
        Input past end of file . . . . . . . . . . . . . . . . . . . . .53
        Input/Output menu. . .1, 19, 23, 25, 28, 30, 32, 36-40, 44, 48, 54
        Installing VERSAMAP. . . . . . . . . . . . . . . . . . . .1, 3, 57
        Ireland. . . . . . . . . . . . . . . . . . . . . . . . .19, 20, 54
        Islands. . . . . . . . . . . . . . . . . . . . . . . 24, 43-48, 59
        Israel . . . . . . . . . . . . . . . . . . . . . . . . . . .43, 47
        Japan. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .59
        Krasovsky. . . . . . . . . . . . . . . . . . . . . . . . . .19, 20
        Labels . . . . . . . . . . . . . . . . . . . . .16, 29, 30, 34, 54
        Lakes. . . . . . . . . . . . . . . . . . . . . . 24, 43, 45-47, 49
        Laser. . . . . . . . . . . . . . . . . . . . . . . . . . 2, 32, 36
        Latin America. . . . . . . . . . . . . . . . . . . . . . . .44, 59
        Latitude . . . . . . . . . . . .1, 5, 6, 16-22, 35, 39, 40, 52, 63
        Latitude and longitude limits. . . . . . . . . . .7, 8, 16, 17, 21
        Layer. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .38
        Letter B . . . . . . . . . . . . . . . . . . . . . . . . . . . . 7
        Letter T . . . . . . . . . . . . . . . . . . . . . . . . . . . . 7
        List box . . . . . . . . . . . . . . . . .7, 8, 24, 34, 35, 44, 48
        Longitude. . . . . . . . . . . . . .1, 5, 6, 16-22, 35, 39, 52, 63
        Lotus. . . . . . . . . . . . . . . . . . . . . . . . . .26, 32, 61
        MAP. . . . . . . . . . . . . . . . 2, 4, 5, 25, 33, 34, 47, 59, 61
        Map Boundaries . . . . . . . . . . . . . . 7, 8, 16-18, 20, 44, 48
        Map Design menu. . . .1, 16, 25, 28, 30, 31, 35-38, 40, 44, 48, 54
        Map Input Filenames. . . . . . . . . . .25, 32, 33, 38, 40, 48, 54
        Map Parameter Report . . . . . . . . . . . . . . 19, 32, 35-37, 40
        Math coprocessor . . . . . . . . . . . . . . . . . . . . . . . . 3
        Menu . . 1, 4-10, 16, 19, 23, 25, 27, 28, 30-32, 35-41, 44, 48, 54
        Menu bar . . . . . . . . . . . . . . . . . . 4-7, 9, 27, 35-37, 41
        Mercator . . . . . . . . . . . . . . . . . . .9-11, 14, 16, 17, 63
        Meridian . . . . . . . . . . . . . . 5, 11, 12, 14, 15, 18, 62, 63
        Mexico . . . . . . . . . . . . . . . . . . . . . . . . . . . . .59
        Micro Doc. . . . . . . . . . . . . . . . . . . . . . 42, 44-46, 61
        Micro World Data Bank II . . . . . . . . .1, 7, 24, 34, 42, 46, 61
        Microsoft Windows. . . . . . . . . . . . . . . . . . . . . . . .56
        Mouse. . . . . . . . . . . . . . . . . . . . . 4, 6, 7, 27, 28, 56
        MP1. . . . . . . . . . . . . . . . . . . . . . . . . . . 2, 33, 51
        MPS. . . . . . . . . . . . . . . . . . . . . . . . . . . 2, 33, 51
        MWDB-II. . . . . . . . . . . . . . . . . . . . .24, 25, 42, 46, 47
        National Grid. . . . . . . . . . . . . . . . . . . . . . . . . .20
        New Zealand. . . . . . . . . . . . . . . . . . . . . . . . . . .44
        North America. . . . . . . . . . . . . . . . . . . .19, 42, 44, 59
        Northernmost latitude of the map . . . . . . . . . . . . . . . .17
        Northing . . . . . . . . . . . . . . . . . . . . . . . . 15, 19-21
        Oahu . . . . . . . . . . . . . . . . . . . . . . . . . . . . 2, 48
        Oblique. . . . . . . . . . . . . . . . . . . . . . . . . . .62, 63
        Oceania. . . . . . . . . . . . . . . . . . . . . . . . . . .44, 59

        VMAP.DOC version 1.51                                    Page  68 






        Oman . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .47
        Ombudsman. . . . . . . . . . . . . . . . . . . . . . . . . . . . 4
        Order form . . . . . . . . . . . . . . .1, 2, 4, 44, 47, 48, 58-60
        Orthographic . . . . . . . . . . . . . . . . . . . .10, 13, 17, 24
        Output file. . . . . . . . . . . . . . . . . . . . . . .27, 38, 39
        Pakistan . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
        Parallel . . . . . . . . . . . . . . . . . .11, 12, 22, 23, 63, 64
        PCX. . . . . . . . . . . . . . . . . 2, 27, 28, 30, 32, 36, 37, 61
        Philippines. . . . . . . . . . . . . . . . . . . . . . . . .19, 59
        PIC. . . . . . . . . . . . . . . . . . . .2, 25-30, 32, 37, 38, 54
        PIC font . . . . . . . . . . . . . . . . . . . . . . . .25, 26, 54
        PKD. . . . . . . . . . . . . . . . . . . . . . . . . 34, 42-45, 61
        PKV. . . . . . . . . . . . . . . . . . . . . .2, 34, 42-45, 59, 61
        PNT. . . . . . . . . . . . . . . . . . . . . . . . . . .25, 33, 46
        Point size . . . . . . . . . . . . . . . . . . . . .25, 29, 34, 54
        Polar. . . . . . . . . . . . . . . . . . . . . .11, 13, 15, 62, 63
        Political boundaries . . . . . . . . . . . . . . 38, 43-45, 47, 50
        Polyline . . . . . . . . . . . . . . . . . . . .33, 39, 40, 52, 53
        Print Map. . . . . . . . . . . . . . . . . . . .27, 28, 30, 32, 36
        Printer. . . . . . . . . . . . . . . . . . . . . . . . . . .32, 36
        Printer port . . . . . . . . . . . . . . . . . . . . . . . . . .36
        PrintGraph . . . . . . . . . . . . . . . . . . . . . . . . . . .26
        PRN. . . . . . . . . . . . . . . .2, 4, 29, 30, 33, 34, 40, 52, 54
        Projection menu. . . . . . . . . . . . . . . . . . . . 1, 5, 6, 10
        Pull-down menu . . . . . . . . . . . . . . . . . . . . . . . . . 9
        Pushbutton . . . . . . . . . . . . . . . . . . . . . . . . . . . 8
        Radius of earth. . . . . . . . . . . . . . . . . . .10, 14, 19, 63
        Railroads. . . . . . . . . . . . . . . . . . . . . . . .38, 47, 50
        Range of map in degrees. . . . . . . . . . . . . . . . . . . . .18
        Recall Map Design. . . . . . . . . . . . . . . . . . . . . .16, 31
        REGISTER.DOC . . . . . . . . . . . . . . . . . . . . . . . . .2, 4
        Registration . . . . . . . . . . . . . . . . . . . . . 1, 3, 4, 58
        Rivers . . . . . . . . . . . . . . . . . . . . . 24, 38, 43-47, 49
        Robinson . . . . . . . . . . . . . . . . . . . . . . . .10, 12, 16
        Run menu . . . . . . . . . 1, 4, 9, 23, 31, 37, 39, 41, 44, 48, 54
        Satellite. . . . . . . . . . . . . . . . . . . . . . . . . . . .18
        Save as ASCII. . . . . . . . . . . . . . . . . .28, 32, 38, 39, 55
        Save as CGM. . . . . . . . . . . . . . . . . . . . .27, 30, 32, 37
        Save as DXF. . . . . . . . . . . . . . . . . . . . . . .27, 32, 37
        Save as PCX. . . . . . . . . . . . . . . . . . .27, 28, 30, 32, 36
        Save as PIC. . . . . . . . . . . . . . . . . . . . . . .27, 32, 37
        Save Great Circle. . . . . . . . . . . . . . . . . . . . . .32, 40
        Save Map Design. . . . . . . . . . . . . . . . . . . . . . .16, 31
        Scotland . . . . . . . . . . . . . . . . . . . . . . . . . .43, 44
        Select Font. . . . . . . . . . . . . . . . . . . . . . .16, 28, 29
        Select Printer . . . . . . . . . . . . . . . . . . . . . . .32, 36
        Shareware. . . . . . . . . . . . . . . . . . . . . . . 2-4, 42, 51
        SigmaPlot. . . . . . . . . . . . . . . . . . . . . . . . . .55, 61
        Size 100%. . . . . . . . . . . . . . . . 4, 37, 39, 41, 44, 48, 54
        Size 70% . . . . . . . . . . . . . . . . . . . . . . . .37, 39, 41
        Slovakia . . . . . . . . . . . . . . . . . . . . . . . .44, 46, 47
        Sources of digital map data. . . . . . . . . . . . . . . . . 1, 42
        Southernmost latitude of the map . . . . . . . . . . . . . . . .17
        Soviet Union . . . . . . . . . . . . . . . . . . . .19, 44, 46, 47

        VMAP.DOC version 1.51                                    Page  69 






        Spheroid . . . . . . . . . . . . . . . . . . . . . . . .19, 20, 64
        Standard Parallel. . . . . . . . . . . . . . . . . . . .22, 23, 64
        States . . . . . . . . . . . . 12, 24, 25, 42-44, 46-48, 51, 58-60
        Stereographic. . . . . . . . . . . . . . . .10, 13, 15, 17, 18, 24
        Streams. . . . . . . . . . . . . . . . . . . . . . . . . . .47, 49
        Suez canal . . . . . . . . . . . . . . . . . . . . . . . . . . .59
        Symbol . . . . . . . . . . . . . . . . . . . . . . . . . . .33, 54
        Tab. . . . . . . . . . . . . . 7, 8, 22, 23, 27, 33, 34, 36-39, 54
        Taiwan . . . . . . . . . . . . . . . . . . . . . . . . . 2, 44, 59
        Text . . . . . . . . . 2, 8, 16, 25-31, 34, 36, 37, 39, 41, 53, 59
        Text # . . . . . . . . . . . . . . . . . . . . . . . . . . .25, 28
        Thailand . . . . . . . . . . . . . . . . . . . . . . . . . . . .19
        U.S. Geological Survey . . . . . . . . . . .25, 34, 42, 47, 48, 65
        U.S. states. . . . . . . . . . . . . . . . . . . . .24, 43, 46, 47
        United Arab Emirates . . . . . . . . . . . . . . . . . . . . . .47
        United States. . . . . . . . . .12, 25, 42, 44, 47, 48, 51, 58, 59
        Universal Transverse Mercator. . . . . . . . . . . . . . . .10, 14
        USGS . . . . . . . . . . . . . . . . . . . 1, 2, 25, 42, 47-50, 60
        USGS DLG . . . . . . . . . . . . . . . . . . . . .2, 25, 42, 47-50
        UTM. . . . . . . . . . 2, 10, 14, 15, 18-21, 29, 30, 33, 34, 52-54
        UTM zone . . . . . . . . . . . . . . . . . . . . . . . . . . 19-21
        VERSAMAP Micro World Database. . . . . . . . . . . . 1, 46, 47, 59
        Vertical perspective . . . . . . . . . . . . . .10, 13, 17, 18, 24
        VGA. . . . . . . . . . . . . . . . . . . . 2-4, 28, 29, 32, 56, 57
        Video. . . . . . . . . . . . . . . . . . . . . . . . . . . .29, 57
        View Disk Directory. . . . . . . . . . . . . . . . . . . . .32, 35
        VM_FIX.MP1 . . . . . . . . . . . . . . . . . . . . . . . . . 2, 51
        VM_FIX.MPS . . . . . . . . . . . . . . . . . . . . . . . . . 2, 51
        VMAP.DOC . . . . . . . . . . . . . . . . . . . . . . . . . . 2, 59
        VMAP.EXE . . . . . . . . . . . . . . . . . . . . . . . . . . 2, 29
        VMAP1.MAP. . . . . . . . . . . . . . . . . . . . . . . .47, 59, 61
        VMAP2.MAP. . . . . . . . . . . . . . . . . . . . . . . . . . . .47
        VMAP3.MAP. . . . . . . . . . . . . . . . . . . . . . .2, 4, 47, 59
        VMAP4.MAP. . . . . . . . . . . . . . . . . . . . .2, 5, 25, 33, 47
        VMAP5.MAP. . . . . . . . . . . . . . . . . . . . .2, 4, 47, 59, 61
        VMAPREAD.ME. . . . . . . . . . . . . . . . . . . . . . . .2, 3, 57
        VMAPUSER.PRN . . . . . . . . . . . . . . . . . . . . . . . . 2, 54
        VMAPUSER.UTM . . . . . . . . . . . . . . . . . . . . . . . . 2, 54
        VMCITY.PRN . . . . . . . . . . . . . . . . . . . . . . . . . .2, 4
        VMOAHU.GRV . . . . . . . . . . . . . . . . . . . . . . . . . 2, 48
        VMTAIWAN.PKV . . . . . . . . . . . . . . . . . . . . . . . . 2, 44
        Wales. . . . . . . . . . . . . . . . . . . . . . . . . . . .43, 44
        Warsaw Pact. . . . . . . . . . . . . . . . . . . . . . . . .19, 20
        WDB-II . . . . . . . . . . . . . . . . . . . . .25, 42, 44, 46, 48
        Westernmost longitude of the map . . . . . . . . . . . . . . . .17
        Windows. . . . . . . . . . . . . . . . . . . . . . . 1, 27, 56, 61
        World Data Bank I. . . . . . . . . . . . . . . . . . . . . .34, 51
        World Data Bank II . . . . .1, 2, 7, 24, 25, 34, 42-44, 46, 59, 61
        World Digitized. . . . . . . . . . . . . . . . . . . . . 2, 34, 51
        X-axis Length. . . . . . . . . . . . . . . . . . . . . . . .35, 55
        Y-axis Length. . . . . . . . . . . . . . . . . . . . . . . .35, 55
        Yemen. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .47
        Yugoslav Republics . . . . . . . . . . . . . . . . . . . . . . .47


        VMAP.DOC version 1.51                                    Page  70