_____________________________________________________________________
         
             AFCALCW a program to calculate Antenna Factor
                     Copyright August 1, 1995
                         by James Eagleson
_____________________________________________________________________

  AFCALCW was written in Turbo C for Windows by Jim Eagleson, 
  WB6JNN/9 to aid in working out FCC related measurements when 
  performing Part 15 certifications as well as making antenna 
  evaluation measurements.

  The basic formula for determining Antenna Factor is:

                AF = 20*LOG(FR/(30.82*SQRT(GR)))

                Where:

                  AF = Antenna Factor.
                  FR = Frequency in MHz.
                  GR = Gain Ratio of Antenna
                       relative to isotropic.

                  GR = 10^(GA/20)
                       
                       (GA = Gain of Antenna(dBi)

  The author of AFCALCW also has a program dealing with Field Strength
  (FSCALCW) which calculates dBuV/m, uV/m, Path Loss, Antenna Factor,
  and other items commonly used for Field and Antenna measurements.
  FSCALC can be obtained by sending $10 or $7.50 plus a disk to:

                        James Eagleson, WB6JNN/9
                         W271 N732 Jill's Drive
                          Waukesha, WI 53188
  
  The program on 3.5" disk will be sent back postpaid and includes
  the source code written in Turbo C.
  ___________________________________________________________________