Personal Communications Library

                       For the C Language


                           (PCL4C)



                        USERS MANUAL





                         Version 4.3

                        March 15, 1995




               This software is provided as-is.
        There are no warranties, expressed or implied.




                     Copyright (C) 1995
                     All rights reserved



                     MarshallSoft Computing, Inc.
                     Post Office Box 4543
                     Huntsville AL 35815

                     Voice 205-881-4630
                     FAX   205|880|0925
                     BBS   205-880-9748


                                _______
                           ____|__     |                (R)
                        --+       |    +-------------------
                          |   ____|__  |  Association of
                          |  |       |_|  Shareware
                          |__|   o   |    Professionals
                        --+--+   |   +---------------------
                             |___|___|    MEMBER















 PCL4C Users Manual                                                Page 1
                     C O N T E N T S





  Chapter                                                   Page

  1.0 Introduction................................................3
      1.1 User Support............................................4
      1.2 ASP Ombudsman...........................................4
      1.3 A Typical Application...................................5
      1.4 Installation............................................6
  2.0 Library Organization........................................7
      2.1 Configuration...........................................7
      2.2 Initialization & Termination............................7
      2.3 Modem Control & Status..................................8
      2.4 Serial I/O..............................................8
      2.5 Error Detection.........................................9
      2.6 General Support.........................................9
  3.0 Library Overview...........................................10
      3.1 Memory Models..........................................10
      3.2 Compilers Supported....................................11
      3.3 Using the Library......................................12
      3.4 Application Notes......................................12
          3.4.1 Terminal Programs................................12
          3.4.2 Door Programs....................................12
          3.4.3 BBS Programs.....................................12
      3.5 Compiling & Linking....................................13
  4.0 Talking to Your Modem......................................14
      4.1 Modem Standards........................................14
      4.2 Flow Control...........................................15
      4.3 MODEM_IO functions.....................................15
      4.4 Modem Initialization...................................16
  5.0 Problems...................................................17
  6.0 Serial Communications......................................18
      6.1 Communications Basics..................................18
      6.2 Standard Port Addresses................................19
      6.3 Running 3 or 4 Ports Concurrently......................20
      6.4 Using Multiport Cards..................................21
          6.4.1 The DigiBoard....................................21
          6.4.2 The BOCA Board...................................21
      6.5 Transmitter Interrupts.................................22
      6.6 RS232 Signals..........................................23
      6.7 National INS8250, INS16450, and INS16550 UARTs.........24
      6.8 Register Summary.......................................25
  7.0 Example Programs...........................................27
      7.1 MINIMAL................................................27
      7.1 SIMPLE.................................................27
      7.2 LOGIN..................................................27
      7.3 DOOR...................................................27
      7.4 SELFTEST...............................................27
  8.0 Legal Issues...............................................28
      8.1 Registration...........................................28
      8.2 License................................................29
      8.3 Warranty...............................................29
  9.0 Summary....................................................30
      9.1 Revision History.......................................30
      9.2 Function Summary.......................................32
      9.3 Further Reading........................................32
 10.0 Other MarshallSoft Computing products for C................33
      10.1 The Personal Protocol Library for C...................33
      10.2 The LZW Data Compression Library for C................33
      10.3 The EMS Expanded Memory Library for C.................33



 PCL4C Users Manual                                                Page 2
  1.0 Introduction


  The  Personal  Communications  Library  for  the  C  Language  (PCL4C) is an
  asynchronous  communications  library  designed  for  experienced   software
  developers  programming  in  C.   Five compilers are supported: Microsoft C,
  Quick C, Borland C, Turbo C, and MIX Power C.  An IBM PC/XT/AT or compatible
  is required.  The PCL features:

  o SMALL, COMPACT, MEDIUM, and LARGE memory models.
  o 38 communications and support functions.
  o Supports the high performance 16550 UART.
  o Supports the PC/4 and PC/8 DigiBoard.
  o Supports the BOCA BB1004, BB1008, and BB2016 boards.
  o Supports hardware (RTS/CTS) flow control.
  o Interrupt driven receiver & (optionally) transmitter.
  o Supports 300 baud to 115,200 baud.
  o Supports COM1 through COM8 (through COM16 with multiport boards)
  o Adjustable receive queues from 8 bytes to 32 KB.
  o Control-BREAK error exit.
  o 18 communications error conditions trapped.
  o Allows 4 ports to run concurrently (more with multiport boards).
  o Complete modem control & status.
  o Written in assembly language for small size & high speed.
  o Terminal program featuring ASCII (with XON/XOFF), XMODEM,
    YMODEM, & YMODEM-G.

  Why should you buy PCL4C ?  Several good reasons are:

    COMPLETE - PCL4C is complete since it provides  absolute  control  of  the
               serial ports (including the high performance INS16550).

     COMPACT - PCL4C  is  very  compact at less than 8 KB.  Your application
               doesn't carry a lot of excess code.

        FAST - PCL4C is fast since it will run at 38400 baud on even slow 8088
               PCs (4.77 MHZ) and at 115200 baud on most everything else.

     SUPPORT - If you get stuck, you talk to the  programmer  that  wrote  the
               code, not a person hired to answer the phone.

         BBS - A BBS is available (2400 to 14400 baud, N81) in order to provide
               immediate support as necessary.

  NEWSLETTER - A  one  year  subscription  to  the  MSC newsletter discusses
               communications problems and solutions (published quarterly).

       PRICE - You get PCL4C for a very reasonable price!

    UPGRADES - Once you buy PCL4C, you can always update to  the  most  recent
               version very inexpensively ($20 plus shipping).
















 PCL4C Users Manual                                                Page 3
  1.1 User Support


  We want you to be successful in developing your applications using PCL4C! We
  depend  on  our  customers to let us know what they need in a communications
  library.  This means we are committed to providing the  best  communications
  library  that we can. If you have any suggestions or comments, please let us
  know!

  We provide customer support for registered customers by voice, FAX, BBS, and
  mail.  We provide limited support for unregistered users by  voice  and  BBS
  only.

  If  you  are  having  a problem using PCL4C, call us at 205-881-4630 between
  1:30 PM and 9:30 PM (CST) Monday through Friday. You can also call at  other
  times and leave a message, and call back later for a reply. Registered users
  (ONLY) can also FAX us at 205-880-0925 at any time (24 hours).

  However,  we  can  only  answer  questions  with  respect to using the PCL4C
  library.  We cannot help you program your application, but we'll be glad  to
  discuss it with you.

  You  may  also  call  our User Support BBS (2400 to 14400 baud, no parity, 8
  data bits, 1 stop bit) at 205-880-9748 and leave a message  (address  it  to
  the SYSOP).  We will usually have a reply ready for you within 24 hours.

  The BBS is available 24 hours per day. All files are in standard ZIP format.
  The  BBS  will  contain  the  latest  shareware  version of all MarshallSoft
  Computing products as well as related files such as:

      BUGS.ZIP     -  Bug report.
      NEWS.ZIP     |  Latest news regarding our products.
      PRODUCTS.ZIP -  List of all shareware products.

  The MarshallSoft  Computing,  Inc.   newsletter  "Comm  Talk"  is  published
  quarterly.  It discusses various communications problems and solutions using
  PCL4C  as  well  as related information. Registered users receive a one year
  complimentary subscription  when  first  registering  and  for  each  update
  purchased.


  1.2 ASP Ombudsman


  MarshallSoft Computing, Inc.  is a member of the  Association  of  Shareware
  Professionals  (ASP).   ASP  wants to make sure that the shareware principle
  works for you.  If you are unable to  resolve  a  shareware-related  problem
  with  an  ASP  member  by contacting the member directly, ASP may be able to
  help. The ASP Ombudsman can help you resolve a dispute or  problem  with  an
  ASP  member,  but  does not provide technical support for members' products.
  Please write to the ASP Ombudsman at  545  Grover  Road,  Muskegon,  MI  USA
  49442-9427,  Fax  616-788-2765,  or send a CompuServe message via CompuServe
  Mail to ASP Ombudsman 70007,3536.














 PCL4C Users Manual                                                Page 4
  1.3 A Typical Application


  In general, there are two classes of applications that use a  communications
  library like PCL4C - those that use a modem to connect to the outside world
  and  those  that  connect directly to a peripheral device. In either case, a
  typical application program using PCL4C might look like the  following  code
  outline:



  +---------------------------------------------------+
  | #include  "pcl4c.h"                               |
  |                                                   |
  | void main(void)                                   |
  | {                                                 |
  |  ...                                              |
  |                                                   |
  |  /* initialize serial comm  system  */            |
  |  SioRxBuf(Port,AllocSeg(1024),Size1024);          |
  |  SioParms(Port,NoParity,OneStopBit,WordLength8);  |
  |  SioReset(Port,Baud2400);                         |
  |                                                   |
  |  ...application code...                           |
  |                                                   |
  |  /* terminate serial comm system  */              |
  |  SioDone(Port);                                   |
  | }                                                 |
  +---------------------------------------------------+



  In  the  above example, SioRxBuf is called to set up the a 1024 byte receive
  buffer; SioParms is called to set up the parity, stop bit  count,  and  word
  length;  SioReset  is called to set the baud rate to 2400 and reset the UART
  (Univeral Asynchronous Receiver / Transmitter).

  The function AllocSeg() allocates a buffer of specified size on the far heap
  and returns the segment SEG such that  SEG:0  points  to  the  buffer.   The
  function AllocSeg() is part of the example code and can be found in the file
  ALLOCSEG.C.

  Before leaving your application, SioDone is  called  to  restore  the  prior
  state of the serial communications system.

  If  you  are using a modem, you also need to be concerned about initializing
  your modem correctly and handling any required flow control.  Refer  to  the
  "Talking to Your Modem" chapter for detailed information.

  If  you  are  using  the versions of the library with transmitter interrupts
  enabled (PCL4C_S2.LIB, PCL4C_M2.LIB, PCL4C_C2.LIB, and  PCL4C_L2.LIB),  then
  SioTxBuf() must  be  called  to  set  up  the  transmitter  buffer  just  as
  SioRxBuf() is called to set up the receive buffer.














 PCL4C Users Manual                                                Page 5
  1.4 Installation


  (1)  Before  installation  of  PCL4C,  your  C  compiler  should  already be
  installed on your system and tested. If you are not familiar with makefiles,
  refer to your compiler manual. If you are using the interactive  environment
  for  Quick  C  or  Turbo  C,  be  sure  to  compile  with  the  memory model
  corresponding to the PCL4C library used, and include the correct library  in
  the  project  file.   Examine  the  file  "FILES.LST"  for a list of all the
  distribution files.

  (2) Make a backup  copy  of  your  distribution  disk.   Put  your  original
  distribution disk in a safe place.

  (3)  Create a work directory on your work disk (normally your harddisk). For
  example, to create a work directory named PCL4C, we first log onto the  work
  disk and then type:

                   MKDIR PCL4C

  (4)  Copy  all  the  files from your backup copy of the distribution disk to
  your work directory.  For example, to copy from the A: drive  to  your  work
  directory, we type:

                  CD PCL4C
                  COPY A:*.*

  (5)  [OPTIONAL]  Delete  the makefiles that you won't need.  For example, if
  you use the Microsoft C compiler, then you want to keep all makefiles ending
  *._M_ but can delete those for Turbo C (*._T_), Quick  C  (*._Q_),  and  MIX
  Power C (*.PRJ).  You may also delete any libraries that you won't need.

  (6)   Compile   SIMPLE.C   and  link  with  the  appropriate  PCL4C  library
  (PCL4C_S.LIB for all but Power C which must use PCL4C_S.MIX). Makefiles  (or
  project files) are provided for each of the supported compilers (Borland C &
  Turbo C use the same makefiles).

       a) Microsoft C: Type MAKE SIMPLE._M_

       b) Microsoft Quick C: Type MAKE SIMPLE._Q_

       c) Borland C: Type MAKE -fSIMPLE._B_

       d) Turbo C: Type MAKE -fSIMPLE._T_

       e) MIX Power C: Type pc/e SIMPLE.PRJ

  SIMPLE.C  should  compile  without any problems as all example code has been
  tested with each of the supported compilers.

  (7)  The  recommended  way  to  test  SIMPLE  is  to run it on two computers
  connected by a null modem cable.  Whatever is typed on one  computer  should
  be displayed on the other. SIMPLE can also be tested by connecting your port
  to a modem.













 PCL4C Users Manual                                                Page 6
  2.0 Library Organization


  The PCL4C library is organized into six categories of  functions.  Refer  to
  the PCL Reference Manual (PCL4C.REF) for details on individual functions.


  2.1 Configuration


  There  are three functions in the configuration category.  SioPorts sets the
  number of PC and DigiBoard (or BOCA board) ports. SioUART is used to  change
  the  UART  base address for a communications port to a non-standard address,
  while SioIRQ is used to assign a nonstandard IRQ line to a port.   (See  the
  chapter IBM Communications Ports for more details on standard UART addresses
  and IRQ lines).

  The  configuration  functions  SioPorts,  SioUART  and SioIRQ must be called
  before calling any other library functions.  Be very careful in using  these
  functions.  Remember that your serial hardware must support the UART and IRQ
  that you specify.  Always test any new configuration immediately.

  SioPorts -  Sets number of PC and DigiBoard (or BOCA board) ports.
  SioUART  |  Sets the UART base address.
  SioIRQ   -  Assigns an IRQ line to a port.

  THE IRQ GOLDEN RULE: You may open (via  SioReset)  only  one  port  per  IRQ
  (except for the DigiBoard and BOCA board).


  2.2 Initialization & Termination


  There are eight functions in the initialization  and  termination  category.
  Together,  SioParms,  SioFIFO,  SioRxBuf,  SioTxBuf, and SioReset initialize
  your serial communications system.  Your application must call SioParms  and
  SioRxBuf  before  calling  SioReset,  and SioReset must be called before any
  serial I/O processing can be done.

  After initialization, SioParms and SioBaud can be called again to change the
  communications parameters without resetting the serial port. SioFlow can  be
  called to enable hardware flow control.

  Before  exiting  from  your  application, SioDone must be called. Failure to
  call SioDone can crash your system later.

  SioRxBuf   - Sets up receive buffer.
  SioTxBuf   | Sets up transmitter buffer.
  SioFIFO    | Sets the interrupt level for the INS16550.
  SioParms   | Sets parity, stop bits, and word length.
  SioReset   | Initialize a serial port for processing.
  SioDone    | Terminates further serial processing.
  SioBaud    | Sets the baud rate of the selected port.
  SioFlow    - Enables / disables flow control.













 PCL4C Users Manual                                                Page 7
  2.3 Modem Control & Status


  There are nine functions in the modem  control  and  status  category  which
  provide  your  application with complete control over the status and control
  bits of your modem.

  There are two modem control bits, "Data Terminal Ready" (DTR)  and  "Request
  To  Send"  (RTS).  These  bits  can  be  read, set, or cleared by SioDTR and
  SioRTS.

  There are four modem status bits, "Data Set Ready" (DSR),  "Clear  To  Send"
  (CTS),  "Ring Indicator" (RI), and "Data Carrier Detect" (DCD). SioModem can
  read any of the modem status bits.  SioDSR, SioCTS, SioRI,  and  SioDCD  can
  only read their respective modem status bit. SioGetDiv reads the  baud  rate
  divisor register so the baud rate can be determined.

  Refer  to  the  chapter entitled "RS232 Signals" for a discussion of each of
  the control and status bits.

  SioDTR    - Set, clear, or read the Data Terminal Ready (DTR) bit.
  SioRTS    | Sets, clears, or reads the Request to Send (RTS) line.
  SioModem  | Reads the modem status register.
  SioDSR    | Reads the Data Set Ready (DSR) modem status bit.
  SioCTS    | Reads the Clear to Send (CTS) modem status bit
  SioDCD    | Reads the Data Carrier Detect (DCD) modem status bit.
  SioRI     | Reads the Ring Indicator (RI) modem status bit.
  SioRead   | Reads the contents of the 7 UART registers.
  SioGetDiv - Reads the baud rate divisor registers.


  2.4 Serial I/O


  There are eight library functions in  the  serial  I/O  category.  Together,
  these functions give the programmer complete control over serial I/O. Higher
  level  functions  such  as  protocols  and smart modem communications can be
  completely implemented in terms of these functions.  Refer  to  the  example
  code.

  SioGetc  and  SioPutc perform all the actual serial I/O.  SioUnGetc "ungets"
  the last serial  byte  read.  SioRxFlush  clears  the  receive  queue  while
  SioTxFlush  clears  the transmit queue. SioLine can be used to test for UART
  errors.  SioRxQue returns the number of bytes in  the  receive  queue  while
  SioTxQue returns the number of bytes in the transmit queue.

  SioGetc    - Reads the next character from the serial line.
  SioPutc    | Transmit a character over a serial line.
  SioUnGetc  | "Un-gets" (puts back) a specified character.
  SioRxFlush | Flush (clears) the receive buffer.
  SioRxQue   | Returns the number of characters in the RX queue.
  SioTxFlush | Flush (clears) the transmit buffer.
  SioTxQue   | Returns the number of characters in the TX queue.
  SioLine    - Reads the line status register.













 PCL4C Users Manual                                                Page 8
  2.5  Error Detection


  There are four functions in the error detection category. They are concerned
  with detecting or reporting communications errors.  Use of  these  functions
  can make your application significantly more robust.

  SioBrkKey  can  be  used  as  an  "emergency"  exit  from  your application.
  SioBrkSig can read or  modify  the  UART  break  bit.  This  is  useful  for
  signalling   the   remote  system  that  a  fatal  condition  has  occurred.
  SioLoopBack can be used to  test  the  integrity  of  your  UART.   SioError
  displays  a  error  message  corresponding  to an error code returned from a
  PCL4C function (every PCL4C function returns a code).

  SioBrkKey - Returns non-zero if the Control-BREAK key was pressed
  SioBrkSig | Asserts, cancels, or detects the RS232 BREAK  signal.
  SioError  - Displays  error  in  text.
  SioLoopBack - Performs a UART loopback test.


  2.6 General Support


  There are six functions in the general support category.  Strictly speaking,
  they are not communications functions but are provided in the PCL4C  library
  because  they  are  not  always available (especially in some older compiler
  run-time libraries).  At any rate, they take  up  a  very  small  amount  of
  additional memory. Registered users can also remove these functions from the
  library if needed.

  SioInfo     - Returns the library version & memory model.
  SioCrtWrite | Use BIOS to write character to the screen.
  SioDelay    | Delays one or more tics (18.2 tics per second).
  SioKeyPress | Use BIOS to detect if keyboard key has been pressed.
  SioKeyRead  | Use BIOS to reads the keyboard.
  SioTimer    - Returns the number of system clock tics.































 PCL4C Users Manual                                                Page 9
  3.0 Library Organization


  3.1 Memory Models


  Because  of  the  segmented  architecture  of  the INTEL CPU, there are four
  memory organizations possible for computer programs.  These  are  named  the
  SMALL,  COMPACT,  MEDIUM,  and  LARGE memory models, which correspond to the
  four combinations of "near" and "far" addresses for code and data.

  Each executable is composed of one or more segments, where each segment  can
  occupy  from  one  byte  to  64  KB of memory.  A "near" address is a 16 bit
  offset in a segment, whereas a "far" address  consists  of  both  a  16  bit
  segment value and a 16 bit offset.

  In the small memory model, code and data each occupy one segment. Thus, near
  addresses are allocated for both code and data.

  In the compact memory model, code occupies one segment while data may occupy
  multiple  segments.  Near addresses are allocated for code but far addresses
  are allocated for data.

  In the medium memory model, data occupies one segment while code may  occupy
  multiple  segments.  Near addresses are allocated for data but far addresses
  are allocated for code.

  In the large memory model, data and code each occupy multiple segments.  Far
  addesses are allocated for both code and data. Thus, both code and data  can
  use as many segments as required.

  Refer  to  your  compiler  manual  for  a  discussion  of  the memory models
  supported by your compiler.

  PCL4C is organized as four  separate  libraries  (PCL4C_S.LIB,  PCL4C_C.LIB,
  PCL4C_M.LIB  and  PCL4C_L.LIB)  corresponding  to  the  four standard memory
  models.  For the MIX Power C compiler, the small, medium, and  large  models
  are  provided  (PCL4C_S.MIX,  PCL4C_M.MIX  and  PCL4C_L.MIX).   MIX  doesn't
  support the compact memory model.

  MODEL      CODE      DATA     Library
  Small      Near      Near     PCL4C_S.LIB & PCL4C_S.MIX
  Compact    Near      Far      PCL4C_C.LIB
  Medium     Far       Near     PCL4C_M.LIB & PCL4C_M.MIX
  Large      Far       Far      PCL4C_L.LIB & PCL4C_L.MIX

  However, one can always use the large memory model library PCL4C_L.LIB  with
  any  memory  model  application  code  by  explicitly  declaring  the  PCL4C
  procedures to be FAR (by prefixing "far" before the name of each function in
  the PCL4C.H file) and declaring your receive buffer to be FAR.  If  you  are
  compiling with the HUGE memory mode, link with PCL4C_L.LIB.

  The   equivalent   libraries   with   transmitter   interrupts  enabled  are
  PCL4C_S2.LIB, PCL4C_C2.LIB, PCL4C_M2.LIB, & PCL4C_L2.LIB.













 PCL4C Users Manual                                                Page 10
  3.2 Compilers Supported


  At this time, five C compilers are supported by PCL4C.

  (1)  Microsoft (Optimizing) C Compiler.

  (2)  Quick C Compiler.

  (3)  Turbo C Compiler.

  (4)  Borland C Compiler.

  (5)  MIX Power C Compiler

  The Microsoft Optimizing C Compiler supports  all  memory  models.  Just  be
  careful  to link with the PCL4C library that corresponds to the memory model
  used. Recall that the small memory model is the default.  Examine the (small
  model) makefiles *._M_ for the Microsoft compiler.

  The Microsoft Quick C Compiler supports all memory models, but be careful to
  link with the PCL4C library that corresponds with  the  memory  model  used.
  Recall  that  the  small  memory  model  is the default for the command line
  compiler (QCL) while  the  medium  memory  model  is  the  default  for  the
  interactive compiler environment.  Examine the (small model) makefiles *._Q_
  for the Microsoft Quick C compiler.

  The Borland and Turbo C Compilers also support all memory models. Be sure to
  link  with the correct PCL4C library corresponding to the memory model used.
  Examine the (small model) makefiles *._T_ for the Turbo C compiler.

  The  MIX  Power  C  Compiler  supports  the  small, medium, and large memory
  models. However, older versions of Power C only  support  the  small  model.
  Examine  the  (small  model)  project  batch  files  *.PRJ  for  the Power C
  Compiler.

  Other compilers may also work with one or more of the  PCL4C  libraries  but
  have  not  been  tested.  Since registered users have the source code to the
  library, it should not be difficult to modify PCL4C for use with any MSDOS C
  compiler.  Give us a call if you have any difficulty.


  3.3 Using the Library


  The  PCL4C  has  been tested on a Tandy 1000 (4.77 MHZ 8088 IBM PC clone), a
  Tandy 3000 (80286 IBM AT clone), a Tandy 1400LT (IBM XT  clone),  a  Gateway
  2000  386 (25 MHZ 80386-DX), and a Gateway 2000 486 (66MHZ 80486-DX).  PCL4C
  has also been tested under MSDOS 2.11, 3.2, 3.3, 4.01, 5.0, 6.0 and 6.2.

  Please examine the PCL4C.H file. Note that COM1 is defined as port zero, not
  port  one.   The  user must assume the responsibilty for passing the correct
  information when calling PCL4C functions.

  If there are any conflicts between PCL4C  definitions  and  those  in  other
  libraries,  the PCL4C definitions can be changed in the PCL4C.H file and any
  file that uses the definition. There is no change necessary for the  library
  code itself.

  The  PCL4C  libraries  contain no references to any runtime libraries.  Only
  BIOS and MSDOS functions are called.






 PCL4C Users Manual                                                Page 11
  3.4 Application Notes


  3.4.1 Terminal Programs


  The  "terminal  program" is the most common class of communications program.
  It is used to call up a BBS or on-line service such as  CompuServe,  America
  On-Line,  etc.   Refer  to  the  programs  SIMPLE and LOGIN in section 7 for
  examples of simple terminal programs.

  A more sophisticated terminal program featuring ASCII, XMODEM,  YMODEM,  and
  ZMODEM  protocol  file  transfers  can be found in our sister product -- The
  Personal Protocol Libray (PPL4C). Source code is included in  the  shareware
  distribution for everything except ZMODEM and the script intepreter.


  3.4.2 Door Programs


  In order to write a door program which "takes over" a  serial  port  without
  resetting  the  port or changing the baud rate, call SioReset() with NORESET
  as the second argument rather than the baud rate. Call  SioGetDiv()  to  get
  the  baud  rate divisor if the baud rate must be determined. Be sure to call
  SioDone()  before  returning  to  the  invoking program. Refer to the DOOR.C
  example program.


  3.4.3 BBS Programs


  If you are designing a BBS program (also known as HOST  programs),  consider
  using  16550  UARTS.   You  should  also choose a multiport card such as the
  DigiBoard or BOCA board if you wish to run more than 4 ports simultaneously.

  If  you  are using an error correcting modem, then you should be sure to set
  flow control and fix your baud rate at the highest possible transfer  rates.
  For  14,400  modems, this means 19200 or 38400. You may need a 16550 UART in
  order to run at the higher speed.

  If you are using an older multi-speed modem (say  1200,  2400,  4800,  9600)
  that doesn't use flow control, you should change your baud rate to match the
  CONNECT message baud rate.
























 PCL4C Users Manual                                                Page 12
  3.5 Compiling and Linking


  Registered  users  may  wish  to  assemble PCL4C.ASM.  Use the /MX switch in
  order to disable automatic conversion from lower case to upper case.  If the
  /MX switch is not used, then all PCL4C function references in C code must be
  in upper case. To assemble using the Microsoft assembler:

  Model    Command

  Small    MASM PCL4C /DSMALL_MODEL   /DMSC_IO /MX;
  Compact  MASM PCL4C /DCOMPACT_MODEL /DMSC_IO /MX;
  Medium   MASM PCL4C /DMEDIUM_MODEL  /DMSC_IO /MX;
  Large    MASM PCL4C /DLARGE_MODEL   /DMSC_IO /MX;

  To enable transmitter interrupts, add "/DSET_TBE" to each MASM command  line
  above.

  For example, to make the (small) model PCL4C.OBJ into a library file:

        DEL PCL4C_S.LIB
        LIB PCL4C_S.LIB+PCL4C,PCL4C.MAP;

  If  you  are using the MIX Power C Compiler, create the MIX object file (you
  will need version 1.3 of MIX which has the /_ switch):

        MIX /_ PCL4C_S

  Similarly with the  other  memory  model  libaries.   See  the  batch  files
  MAKE_S.BAT,   MAKE_C.BAT,   MAKE_M.BAT,   and   MAKE_L.BAT.  Similiarly  for
  MAKE_ST.BAT, MAKE_CT.BAT, MAKE_MT.BAT, and MAKE_LT.BAT.

  To compile and link (small model) using Microsoft C:

        CL /AS SIMPLE.C /LINK PCL4C_S.LIB

  To compile and link (small model) using Microsoft Quick C:

        QCL /AS SIMPLE.C /LINK PCL4C_S.LIB

  To compile and link (small model) using Borland C:

        BCC -ms SIMPLE.C PCL4C_S.LIB

  To compile and link (small model) using Turbo C:

        TCC -ms SIMPLE.C PCL4C_S.LIB

  To compile and link (small model) using Power C:

        PC /ms SIMPLE.C
        PCL SIMPLE PCL4C_S.MIX

  Makefiles or project files are  provided  for  all  example  code.   Borland
  makefiles  end  with  the  extension  '._B_', Turbo C makefiles with '._T_',
  Microsoft C makefiles end with '._M_', Microsoft Quick C makefiles files end
  with '._Q_', and Power C project batch files end with '.PRJ'.

  The  PCL4C  libraries  may  also  be  used   with   integrated   development
  environments.  Place all required files along with the library corresponding
  to the memory model being used into the project file.






 PCL4C Users Manual                                                Page 13
  4.0 Talking to Your Modem


  A  modem  is  used  to  extend  the distance over which you may communicate.
  Without a modem, your RS232 cable is limited to a maximum  of  approximately
  50 feet.  But with a modem, you can communicate literally around the world.

  Also refer to Section 4.3 for details on MODEM_IO functions. These functions
  faciliate communications with modems.


  4.1 Modem Standards


  Two modems can communicate over a telephone line only if they are both using
  the  same  signaling frequencies and modulation, which are determined by the
  the modem standards used.  Modem standards can be divided into  three  sets:
  (1) speed, (2) data compression used, and (3) error control.

  The  Bell  standards  (103  &  212A)  are  those  of  AT&T.   The CCITT (The
  International Consultative Committee for Telephone and Telegraph)  standards
  are designated as "V. ".


  Speed


  Bell 103  -   300 baud
  Bell 212A |  1200 baud
  V.21      |   300 baud
  V.22bis   |  1200 & 2400 baud
  V.32      |  4800 & 9600 baud
  V.32bis   |  4800, 7200, 9600, 12000, and 14400 baud
  V.34      -  through 28800 baud

  Data Compression


  MNP 5     -  Microcom Networking Protocol (proprietary).
  V.42bis   -  International data compression standard.


  Error Control


  MNP 2,3,4 -  Three level error correction (public domain).
  V.42      -  International error correction standard.


  Most of the newer high speed modems use  several  of  the  above  standards.
  However,  not  all  combinations of modem makes communicate easily with each
  other, especially at high speeds (9600 and up).















 PCL4C Users Manual                                                Page 14
  4.2 Flow Control


  With modems using data compression, the modem to modem connection  will  run
  at  various  speeds  depending  on the quality of the line.  The computer to
  modem connection will be at a fixed baud rate. Therefore, a  protocol  (flow
  control)  is  necessary to synchronize the data flow between a modem and the
  computer to  which  it  is  connected.   Refer  to  your  modem  manual  for
  information on flow control protocols supported.

  Two  flow  control  protocols  are  used  by  most modems which require flow
  control.  Software flow control is called "XON/XOFF"  (other  software  flow
  control  character  pairs  are defined but operate the same as XON/XOFF) and
  hardware flow control is called "RTS/CTS".  Most modems which  require  flow
  control enable hardware flow control by default.

  In XON/XOFF (software) flow control, the computer suspends transmitting data
  if it receives a XOFF character (13  hex)  from  the  modem,  and  continues
  transmitting  when  it  receives  a XON character (11 hex).  Similiarly, the
  computer can signal the modem not to send any more data  by  transmitting  a
  XOFF  to  it,  and  can tell the modem to continue transmission be sending a
  XON.

  In RTS/CTS (hardware) flow control, the RTS line is used by the computer  to
  signal  the  modem  ,  while the CTS line is used by the modem to signal the
  computer.  The RTS line is set OFF by the computer  to  tell  the  modem  to
  suspend  transmission,  and  set  to  ON  to  tell  the  modem  to  continue
  transmission.  The CTS line is set to OFF by the modem to tell the  computer
  to  stop  transmitting,  and  set  to  ON  to  tell the computer to continue
  transmitting.

  Given the choice, always choose hardware flow  control  over  software  flow
  control  so  that  all  data  transmission is transparent.  If hardware flow
  control is not the default (which it almost always is),  you  should  modify
  your modem initialization string to turn hardware flow control on.

  Both  software  and  hardware flow control is easy to implement using PCL4C.


  4.3 MODEM_IO Functions


  The file MODEM_IO.C contains several functions that ease communicating  with
  your  modem.  Look in the LOGIN.C code for examples of their use. Registered
  users can also see examples in the script interpreter SI.C.

       ModemSendTo   : Sends string (including control chars) to the modem.
       ModemWaitFor  : Waits for a particular string from the modem, passing
                       all else through.
       ModemQuiet    : Waits for continuous quiet of specified duration.
       ModemHangup   : Hangs up the modem.
       ModemCmdState : Goes into the modem's command state.
       ModemEcho     : Echos all serial incoming bytes to the display.














 PCL4C Users Manual                                                Page 15
  4.4 Modem Initialization


  If your application uses a modem (as opposed to using a null  modem  cable),
  then  you should always send an initialization string to your modem if it is
  a programmable modem such as those made by  Hayes.   Communication  programs
  such as PROCOMM and TELIX always send such a string automatically as soon as
  they start up.

  The particular initialization string depends on the make of your modem.  For
  Hayes  and  Hayes  AT  command  set  compatible modems, the following string
  (followed by a carriage return) may work:

       AT E1 S7=60 S11=60 V1 X1 Q0 S0=0

  Refer to your Modem User's Guide for a full discussion of these commands.  A
  brief description is as follows:

  AT     Modem attention command.
  E1     Modem will echo what you send to it.
  S7=60  Wait 60 seconds for carrier and/or dial tone.
  S11=60 Use 60 milliseconds for tone dialing duration & spacing.
  V1     Display result code as words (not numbers).
  X1     Use the extended result message (CONNECT XXXX) set.
  Q0     Modem returns result codes.
  S0=0   Do not answer RING.

  If  your application will answer incoming calls, then set the S0 register to
  the ring on which to automatically answer.

  If you send the above codes by using SioPutc (as opposed to typing them from
  the keyboard), then follow these guidelines:

  (1) Send an initial carriage return before the initialization string.

  (2) Pause at least two tics (18 tics to the  second)  after  each  character
  sent  as  your  modem needs the time to perform its own internal processing.
  Pause a little longer if your modem is  not  accepting  your  initialization
  string.

  (3)  Pause  one  and a half seconds after sending any initialization command
  such as ATZ or AT&F since your modem must do quite a bit of processing.

  If you experience any problems in initializing your Hayes modem, you  should
  first reset it to factory settings by sending:

       AT&F

  Your modem may require more initialization than presented  above.  Refer  to
  your  modem manual for details. If you have a communications program such as
  ProComm or Telix that is known to initialize your modem correctly, then  you
  may wish to use the same initialization string.

  Refer to the LOGIN program (functions ModemSendTo  and  ModemWaitFor  in  the
  file  MODEM_IO.C)  for  an  example of sending an initialization string to a
  Hayes compatible modem.











 PCL4C Users Manual                                                Page 16
  5.0 Problems


  If  you  cannot  get your application to run properly, first compile and run
  the terminal emulator program SIMPLE provided on your distribution  disk.

  If your application does not run but SIMPLE runs correctly,  then  you  have
  most  likely  made  a programming mistake in your application.  MarshallSoft
  Computing cannot debug your  application,  especially  over  the  telephone!
  However,  consider each of the following when searching for an error in your
  application.

  1.  Have you included the file PCL4C.H in your application ?

  2.  Did you link with the correct PCL4C library ?  This is the most probable
  cause  if your application 'hangs' as soon as it starts and you must reboot.
  The function SioInfo('M') returns the model ID under which the  library  was
  assembled.

  3.  Is your receive buffer large enough ? If you are using 1K data blocks in
  YMODEM,  then  your  receive  buffer should be at least 1K (2K if baud rates
  above 19200 are to be used).

  4.  Have you selected too high a baud rate (if you are using a slow PC) ? If
  only one COM port is being run, you should be able to run at 38400  baud  on
  8088 machines and 115200 on most 286 and all 386 and 486 machines.

  5.   Are  you attempting to run another application in the background ?  Try
  running without any other programs running in the background (unload all TSR
  programs).

  6.  If you are running two COM ports simultaneously, are you using  separate
  receive buffers ? (you should).

  7.   Did SioReset return a zero value ?  If not, then you must call SioReset
  again. See SIMPLE.C for an example.

  8.  Did you send the proper initialization string to your modem  ?  Did  you
  set DTR and RTS ? (you should).

  9.   Do  you  have more than one COM1 port, etc.  For example, if you have a
  COM1 port on your motherboard, you cannot add another  COM1  port  or  modem
  board that uses COM1 without first disabling the COM1 on the motherboard.

  10.   Your  first  comm  port should be COM1.  If you have a second port, it
  should be COM2, not COM3 or COM4.

  11.  Are you passing the proper segment of the receive (or transmit) buffer?
  See SIMPLE.C for an example.


















 PCL4C Users Manual                                                Page 17
  6.0 Serial Communications


  6.1 Communications Basics


  The heart of serial  communications  is  the  UART  (Universal  Asynchronous
  Receiver  Transmitter).   The  IBM PC/XT/AT and compatibles use the INS8250,
  INS16450, or the INS16550 UART.  The purpose of the UART is:

  (1) To convert bytes from the CPU (Central Processing Unit), into  a  serial
  format  by  adding  the  necessary start, stop, and parity bits to each byte
  before transmission, and to then transmit each bit at the correct baud rate.

  (2) To convert the incoming stream (at a specified baud rate) of serial bits
  into bytes by removing the start, stop, and parity bits  before  being  made
  available to the CPU.

  The  UART  is part of the serial interface circuitry which allows the CPU to
  send and receive signals over the RS232 lines. This  can  be  diagrammed  as
  follows:


                        Serial Interface
                     +-------------------+
                     |                   |
  +-----+  Data Bus  |     +------+      |    RS232 Signals
  | CPU +------------+     | UART |      +----------------*
  +-----+            |     +------+      |
                     |                   |
                     +-------------------+


  The INS8250/16450/16550 UART is capable of operating in one  of  two  modes,
  "polled" and "interrupt driven".  The serial communications functions in the
  BIOS  uses  the  polled method.  In this approach, the CPU is typically in a
  loop asking the UART over and over again if it has a byte ready. If it does,
  the polling code returns the byte.  But, if the next byte  comes  in  before
  the polling code is executing again, then that byte is lost.

  In  the  interrupt driven approach (used by PCL4C for incoming data), when a
  byte is received by the UART, an interrupt is generated and  the  "Interrupt
  Service  Routine"  (ISR)  is  executed  immediately,  suspending temporarily
  whatever else is executing. The ISR then moves the byte to a buffer so  that
  your  application  program  can  later  read it. Refer to section 6.6 "RS232
  Signals", and section 6.7 "National INS8250, INS16450  and  INS16550  UARTs"
  for further information on these topics.




















 PCL4C Users Manual                                                Page 18
  6.2 Standard Port Addresses


  There  are  a  few  things to know about how serial communications ports are
  used by IBM PC/XT/AT and compatible computers.  The  standard  IBM  PC/XT/AT
  configuration values are as follows:

  Port    Reg.   IRQ  Vector
  COM1    3F8H    4     12
  COM2    2F8H    3     11
  COM3    3E8H    4     12
  COM4    2E8H    3     11

  (Refer to your DigiBoard manual for DigiBoard addresses, or your BOCA  board
  manual for BOCA port addresses).

  PCL4C  assumes the above values.  If necessary, the UART base address can be
  changed by SioUART, and IRQ lines can be re-assigned  by  SioIRQ.   Remember
  that  each  port to be used concurrently must have a unique IRQ line.  Refer
  to the PCL4C Reference Manual for specific details.

  When installing new  communications  cards,  the  following  guidelines  are
  recommended:

  (1)  Be  sure to read the documentation for the hardware you are installing.
  Pay special attention to UART base addresses and IRQ lines, particularly  if
  trying to set up a non-standard configuration.

  (2)  If  you  have  a  choice in base addresses and IRQ lines, always choose
  standard values as defined above.

  (3) The first port should be COM1, the second COM2, etc.  Do NOT  skip  over
  any port.

  (4)  Use SioUART to zero all unused ports (for example, call SioUART(COM4,0)
  if there is no COM4 port installed).

  (5) Be carefull not to configure two ports for the  same  address.  This  is
  easier to do than you may believe.

  (6)  Choose  an  external  modem over an internal one.  It is much easier to
  debug problems with an external modem than an internal one.

  (7) Select hardware flow control (RTS/CTS) if flow control is  required  and
  hardware flow control is not the default.

  (8)  Always  test your port as soon as it is installed. Try several programs
  that use the communications ports.



















 PCL4C Users Manual                                                Page 19
  6.3 Running 3 or 4 Ports Concurrently


  PCL4C supports up to 4 serial ports running concurrently (more if you have a
  DigiBoard or BOCA board).  One free interrupt for  each  port  is  required.
  Refer to the next section if you have a DigiBoard or BOCA board.

  Interrupts  IRQ4  and  IRQ3  are  dedicated to the communications ports in a
  standard IBM PC/XT/AT configuration.  IRQ4 is shared between COM1  and  COM3
  while IRQ3 is shared between COM2 and COM4.  This means that you can run two
  ports simultaneously provided that they don't share an interrupt.

  Suppose that you wish to run 3 ports simultaneously. To begin, you must have
  3  serial  UARTs  installed  on your computer.  Assume, for purposes of this
  discussion, that COM1 is installed on your motherboard, and  that  you  have
  purchased a new 2 port serial communications board.

  You  should  be able to configure the first serial board port as COM2, which
  uses IRQ3.  Refer to the manual that came with your serial board.

  In order to run the third serial port concurrently with the  first  two,  an
  unused  interrupt  must be found.  If your serial card can use only IRQ3 and
  IRQ4, then there is no way to run a third line since IRQ4 and IRQ3 are  used
  for COM1 and COM2.

  However,  many serial cards can use other IRQs, typically IRQ2 through IRQ5.
  Since IRQ5 is normally used  for  a  second  printer  port,  it  is  a  good
  candidate  for  COM3.  To use IRQ5 for the third serial port, first set your
  serial card to use IRQ5 for COM3 (refer to your serial card manual) and then
  add the following line to your applications code before calling SioReset:

         SioIRQ(COM3,IRQ5);

  Don't forget to disable any device that might use IRQ5,  such  as  a  second
  printer  port  or  a  music  card.   Unfortunately,  there is no easy way to
  determine that you have no conflicts until you actually attempt to  use  the
  IRQ.  If  there  are  conflicts, your system will probably hang and you will
  have to reboot.

  To run a fourth serial port, another  free  IRQ  must  be  found.   On  some
  systems, IRQ7 can be used. To use IRQ7 for the fourth serial port, first set
  your serial card to use IRQ7 for COM4 and then add:

         SioIRQ(COM4,IRQ7);

  To  summarize,  your  serial  card must be able to generate the correct IRQ,
  which is not already being used. Refer to the entry for the SioIRQ  function
  in the PCL4C Reference Manual.



















 PCL4C Users Manual                                                Page 20
  6.4 Using Multiport Cards


  The  PCL4C  library  supports  the dumb Digiboard (PC/4 & PC/8) and the dumb
  BOCA board (BB1004, BB1008, and BB2016).

  6.4.1 The DigiBoard

  PCL4C supports the DigiBoard PC/4 and PC/8. In order to use  the  DigiBoard,
  you  must  configure  PCL4C  using  the  SioPorts(), SioUART(), and SioIRQ()
  functions.

  Your  PC's  ports must be partitioned into "standard" PC ports and dumb card
  ports.  Remember that standard PC ports cannot share IRQs like the DigiBoard
  (or BOCA board) can. If you are using IRQ4 and IRQ3 for  standard  PC  ports
  COM1  and  COM2, then you cannot use either for DigiBoard ports (try IRQ5 or
  IRQ7).

  Suppose  that  COM1 through COM2 are standard PC ports (using IRQ4 and IRQ3)
  and you have installed a PC/8 DigiBoard  that  you  wish  to  use  for  COM3
  through  COM10 using interrupt line IRQ5.  You choose to use the recommended
  DigiBoard UART addresses starting at 0x100:

  SioPorts(10,COM3,0x140,DIGIBOARD);  /* COM3 = 1st DigiBoard port */
  Address = 0x100;                    /* 1st DigiBoard UART address */
  for(Port=COM3;Port<=COM10;Port++)   /* look at each port */
     {SioUART(Port,Address);          /* set the UART address */
      Address  += 8;                  /*  compute next address */
      SioIRQ(Port,IRQ5);              /* set the DigiBoard IRQ */
     }

  The DigiBoard uses 0x140 for the status address for odd interrupts and 0x141
  for even interrupts.

  Digiboard  may  be  contacted  at  6400 Flying Cloud Drive, Eden Prairie, MN
  55344.  Telephone 612-943-9020 or FAX 612-943-5398.

  6.4.2 The BOCA Board

  PCL4C supports the  dumb  BOCA  board.  As  with  the  DigiBoard,  you  must
  configure PCL4C before using the BOCA board.

  For  example,  to  configure the BOCA BB2016 to use COM1 to COM16, with base
  addresses starting at 0x100 and IRQ5:

    SioPorts(16,COM1,0x107,BOCABOARD);/* COM3 = 1st BOCA board port */
    Address = 0x100;                  /* 1st BOCA UART address */
    for(Port=COM1;Port<=COM16;Port++) /* look at each port    */
      {SioUART(Port,Address);         /* set the UART address */
       Address += 8;                  /* compute next address */
       SioIRQ(Port,IRQ15);            /* set the BOCA IRQ */
      }

  BOCA may be contacted at BOCA Research, Inc., 6413  Congress  Avenue,  Suite
  130, Boca Raton, FL 33487.  Phone 407-241-8088, FAX 407-997-0918.












 PCL4C Users Manual                                                Page 21
  6.5 Transmitter Interrupts


  Beginning with version 4.0 of PCL4C, transmitter interrupts are supported by
  the   library.   Separate  libraries  are  provided,  one  with  transmitter
  interrupts enabled and one without.  When  transmitter  interrupts  are  NOT
  enabled, the following logic occurs everytime you call SioPutc():

   1. Wait for transmit buffer to become empty. The transmit
      buffer may not be empty if the previous transmit is not
      completed (the UART breaks down the byte & sends 1 bit
      at a time).

   2. When the transmit buffer is empty, the byte from the
      SioPutc() call is loaded into the transmit buffer and
      control is returned to the caller.

  Note that you can not write to the UART any faster than the UART baud rate.

  When transmitter interrupts are enabled, the byte from SioPutc() is put into
  a previously prepared (by SioTxQue) transmitter queue. The interrupt service
  routine fetches bytes from this queue as soon as the previous byte has  been
  sent.

  While  you can now call SioPutc() faster than the baud rate, bytes are still
  transmitted at the given baud rate.

  The  above  sounds  like  transmitter  interrupts  are  the   way   to   go.
  Unfortunately,  this  is often NOT the case.  Most applications will perform
  better if transmitter interrupts are NOT enabled.

  The  reason  is that transmitter interrupts double the amount of code in the
  time critical interrupt service routines.  While the library is processing a
  transmitter interrupt (which can take a while), incoming bytes  can  not  be
  processed.  What this means is that a given machine can run at a higher baud
  rate without transmitter interrupts. This problem is compounded when running
  multiple ports simultaniously.

  However, there are a few application areas where transmitter interrupts  are
  preferable.   If  your  application  will  be transmitting blocks of data at
  fairly slow baud rates you might profit from enabling transmitter interrupts
  provided that there is something else for the processor to do (which is  NOT
  the case in most protocols).

  Recall  that  PCL4C_S2.LIB  (small),  PCL4C_C2.LIB  (compact),  PCL4C_M2.LIB
  (medium), and PCL4C_L2.LIB (large) are the four memory model libraries  with
  transmitter interrupts enabled.




















 PCL4C Users Manual                                                Page 22
  6.6 RS-232 Signals


  RS-232  is  the  name  of the serial data interface standard used to connect
  computers to modems.  Most IBM compatible computers are built with at  least
  one serial port and use either DB9 (9 pin) or DB25 (25 pin) connectors.

  A  summary  of  these  pins  and  their function follows.  For more detailed
  information, refer to one of the many books dealing with RS-232 interfacing.

  Signal Ground Pin 7 (DB25), Pin 5 (DB9)

  The SG line is used  as  the  common  signal  ground,  and  must  always  be
  connected.

  Transmit Data Pin 2 (DB25), Pin 3 (DB9)

  The TX line is used to carry data from the computer to the modem.

  Receive Data Pin 3 (DB25), Pin 2 (DB9)

  The RX line is used to carry data from the modem to the computer.

  Data Terminal Ready Pin 20 (DB25), Pin 4 (DB9)

  The  DTR  line is used by the computer to signal the modem that it is ready.
  DTR should be set high when talking to a modem.

  Data Set Ready Pin 6 (DB25), Pin 6 (DB9)

  The DSR line is used by the modem to signal the computer that it is ready.

  Request to Send Pin 4 (DB25), Pin 7 (DB9)

  The RTS line is used to "turn the line around" in half  duplex  modems,  and
  for hardware flow control in most modems that require flow control.

  Clear to Send Pin 5 (DB25), Pin 8 (DB9)

  The  CTS  line  is used to "turn the line around" in half duplex modems, and
  for hardware flow control in most modems that require flow control.

  Data Carrier Detect Pin 8 (DB25), Pin 1 (DB9)

  The DCD line is used by the modem to signal the computer that a data carrier
  signal is present.

  Ring Indicator Pin 22 (DB25), Pin 9 (DB9)

  The RI line is asserted when a 'ring' occurs.

















 PCL4C Users Manual                                                Page 23
  6.7 National INS8250, INS16450, and INS16550 UARTs


  The Personal Communications  Library  is  based  on  the  standard  National
  INS8250,  INS16450,  and INS16550 UARTs. The 8250 was the original UART used
  in the IBM PC, whereas the 16450 is a faster version found on most 286 &  up
  machines. The 16550 contains a 16 byte FIFO to further reduce communications
  overhead. These UARTs consists of 8 register ports as follows:

  Offset    R/W   Register
    0       R/W   Receiver (read) / Transmitter (write)
    1       R/W   Interrupt Enable (read)
    2       R     Interrupt Identification
    2       W     FIFO control (INS16550 only)
    3       R/W   Data Format (Line Control)
    4       R/W   RS-232 (Modem) Control
    5       R/W   Line Status
    6       R/W   RS-232 (Modem) Status
    7       R/W   Not used.

  For  the standard PC ports (not DigiBoard or BOCA ports), the UART registers
  are based at 3F8h (COM1), 2F8h (COM2), 3E8h (COM3), and 2E8h  (COM4).   COM1
  and COM3 share interrupt request line IRQ4 while COM2 and COM4 share request
  line  IRQ3.   This  means  that  COM1  and  COM3 can't be used concurrently.
  Similarly for COM2 and COM4.

  If you have a DigiBoard (or BOCA board) installed, you will have 4  or  more
  additional  ports  using  INS16450 or INS16550 UARTS.  The default DigiBoard
  and BOCA board ports are located at 100h, 108h, 110h,  etc.  Refer  to  your
  DigiBoard (or BOCA board) manual.

  Four  sources  of  interrupts  are  possible  with  the  8250 and 16550: (1)
  receiver error or BREAK, (2) receiver data ready, (3) ready to transmit, and
  (4) RS232 input.   These  four  sources  of  interrupts  are  summarized  as
  follows:

  Source of Interrupt        Action Required to Clear
  Receiver error or BREAK.   Read Line Status register.
  Receiver data.             Read data from data register.
  Transmitter Buffer Empty.  Write to data register or read IID reg.
  RS232 input.               Read Modem Status register.

  However,  PCL4C  only  enables the receiving data interrupt. This means that
  interrupts can only be caused by incoming data.

  If you are not familiar with the INS8250, several good books are  available.
  Refer  to the Serial Communications chapter for recommendations.  Although a
  knowledge of the 8250 is not necessary to use PCL4C, a general knowledge  of
  the theory of asynchronous serial communications is recommended.


















 PCL4C Users Manual                                                Page 24
  6.8 Register Summary


  REG 0 : Data Register

  Reading  from  the  data  register  fetches  the next input byte, once it is
  ready.  Writing to the data register transmits the byte written to  it  over
  the serial line.

  REG 1 : Interrupt Enable 

  The  Interrupt Enable register enables each of four types of interrupts when
  the appropriate bit is set to a one.

  bit 3 : Enable interrupt on RS232 input.
  bit 2 : Enable interrupt on receiver error or break.
  bit 1 : Enable interrupt on transmitter buffer empty (TBE).
  bit 0 : Enable interrupt on received data (RxRDY).

  REG 2 : Interrupt Identification (IID)

  Reading  the Interrupt Identification (read only) register once an interrupt
  has occurred identifies the interrupt as follows:

  Bit 2  Bit 1  Bit 0  Priority    Interrupt
    0      0      1      none      none
    1      1      0      0 (high)  Serialization or break.
    1      0      0      1         Received data.
    0      1      0      2         Transmitter Buffer Empty.
    0      0      0      3 (low)   RS232 Input.

  In the INS16650, REG 2 (write only)  is  also  the  FIFO  control  register.
  Writing bits 6 & 7 will set the FIFO trigger level (number of bytes received
  before an interrupt is generated).

  Bit 7  Bit 6   Trigger             Bit 7  Bit 6   Trigger
   0      0      1 byte               1      0      8 bytes
   0      1      4 bytes              1      1      14 bytes

  REG 3 : Line Control

  RS232 line parameters are selected by writing to this register.

  bit 7   : DLAB = 0
  bit 6   : BREAK on(1), off(0).
  bits 5-3: Parity None(000),ODD(001),EVEN(011),MARK(101),SPACE(111)
  bit 2   : One stop bit(0), two stop bits(1).
  bits 1-0: Data bits = 5 (00), 6(01), 7(10), 8(11).

  When  the Divisor Latch Access Bit (DLAB) is 1, registers 0 and 1 become the
  LS and MS bytes of the Baud Rate Divisor registers.

  Baud   Divisor      Baud  Divisor      Baud  Divisor
   300    0180        4800   0018       38400   0003
  1200    0060        9600   000C       57600   0002
  2400    0030       19200   0006      115200   0001











 PCL4C Users Manual                                                Page 25
  REG 4 : Modem Control

  RTS, DTR, loopback testing, and  General  Purpose  Outputs  #1  and  #2  are
  controlled by the Modem Control register as follows:

  bit 4 : Enable local loopback.
  bit 3 : Enable GP02. Necessary for 8250 interrupts.
  bit 2 : Enable GP01.
  bit 1 : Set / clear RTS.
  bit 0 : Set / clear DTR.

  REG 5 : Line Status

  Reading  the  Line Status register provides status information as follows (1
  for TRUE, 0 for FALSE) :

  bit 6 : Transmitter Empty.
  bit 5 : Transmitter Buffer Empty (TBE).
  bit 4 : BREAK detect.
  bit 3 : Framing error.
  bit 2 : Parity error.
  bit 1 : Overrun error.
  bit 0 : Data Ready.

  REG 6 : Modem Status

  Reading the Modem Status register provides the following status  information
  (1 for TRUE, 0 for FALSE) :

  bit 7 : DCD status.
  bit 6 : RI status.
  bit 5 : DSR status.
  bit 4 : CTS status.
  bit 3 : Delta DCD status.
  bit 2 : Delta RI status.
  bit 1 : Delta DSR status.
  bit 0 : Delta CTS status.

  The  delta  bits  (bits 0 through 3) are set whenever one of the status bits
  (bits 4 through 7) changes (from 0 to 1 or from 1 to 0) since the last  time
  that  the  Modem Status register was read. Reading the Modem Status register
  clear the delta bits.

  REG 7 : Scratch Register

  There is no function associated with register 7.  It does not exist in early
  versions of the 8250.




















 PCL4C Users Manual                                                Page 26
  7.0 Example Programs

  Four  example  programs  are  include with PCL4C.  In addition, the Personal
  Protocol Library for C (PPL4C) includes  the  terminal  program  TERM  which
  features  ASCII,  XMODEM,  YMODEM,  and ZMODEM protocol transfers.  Complete
  source code is included in the shareware product for all  of  the  protocols
  above  except  ZMODEM.   In  order  to  get  ZMODEM  source,  PPL4C  must be
  registered.

  7.1 MINIMAL

  MINIMAL is the simpliest possible communications program. It reads from  the
  serial port & displays on the screen and reads from the keyboard & sends out
  over the serial line. COM1 and 9600 baud are hard coded for simplicity.

  7.2 SIMPLE

  SIMPLE  is  a simple terminal program. It operates like MINIMAL, except that
  you specify both a port and a baud rate. For example.

      SIMPLE 1 9600

  7.3 LOGIN

  LOGIN is programmed to dial our support BBS (205-880-9748)  and  log  on  as
  GUEST.  Start LOGIN like SIMPLE by providing a COM port and a baud rate. For
  example,

     LOGIN 1 38400

  7.4 DOOR

  The  DOOR program is a simple communications program which can "take over" a
  serial port.  For example, say you  are  running  PROCOMM,  PCPLUS,  or  any
  communications  program  with  a  DOS  gateway.  Select the DOS gateway from
  PROCOMM (or whatever) and then type

     DOOR 1

  at the DOS prompt to take over port COM1.

  7.5 SELFTEST

  The SELFTEST.C program is designed to test your serial ports  provided  that
  you  have two ports which can be connected together with a null modem cable.
  SELFTEST can also be used to test your multiport board.

  For example, to test PC port COM1 against COM2, type:

     SELFTEST PC 1 2

  SELFTEST  may  need  to  be  configured  for  non-standard  PC ports or your
  multiport board. Refer to the SELFTEST source code for more information.














 PCL4C Users Manual                                                Page 27
  8.0 Legal Issues

  8.1 Registration


  If  you  wish to register the PCL4C library, please send $65 plus $3 S&H ($6
  outside of North America) to:

           MarshallSoft Computing, Inc.
           Post Office Box  4543
           Huntsville AL 35815

  Multiple copies are available: $50 for 3 to 9, $35 for 10 to 19, and $25 for
  20 or more. A site license is also available for $495 (includes  5  sets  of
  printed documentation). We pay shipping.

  We accept American Express (account number, expiration date, exact  name  on
  your card, and complete AmEx billing address required), checks in US dollars
  drawn  on  a  US  bank, purchase orders (POs) from recognized US schools and
  companies listed in Dun & Bradstreet, and  COD  (street  address  and  phone
  number required) within the USA (plus a $3 COD charge).

  You  can  also  order PCL4C from The Public Software Library (PSL) with your
  MC, Visa, AmEx, or Discover card by  calling  800-242-4PSL  (from  overseas:
  713-524-6394)  or  by  FAX  at 713-524-6398 or by CompuServe at [71355,470].
  THESE  NUMBERS ARE FOR ORDERING ONLY. The product number for PCL4C is 10908.
  Please have your credit card billing address ready.

  If you wish to update from an older version of PCL4C, send $20 plus  $3  S&H
  ($6  outside  of  North  America).   Updates  must  be ordered directly from
  MarshallSoft Computing.

  The registered package includes:


  o  Small,Compact,Medium, & Large libs w/o shareware screens.
  o  Assembler source code for the library.
  o  Laser printed Users and Reference Manuals.
  o  Telephone, FAX, and BBS support for one year.
  o  Utility program (EXAMPORT) which displays  a  detailed  formatted  report
     for any serial port.


  Print the file INVOICE.DOC if an invoice is needed. The registered user will
  receive the latest version of PCL4C shipped by two day priority mail (packet
  airmail overseas).  A 3.5" diskette is provided unless a 5.25"  diskette  is
  requested.




















 PCL4C Users Manual                                                Page 28
  8.2 License


  MarshallSoft  Computing,  Inc. grants the registered user of PCL4C the right
  to use one copy of the PCL4C library (in object form) on a  single  computer
  in  the  development  of  any software product (other than libraries such as
  PCL4C).  The user may not use the library on more than one computer  at  the
  same  time.   The  source code for the library (PCL4C.ASM) is copyrighted by
  MarshallSoft Computing and may not be released in whole or in part.

  Products  developed  using  PCL4C can include the object form of the library
  and may be distributed without any royalty.


  8.3 Warranty


  MARSHALLSOFT COMPUTING, INC.  DISCLAIMS  ALL  WARRANTIES  RELATING  TO  THIS
  SOFTWARE,  WHETHER  EXPRESSED  OR  IMPLIED, INCLUDING BUT NOT LIMITED TO ANY
  IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR  PURPOSE,
  AND  ALL  SUCH WARRANTIES ARE EXPRESSLY AND SPECIFICALLY DISCLAIMED. NEITHER
  MARSHALLSOFT COMPUTING, INC. NOR ANYONE ELSE WHO HAS BEEN  INVOLVED  IN  THE
  CREATION,  PRODUCTION,  OR DELIVERY OF THIS SOFTWARE SHALL BE LIABLE FOR ANY
  INDIRECT, CONSEQUENTIAL, OR INCIDENTAL DAMAGES ARISING OUT  OF  THE  USE  OR
  INABILITY  TO  USE  SUCH  SOFTWARE EVEN IF MARSHALLSOFT COMPUTING, INC.  HAS
  BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES OR CLAIMS. IN NO EVENT SHALL
  MARSHALLSOFT COMPUTING, INC.'S LIABILITY FOR ANY SUCH  DAMAGES  EVER  EXCEED
  THE  PRICE  PAID FOR THE LICENSE TO USE THE SOFTWARE, REGARDLESS OF THE FORM
  OF THE CLAIM. THE PERSON USING THE SOFTWARE BEARS ALL RISK AS TO THE QUALITY
  AND PERFORMANCE OF THE SOFTWARE.

  Some states do not allow  the  exclusion  of  the  limit  of  liability  for
  consequential  or  incidental damages, so the above limitation may not apply
  to you.

  This agreement shall be governed by the laws of the  State  of  Alabama  and
  shall  inure  to  the  benefit  of  Marshallsoft  Computing,  Inc.   and any
  successors, administrators, heirs and  assigns.  Any  action  or  proceeding
  brought  by either party against the other arising out of or related to this
  agreement shall be brought only in a STATE or  FEDERAL  COURT  of  competent
  jurisdiction  located in Madison County, Alabama. The parties hereby consent
  to in personam jurisdiction of said courts.

























 PCL4C Users Manual                                                Page 29
  9.0 Summary


  9.1 Revision History


  Version 1.0 - 14 January 1991 - original release.

  Version 1.1 - 11 March 1991

  o  Added SioUnGetc() function to library.

  Version 1.2 - 1 June 1991

  o  SioParms() bug - could not call before SioReset.
  o  SioReset() bug - was not saving & restoring all regs.

  Version 1.3 - 1 July 1991

  o  Added NORESET option to SioReset.
  o  Added SioDSR, SioCTS, SioDCD, SioLoopBack, and SioRI.

  Version 2.0 - 1 Nov 1991

  o  Reorganized as four memory model libraries.
  o  Added SioModel function to library.
  o  Added support for Quick C and Power C.

  Version 2.1 - 1 Dec 1991

  o  Fixed bug due to Microsoft Assembler (MASM 5.0,5.1) error.

  NOTE:  MarshallSoft incorporated as "MarshallSoft Computing, Inc."
  on December 23rd, 1991.

  Version 3.0 - 15 Jan 1992

  o  Added SioUART function.
  o  Added "UART undefined" error code.
  o  Added "Bad or missing UART" error code.
  o  Added "Port already enabled" error code.
  o  Added "Cannot enable both COM1 & COM3 ..." error code.
  o  Fixed several minor bugs (using new automated testing).

  Version 3.1 - 1 March 1992

  o  Added SioFIFO (INS16550 support).
  o  Added SioIRQ function.
  o  Increased maximum receive buffer size to 32K bytes.


















 PCL4C Users Manual                                                Page 30
  9.1 Revision History (continued)


  Version 3.2 - 1 May 1992


  o  Modified SioReset so that it no longer clears DTR & RTS.
  o  Modified SioModel & renamed to SioInfo.
  o  Fixed bug in SioDone when using 2 ports simultaneously.
  o  Added SioFlow to library.
  o  Added YMODEM-G protocol to TERM program.

  Version 3.3 - 3 August 1992

  o  Fixed bug in SioUnGet when using 2 ports simultaneously.
  o  Add SioRead function.

  Version 3.4 - 4 Jan 1993

  o  Library modified to use up to four ports simultaneously.
  o  SioIRQ was modified to include a third argument.
  o  EXAMPORT utility distributed to registered users.

  Version 3.5 - 15 May 1993

  o  Supports dumb DigiBoards ( PC/4 and PC/8).
  o  Two new error traps added ("No such IRQ" & "No such ISR").
  o  ASCII file transfer protocol added to TERM (with XON/XOFF).

  Version 4.0 - 18 Oct 1993

  o  The library supports transmitter interrupts.
  o  Corrects bug in Ver 3.5 requiring calling SioIRQ for COM3/4.
  o  All example code compiles with supported C++ compilers.
  o  The SioIRQ() function has been simplified.

  Version 4.1 - 1 May 1994

  o  Transmitter FIFO enabled.
  o  Minor internal modifications.
  o  Supports dumb BOCA boards (BB1004, BB1008, & BB2016).
  o  Port definition extented to COM16.

  Version 4.2 - 1 Sept 1994

  o  A flow control bug was fixed.
  o  SioGetDiv function added.
  o  SioRxBuf & SioTxBuf function modified.

  Version 4.3 - 15 March 1995

  o  BREAK detection bug fixed,
  o  Port definitions extended to COM20.
  o  Support for IRQ8 through IRQ15.
  o  Line status bits preserved.

  (The TERM program moved to PPL4C)










 PCL4C Users Manual                                                Page 31
  9.2 Function Summary


  Refer to the PCL4C Reference Manual (PCL4C.REF) for detailed information  on
  the  communications  and  support  functions.  A  one  line  summary of each
  function follows:


  SioBaud     Sets the baud rate of the selected port.
  SioBrkKey   Returns non-zero if the Control-BREAK key was pressed.
  SioBrkSig   Asserts, cancels, or detects BREAK signal.
  SioCrtWrite Write character to the screen.
  SioCTS      Reads the Clear to Send (CTS) modem status bit.
  SioDCD      Reads the Data Carrier Detect (DCD) modem status bit.
  SioDelay    Delays one or more tics (18 tics per second).
  SioDone     Terminates further serial processing.
  SioDSR      Reads the Data Set Ready (DSR) modem status bit.
  SioDTR      Set, clear, or read the Data Terminal Ready (DTR) bit.
  SioError    Displays error in text.
  SioFIFO     Sets the interrupt level for the INS16550.
  SioFlow     Enables / disables hardware flow control.
  SioGetc     Reads the next character from the serial line.
  SioGetDiv   Reads the baud rate divisor registers.
  SioKeyPress Detects if keyboard has been pressed.
  SioKeyRead  Reads the keyboard.
  SioInfo     Returns library version number & memory model.
  SioIRQ      Assigns an IRQ line to a port.
  SioLine     Reads the line status register.
  SioLoopBack Performs a UART loopback test.
  SioModem    Reads the modem status register.
  SioParms    Sets parity, stop bits, and word length.
  SioPorts    Sets # ports, 1st DigiBoard / BOCA port & status reg.
  SioPutc     Transmit a character over a serial line.
  SioRead     Reads any of 7 UART ports.
  SioReset    Initialize a serial port for processing.
  SioRI       Reads the Ring Indicator (RI) modem status bit.
  SioRTS      Sets, clears, or reads the Request to Send (RTS) line.
  SioRxBuf    Sets up receive buffer.
  SioRxFlush  Flushes (clears) the receive buffer.
  SioRxQue    Returns the number of characters in the receive queue.
  SioTimer    Returns the number of system clock tics.
  SioTxBuf    Sets up transmit buffer.
  SioTxFlush  Flushes (clears) the transmit buffer.
  SioTxQue    Returns the number of characters in the transmit queue.
  SioUART     Sets the UART base address.
  SioUnGetc   "Un-gets" (puts back) a specified character.


  9.3 Further Reading


  The best way to learn about serial communications is to read a good book  on
  the subject. Several good texts are available.  Two that I like are:

  (1) C  Programmers's  Guide to Serial Communications by Joe Campbell (SAMS)
  (2) Mastering Serial Communications by Peter Gofton (SYBEX).











 PCL4C Users Manual                                                Page 32
  10.0 Other MarshallSoft Computing Products


  10.1 The Personal Protocol Library for C/C++


  The  Personal  Protocol  Library  for C (PPL4C) consists of a C/C++ language
  library which implements XMODEM, XMODEM-CRC,  XMODEM-1K,  XMODEM-G,  YMODEM,
  YMODEM-G,  and  ZMODEM  file  transfer  protocols.   A  script  compiler and
  interpreter is also included which is capable of such tasks as automatically
  logging onto a BBS and downloading a file or retrieving mail. Three  example
  script programs are included.

  The protocol library (PPL4C) requires the  Personal  Communications  Library
  for C (PCL4C).

  The Personal Protocol Library for C is available for $40 plus $3 S&H ($6 S&H
  overseas).


  10.2 The LZW Data Compression Library for C


  LZW4C  is  an  implementation  of  the  LZW (Lempel-Ziv-Welch) algorithm for
  compressing and decompressing data.  LZW  does  particularly  well  on  text
  files, achieving better than a 50 % compression ratio for many files.

  The  LZW  algorithm  is  considered  to  be  one of the best general purpose
  algorithms  available  today.   The  new  high  speed  modems  that   employ
  on-the-fly  data  compression  (such as MNP 5.0 & the V.42 bis international
  standard) use the LZW algorithm, as well as such well known utility programs
  such as PKZIP.

  The LZW Data Compression Library for C is available for $45 plus $3 S&H  ($6
  S&H overseas).


  10.3 The EMS Expanded Memory Library


  The  EMS4C library implements version 3.2 of the LIM (Lotus-Intel-Microsoft)
  specification for expanded memory. It will run with either  version  3.2  or
  4.0 of the LIM specification.

  The  EMM4C  library  (included with the EMS4C library) is an expanded memory
  manager which allows C programmers  to  allocate  and  free  EMS  (expanded)
  memory  similiar  to  malloc() and free() in the standard C runtime library.
  Both EMM4C and EMS4C require that your system be  configured  with  expanded
  (EMS)  memory.  But,  386  &  up systems can use extended memory as expanded
  memory.

  The EMS Expanded Memory Library for C is available for $35 plus $3  S&H  ($6
  S&H overseas).














 PCL4C Users Manual                                                Page 33