CDRILL

                                   Version 3.5

                                   March, 1995

                               Copyright (c) 1995

                               By:  Richard Zakas

          WHAT IS IT ?
          ------------
            CDRILL is a utility program that provides machinists and CNC
          programmers an easy method to compute the depth to move a center
          drill to produce a center of a given diameter.




                               LIMIT OF LIABILITY

          CDRILL is distributed as-is.  The author disclaims all 
       warranties, expressed or implied.  The author will assume no 
       liability for damages either from the direct use of this product or
       as a consequence of the use of this product.  This offer is a limited
       time offer and pre-empts any previous offer.



                                    SHAREWARE

         This is a shareware version of CDRILL, and it is fully functional.
       You are encouraged to try this SHAREWARE version, and if you find it
       of value, to register your copy.  You are granted a limited license 
       to use this shareware version for a "reasonable" period of time.  The
       registration fee is $12.50 U.S., and $17.50 outside the U.S.   This
       registration fee entitles you to use CDRILL beyond a trial period.
       Registered users will also be able to upgrade their copy of CDRILL,
       by removing the registration screen.  When sending in your registration,
       you MUST mention the version you are registering, where you obtained 
       CDRILL, and the registration fee.  Any suggestions or comments are 
       always appreciated, so if you have something you want included or 
       changed in the program, please write.

       Checks can be made to:

                                                      Richard Zakas
                                                      1615-12 Gander Cove Lane
                                                      Matthews, NC  28105



                              USING CDRILL

          CDRILL is run from the DOS command line.   Type CDRILL and then
        press <ENTER>.  When the main screen comes up you will see a chart
        of various center drill sizes and the center sizes each one
        is capable of producing.  For example, if you needed to produce a
        .330 dia center, looking at the chart you can use a # 5, 6, 7, or
        8 center drill.  You pick  6           So.......


        
        Enter Dia. of Center needed:  .330 <ENTER>

        Enter Center Drill to use:  6 <ENTER>


             and then the program calculates the drill depth needed to
             produce a .330 center using a #6 center drill.


        Drill Depth is : .37824
        

         
          NOTE:
       =====================================================================    
          Center drill sizes 11 to 18 are protected center drills.  Normally
       you would not use the 120 degree protion of the center drill.  But
       if a 120 degree break is needed, the program will accurately 
       calculate the distance needed to achieve the break.  





           /LAP      command line switch

           Use this command line switch on laptop & vga monochrome systems
           to get a useable color palette.

              example  A:>    CDRILL /LAP



                                DISTRIBUTION

              You to make as many copies as you wish for distribution
        (in its unaltered original form, including all documentation) to others
        on the same evaluation basis.