XSUM			User's Manual			XSUM


NAME
	crc, mdx - generate checksums of a file or files

SYNOPSIS
	crc [options | filespec] ...
	mdx [options | filespec] ...

VERSION
	crc version 1.07
	mdx version 1.05

DESCRIPTION
	crc and mdx compute the checksum of a file or a set of files.
	crc computes the 32-bit Cyclical Redundancy Check (CRC-32) and
	mdx computes the 128-bit Message Digest (MD4 or MD5).
	Running either one with no parameters will give a quick
	summary of function and options.

OUTPUT
	The output of both programs is written to standard output
	(stdout), and can be redirected to a file.  The title and
	any error messages will be sent to standard error (stderr).

	The basic output of crc is formatted as:

		e0c8a642  filename

	and the basic output of mdx is formatted as:

		e0c8a642e0c8a642e0c8a642e0c8a642  MDx  filename

	where x is replaced by 5 or 4 to indicate MD5 or MD4.

	In addition, each program has an extended output mode where extra
	information is given about each file processed.  This information
	includes the file size, the file time (with seconds) and the file
	date (with century).

	The extended output of crc is formatted as:

		e0c8a642  1,234,567,890  23:36:18  01-Jan-1980  filename

	and the extended output of mdx is formatted as:

		e0c8a642e0c8a642e0c8a642e0c8a642  MDx  filename
		     1,457,664  08:45:58  05-Feb-1995



								1





XSUM			User's Manual			XSUM


	Be advised that a file which has its seconds set to 62 or its
	year set ahead a century (e.g., 2095 instead of 1995) may be
	infected with a virus.  This is not necessarily the case, but
	there are some viruses which mark infected files in this way.

OPTIONS
	filespec	The name of a file or a pattern which matches
			several files.  The drive and path may be
			specified, and there is no limit to the number
			of files matched.  Also, as many filenames or
			patterns as will fit on the command line may
			be given.

	The following options apply only to mdx:

		-4	Use the MD4 algorithm.

		-5	Use the MD5 algorithm (default).

		-n	Don't use the faster 386 code.

		-nn	Don't check for the presence of a 386 processor.

	The -4 and -5 options may be used more than once on the command
	line.  Whichever was last given affects which algorithm is used,
	so MD4 and MD5 message digests can be computed on the same run.
	For example,

		mdx -4 *.exe *.com *.sys -5 *.txt *.doc *.man

	would calculate the MD4 digests of all the programs in the
	current directory, and the MD5 digests of all the text.  Or,

		mdx foo.bar -4 foo.bar

	would calculate both numbers for the file foo.bar.

	The -n and -nn options allow you to run the standard MD5 code
	instead of the faster 386-specific code.  The only reason you
	would want to do this is to make a speed comparison.  Normally
	mdx uses an enhanced 32-bit version of the MD5 translate
	function, if it detects a 386 or better processor.  Just in case
	this causes a problem (which it shouldn't), you can force mdx to
	use the slower (but compatible) code with the -n switch, or even
	suppress the test for the 386 entirely with the -nn switch.




								2





XSUM			User's Manual			XSUM


	The following options apply to both mdx and crc:

		-h	show the help screen.

		-e	display extended file information.

	The -h switch shows the same usage summary that is given if
	the programs are run with no parameters.

	The -e switch selects the extended output format which
	includes the file size, time, and date.

ERRORS
	All errors are of the form prg: message where prg is either
	crc or mdx.

	prg: error opening file name

		The file name could not be opened for reading.  It
		may be locked by another application.

	prg: error reading file name

		An error occurred while reading file name.  The
		disk may be damaged.

	prg: no files found to process

		None of the filespecs given on the command line
		matched any files.

	prg: program has been modified

		On startup, the program checks itself to see if it
		has been modified.  This provides some protection
		against viruses however it will not detect stealth
		viruses.

		If the self-check fails, the program displays this
		message and exits.

	prg: integrity cannot be verified

		If the self-check cannot be performed then this message
		is displayed, and the program continues.  This could
		happen if the self-checking information is tampered
		with, or if the program is run under DOS 2.x.


								3





XSUM			User's Manual			XSUM



	Note that the self check code is smart enough not to be bothered
	by the addition of validation data, which certain anti-virus
	programs foolishly append to the executable file, nor is it
	bothered if the compressed executables are expanded.

AUTHOR
	crc and mdx were written by David R. Conrad, who can be reached
	in the following ways, in order of preference:

		Internet	ab411@detroit.freenet.org
		Mail		432 Alter Rd.
				Detroit, MI 48215-3105 USA

	Users who have sent email to David_Conrad@mts.cc.wayne.edu will
	please note that that address is (temporarily) disabled, and
	any mail sent to it may not be read in a timely manner, if at
	all.  Please use the Greater Detroit FreeNet address instead.

ACKNOWLEDGEMENTS
	These programs would not exist without the code of Gary S. Brown
	which I obtained by way of Rahul Dhesi, and of course the work
	of Ron Rivest, both in developing MD4 and MD5 and in writing
	the reference implementations thereof.  I would also like to
	thank Phil Karn.  Without his md5trans code mdx would run much
	slower.  The 386 detection is based on the p87test program by
	Terje Mathisen.  My special thanks to Vesselin Bontchev who made
	several excellent suggestions which have helped with the
	development of mdx.

LEGALITIES
	crc and mdx are Copyright 1993-1995 David R. Conrad.
	All rights reserved.

	The CRC-32 implementation used was extracted from the source
	of brik by Rahul Dhesi, and is from the zmodem source code,
	and is Copyright 1986 Gary S. Brown.  Used with permission.

	MD4 is the RSA Data Security, Inc. MD4 Message-Digest Algorithm,
	Copyright 1990 RSA Data Security, Inc.  Used with permission.

	MD5 is the RSA Data Security, Inc. MD5 Message-Digest Algorithm,
	Copyright 1991 RSA Data Security, Inc.  Used with permission.

	MD5trans is a public domain implementation of the MD5 translate
	function written by Phil Karn.  Used with permission.



								4





XSUM			User's Manual			XSUM


	David R. Conrad hereby disclaims all warranties relating to
	this software, whether express or implied, including without
	limitation any implied warranties of merchantability or fitness
	for a particular purpose.  I will not be liable for any special,
	incidental, consequential, indirect or similar damages due to
	loss of data or any other reason.  In no case can Rahul Dhesi,
	Gary S. Brown, Phil Karn, or RSA Data Security, Inc. be held
	liable in any way for damages resulting from the use of this
	software or otherwise related to this software.

	crc and mdx are freeware, meaning that they are copyrighted
	but can be used and distributed free of charge, as long as they
	are distributed in an unmodified form.




































								5