FILE:   HST1440.DOC      Version 3.1              (C) Pat Kelly 1990

                        FORMATED FOR OUTPUT:
                        JUST ENTER    COPY HST1440.DOC PRN   AT 'DOS' LEVEL
                        TO PRINT IT     (24 pages)

   ADDRESS COMMENTS TO:   PAT KELLY ON  EXEC-PC BBS 1-414-789-4300 [9600 8 N 1]
                    or    RG MORROW ON  CRS     BBS 1-416-629-0168 [9600 8 N 1]

                        US ROBOTICS COURIER HIGH SPEED MODEMS
                                  -Encompassing-
                                COURIER HST DUAL STANDARD
                                COURIER HST
                                COURIER V.32
                      as shown on the cover of my manual


        PRELIMINARY CONSIDERATIONS
        ==========================
        I AM ASSUMING YOUR MODEM MANUAL IS SIMILAR TO THE ABOVE.
        MY COMMENTS ETC. WERE TESTED USING 'TELIX V3.12' AND 'TELEMATE V2.10'
        ON A SOUPED UP IBM XT WITH A NEC V20 CHIP, A 8MHZ SECONDARY CLOCK, AND
        A MATH CO-PROCESSOR. THEY WERE ALSO TESTED ON AN ALR 386/33 MACHINE
        OPERATING AT LANDMARK SPEEDS OF 51 mhz and 134 mhz (math coprocessor).
        THE RESULTS SHOULD BE SIMILAR ON OTHER COMPUTERS AND WITH OTHER
        COMMUNICATION PROGRAMS.

        THE REASON FOR THIS DOCUMENT IS THAT I HAVE DOWN-LOADED VARIOUS
        'HST' SET-UP FILES, ETC. FROM ASSORTED BBS'S AND HAVE FOUND THAT
        WHILE THEY ALL SAY THEY ARE DOING THE SAME THING, THEY SURE GO ABOUT
        IT IN A VARIETY OF WAYS. IN ALL THE DOWN-LOADS I HAVE FOUND MANY
        ITEMS WHICH WERE UNCLEAR AND SEEMED TO BE CONTRADICTORY FROM ONE
        EXPLANATION TO ANOTHER. THUS, I HAVE MADE MY OWN AND TRIED TO GIVE
        REASONS, EXPLANATIONS, AND REFERENCES FOR EACH OF MY ACTIONS. IN
        SO DOING I HAVE GONE THROUGH THE HST MANUAL AND VARIOUS PUBLICATIONS
        IN ORDER TO UNDERSTAND (?) AND BE ABLE TO EXPLAIN WHAT I HAVE DONE.
        ANOTHER REASON FOR DOING IT THIS WAY IS TO ENABLE ME TO EXPLAIN IT
        TO MY COMPUTER STUDENTS ( HA - THERE WAS ANOTHER MOTIVE AFTER ALL ).

        COMMENTS, CORRECTIONS, CONTRIBUTIONS (MONEY OR OTHER) MAY BE SENT
        TO ME VIA THE ABOVE BBS'S OR TO THE ADRESS GIVEN AT THE END OF THIS
        CODUMENT.

        HARDWARE
        ========
        THE HST HAS 10 DIP SWITCHES:
        1 DATA TERMINAL READY OVERRIDE    6 CARRIER DETECT OVERRIDE
        2 VERBAL/NUMERIC RESPONSE CODES   7 RESULT CODES
        3 RESULT CODE DISPLAY             8 'AT' COMMAND SET RECOGNITION
        4 COMMAND MODE LOCAL ECHO         9 NORMAL MODE ESCAPE CODE
        5 AUTO ANSWER                    10 POWER-ON SOFTWARE DEFAULTS

        IN THE FOLLOWING: U=UP open or off       D=DOWN closed or on

                            1   2   3   4   5   6   7   8   9  10
        FACTORY SETTINGS    U   U       U       U   U       U  U   rest are D
        (ACCORDING TO THE addendum settings in the manual)


PAGE 2
        COMMENTS:
          1 - U  DTR NORMAL: RS232C PIN 20 TO COMPUTER CONTROLS MODEM
          2 - U  ENABLE VERBAL (WORD) MESSAGES FOR MODEM CODES
          3 - D  DISPLAY RESULT CODES ( BUSY, RINGING, ETC.)
          4 - U  ECHO OFF-LINE COMMANDS (SO YOU CAN SEE WHAT YOU TYPE)
          5 - D  SUPPRESS AUTO ANSWER (MODEM WILL not ANSWER PHONE)
                 ( SET AT S0=1 FOR host MODE {EXPLAINED BELOW} )
          6 - U  NORMAL CARRIER DETECT: RS232C PIN 8 INDICATES MODEM IS ON-LINE
          7 - U  SINGLE PHONE USAGE / or NORMAL RESULT CODES
          8 - D  ENABLE 'AT' COMMAND SET (TO PROGRAM THE MODEM'S nram MEMORY)
          9 - U  DISCONNECT WITH +++ (MY LONG DISTANCE BILL SUFFERED WHEN I
                                      DID not DO THIS)
         10 - U  USE NRAM DEFAULTS ( AS OPPOSED TO FACTORY DEFAULTS)

        WHEN YOU NOW TURN ON YOUR MODEM THE    TR   MR   RS   CS
        (Terminal Ready-Modem Ready-Request to Send-Clear to Send)
        LIGHTS SHOULD BE ON. YOU MAY ONLY HAVE THE 'MR' AND 'CS' LIGHTS
	ON UNTIL YOU RUN YOUR COMMUNICATION PROGRAM.

        SOFTWARE
        ========
        THE DISCUSSION AT HAND WILL BE IN TERMS OF TWO (2) COMMUNICATION
        PACKAGES ( TELIX V3.12  and  TELEMATE V2.10). IN BOTH CASES I ASSUME
        THERE IS no CONFIGURATION FILE PRESENT. IF THERE IS JUST DELETE IT AS
        WE WANT TO START FROM SCRATCH.

        FOR TELIX:     (RUN THE PROGRAM    TELIX.EXE)
        QUESTION                        RESPONSE
        --------                        --------
Screen 1
        ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
        ³ Welcome to Telix!               Since the configuration file ³
        ³ can not be found, it is assumed that you are a new user. Af- ³
        ³ ter you  answer a  few questions,  a new  configuration file ³
        ³ will be  written to the disk. This file contains the default ³
        ³ settings of many parameters (ie what they should be when you ³
        ³ start a Telix session).  You will probably want to change at ³
        ³ least a few of them, for example the colors to use for menus ³
        ³ and screen text.  If your modem is  not Hayes compatible you ³
        ³ will want to redefine the strings that Telix uses to control ³
        ³ it.  Pressing Alt-O once you are in Terminal Mode allows you ³
        ³ to go to  the Telix Configuration Menu and  change these de- ³
        ³ faults.                                                      ³
        ÔÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                     ³                                  ³
                     ³ Which video display do you have? ³
                     ³                                  ³
                     ³ Monochrome monitor and text card ³
 I PICKED THIS ONE   ³ Colour monitor and colour card   ³*
                     ³ B&W monitor and colour card      ³
                     ³                                  ³
                     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


PAGE 3

SCREEN 2
            ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍµ Baud ÆÍ¸
            ³                                                      ³          ³
            ³  What is the maximum baud rate your modem supports?  ³     300  ³
            ³                                                      ³    1200  ³
            ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³    2400  ³
                                                                   ³    4800  ³
                                                                   ³    9600  ³
                                                                   ³   19200  ³
PICK THIS RATE (38400)                                             ³   38400  ³*
                                                                   ³   57600  ³
                                                                   ³  115200  ³
                                                                   ³          ³
                                                                   ÔÍÍÍÍÍÍÍÍÍÍ¾
SCREEN 3
                ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍ¸
                ³                                             ³            ³
I PICKED THIS   ³  Which com port is the modem connected to?  ³ Com port 1 ³*
YOUR'S MAY VARY ³                                             ³ Com port 2 ³
                ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³ Com port 3 ³
                                                              ³ Com port 4 ³
                                                              ³ Com port 5 ³
                                                              ³ Com port 6 ³
                                                              ³ Com port 7 ³
                                                              ³ Com port 8 ³
                                                              ³            ³
                                                              ÔÍÍÍÍÍÍÍÍÍÍÍÍ¾
SCREEN 4
         ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
         ³                                                   ³
YES      ³ Do you want a status line on the screen?  Yes  No ³*
         ³                                                   ³
         ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
SCREEN 5
                The TELIX program now runs in 'normal' mode.

Telix Copyright (C) 1986-89 Exis Inc. and Colin Sampaleanu. All rights reserved.
Version 3.12, released 12-1-89.

Registered to: Pat Kelly    Serial #: A1007734

Press ALT-Z for help on special keys.

ATZ
OK
AT S7=45 S0=0 V1 X1
OK


PAGE 4


        HERE IS A SUMMARY OF THE ABOVE.
        ==============================
        MONITOR TYPE AND CARD           I USED COLOR MONITOR AND COLOR CARD
        MAXIMUM BAUD                    38400
        COM PORT                        1   (YOURS MAY VARY)
        STATUS LINE                     YES (I LIKE TO 'SEE' WHAT IS HAPPENING)

        TELIX NOW RESPONDS: ( explanations of actual items will come later)
        ATZ                             RESET MODEM TO NRAM DEFAULTS
        OK                              MODEM SAYS     OK
        AT S7=45 S0=0 V1 X1             SET VARIOUS MODEM DEFAULTS
        OK                              MODEM SAYS     OK


        FOR TELEMATE:

        RUN THE PROGRAM 'TMINST.EXE' TO CREATE THE CONFIGURATION FILE 'TM.CNF'.
        WHEN THE MENU 'POPS UP' EXIT AND SAVE THE SET-UP (WE WILL ALTER IT
        LATER). NOW RUN THE PROGRAM 'TM.EXE'.
        TELEMATE NOW RESPONDS:
        AT S0=0 Q0 E1 X4                SET VARIOUS MODEM DEFAULTS
        OK                              MODEM SAYS     OK
        PROGRAM ENTER PHONE DIRECTORY   PRESS THE 'ESC'KEY TO GET TO COMMAND
                                        MODE AND YOU WILL SEE THE 'AT ...' LINE
                                        (shown at left side of page.)

        PROGRAM USAGE TO SET MODEM RAM MEMORY (NRAM)
        ============================================

        IT IS NOW ASSUMED THAT YOU ARE IN YOUR COMMUNICATION PACKAGE AT THE
        COMMAND (TERMINAL) LEVEL.
        IE.: THE 'AT...' AND 'OK' LINES ARE SHOWING ON THE SCREEN.

        DEFINITION: 'AT' IS THE PREFIX FOR GIVING COMMANDS TO YOUR HST MODEM.
        ----------

        THE FOLLOWING ARE SOME COMMANDS YOU CAN ENTER TO SEE HOW YOUR MODEM
        IS SET-UP.


PAGE 5


ACTION                                COMMENT
======                                =======
AT   (YOU TYPE 'AT')                  SEE IF COMPUTER & MODEM ARE COMMUNICATING
OK                                    MODEM SAYS   OK

ATZ  (YOU TYPE 'ATZ')                 LOAD NRAM DEFAULTS (EXPLAINED BELOW)
OK                                    MODEM SAYS   OK

ATI0 (YOU TYPE 'ATI0')                ASK FOR MODEM'S PRODUCT CODE
1442                                  MAY BE DIFFERENT FOR YOUR MACHINE. MINE
OK                                    WAS MADE IN JUNE 1990.

ATI1 (YOU TYPE 'ATI1')                ASK FOR ROM CHECKSUM
166D  EB6D  BC2C   412B               MODEM DISPLAYS CHECKSUM
OK

ATI2 (YOU TYPE 'ATI2')                ASK MODEM TO CHECK IT'S 'RAM'
OK

ATI3 (YOU TYPE 'ATI3')                SHOW MODEM'S CALL DURATION TIME
00:00:00                              ZERO AS WE HAVEN'T GONE ON-LINE YET
OK

        ACTION                                  COMMENT
        ======                                  =======
ATI4 (YOU TYPE 'ATI4')                     
USRobotics Courier 14400 HST Dual Standard Settings...

 B1  C1  E1  F1  M1  Q0  V1  X1              SHOW factory SETTINGS WITH SLIGHT
 BAUD=38400  PARITY=N  WORDLEN=8             VARIANCES AS WE HAVE SET OUR
 DIAL=PULSE  ON HOOK   TIMER                 TERMINAL PROGRAM WHICH WILL AFFECT
                                             SOME OF THESE VALUES.
 &A1  &B0  &C1  &D2  &G0  &H0  &I0  &J0  &K1 THESE VALUES & THEIR MEANINGS ARE:
 &L0  &M4  &N0  &P0  &R1  &S0  &X0  &Y1      C=1 TRANSMITTER ENABLED
                                             E=1 COMMAND MODE ECHO ON
 S00=000   S01=000   S02=043   S03=013       F=1 ON-LINE ECHO OFF
 S04=010   S05=008   S06=002   S07=060       M=1 SPEAKER ON UNTIL CARRIER DETECT
 S08=002   S09=006   S10=007   S11=070       Q=0 SHOW RESULT CODES-BUSY,RING,ETC
 S12=050   S13=000   S14=001   S15=000       V=1 SHOW CODES AS MESSAGES
 S16=000   S17=000   S18=000   S19=000       X=1 RESULT CODE OPTIONS
 S20=000   S21=010   S22=017   S23=019       B=1 USE U.S.A. ANSWER SEQUENCE
 S24=150   S25=000   S26=000   S27=000
 S28=008   S38=000                         NOTE: V=1 MATCHES DIP SWITCH 2 UP
                                                 Q=0 MATCHES DIP SWITCH 3 DOWN
 LAST DIALED #:                                  E=1 MATCHES DIP SWITCH 4 UP



PAGE 6

OK
   MORE NOTES: THESE PERTAIN TO THE ABOVE '&' OPTIONS (FACTORY DEFAULTS).
               WE WILL CHANGE SOME OF THESE AND PUT THEM IN 'NRAM' MEMORY.
               (THIS IS WHY WE SET DIP SWITCH 10 UP.)
   CODE  MEANING                                 COMMENT
   ====  =======                                 =======
   &A1 - /ARQ CODES WILL BE DISPLAYED            CHANGE TO A2 (ALLOW EXTRA CODES)
   &B0 - BAUD RATE                               CHANGE TO B1 (LOCK BAUD RATE)
   &G0 - NO GUARD TONE (U.S/CANADA DEFAULT)      WE WILL KEEP THIS
   &H0 - HARDWARE/SOFTWARE FLOW CONTROL          CHANGE TO H1
                                                 (TO H1 HARDWARE CONTROL ONLY)
   &I0 - FLOW CONTROL DISABLED (DEFAULT)         WE WILL KEEP THIS (NO XON/XOFF)
   &J0 - SINGLE (MULTIPLE) PHONE LINE            WE WILL KEEP THIS (SINGLE)
   &K0 - DATA COMPRESSION DISABLED               WE WILL KEEP THIS (AS MOST
                                                 FILES ON BBS'S ARE 'ZIPPED')
   &L0 - NORMAL (LEASED) LINE                    WE WILL KEPP THIS (NORMAL)
   &M4 - NORMAL/ARQ MODE                         WE WILL KEEP THIS (MODEM WILL
                                                 TRY HST ARQ MODE IF POSSIBLE)
   &N0 - GET HIGHEST POSSIBLE BAUD WITH REMOTE   WE WILL KEEP THIS
   &P0 - NORTH AMERICAN DIAL PULSE RATE          WE WILL KEEP THIS
   &R2 - MODEM SENDS DATA TO TERMINAL ONLY       WE WILL KEEP THIS
         WHEN 'RequestToSend' IS HIGH
   &S0 - DSR CONTROL 'DataSetReady'              WE WILL KEEP THIS
   &X0 - MODEM TRANSMITTER MODE                  WE WILL KEEP THIS
   &Y1 - DESTRUCTIVE BREAK (ABORT TRANSFER)      WE WILL KEEP THIS

   THE Sxx ARE REGISTERS AS OUTLINED IN THE HST USER MANUAL. ONES WHICH MIGHT
   CHANGE ARE: S07=DIAL TIME IN SECONDS, S15= TURN MNP LEVEL 4 (DATA FRAME
   OPTIMIZATION) ON=0 OR OFF=1, S19=INACTIVITY TIMER, S22=XON CHAR (ASCII 17),
   S23=XOFF CHAR (ASCII 19).

   WE WILL ALTER SOME OF THE ABOVE SHORTLY.

        ACTION                                  COMMENT
        ======                                  =======

ATI5 (YOU TYPE 'ATI5')                           SEE THE NRAM (Nonvolatile
                                                 Random Access Memory) SET-UP
USRobotics Courier 14400 HST Dual Standard NRAM Settings...

   DIAL=PULSE  B1  F1  M1  X1
   BAUD=2400   PARITY=N  WORDLEN=8

   &A1  &B0  &G0  &H0  &I0  &J0  &K1  &L0
   &M4  &N0  &P0  &R1  &S0  &X0  &Y1


PAGE 7

   S02=043   S03=013   S04=010   S05=008
   S06=002   S07=060   S08=002   S09=006
   S10=007   S11=070   S12=050   S13=000
   S15=000   S19=000   S21=010   S22=017
   S23=019   S24=150   S26=000   S27=000
   S28=008   S38=000

   STORED PHONE #0:
                #1:
                #2:
                #3:

OK
OK
ATI6 (YOU TYPE 'ATI6')                           SEE A DIAGNOSTIC SUMMARY OF
                                                 A MODEM SESSION
USRobotics Courier 14400 HST Dual Standard Link Diagnostics...

Chars sent                     0        Chars received                 0
Chars lost                     0
Octets sent                    0        Octets received                0
Blocks sent                    0        Blocks received                0
Blocks resent                  0

Retrains Requested             0        Retrains Granted               0
Line Reversals                 0        Blers                          0
Link Timeouts                  0        Link Naks                      0

Data Compression        Off
Equalization            Long
Fallback                Disabled

No Connection

OK
ATI7 (YOU TYPE 'ATI7')                           SEE YOUR MODEM'S CONFIGURATION
                                                 PROFILE
Configuration Profile...

Product type           External
Options                HST,V32
Clock Freq             10.0Mhz
Eprom                  64k
Ram                    32k

Supervisor date        06/04/90
IOP date               05/17/89
DSP date               09/18/89

Supervisor rev         2.1
IOP rev                1.0
DSP rev                2
R9696 rev              204C
OK


PAGE 8
        ACTION                                  COMMENT
        ======                                  =======

ATI8 (YOU TYPE 'ATI8')                ASK MODEM WITH AN INVALID COMMAND
ERROR                                 MODEM ANSWERS 'ERROR'

        OTHER COMMANDS YOU CAN TRY ARE:
        AT$     DISPLAY THE BASIC 'AT' COMMAND SET
        AT&$    DISPLAY THE EXTENDED 'AT' COMMAND SET
        ATS$    DISPLAY THE S-REGISTER FUNCTIONS
        ATD$    DISPLAY THE MODEM'S DIAL COMMAND SUMMARY

        THE ABOVE WILL PRODUCE RESULTS SIMILAR TO THE FOLLOWING:

AT$
HELP,  Command Quick Reference (CTRL-S to Stop, CTRL-C to Cancel)

&$    HELP, Extended Commands        In    n=5  NRAM Settings
A     Answer Call                          n=6  Link Diagnostics
A/    Repeat Last Command            Kn    n=0  Call Duration Mode
Bn    n=0  CCITT Answer Sequence           n=1  Real Time Clock Mode
      n=1  Bell Answer Sequence      Mn    n=0  Speaker Off
Cn    n=0  Transmitter Off                 n=1  Speaker On Until CD
      n=1  Transmitter On                  n=2  Speaker Always On
Dn    Dial a Telephone Number              n=3  Speaker Off During Dial
      n=0..9#*TPR,;"W@!()-           O     Return On-Line
DSn   Dial Stored Phone Number       Qn    n=0  Result Codes Sent
D$    HELP, Dial Commands                  n=1  Quiet (No Result Codes)
En    n=0  Do not echo Chars         Sr=n  Sets Register "r" to "n"
      n=1  echo Command Chars        Sr?   Query Register "r"
Fn    n=0  Half duplex               S$    HELP, S Registers
      n=1  Full duplex               Vn    n=0  Numeric Responses
Hn    n=0  On Hook (Hang Up)               n=1  Verbal Responses
      n=1  Off Hook                  Xn    n=0  Basic Result Codes
In    n=0  Product Code                    n=1  Extended Result Codes
      n=1  Checksum                        n=2-7  Advanced Result Codes
      n=2  RAM Test                  Z     Software Reset
      n=3  Call Duration/Clock       >     Repeat Command String
      n=4  Current Settings          $     HELP,  Command Summary
OK


PAGE 9

AT&$
HELP, Extended Commands (CTRL-S to Stop, CTRL-C to Cancel)

&An   n=0  Disable /ARQ Result Codes      &Mn   n=0  Normal Mode
      n=1  Enable /ARQ Result Codes             n=1  Synchronous Mode
      n=2  Enable /extra Result Codes           n=4  ARQ/Normal Mode
&Bn   n=0  Floating DTE Speed                   n=5  ARQ Mode
      n=1  Fixed DTE Speed                &Nn   n=0  Highest Link Speed
      n=2  DTE Speed Fixed When ARQ             n=1  300 bps
&Cn   n=0  CD Always On                         n=2  1200 bps
      n=1  Modem Controls CD                    n=3  2400 bps
&Dn   n=0  Ignore DTR                           n=4  4800 bps
      n=1  Reserved                             n=5  7200 bps
      n=2  DTE Controls DTR                     n=6  9600 bps
&F    Load Factory Configuration                n=7  12000 bps
&Gn   n=0  No Guard Tone                        n=8  14400 bps
      n=1  550 Hz Guard Tone              &Pn   n=0  N. American Pulse Dial
      n=2  1800 Hz Guard Tone                   n=1  UK Pulse Dial
&Hn   n=0  Disable TX Data Flow Control   &Rn   n=0  CTS Follows RTS
      n=1  CTS                                  n=1  Ignore RTS
      n=2  Xon/Xoff                             n=2  RX Data to DTE/RTS high
      n=3  CTS and Xon/Xoff               &Sn   n=0  DSR Always On
&Gn   n=0  No Guard Tone                        n=8  14400 bps
      n=1  550 Hz Guard Tone              &Pn   n=0  N. American Pulse Dial
      n=2  1800 Hz Guard Tone                   n=1  UK Pulse Dial
&Hn   n=0  Disable TX Data Flow Control   &Rn   n=0  CTS Follows RTS
      n=1  CTS                                  n=1  Ignore RTS
      n=2  Xon/Xoff                             n=2  RX Data to DTE/RTS high
      n=3  CTS and Xon/Xoff               &Sn   n=0  DSR Always On
&In   n=0  Disable RX Data Flow Control         n=1  Modem Controls DSR
      n=1  Xon/Xoff                             n=2  Pulse DSR, CTS Follows CD
      n=2  Xon/Xoff Chars Filtered              n=3  Pulse DSR
      n=3  HP Enq/Ack Host Mode           &Xn   n=0  DCE Synchronous Clock
      n=4  HP Enq/Ack Terminal Mode             n=1  DTE Synchronous Clock
      n=5  Xon/Xoff for non-ARQ Mode            n=2  RX Clock is Source
&Jn   n=0  Single Phone Line, RJ11 Jack   &Yn   n=0  Destructive
      n=1  Multiple Lines, RJ12/13 Jack         n=1  Destructive/Expedited
&Kn   n=0  Disable Data Compression             n=2  Nondestructive/Expedited
      n=1  Auto Data Compression                n=3  Nondestructive/Unexpedited
      n=2  Enable Data Compression        &Zn=s Store Phone Number
      n=3  Selective Data Compression     &Zn=L Store Last Phone Number
&Ln   n=0  Disable Leased Line            &Zn?  Query Phone Number
      n=1  Enable Leased Line             &W    Store Current Configuration

OK


PAGE 10

ATS$
HELP, S Register Functions (CTRL-S to Stop, CTRL-C to Cancel)

S0  Ring to Answer On                   S16 Test Modes
S1  Counts # of Rings                         1 = Analog Loopback
S2  Escape Code Char                          2 = Dial Test
S3  Carriage Return Char                      4 = Test Pattern
S4  Line Feed Char                            8 = Remote Digital Loopback
S5  Backspace Char                           16 = Reserved
S6  Wait Time/Dial Tone (sec)                32 = Reserved
S7  Wait Time/Carrier (sec)                  64 = Reserved
S8  Comma Time (sec)                        128 = Reserved
S9  Carrier Detect Time (1/10sec)       S17 Reserved
S10 Carrier Loss Time (1/10sec)         S18 Reserved
S11 Dial Tone Spacing (msec)            S19 Inactivity Timeout (min)
S12 Escape Code Time (1/50sec)          S20 Reserved
S13 Bit Mapped                          S21 Break Length (1/100sec)
      1 = Reset On DTR Loss             S22 Xon Char
      2 = Do Originate in Auto Answer   S23 Xoff Char
      4 = No Pause Before Result Codes  S24 DSR Pulse Time (1/50sec)
      8 = Do DS0 On DTR                 S25 Reserved
     16 = Do DS0 On Reset               S26 RTS/CTS Delay Time (1/100sec)
     32 = Disable HST                   S27 Bit Mapped
     64 = Disable MNP Level 3                 1 = V21 Mode
    128 = Hardware Reset                      2 = Disable TCM
S14 Reserved                                  4 = Disable V32
S15 Bit Mapped                                8 = Reserved
      1 = Disable High-Freq EQ               16 = Disable MNP Fallback
      2 = Disable Online Fallback            32 = Disable V42 Detection Phase
      4 = Disable 450 bps Back Channel       64 = Shift Rate (0=19.2K, 1=38.4K)
      8 = Reduced Non-ARQ TX Buffer         128 = Enable HS DTE Shift
     16 = Disable MNP Level 4           S28 V32 Handshake Time (1/10sec)
     32 = Set DEL=Backspace             S38 Disconnect Wait Time (sec)
     64 = Unusual MNP-Incompatibility
    128 = Custom Applications

OK


PAGE 11

ATD$
HELP, Dial Commands (CTRL-S to Stop, CTRL-C to Cancel)

0-9 Digits to Dial
*   Auxiliary Tone Dial Digit
#   Auxiliary Tone Dial Digit
T   Tone Dialing
P   Pulse Dialing
R   Call an Originate Only Modem
,   Pause (Wait for S8 Time)
;   Remain in Command Mode After Dialing
"   Used to Dial Alpha Phone #'s
W   Wait for 2nd Dial Tone (X3-X7)
@   Wait for an Answer (X3-X7)
!   Flash Switch Hook

OK

        PROGRAMMING THE MODEM'S NRAM
        ============================
        NOW EXIT YOUR TERMINAL PROGRAM AND RE-ENTER IT (I USED TELIX). WE ARE
        NOW GOING TO PROGRAM THE MODEM'S NRAM. MAKE SURE YOU ARE AT TERMINAL
        MODE.

ACTION                                        COMMENTS
======                                        ========
ATZ                                           SET MODEM TO NRAM DEFAULTS
OK
AT B1 C1 E1 F1 M1 Q0 V1 X6                    AT - INVOKE COMMAND LEVEL
OK
           B1 - SET U.S. ANSWER SEQUENCE
           C1 - ENABLE TRAMSMITTER
           E1 - COMMAND MODE ECHO ON
           F1 - ONLINE ECHO OFF
           M1 - SPEAKER ON THROUGH CD(DIAL)
           Q0 - SHOW RESULT CODES
           V1 - VERBAL RESULT CODES
           X6 - ALL ADVANCED RESULT CODES

AT &A2 &M4 &K0 &H1 &R2 &I0 &B1 &N                   AT - INVOKE COMMAND LEVEL
OK
                 THE & INDICATES EXTENDED COMMAND LEVEL COMMANDS
          &A2 - SHOW /ARQ EXTENDED RESULT CODES
          &M4 - SET NORMAL/ARQ MODE
          &K0 - DISABLE DATA COMPRESSION
          &H1 - HARDWARE (CTS) FLOW CTRL
          &R2 - ENABLE HARDWARE RTS CTRL
          &I0 - DISABLE RECEIVE DATA CTRL
          &B1 - FIX DTE BAUD RATE
          &N  - SET HIGHEST BAUD POSSIBLE
OK


PAGE 12

AT &W                                               WRITE IT ALL TO RNAM
OK
ATI5                                                CHECK IT OUT!
USRobotics Courier 14400 HST Dual Standard NRAM Settings...

   DIAL=PULSE  B1  F1  M1  X6
   BAUD=38400  PARITY=N  WORDLEN=8

   &A1  &B1  &G0  &H1  &I0  &J0  &K0  &L0
   &M4  &N0  &P0  &R2  &S0  &X0  &Y1

   S02=043   S03=013   S04=010   S05=008
   S06=002   S07=060   S08=002   S09=006
   S10=007   S11=070   S12=050   S13=000
   S15=000   S19=000   S21=010   S22=017
   S23=019   S24=150   S26=000   S27=000
   S28=008   S38=000

   STORED PHONE #0:
                #1:
                #2:
                #3:

OK

        NOW I EXITED THE COMMUNICATION PROGRAM AND RE-ENTERED IT TO SEE HOW
        THINGS WORKED OUT!

        ACTION                                  COMMENT
        ======                                  =======

ATI4                                            SEE HST SETTINGS
USRobotics Courier 14400 HST Dual Standard Settings...

   B1  C1  E1  F1  M1  Q0  V1  X1
   BAUD=38400  PARITY=N  WORDLEN=8
   DIAL=PULSE  ON HOOK   TIMER

   &A1  &B1  &C1  &D2  &G0  &H1  &I0  &J0  &K0
   &L0  &M4  &N0  &P0  &R2  &S0  &X0  &Y1

   S00=000   S01=000   S02=043   S03=013
   S04=010   S05=008   S06=002   S07=045
   S08=002   S09=006   S10=007   S11=070
   S12=050   S13=000   S14=001   S15=000
   S16=000   S17=000   S18=000   S19=000
   S20=000   S21=010   S22=017   S23=019
   S24=150   S25=000   S26=000   S27=000
   S28=008   S38=000

   LAST DIALED #:

OK


PAGE 13


ATI5                                            CHECK OUT NRAM SETTINGS
USRobotics Courier 14400 HST Dual Standard NRAM Settings...

   DIAL=PULSE  B1  F1  M1  X6
   BAUD=38400  PARITY=N  WORDLEN=8

   &A1  &B1  &G0  &H1  &I0  &J0  &K0  &L0
   &M4  &N0  &P0  &R2  &S0  &X0  &Y1

   S02=043   S03=013   S04=010   S05=008
   S06=002   S07=060   S08=002   S09=006
   S10=007   S11=070   S12=050   S13=000
   S15=000   S19=000   S21=010   S22=017
   S23=019   S24=150   S26=000   S27=000
   S28=008   S38=000

   STORED PHONE #0:
                #1:
                #2:
                #3:

OK
AT&F                                            LOAD ROM FACTORY SETTINGS
OK

        ACTION                                  COMMENT
        ======                                  =======
ATI4                                            SEE, THEY ARE THERE!
USRobotics Courier 14400 HST Dual Standard Settings...

   B1  C1  E1  F1  M1  Q0  V1  X1
   BAUD=38400  PARITY=N  WORDLEN=8
   DIAL=PULSE  ON HOOK   TIMER

   &A1  &B0  &C1  &D2  &G0  &H0  &I0  &J0  &K1
   &L0  &M4  &N0  &P0  &R1  &S0  &X0  &Y1

   S00=000   S01=000   S02=043   S03=013
   S04=010   S05=008   S06=002   S07=060
   S08=002   S09=006   S10=007   S11=070
   S12=050   S13=000   S14=001   S15=000
   S16=000   S17=000   S18=000   S19=000
   S20=000   S21=010   S22=017   S23=019
   S24=150   S25=000   S26=000   S27=000
   S28=008   S38=000

   LAST DIALED #:

OK


PAGE 14


ATI5                                            CHECK OUT THE NRAM SETTINGS
USRobotics Courier 14400 HST Dual Standard NRAM Settings...

   DIAL=PULSE  B1  F1  M1  X6
   BAUD=38400  PARITY=N  WORDLEN=8

   &A1  &B1  &G0  &H1  &I0  &J0  &K0  &L0
   &M4  &N0  &P0  &R2  &S0  &X0  &Y1

   S02=043   S03=013   S04=010   S05=008
   S06=002   S07=060   S08=002   S09=006
   S10=007   S11=070   S12=050   S13=000
   S15=000   S19=000   S21=010   S22=017
   S23=019   S24=150   S26=000   S27=000
   S28=008   S38=000

   STORED PHONE #0:
                #1:
                #2:
                #3:

OK
ATZ                                             LOAD NRAM SETTINGS AS DEFAULT
OK

        ACTION                                  COMMENT
        ======                                  =======

ATI4                                            AGAIN, SEE, THEY ARE THERE!
USRobotics Courier 14400 HST Dual Standard NRAM Settings...

   DIAL=PULSE  B1  F1  M1  X6
   BAUD=38400  PARITY=N  WORDLEN=8

   &A1  &B1  &G0  &H1  &I0  &J0  &K0  &L0
   &M4  &N0  &P0  &R2  &S0  &X0  &Y1

   S02=043   S03=013   S04=010   S05=008
   S06=002   S07=060   S08=002   S09=006
   S10=007   S11=070   S12=050   S13=000
   S15=000   S19=000   S21=010   S22=017
   S23=019   S24=150   S26=000   S27=000
   S28=008   S38=000

   STORED PHONE #0:
                #1:
                #2:
                #3:

OK


PAGE 15

ATI5
                                                VIEW THE NRAM SETTINGS
USRobotics Courier 14400 HST Dual Standard NRAM Settings...

   DIAL=PULSE  B1  F1  M1  X6
   BAUD=38400  PARITY=N  WORDLEN=8

   &A1  &B1  &G0  &H1  &I0  &J0  &K0  &L0
   &M4  &N0  &P0  &R2  &S0  &X0  &Y1

   S02=043   S03=013   S04=010   S05=008
   S06=002   S07=060   S08=002   S09=006
   S10=007   S11=070   S12=050   S13=000
   S15=000   S19=000   S21=010   S22=017
   S23=019   S24=150   S26=000   S27=000
   S28=008   S38=000

   STORED PHONE #0:
                #1:
                #2:
                #3:

OK

        GREAT, SO FAR EVERYTHING IS PROGRESSING NICELY.

        SETTING COMMUNICATION PROGRAM PARAMETERS
        ========================================
        TELIX
        -----
        FIRST WE WILL DO IT USING TELIX V3.12:
        ENTER TELIX: (and set the options as shown below)

 N O T E:                     ( *'ed lines show where changes are.)
 ========

Telix Copyright (C) 1986-89 Exis Inc. and Colin Sampaleanu. All rights reserved.
Version 3.12, released 12-1-89.

Press ALT-Z for help on special keys.

ATZ
OK
AT S7=60 S0=0 V1 X6
OK


PAGE 16
                                                        PRESS ALT O FOR MENU

               ÕÍµ Configure Telix ÆÍÍÍÍÍÍÍÍÍÍÍÍ¸
               ³                                ³
               ³ Change which default settings? ³
               ³                                ³
               ³      Screen and color          ³
        --->   ³      Terminal options          ³
               ³      General options           ³
               ³      Modem and dialing         ³
               ³      Filenames and paths       ³
               ³      Ascii transfers           ³
               ³      Protocol options          ³
               ³      Kermit transfers          ³
               ³      Comm port setup           ³
               ³      Write setup to disk       ³
               ³      Exit                      ³
               ³                                ³
               ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


   ÕÍµ Terminal options ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                        ³
*  ³ A - Baud 38400   Parity None    Data length 8    Stop bits 1           ³
   ³ B - COM1                                                               ³
   ³                                                                        ³
   ³ C - Default terminal type ........... ANSI-BBS                         ³
   ³ D - Status line ..................... Bottom                           ³
   ³ E - Local echo ...................... Off                              ³
   ³ F - Add Line Feeds after CRs ........ Off                              ³
   ³ G - Strip high bit (incoming data) .. Off                              ³
   ³ H - Received Backspace destructive .. On                               ³
   ³ I - Backspace key sends ............. BS                               ³
*  ³ J - XON/XOFF software flow control .. Off                              ³
*  ³ K - CTS/RTS hardware flow control ... On                               ³
*  ³ L - DSR/DTR hardware flow control ... Off                              ³
   ³ M - Compuserve Quick B transfers .... On                               ³
   ³ N - Zmodem auto-downloads ........... On                               ³
   ³ O - Answerback string (ENQ) .........                                  ³
   ³                                                                        ³
   ³                                                                        ³
   ³ Change which setting?       (Return or Esc to exit)                    ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


PAGE 17

   ÕÍµ General settings ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                        ³
   ³ A - Sound ...................... On                                    ³
   ³ B - Alarm sound ................ On                                    ³
   ³ C - Keep aborted downloads ..... On                                    ³
   ³ D - Show free disk space ....... On                                    ³
   ³ E - Use of Quick Dialing bar ... On                                    ³
   ³ F - Confirm hang-up ............ Off                                   ³
   ³ G - Usage Log on by default .... Off                                   ³
   ³ H - Scroll Back buffer size .... 10  (KBytes)                          ³
*  ³ I - Capture file buffer size ... 4   (KBytes)                          ³
   ³ J - Date format ................ MMDDYY                                ³
   ³ K - Date separator character ... -                                     ³
*  ³ L - Time format ................ 24-Hour                               ³
   ³ M - Time separator character ... :                                     ³
   ³ N - Use enhanced keyboard ...... On                                    ³
   ³ O - Shell: 16550 buffer on ..... On                                    ³
   ³                                                                        ³
   ³                                                                        ³
   ³ Change which setting?       (Return or Esc to exit)                    ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

 ÕÍµ Modem and dialing parameter setup ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³                                                                            ³
*³ A - Init string ......... ATZ^M~~~AT S7=60 S0=0 ^M~                        ³
*³ B - Dialing prefix 1 .... ATDP     (use ATDT for touch tone LINE)          ³
*³ C - Dialing prefix 2 .... ATDP                                             ³
*³ D - Dialing prefix 3 .... ATDP                                             ³
 ³ E - Dialing suffix ...... ^M                                               ³
 ³ F - Connect string ...... CONNECT                                          ³
 ³ G - No connect strings .. NO CARRIER             BUSY                      ³
 ³                           VOICE                  NO DIAL TONE              ³
 ³ H - Hang-up string ...... ~~~+++~~~ATH0^M                                  ³
 ³ I - Auto answer string .. ATS0=1^M                                         ³
 ³ J - Dial cancel string .. ^M                                               ³
 ³                                                                            ³
*³ K - Dial time ........... 60                                               ³
 ³ L - Redial pause ........ 1                                                ³
*³ M - Auto baud detect .... Off                                              ³
 ³ N - Drop DTR to hangup .. On                                               ³
 ³                                                                            ³
 ³                                                                            ³
 ³ Change which setting?       (Return or Esc to exit)                        ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


PAGE 18

   ÕÍµ Filenames and paths ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                        ³
   ³ A - Download directory:                                                ³
   ³                                                                        ³
   ³ B - Upload directory:                                                  ³
   ³                                                                        ³
   ³ C - Script directory:                                                  ³
   ³                                                                        ³
   ³ D - Default Capture file:                                              ³
*  ³      SESSION.DOC                                                       ³
   ³ E - Default Usage Log name:                                            ³
   ³      TELIX.USE                                                         ³
   ³ F - Directory program:                                                 ³
   ³                                                                        ³
   ³ G - Screen Image file:                                                 ³
   ³      TELIX.IMG                                                         ³
   ³ H - Editor name:                                                       ³
   ³                                                                        ³
   ³                                                                        ³
   ³ Change which setting?       (Return or Esc to exit)                    ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

           ÕÍµ ASCII file transfer settings ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
           ³                                                     ³
           ³  A - Strip high bit ...... Off                      ³
           ³  B - Remote abort char ... 0    (ASCII)             ³
           ³                                                     ³
           ³ Uploads                                             ³
           ³  C - Local echo .......... Off                      ³
           ³  D - Expand blank lines .. On                       ³
           ³  E - Pace character ...... 0    (ASCII)             ³
           ³  F - Line pacing ......... 10   (1/10 seconds)      ³
           ³  G - Character pacing .... 0                        ³
           ³  H - CR translation ...... None                     ³
           ³  I - LF translation ...... None                     ³
           ³                                                     ³
           ³ Downloads                                           ³
           ³  J - CR translation ...... None                     ³
           ³  K - LF translation ...... None                     ³
           ³                                                     ³
           ³                                                     ³
           ³ Change which setting?       (Return or Esc to exit) ³
           ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


PAGE 19

 ÕÍµ File transfer protocols ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³                                                                            ³
 ³ External           Key   Protocol     Upload    Download   BAT or    DL    ³
 ³ Protocols                  Name      Filename   Filename   Script   Name   ³
 ³                                                                            ³
 ³ A.................                                                         ³
 ³ B.................                                                         ³
 ³ C.................                                                         ³
 ³ D.................                                                         ³
 ³                                                                            ³
*³ E: File xfer disk buf. size (Kb) ... 4                                     ³
 ³ F: Relaxed Xmodem timing ........... Off                                   ³
 ³ G: Filename guessing ............... Only if sure                          ³
 ³ H: Zmodem receive crash recovery ... Off                                   ³
 ³ I: Zmodem send crash recovery ...... Off                                   ³
*³ J: Allow Zmodem 32 bit CRCs ........ On                                    ³
 ³ K: Zmodem window size (Kb) ......... 0                                     ³
 ³ L: Zmodem file type (translation) .. Either                                ³
 ³                                                                            ³
 ³                                                                            ³
 ³ Change which setting?       (Return or Esc to exit)                        ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
        ÕÍµ Kermit Settings ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
        ³                                                             ³
        ³ A - Control quote character .. 35   (Ascii)                 ³
        ³ B - Padding character ........ 0    (Ascii)                 ³
        ³ C - Number of pad chars ...... 0                            ³
        ³ D - Maximum packet size ...... 94                           ³
        ³ E - Start of packet char ..... 1    (Ascii)                 ³
        ³ F - End-of-line-character .... 13   (Ascii)                 ³
        ³ G - File type ................ Binary                       ³
        ³                                                             ³
        ³ Change which setting?       (Return or Esc to exit)         ³
        ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
           ÕÍµ Comm port setup ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
           ³                                                     ³
           ³              Start     IRQ                          ³
           ³             Address    Line                         ³
           ³                                                     ³
           ³ A: COM1 ..... 3f8       4                           ³
           ³                                                     ³
           ³ B: COM2 ..... 2f8       3                           ³
           ³                                                     ³
           ³ C: COM3 ..... 3e8       4                           ³
           ³                                                     ³
           ³ D: COM4 ..... 2e8       3                           ³
           ³                                                     ³
           ³ E: COM5 ..... 3f8       4                           ³
           ³                                                     ³
           ³ F: COM6 ..... 3f8       4                           ³
           ³                                                     ³
           ³ G: COM7 ..... 3f8       4                           ³
           ³                                                     ³
           ³ H: COM8 ..... 3f8       4                           ³
           ³                                                     ³
           ³ Change which setting?       (Return or Esc to exit) ³
           ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


PAGE 20

        NOW SAVE ALL CHANGES. EXIT TELIX AND RE-ENTER IT TO ACTIVATE THE
        CHANGES. NOW GO TO DIALING DIRECTORY AND ENTER A LINE. FOR EXAMPLE,
        FOR EXEC-PC  ENTER     1-414-789-4300    38400 8 N 1
        FOR CRS      ENTER     1-416-629-0168    38400 8 N 1
        FOR RUSTY    ENTER     1-216-726-3589    38400 8 N 1
        NOTE:THE MODEM DEFAULT IS 38400, BUT WE MAY USE 19200 ABOVE. I HAVE
        FOUND THAT IF ONE USES 38400 ABOVE, CRC ERRORS MAY CREEP IN AND THE
        BAUD RATE DROPS TO A VERY LOW VALUE. USING 19200 ON THE OTHER HAND
        WORKS VERY WELL AND BECAUSE 38400 IS A HARDWARE DEFAULT, THE ACTUAL
        DATA TRANSFER OF A 'ZIP' FILE USUALLY EXCEEDS 9600 BAUD VERY NICELY.
        IF FACT THE COVETED 14000-16000 RATES ARE ACHIEVED.
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³  THE 38400 OPTION WORKS WELL FOR ME ON      TELIX.    ³
         ³  THE 19200 OPTION WORKS WELL FOR ME ON      TELEMATE. ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
       TELEMATE
       --------
       NOW WE WILL DO IT USING TELEMATE V2.10: (TM /O)
        ENTER TELEMATE: (and set the options as shown below)
                        ( *'ed lines show where changes are.)

Telemate Version 2.10                  Registered to: [ REGISTERED ]
Copyright (c) 1988-1990 Tsung Hu.  All rights reserved.

Press F1 for help on function keys.


ATZ
OK
                        ENTER  ALT O FOR OPTIONS MENU
                                                   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                   ³  General        ³
                                                   ³  Dial setup     ³
                                                   ³  Directory      ³
                                                   ³  Terminal       ³
                                                   ³  Communication  ³
                                                   ³  Protocol       ³
                                                   ³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
                                                   ³  Load options   ³
                                                   ³  Save windows   ³
                                                   ³  Save options   ³
                                                   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


PAGE 21
           General
           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
           ³  ÚÄ DOS Shell ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
           ³  ³  [ ] Swap Telemate to XMS/EMS                     ³  ³
           ³  ³  [X] Swap Telemate to disk                        ³  ³
           ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
           ³  ÚÄ Mouse ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
*          ³  ³  Type  ( ) None   (x) MicroSoft  ( ) MouseSystem  ³  ³
*          ³  ³  Port  (x) None   ( ) COM1       ( ) COM2         ³  ³
           ³  ³  Speed ( ) Slow   ( ) Medium     (x) Fast         ³  ³
           ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
           ³  ÚÄ Display ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿   ÚÄ Log ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
           ³  ³  [X] Scroll Bars       ³   ³  [X] Log Filter      ³  ³
           ³  ³  [X] Menu Bar          ³   ³  [X] Usage Log       ³  ³
*          ³  ³  [X] Status Line       ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
*          ³  ³  [X] 24 hour format    ³   ÚÄ Sound ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
           ³  ³  Scroll Back      100  ³   ³  [X] Music           ³  ³
           ³  ³  Editor Margin     70  ³   ³  [X] Bell            ³  ³
           ³  ³  Message Pause      1  ³   ³  Alarm Sound      1  ³  ³
           ³  ³  Error Pause        2  ³   ³  Alarm Time       3  ³  ³
           ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
           ³              ÉÍÍÍÍ»              ÚÄÄÄÄÄÄÄÄ¿             ³
           ³              º OK º              ³ Cancel ³             ³
           ³              ÈÍÍÍÍ¼              ÀÄÄÄÄÄÄÄÄÙ             ³
           ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
     Dial setup
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³                                                                     ³
*    ³  Prefix   (x) 1 "ATDP "       (ATDP=Pulse  ATDT=Touch Lines )       ³
     ³           ( ) 2 "ATDT "                                             ³
     ³           ( ) 3 ATDT 001,                                           ³
     ³           ( ) 4 ATDT 9,                                             ³
     ³                                                                     ³
     ³  Suffix   (x) 1 ^M                                                  ³
     ³           ( ) 2 ^M                                                  ³
     ³           ( ) 3 ^M                                                  ³
     ³           ( ) 4 ^M                                                  ³
     ³                                                                     ³
     ³  Connect String     CONNECT                [ ] Auto Baud Detect     ³
     ³                                                                     ³
*    ³                                            Dial Time           60   ³
     ³                                            Redial Pause         2   ³
     ³  Busy String        NO CARRIER             Redial Attempt       0   ³
     ³                     BUSY                                            ³
     ³                     NO CONNECT             ÉÍÍÍÍ»    ÚÄÄÄÄÄÄÄÄ¿     ³
     ³                     NO DIALTONE            º OK º    ³ Cancel ³     ³
     ³  Cancel String      ^M                     ÈÍÍÍÍ¼    ÀÄÄÄÄÄÄÄÄÙ     ³
     ³                                                                     ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


PAGE 22

          Directory    (YOUR CHOICES MAY VARY)
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³                                                          ³
*         ³  Telemate    C:\COMMUN\TM\                               ³
          ³                                                          ³
*         ³  Upload      C:\COMMUN\                                  ³
          ³                                                          ³
*         ³  Download    C:\COMMUN\                                  ³
          ³                                                          ³
*         ³  Script      C:\COMMUN\TM\                               ³
          ³                                                          ³
          ³  Edit                                                    ³
          ³                                                          ³
*         ³  Log         C:\COMMUN\TM\                               ³
          ³                                                          ³
*         ³  V. Memory   H:   (Ram disk)                             ³
          ³                                                          ³
          ³             ÉÍÍÍÍ»                  ÚÄÄÄÄÄÄÄÄ¿           ³
          ³             º OK º                  ³ Cancel ³           ³
          ³             ÈÍÍÍÍ¼                  ÀÄÄÄÄÄÄÄÄÙ           ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
     Terminal
     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³                                                                    ³
     ³  Terminal     ( ) TTY  (x) ANSI  ( ) VT52  ( ) VT102               ³
     ³                                                                    ³
     ³  Connection   (x) Modem          ( ) Computer                      ³
     ³                                                                    ³
     ³  ÚÄ Toggles ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿   ÚÄ Paste/ASCII Upload ÄÄÄÄÄÄÄÄ¿  ³
     ³  ³  [ ] Add Line Feed         ³   ³  [X] Expand Blank Line      ³  ³
     ³  ³  [X] Add Return            ³   ³  Line Pacing             0  ³  ³
     ³  ³  [ ] Local Echo            ³   ³  Char Pacing             0  ³  ³
     ³  ³  [X] Auto Wrap             ³   ³  Pace Character          0  ³  ³
     ³  ³  [X] Destructive Backspace ³   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
     ³  ³  [ ] Strip High Bit        ³   ÚÄ Macro/Script ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
     ³  ³  [ ] Confirm Hang Up       ³   ³  Extended Pacing         0  ³  ³
     ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
     ³  ÚÄ Control ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿   ÚÄ Quote ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
*    ³  ³  [ ] XON/XOFF Flow         ³   ³  [X] Initial(@) Guessing    ³  ³
*    ³  ³  [X] RTS/CTS Flow          ³   ³  Prefix         @>          ³  ³
     ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
     ³                                                                    ³
     ³                  ÉÍÍÍÍ»                ÚÄÄÄÄÄÄÄÄ¿                  ³
     ³                  º OK º                ³ Cancel ³                  ³
     ³                  ÈÍÍÍÍ¼                ÀÄÄÄÄÄÄÄÄÙ                  ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


PAGE 23
        Communication
        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ³                                                              ³
*       ³  Modem Init String     ATZ~~~AT S0=0 ^M~                     ³
*       ³  Modem HangUp String   ^#~~~+++~~~ATH0^M~                    ³
*       ³  Auto Answer String    ~~~+++~~~AT S0=1^M~                   ³
        ³  Answer Back String                                          ³
        ³                                                              ³
        ³                                                              ³
*       ³  Port          (x) COM1  ( ) COM3  ( ) COM5  ( ) COM7        ³
        ³                ( ) COM2  ( ) COM4  ( ) COM6  ( ) COM8        ³
        ³                                                              ³
        ³  Baud Rate     ( ) 300        ( ) 4800       (x) 38400       ³
*       ³                ( ) 1200       ( ) 9600       ( ) 57600       ³
        ³                ( ) 2400       ( ) 19200      ( ) 115200      ³
        ³                                                              ³
        ³  Parity        (x) None       ( ) Even       ( ) Odd         ³
        ³  Data Bits     ( ) 7          (x) 8                          ³
        ³  Stop Bits     (x) 1          ( ) 2                          ³
        ³                                                              ³
        ³                 ÉÍÍÍÍ»              ÚÄÄÄÄÄÄÄÄ¿               ³
        ³                 º OK º              ³ Cancel ³               ³
        ³                 ÈÍÍÍÍ¼              ÀÄÄÄÄÄÄÄÄÙ               ³
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
   Protocol
   ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
   ³                              ÚÄ ASCII ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
*  ³   [X] Filename Guessing      ³ Upload  Download                     ³  ³
*  ³   [X] Check Disk Space       ³   [ ]     [ ]    Strip High Bit      ³  ³
   ³                              ³   [ ]     [ ]    Translation         ³  ³
   ³  ÚÄ Zmodem ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿   ³   [ ]     [ ]    Strip CR            ³  ³
   ³  ³  [X] Recovery         ³   ³   [ ]     [ ]    Strip LF            ³  ³
*  ³  ³  [X] Auto-Download    ³   ³   [ ]     [ ]    Add CR before LF    ³  ³
   ³  ³  [ ] ASCII-Upload     ³   ³   [ ]     [ ]    Add LF after  CR    ³  ³
   ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
   ³                                                                        ³
   ³  ÚÄ External Protocols ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿  ³
   ³  ³  Protocol       Upload      Download   Prompt   Auto-Download    ³  ³
   ³  ³  Name      Key  Batch       Batch      DL Name  Sequence         ³  ³
   ³  ³  BiModem    I   BI-MODEM    BI-MODEM     [ ]                     ³  ³
   ³  ³  Jmodem     J   JMODEM-U    JMODEM-D     [X]                     ³  ³
   ³  ³  Kermit     K   KERMIT-U    KERMIT-D     [ ]                     ³  ³
   ³  ³  Puma       P   PUMA-U      PUMA-D       [ ]    ^V^H^V^H^VPuma^  ³  ³
   ³  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ  ³
   ³                                                                        ³
   ³                     ÉÍÍÍÍ»                 ÚÄÄÄÄÄÄÄÄ¿                  ³
   ³                     º OK º                 ³ Cancel ³                  ³
   ³                     ÈÍÍÍÍ¼                 ÀÄÄÄÄÄÄÄÄÙ                  ³
   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
        BE SURE TO SAVE THE NEW SET-UP.
        N O T E: When entering phone numbers into the telephone directory
        =======  I found that using 38400 caused a lot of CRC errors and
                 resulted in very POOR speeds. Using 19200 as the speed in
                 the individual phone directory lines (program and modem
                 still are set at 38400) cured the problem quite nicely, and
                 still enabled me to achieve the desired high transfer rates.
                    If anyone knows the reason for this, please get in touch
                 with me.


PAGE 24

        MODEM NRAM TELEPHONE NUMBERS
        ============================
        LASTLY, AT THE TERMINAL LEVEL ONE CAN ENTER UP TO 4 PHONE NUMBERS.
        FOR EXAMPLE:
        AT&Z0=P1 414 789 4300  FOR EXEC-PC   and
        AT&Z1=P1 416 629 0168  FOR CRS

        NOW WHEN ONE USES THE MODEM ONE CAN DIAL USING THE NRAM OPTIONS
        AS FOLLOWS:

ATDS1                                   (MAKE SURE 19200 BAUD IS USED)
Dialing...P14166290168
RINGING

CONNECT 9600/ARQ
CONNECT 19200 / 06-27-90 (20:31)
(Error Correcting Modem Detected)

CRS Premium Bulletin Board - Node 38 - USR HST 14400
PCBoard (R) v14.5/U (beta 06/26/90 13:44) - Node 38

        NOW ENTER  CTRL H TO HANG UP AND WE GET:

NO CARRIER
+++ATH0
OK

ATDS0                                   (MAKE SURE 19200 BAUD IS USED)
Dialing...P14147894300
RINGING

CONNECT 9600/ARQ

(NODE# 206)
Exec-PC(tm) Network BBS v3.73  Copyright (c) 1980-1990 Exec-PC
                               EXEC-PC (R) Reg. U.S. Pat. and Tm. Off.
              The Business Knowledge Exchange


        WELL THERE IT IS!  MY MODEM NOW WORKS WITH NO PROBLEM ON ALL THE
        BBS'S I HAVE TRIED.
        FILES INCLUDED:
                TELIXOLD.CNF    TELIX CONFIG FILE AT START
                TMOLD.CFG       TELEMATE CONFIG FILE AT START
                TM.CFG          TELEMATE CONFIG FILE AFTER FULL SET UP
                TELIX.CNF       TELIX CONFIG FILE AFTER FULL SET UP
                HST1440.DOC     THIS MAMMOTH TOME!

        COMMENTS, CORRECTIONS, ETC. ARE WELCOME.
                P.A. KELLY
                30 SOUTHAMPTON DR. S.W.
                CALGARY, ALBERTA, CANADA, T2W 0T5

                        - END OF FILE -