USRobotics Courier HST Qmodem Service Script Production Release 2.0A
--------------------------------------------------------------------
(c) Copyright Dan Moore, 1987-1989

The USRobotics logo, Courier, and HST are trademarks of
USRobotics, Inc.

QModem and QModem SST are trademark of John Friel III and the
Forbin Project, Inc.

NOTE: sidebars ³ in the left margin indicate documentation
      changes from the previous release.


USE RESTRICTION AND DISCLAIMER

This script is copyrighted solely to prevent others from reaping
financial gain through its sale and/or use.  Permission has been
given to John Friel III and the Forbin Project, Inc., to
distribute this script as part of the QModem SST program
package, release 4.0 for private use only.

The HST20A script and its accompanying files and documentation
may not be distributed as part of any other computer
communication hardware or software package without the written
permission of the author.  This script may be copied and
distributed freely by private individuals who wish to share it
with others as long as no specific charge is assessed for this
service other than minimal fees (not to exceed $5) to cover the
distribution medium.

Permission is hereby granted to System Operators of active
Bulletin Boards to post the HST20A.ZIP file for public
distribution.  Due to the easily modifiable nature of QModem
scripts,  modified versions of the script should bear a
different name and have their origin clearly identified.  The
³NAME of the script is copyrighted as well as its contents. The
³HST20A.ZIP file may not be modified for any purpose whatsoever.


COMMERCIAL USES OF THE HST SCRIPT

The series of HSTxx Qmodem Scripts may not be used for
marketing, demonstrations, advertising, problem diagnosis or
correction OR FOR ANY COMMERCIAL OR BUSINESS PURPOSES by modem
manufacturers, their agents, dealers, resellers, or any company
or individual involved in the sale, marketing, maintenance, or
business use of modems or other computing devices WITHOUT
A COMMERCIAL LICENSE TO USE THE SCRIPT.  Superficial editing of
the script's code to mask its origin and avoid licensing
costs is a violation of the author's copyright, and will be
pursued to the full extent of the law.

³To obtain a commercial- or business-use license for the HST
³script(s), refer to the LICENSE.DOC file in the HST20A.ZIP
³file.



HST MODEM DEPENDENCY

³The HST20A script will operate satisfactorily on USRobotics HST
³modems with ROM levels 961, 963, 964, and 1440.  To determine
³the HST's ROM level, run the HST20A script or type ATI0<Enter>
³while in Qmodem terminal mode.

³If your HST modem is NOT at level 964 or 1440, I strongly
³recommend that you get it upgraded.  The cost if extremely
³reasonable and the upgrade is performed quickly by USR.  You
³will gain MNP levels 4 and 5.  Compared to ROM level 963/961,
³releases 964 and 1440 will gain you an additional 100cps for
Ymodem/G transfers of binary or compressed files, and will
outright double your effective transfer speed for uncompressed
text files when MNP 5 compression is used.   For details on the
HST upgrade program, call USR Technical Support at 800-982-5151
(in Illinois, call 312-982-5151).


QMODEM RELEASE DEPENDENCY

³The HST20A script will operate with Qmodem 4.0 and later releases
of Qmodem.  This script relies on certain features of the Qmodem
release 4.0 Script Language and it WILL NOT OPERATE under pre-4.0
releases of Qmodem.


OPERATIONAL SUMMARY

³HST20A.SCR is intended as a configuration and setup help for the
USR HST modem.  Although it facilitates much of the modem's
setup tasks, some knowledge of the HST's operation and
technology is required, as well as a basic understanding of
computer communications.

If you are using HST20A to set up your USR Courier HST for use
with  Qmodem 4.0, the QM menu options will perform all firmware
configuration, leaving physical switch changes up to the you
(correct switch settings are displayed as part of the
script's operation).

³HST20A automatically detects the ROM release level of your modem.
³If your USR HST modem is at ROM level 964 or 1440 (the latest ROM
³levels at the time of this release), HST20A will allow you
³access to a second level of menu via the "AD" main menu option.
³This second menu accesses HST features only available in
³964- or 1440-level modems, such as data compression (MNP level
5), settings for the new S-register 15, 4800/7200 link rate
settings, and the new modem configuration screen.  Advanced
Functions are NOT supported for ROM releases prior to 964.


SETTING UP THE HST FOR QMODEM OPERATION

It is likely that you will have to change the modem's switches
from their default factory settings to the setup recommended in
³the menu's QM option.  Unfortunately, HST20A can't quite "reach
out and touch switches"; you must do this yourself.  The script
makes you aware of this requirement.  

Another very important part of the modem setup is the
configuration of QModem itself.  With release 4.0 of Qmodem,
this is done with the Alt-N command (with release 3.1A of
Qmodem, setup was performed with the QINSTALL Program).

The QMSETUP.DOC file, included in this ARChive, will help
help you select the proper QModem configuration parameters for
the HST modem.

I recommend that you keep your HST manual handy while you
experiment with the script.  Bug reports or suggestions for
changes or improvements should be reported to me on the Qmodem
Conference Echo carried by the InterLink and SmartNet BBS Mail
Networks.   


FRIENDLY WARNING

³HST20A can and will make permanent changes to the modem's
internal configuration.  Once a setting has been changed,
writing the change to Non-Volatile RAM (NRAM) implements the
change until that setting is changed and written to NRAM again.
Changes to NRAM are maintained even when the modem power is OFF.
If you have a working set of modem settings and wish to
experiment, do not copy the changes to NRAM.  The next hardware
reset or power-off / power-on sequence will re-establish the
last NRAM settings.  The HSTINTRO.DOC file describing the HST's
basic internal operation is included in this ARChive; you may
wish to review it to gain a better understanding of the modem's
operation.


MODEM COMMAND FILES

New in release 2.0 of the HST script is the support for special
"Modem Command Files", which can be read from disk and sent
directly to your modem.  Modem Command Files are not intended
for the HST novice.  Until you become familiar with the various
modem commands and parameters, as documented in the HST User's
Manual, you may wish to leave this feature alone.

INVOKING A COMMAND FILE

Modem command files may be invoked from the standard HST20 menu
with the CF option.  You will be prompted for the command file
name ONLY.  Once the command file is executed, the standard
³HST20A menu will be re-displayed.

³If you are using HST20A solely to execute a command file, you can
specify the command file name in response to the "Script
³Parameters" prompt.  When this method is used, HST20A terminates
after the last command has been executed.  This feature allows
³the use of HST20A as an autoexec script.

CREATING COMMAND FILES

Modem command files are created with any standard ASCII text
editor or word processing program with the ability to save
standard, unformatted ASCII files (each line in the file must
end with the standard carriage return/line feed characters).
Modem command files (.HSF) must be stored in your Qmodem script
directory, as defined in the Alt-N/D/S setup.  Any filename is
valid, but the .HSF file extension MUST be used.

Each line in a .HSF file may contain a VALID HST modem command,
³or one of the following HST20A-only commands, starting in the
first column:

³	@PROMPT  HST20A will pause and issue a "Press <Enter> to
                       continue..." prompt.

        @CLRSCR  Clear the screen before issuing the next modem 
                 command.

³	@CMD     Issue the script command in the next line.  See
                 the section on AUTOEXEC and HST20A programming
                 for additional details on this powerful
                 and potentially dangerous command. 

³The @PROMPT suspends HST20A operation and is used when lengthy
modem responses are displayed, to prevent the modem's output
from scrolling off the screen when the following command is
executed. 

The @CLRSCR command is purely cosmetic; its only effect is to
cause the next command to be displayed at the top of the screen.

Commands sent to the HST modem may not exceed 40 characters in
length, not including the AT prefix and imbedded spaces.  Make
sure that lines in command files abide by this restriction.
This restriction is imposed by the modem, not the script
language or Qmodem.

COMMAND FILE PROCESSING

³HST20A will send each line in the command file to the modem and
echo it to the screen.  The standard "OK" return code is expected
from the modem in response to each command.  If this return code
is not received within 5 seconds, the script will force a timeout
and will terminate with an appropriate error message. 

Following is a sample 4-line command file: (Note: this file  is
³included in the HST20.ZIP file under the name TEST20.HSF)

***start of file***
AT&M4&K0
@PROMPT
ATI5
@PROMPT
@CLRSCR
ATI4
@PROMPT
***end of file***

- The first command enables MNP and auto MNP detect, and
  disables MNP level 5 data compression.

- The second command causes the script to pause and display the
  "Press <Enter> to continue " prompt following the OK response. 

- The third command requests the HST to display NRAM settings. 

- The fourth command causes the script to pause and display the
  "Press <Enter> to continue " prompt following the NRAM display. 

- The fifth command clears the screen

- The sixth command requests the HST to display RAM settings.

- The seventh and last command causes the script to pause and
  display the "Press <Enter> to continue " prompt following the
  RAM display.


³THE AUTOEXEC COMMAND FILE AND DYNAMIC HST20A PROGRAMMING

³If HST20A is called WITHOUT any parameters AND file called
AUTOEXEC.HSF is found in your Qmodem 4.0 script directory, the
file will be loaded and executed automatically, in a manner
similar to the DOS AUTOEXEC.BAT facility.

³In addition to the AUTOEXEC.HSF facility, the HST20A script is
externally  programmable via .HSF command files and the @CMD
keyword, mentioned earlier.

When the keyword @CMD is found in a modem command file, the line
which immediately follows will be executed as a SCRIPT command,
rather than as a modem command.  For example, the two lines:

@CMD
SETCOMM CJLM

when found in a .HSF file, will cause the serial port to be set
to 2400-N-8-1, as instructed by the SETCOMM Qmodem 4.0 script
command.  Any script command which requires WORD operands
(explicitly stated operands not bound by quotes) or no operand
at all can be executed following the @CMD keyword.  One of the
script commands which can be executed in this fashion is SYSTEM,
which actually terminates Qmodem and returns to DOS.  For
example, the following .HSF file will change the HST's NRAM
setup to use a CCITT answer sequence and will also decrease the
remote carrier length requirements in preparation for a call to
Singapore.  It will then invoke a second script called SINGAPORE
which will dial a bulleting board system there and upload a
file.  Once the SINGAPORE script terminates, the normal HST
parameters will be restored and Qmodem will be terminated:

ATB1
ATS9=4
@CMD
SCRIPT SINGAPORE
ATB0
ATS9=6
@CMD
SYSTEM Y

NOTE: The SINGAPORE script must terminate with a RETURN command
rather than an EXIT command.  IF EXIT is used, the process will
terminate at that point and control will never be returned to
³the HST20A script.


The combination script command files, AUTOEXEC.HSF, and @CMD is
an extremely powerful one, which gives you almost total control
over Qmodem externally, without making a single change to the
³HST20A script.  I recommend that you experiment very carefully 
with these features and test them thoroughly before using them
for productive purposes. 


SUPPORT

I will attempt to correct problems with this script, as well as
keep it current with releases of the HST's firmware and Qmodem
software as time allows.  This is a personal effort which I
am sharing, but for which I receive no remuneration (except from
commercial or business users of the script, and I am still
waiting for those).  Please make no unreasonable demands for
support, especially for things that are not broken; you got this
for free and if it does not perform as you would like it to, you
have a God-given right not to use it.  You may also chose to
alter the script to meet your unique requirements, although the
new Command File facility should address all specific needs not
³covered in the script's generic menus.  If you modify HST20A,
please do not distribute your version under its original name.
If you have questions or suggestions,  I can be contacted under
my name on the Qmodem Support Conference Echo on the InterLink
or SmartNet networks.



Dan Moore
3/3/1989