COPYRIGHT NOTICE

	                   MODEM - Modem Control Software
	              (C) Copyright 1989, 1990 - Ralph D. Miller
	                P. O. Box 38247, Tallahassee, FL 32315
	
	   Permission is  herewith given  for any  possessor of  the
	software to  reproduce and transmit this software package to
	third parties   provided that the following three conditions
	are met:
	
	      1)  No alterations or  deletions  of any kind are made
	          to the operating software or documentation.
	
	      2)  The software is distributed  without charge of any
	          kind by  the distributor, other than the customary
	          fees (not to exceed $10) in the case of a licensed
	          disk-copying service or User Group. Bulletin Board
	          distribution is encouraged.
	
	      3)  The software is not  distributed packaged with any
	          hardware product or system of any type.
	
	
	   Distribution of  MODEM  in  violation  of  any  of  these
	conditions constitutes an infringement of copyright.



	                              DISCLAIMER
	
	   Ralph D. Miller makes no warranties as to the contents of
	this  document   or  the   software  herein   described  and
	specifically   disclaims    any   implied    warranties   of
	merchantability or  fitness for  any particular     purpose.
	Ralph D.  Miller further  reserves the right to make changes
	to   the specifications  of the program and contents of this
	manual  without     obligation   to  notify  any  person  or
	organization of such changes.
	

















                              -1-











	
	MODEM14.EXE - What Is It?
	
	     MODEM14 is a tool  which  will  help  you  control  and
	eventually to  "demystify" your modem. This present  version
	will be  most useful  to owners  of 2400 baud Hayes or Hayes
	compatible modems  with non-volatile memory (in other words,
	"no dipswitches").  
	
	
	
	1200 and  300 baud  are supported  by the  MODEM14.EXE prog-
	ram (9600  in future versions), but anything controlled by a
	DIP switch  on your  modem probably won't have an AT command
	that can over-ride it.
	
	MODEM14  provides  suggested  settings  for  all  the  modem
	parameters it  controls.  These  suggestions  are  based  on
	popular telecommunications  packages such as ProComm, Telix,
	and the like.
	
	If  you  are  having  trouble  getting  your  communications
	program to function properly, we recommend the following:
	
	1) Change the Modem Initialization String in your com-
	   munications program to "ATZ". Don't include the quotes.
	   Your communications program's manual should contain
	   details on changing the default init string. Be sure
	   to include the character that represents a carriage
	   return at the end of the string if your program needs
	   one (example: ProComm 2.4.2 uses "!" by default).
	
	   You may want to make note of the old string, in case you
	   later want to refer back to it.
	
	2) Exit your comm program and load MODEM14, answering the
	   SETUP questions.
	
	3) Use the &F option to restore the modem to it's factory
	   default settings.
	
	4) Step through each selection of the AT Commands menu,
	   working from left to right on the top row and then
	   the bottom row, setting the options in each case to the
	   suggested value. Be certain to set the Q option to Q0,
	   and be certain to SKIP the &F option. You should end
	   with the &W option.
	
	5) Reload your communications program.
	




                              -2-








	
	It may  very well function correctly now! If not, you should
	be in  a much  better position  to experiment  and find  any
	less-common setting(s) your system requires.
	
	
	Selecting an  AT Command  is done merely by moving the light
	bar onto that command and pressing the <enter> key. Whatever
	options are  available for  that command  then appear in the
	Options Window.  Selection is made in the same way. Commands
	that are  associated with the command selected are displayed
	in the  'Associated With' Window. Additional information may
	be included therein as well.
	
	
	As you  build a  string, whatever would be sent to the modem
	with the "Send" command at any particular time is maintained
	in the  "Current Init  String" Window. Please note that this
	is NOT  necessarily the  current configuration  of the modem
	itself, but  the string  you've built  to send.  Sending the
	string should  be followed  by use  of the &W command if you
	want to  write it to the modem's non-volatile memory so that
	it will  still be  there when the modem is re-powered or re-
	initialized with an ATZ command.
	
	Should you exit the program with <F1> (function key) instead
	of the  <escape> key,  a small  file will  be written to the
	default directory.  This file contains the values stored for
	items included  in the  initialization string.  If this file
	exists,  the  program  will  restore  those  values  to  the
	"Current  Init   String"  window   when  MODEM   is  loaded.
	Otherwise, the values will be the defaults we've chosen.
	
	One exception is the Q command, which allows responses to be
	generated by the modem only when it is set to 0. If you have
	Q set  to 1, MODEM will change it when it loads. However, it
	will not  write that  change  to  the  modem's  non-volatile
	memory unless you do it with the &W command. Should you, for
	some reason, desire Q=1, just change it back via selecting Q
	in the  AT  Commands  Window.  Remember,  though,  that  the
	program can't  report modem  responses when  the modem isn't
	issuing any.
	
	When you select a command option, "Accepted" should flash in
	the Options  window assuming  your modem accepts the command
	and is  set to  issue responses  (as discussed above). If it
	flashes "Error!"  instead,  try  sending  the  command  once
	more... modems  are quirky things, at best. If it just won't
	take a  command, though,  it's probably  not quite as Hayes-
	compatible as  you'd hoped,  or uses  DIP switches  for that
	command.  As this suggests,  MODEM14 can be utilized to help
	to ascertain the compatibility of a modem.
	




                              -3-








	One problem  we've run  into is  when a  person buys  a used
	computer with  an internal  modem and  a second COM port but
	isn't sure  whether the  modem is  using COM1  or COM2. Just
	tell MODEM14 it's COM1... if it's  actually 2,  you'll get a
	"can't find  modem  message".  Run  the  program  again  and
	specify COM2.
	
	The &F  command is  included to  get a  modem back  to  it's
	factory configuration,  as a  starting point. There are many
	registers in a modem which seldom need be changed by any but
	quite specialized  systems, but we tend to get them adjusted
	anyway when  we're having  trouble. When a number are out in
	left  field,  some  very  puzzling  situations  can  result.
	Therefore, the  &F, which resets the entire device, not just
	the commonly  written registers such as we address with this
	program.

	
	However, it  was a  dangerous command  to include, as far as
	the purposes  of this  program (making  the modem easier for
	you to  deal with)  are concerned,  because if you do an &F,
	you'll undo  whatever you've  built with  the  rest  of  the
	program, but  since the  shareware version doesn't query the
	modem (and  not all  modems respond  to queries  anyway) the
	"Current Init  String" will  still display the string you've
	painstakingly built! Therefore, it's recommended you use the
	&F command very conservatively.

	
	The Z  command, if sent at the wrong time, can cause similar
	confusion. Z  will reload  the configuration resident in the
	modem that  was in  effect when  &W was  last  sent  to  it.
	Therefore, Z should really only be sent in order to "go back
	to square  one", giving  up any  changes that have been made
	since &W was last sent.

	
	One area  that really  bears investigation  is your  current
	command string specified in the setup of your communications
	program. For  instance, ProComm  2.4.2 was written at a time
	when  X1   was  a   better  default  than  X4,  due  to  the
	capabilities  of   modems  in  popular  price  ranges  then.
	Therefore, the  authors used  it as  a default, written when
	the program  is initialized  (if it  hasn't been  changed in
	SETUP). Nowadays,  however, X1  severely under-utilizes  the
	capabilities of  the 2400  baud "dipswitch-less"  modems. We
	recommend that  you make your initialization command ATZ, as
	explained previously.

	
	A little playing  with MODEM14  makes its functions  and use
	self-evident. We  tried hard  to keep  it on one screen, and
	except for  the initial  setup questions were able to do so.

	
	
	Thanks for using MODEM14, and have an OUTSTANDING day!


                              -4-





	History:

	Version 1.0, 22 October, 1989 - first public release.

        Version 1.1, 23 October, 1989 - corrected the illogical
                     placement of the Z command and the zip
                     code given for ordering the registered
                     version.

        Version 1.2, 2 November, 1989 - small timing changes 
                     were implemented to better serve 300 and
                     some 1200 baud modems.

        Version 1.3, 23 January, 1990 - minor cosmetic changes.

        Version 1.4, 9 August, 1990 - Added the '&AD' function 
                     in order to get something back out of
                     all this work!














































                              -5-