SPM.DOC    Copyright (c) 1991 Information Technology, Ltd.



          What is LiteSPM?
          ---------------

          LiteSPM(tm), or SPM for short, is a background(TSR) Serial Port
          Monitor. Once started, it sits quietly in the background, and
          listens to one of the system's serial ports. SPM writes the
          information that it receives to a disk file at either intervals
          you choose, or at a predefined, by SPM, point, whichever comes
          first.

          Why Use LiteSPM?
          ----------------

          We originally designed LiteSPM for use with the newer generation
          of telephone systems. Many telephone systems in use today have a
          provision for periodically sending data to a serial (RS232)
          device. Frequently, a standard printer records this information.
          At some later time, the printed information will be entered into
          a computer for the purposes of analysis and billing.

          With SPM you can bypass the data entry step. SPM records the
          information directly on your disk, but doesn't tie up your
          system. The result is a saving in both time and money.

          SPM has other uses. Since SPM will record anything, it can
          monitor and record any type of serial information. The
          information does not have to be ASCII characters. And SPM does
          not interpret or alter the data it receives in any way. It can
          monitor and record information from laboratory systems,
          manufacturing equipment, scales, or anything, in fact, that can
          produce serial (RS232) output.

          IMPORTANT NOTE:
          ----------------
          The above does not apply to modems. In general, modems require
          special initialization sequences to function properly. Modem
          support MAY be added in a future version of SPM.

          What Is Required?
          -----------------
          SPM requires about 24K of free memory and 1 serial port and at
          least MS-DOS 2.1, nothing more, nothing less. If you are
          fortunate and have MS-DOS 5.XX, you may load SPM into upper
          memory. See your MS-DOS documentation for details on the LOADHIGH
          command.

          SPM is flexible as well. You can configure SPM using command line
          switches, selecting the serial port, baud rate, parity, end of
          line characters, and path name of the file that SPM should use.
          Once SPM is running, you can instruct SPM to rename its file so
          that you can process it. Of course, SPM can be unloaded on
          command.

          Installation Instructions

                                     Page 1


          SPM.DOC    Copyright (c) 1991 Information Technology, Ltd.



          -------------------------
          You may install SPM by copying the file SPM.EXE into any
          directory on your system's disk. We recommend that you place SPM
          in a directory that is usually on the DOS path, but that is not a
          requirement, it will just make your life somewhat easier. Once
          you have copied SPM.EXE, you are ready to go.

          Starting SPM
          ------------
          To use SPM, you may simply type

                    SPM

          to start SPM with its default parameters. Normally, however, you
          will want to change one or more of these parameters. The command
          line switches to do this are described below.

          The more general form of the SPM command is

               SPM -cn -bnnnn -pX -eXXX -hX -fXXXXXXXXXXXXXXX | -u

          where:


                 -a      turns on the optional alert signal. As each log
                    record is written, a tone is sounded. Once activated,
                    the alert signal can only be deactivated by unloading
                    and reloading SPM.
                 -cn     specifies the COM port SPM is to monitor, values
                    of n may range from 1 to 4. If you intend to use COM3
                    or COM4, please see the information about these ports
                    below.  The default value is 1.


                 -bnnnn  specifies the baud rate SPM is to use. The rate
                    may range from 300 to 9600. The default value is 2400.


                 -pX     specifies the parity of the data that SPM will
                    monitor. Values of X may be E - even parity, O - odd
                    parity, or N - no parity.  The default value is N.

                 -eXXX   defines the character string that SPM is recognize
                    as the end of a record. By default, SPM recognizes
                    CR-LF as the end of record. To specify a new end of
                    record string, use the -e switch followed by up to 6
                    characters enclosed in quotes ("). Control characters
                    are specified by using the common notation ^ followed
                    by the ASCII character to be used.  To specify a CR,
                    for example, you would use ^M. Control sequences like
                    ^M count as a single character.




                                     Page 2


          SPM.DOC    Copyright (c) 1991 Information Technology, Ltd.



                 -hX     specifies the type of handshaking that SPM is to
                    use. By default, there is no handshaking. If you wish
                    to use XON-XOFF handshaking, specify X. To use DSR/DTR
                    handshaking specify D. To use RTS/CTS handshaking
                    specify R. Note that to use handshaking, the device
                    that SPM is monitoring must support handshaking.


                 -fXXXXXXXXXXXX defines the full path name of the file
                    into which SPM will place the information it captures.
                    By default, the name of the file is SPM.LOG. SPM.LOG
                    will be placed in the default directory in use when
                    SPM was started. We STRONGLY recommend that you
                    specify a full path name to avoid problems.

                 -u Unload SPM from memory. As with any TSR, SPM will only
                    unload successfully if it is the last TSR in memory.

          Examples
          --------

                    SPM -c1 -b1200

          This command starts SPM on COM1 using 1200 baud. All other
          parameters are defaulted.


                    SPM -c3

          This command starts SPM on COM3, with all parameters defaulted.
          If you intend to use COM3 or COM4, please review the section on
          COM3 and COM4.


               SPM -c1 -fd:\logfiles\spm.log

          In this example, SPM will monitor COM1 at 2400 baud. The data
          that SPM receives will be placed in SPM.LOG in the logfiles
          directory on drive D.


               SPM -c1 -e"^M"

          Start SPM on COM1. The end of line string is Ctrl-M (or Carriage
          Return).


               SPM -c2 -hr -f\logfiles\spm0630.log

          Here,  SPM is started on COM2.  The device that SPM is monitoring
          recognizes RTS/CTS hardware flow control.  All data is placed in
          the file spm0630.log in the logfiles directory of the current
          drive.


                                     Page 3


          SPM.DOC    Copyright (c) 1991 Information Technology, Ltd.





               SPM -fC:\logfiles\spm0630.old

          With SPM already running, the -f argument renames the existing
          logfile to SPM0630.old. We specify the full path name in case the
          logfile is in another working directory or on another drive. The
          next time SPM needs to write data, a new log file with the
          original path name will be created.














































                                     Page 4


          SPM.DOC    Copyright (c) 1991 Information Technology, Ltd.




               SPM -u

          Unload SPM when it is safe to do so. Flush any unwritten data to
          the log file.


          Using COM3 and COM4
          -------------------

          SPM can be used with COM3 and COM4.  To do so successfully, your
          serial ports must be setup so that the base port address of COM3
          is 3e8H (2e8H for COM4); In addition, the COM3 interrupt must be
          IRQ4 (IRQ3 for COM4). If your serial ports can be set to these
          values, then you should have no difficulty using COM3 or COM4.

          Tips and Techniques
          -------------------

          In general, the loading of SPM is best done in your system's
          autoexec.bat file. If this is not convenient or not sufficiently
          flexible, you may use another method to load SPM.

          If the data you are attempting to capture with SPM is
          identifiable as discreet records, we STRONGLY urge you to use the
          -e switch to define the characters that identify the end of the
          record. While SPM will never loose information, including the -e
          switch helps insure that SPM will place discreet records in the
          log file. Put another way, when you use the -e switch correctly,
          the log file should never contain partial records.

          SPM can survive in a network environment. In a network
          environment, you may specify that the SPM log file be placed on a
          network drive.

          DO NOT attempt to directly process the current SPM log file. We
          have included the rename facility so that you can keep SPM
          active, yet access the data in a convenient fashion.  Of course,
          the simplest way to accomplish this is through the use of a .bat
          file. Typically, the bat file would instruct SPM to rename the
          log file, process the data, then delete the file. 

          DO specify the complete path name of the SPM log file when using
          the -f pathname switch. This is particularly important when you
          use the -f switch to rename the current log file.

          DO NOT delete the current SPM log file while SPM is active. While
          you might do so successfully, on occasion, there is no way to
          insure that SPM will not attempt to write to the file while you
          are deleting it. If this should happen, the results are
          unpredictable. At best there would be some data loss. At worst, a
          system hang might result.



                                     Page 5


          SPM.DOC    Copyright (c) 1991 Information Technology, Ltd.



          DO pay attention to the hardware flow control signal restrictions
          when you select either DTR/DSR or RTS/CTS flow control. LiteSPM
          assumes that these signals are active HIGH signals. Check your
          hardware reference carefully if you have difficulty that seems to
          be related to hardware flow control.

          Serial port wiring can be one of the most difficult areas to
          understand, since some equipment manufacturers have chosen to
          bend the standards. If you plan to do a lot of work in this area,
          we recommend that you acquire a good quality breakout box to help
          you make the right connections. A breakout box will let you
          monitor and experiment with the various RS232 signals quickly and
          conveniently without spending time soldering unknown connections.
          One such device that we use is the Blue Box 100, manufactured by
          International Data Sciences, 7 Wellington Road, Lincoln, RI
          02865. You can contact them at (401) 333-6200 for current pricing
          and availability.

          Problems And Questions
          ------------------------
          If you are having difficulty using LiteSPM, and you are a
          registered user, please feel free to contact us by telephone. If
          you want to register LiteSPM, see the file REGISTER.DOC for
          additional information. We will also respond to Electronic Mail
          on Compuserve (ID 70166,1152) or GEnie (ID I.TECH). Finally, we
          will be happy to respond to mail inquiries by conventional
          first-class mail. Regrettably, we are not equipped for FAX
          service at this time.

          And if you have special requirements for SPM, please feel free to
          contact us as well.
























                                     Page 6