B A L L I S T I C

                                  Version  3.10




                    (C) Copyright 1988 by William R. Frenchu









                                   DISCLAIMER

        Reloading  small arms ammunition can be a DANGEROUS pastime.  The
        purpose of this program is NOT to teach the fundamentals of  this
        fascinating hobby but rather to aid the hobbyist in assessing the
        performance of the ammunition he has produced. It is assumed from
        the outset that the user of this program is acquainted with basic
        reloading  techniques. For review, a list of  references  wherein
        may be found the necessary instruction is included in Appendix  B
        of this document. DO NOT ATTEMPT TO PRODUCE AMMUNITION FOR  YOUR-
        SELF  OR  OTHERS UNTIL YOU ARE COMPLETELY FAMILIAR WITH  ALL  THE
        FUNDAMENTALS OF RELOADING. ALWAYS START WITH THE MINIMUM LOAD AND
        WORK SLOWLY UP TO (NEVER EXCEED) THE MAXIMUM LISTED LOAD.

        Although  every reasonable care was taken to insure the  accuracy
        of this program, it is provided "AS IS" and without warranties as
        to performance of merchantability or any other warranties whether
        expressed  or implied, including, but not limited to warranty  of
        fitness for a particular purpose. Good data processing  procedure
        dictates that any program be tested with non-critical data before
        relying on it. The user must assume the entire risk of using  the
        program. The author will assume NO responsibility for any  damage
        or injury that may occur.


                             User Supported Software

        This  program may be copied and freely distributed for  any  non-
        commercial use provided all accompanying files and  documentation
        are  included  WITHOUT MODIFICATION. See Appendix E  for  further
        information (and the usual pitch for cash).




                                TABLE OF CONTENTS
                                -----------------


        1. About the Program ....................................... 1
          A. General ............................................... 1
          B. Program files ......................................... 1
          C. System requirements ................................... 1
          D. Program limitations ................................... 2
          E. Notation .............................................. 2
          F. What's new ............................................ 2
          G. The future ............................................ 3
          H. Acknowledgments ....................................... 3

        2. Using the Program ....................................... 4
          A. Starting the program .................................. 4
          B. Command line arguments ................................ 4
          C. Calculating the ballistic coefficient ................. 4
          D. The ballistic table ................................... 5
          E. Sight (trajectory) tables ............................. 5
          F. Plotting the trajectory ............................... 5
          G. Modifying the ballistic coefficient ................... 6
          H. Changing the cross wind value ......................... 6
          I. Changing the input function table ..................... 7
          J. Miscellaneous functions menu .......................... 7
          K. Calculating recoil .................................... 7
          L. Calculating minimum twist ............................. 8
          M. Calculating the point blank range ..................... 8
          N. DOS Shell ............................................. 9

        3. The Configuration File .................................. 10
          A. Using the configuration file .......................... 10
          B. Allowable parameters .................................. 10

        4. Sources of Data ......................................... 12
          A. Altitude .............................................. 12
          B. Ballistic coefficient ................................. 12
          C. Bullet weight, length and caliber ..................... 12
          D. Gun and powder weight ................................. 12
          E. Specific gravity of bullet alloys ..................... 13
          F. Temperature, atmospheric pressure and wind ............ 13
          G. Velocity .............................................. 13

        5. Using GENTABLE and READTABLE ............................ 15
          A. Using the pre-programmed functions .................... 15
          B. Creating custom function tables ....................... 15
          C. Checking the function file ............................ 16

        Figures .................................................... 17

        Appendix A, Glossary ....................................... 21
        Appendix B, Information Sources ............................ 24
        Appendix C, Coefficients for Several Factory Cartridges .... 25
        Appendix D, Specific Gravities of Bullet Alloys ............ 28
        Appendix E, User Supported Software ........................ 29

        Registration Form .......................................... 30






        1.  ABOUT THE PROGRAM

        A. General
             BALLISTIC  is a Turbo C (v1.5) program written  to  generate
        ballistic  tables for shooters. Given certain  easily  obtainable
        data,  it  calculates such useful information  as  the  ballistic
        coefficient,  remaining  velocity, energy, momentum,  drop,  wind
        deflection, maximum height, time of flight and lead (for a moving
        target)  at a given range. In addition, it can be used to  deter-
        mine the amount of recoil generated by a cartridge and gun, esti-
        mate the minimum twist necessary for bullet stabilization, calcu-
        late point blank ranges and produce trajectory tables for estima-
        ting  "holdover". Finally, BALLISTIC will produce a plot  of  the
        bullet's  trajectory versus range. It does all this by  comparing
        the  bullet in question to a "standard bullet" with a well  known
        trajectory.  As this data is calculated before use by a  separate
        program (GENTABLE), the user's ballistic tables are produced very
        quickly.

        B. Program files
             The  following files should be included in any  distribution
        of BALLISTIC:

          BAL-GEN.EXE  -GENTABLE  :Creates function tables for BALLISTIC.
          BAL-READ.EXE -READTABLE :Optionally checks function table.
          BAL-READ.ME! -Describes version, etc.
          BALISTIC.EXE -BALLISTIC :Executable file.
          BALISTIC.DOC -This file.
          BALISTIC.REV -BALLISTIC Revision history.

        C. System Requirements
             BALLISTIC  should run on most IBM BIOS-compatible  computers
        using PC/MS-DOS 3.0 or above. It requires 256k of free memory and
        at  least one disk drive.  Non-graphic functions are directed  to
        the  default  display. Graphic output  (for  Shareware  versions)
        require  a  VGA, EGA, CGA, AT&T or  Hercules  compatible  display
        card. (At this time graphic functions for the Toshiba 3100 series
        are NOT supported due to incompatibilities between their  display
        board  and the AT&T board it is supposed to emulate.  The  author
        has  access to a patch that should allow a special version to  be
        compiled, but no way to test it.) Registered versions can be sup-
        plied  that additionally support the higher resolution  modes  of
        the MCGA, IBM 8514, PC-3270 or Everex EGA+.
             BALLISTIC  has been tested and found to operate properly  on
        the following systems:

          PC/XT with Hercules monochrome or "EGA Wonder" adapter
          PC/AT with CGA or EGA adapter
          NEC MultiSpeed Portable
          BIOS Model G (V40 CPU)
          AT&T 6300
          Compaq Plus with Compaq CGA-type adapter
          Compaq DeskPro 386 with Compaq EGA-type adapter



        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 1




        D. Program limitations
             Any  program of this type will have certain limitations  re-
        garding its use and accuracy and BALLISTIC is no exception. These
        discrepancies  between  actual and calculated  performance  arise
        primarily  because of the inability of the user to measure  input
        values exactly and certain approximations the program uses in its
        calculations. Assuming that the input values are known to 1%  the
        average user should find agreement with published data to be 1-2%
        for all velocity and trajectory calculations. The recoil section,
        due to the more approximate nature of the calculation,  shouldn't
        be  considered more than 10-15% accurate. In any case, while  the
        numbers  produced  by  the program are believed  to  be  accurate
        enough for all practical purposes, they are meant only as a guide
        to ammunition performance. How a particular load performs with  a
        given gun can ONLY be determined by actual firings.
             While  Ingalls'  ballistic table is  historically  the  most
        commonly used for this sort of work, several others are likely to
        be encountered. (Many manufacturer, for instance, favor the  "G1"
        table.) For the types of bullets most often used by reloaders the
        results  will be very similar regardless of the table  used.  In-
        deed, the variation between handloads or factory ammunition  ran-
        domly  selected from the same lot will probably be  greater  than
        the  discrepancies  noted between different  tables  over  normal
        shooting ranges. For best results, one should try to use the same
        input  function to produce the table that was initially  used  to
        calculate  the ballistic coefficient. However, this isn't  always
        possible,  as in the case where a published coefficient was  cal-
        culated using a table to which the program doesn't have access.

        E. Notation
             Throughout  this document, keys to be pushed in response  to
        program  prompts  are enclosed in angle  brackets.  For  example,
        "press  <1>" means to press number 1 on the keyboard. For  "press
        <ENTER>",  use the key labeled either "return" or  "enter".  "En-
        tering" a value will require that the <ENTER> key be pressed when
        finished, i.e., to "enter 10" press <1><0><ENTER>.

        F. What's New
             There have been several additions to the program since  ver-
        sion 3.01. Some of these include:

           1. Directory  under  New Table menu now prints  out  in  wide,
              pause mode.
           2. Shell  now  changes the environment by adding  a  temporary
              "reminder" to the prompt string.
           3. Plotting now has user definable axes.
           4. Plot now labels range tic-marks and line of sight.
           5. Added lead for moving targets to table.
           6. Added Help screen to Plot function.
           7. Added grid toggle to Plot function and configuration file.
           8. Documentation now includes specific gravity information for
              non-lead alloys.
           9. Added ability to save and recall a plot for graphic compar-
              ison of trajectories.
          10. Added graphics screen dump for several printers. (And PTYPE
              configuration option.)


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 2




          11. Increased maximum number of intervals to 50.
          12. Added new command line options to READTABLE. BALREMOV is no
              longer necessary.
          13. Improved configuration file. No more problems with  leading
              or trailing blanks.
          14. Added  Greenhill  number to configuration  file  and  twist
              menu.

        G. The Future
             BALLISTIC  isn't perfect (or even necessarily finished).  It
        is  hoped, for instance, that future releases will incorporate  a
        "Powley  Computer"  type computation for  estimating  the  powder
        charge necessary for a given velocity. The ability to make calcu-
        lations based on distances given in meters or yards would also be
        a  welcome improvement, as would an on-line database relating  to
        commercially loaded cartridges. Additional features the author is
        considering include: context sensitive help, reading/writing load
        data  to  DBase  or Symphony  compatible  files,  uphill/downhill
        shooting corrections, and recalling of multiple plots.
             The  author is interested in adding new function  tables  if
        reliable data can be found. He is currently on the lookout for  a
        copy  of BRITISH TEXTBOOK OF SMALLARMS or listings of the "J"  or
        "G5" tables. Also of interest is additional specific gravity data
        for  commonly used bullet casting alloys, and information on  the
        types  of materials being used in the "new" non-lead  bullet  de-
        signs (i.e., bronze) AND the "old" ones (steel). All things  will
        come  to  those users who wait (and support  BALLISTIC  with  the
        voluntary contribution!)
             All in all, BALLISTIC seems likely to fill the needs of many
        shooting  buffs.  Included  in the documentation   is  a  section
        listing sources for further reading on small arms ballistics  and
        reloading. The local gun shop or public library may have  others.
        READ some of them!.. AND the disclaimers. Then enjoy the program.

        H. Acknowledgments
             The  author  is indebted to the following people  for  their
        help, support, and the many suggestions they made. Without  dedi-
        cated  users such as these, the program would never have  reached
        its current level of sophistication:

                                  Bart Carfizzi
                                   Jim Kreiser
                                  James Roberts
                                Donald Terwilliger
                                 Dave Zarodnansky

             Special  thanks of course, are due to the author's wife  and
        family,  Susan, Billy and Karen, for understanding (or  at  least
        putting  up  with!) the author's wild mood  swings,  ranting  and
        raving  as  various parts of BALLISTIC (which were  working  just
        fine  yesterday!) stopped working  for no apparent reason.  Thank
        you.






        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 3






        2.  USING THE PROGRAM

             The goal in writing BALLISTIC was to produce a program which
        was at once versatile and relatively easy to use. While there  is
        still room for improvement, some success in both of these  direc-
        tions has been achieved. The program is primarily menu driven and
        prompts  whenever input data is required. Additionally, data  en-
        tered  (or calculated) in one section of the program need not  be
        re-entered  unless the user wants to change the value.  Data  the
        program  knows about are displayed during the prompts. To  accept
        the displayed value press <ENTER>. To change it, simply type  the
        new data over the old, then press <ENTER>. (The table title  must
        ALWAYS  be entered explicitly.) To correct typing errors  on  the
        current line, use the <BACKSPACE> key, NOT the <DELETE> key.  Im-
        proper  entries on previous lines can be corrected by  using  the
        <ESC>  key to "back up" to the bad line, then retyping the  data.
        In  most  cases, obviously improper data will be refused  and  an
        acceptable  range displayed. Input filenames will be checked  for
        existence before they are accepted.

        A. Running the Program for the First Time
             Prior  to  running BALLISTIC for the first  time,  the  file
        containing  the  function table required by the program  must  be
        generated  using GENTABLE (v3.00 or above, see Section  5).  This
        file  will  contain the version number of the  GENTABLE  used  to
        create it, the function name, some atmospheric data, the  maximum
        and minimum velocity and S and T value pairs. Once this file  has
        been  created (and optionally checked using READTABLE)  BALLISTIC
        can  be invoked. Only BALISTIC.EXE and a function file  need  ac-
        tually be present on the disk when running the program.

        B. Command Line Arguments
            BALLISTIC is started by simply typing its filename (BALISTIC)
        at  the DOS prompt, optionally following it with one or  both  of
        the  following arguments. "-BIOS" will cause all video output  to
        be  done using BIOS calls rather than direct screen  writes.  The
        second argument, "-F" followed (with NO spaces) by the name of  a
        BALLISTIC  function  file, causes the named function file  to  be
        loaded instead of the default file BALISTIC.TAB.
             BALLISTIC will first attempt to read the configuration  file
        (BALISTIC.CFG, see Section 3), then search for the default  func-
        tion  file  (either BALISTIC.TAB or the  command  line  specified
        file),  prompting the user for the name of an alternate  if  it's
        not  found.  The default file type is ".TAB" which  need  not  be
        entered. (To enter a filename with no extension enter "filename."
        with the trailing period.) BALLISTIC will next read the  function
        file,  make a check to determine its validity (a simple  checksum
        procedure), and present the user with the main menu. (Fig. 1)

        C. Calculating a Ballistic Coefficient
             The first step in developing a ballistic table is to  deter-
        mine  the  ballistic coefficient. If this value cannot  be  found
        explicitly  in one of the sources described in section  4B,  main
        menu  choice  2 may be used to calculate it. Press  <2>  and  the


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 4




        program will prompt for an initial and final velocity, the  range
        and some atmospheric data. After this has been entered, the  cal-
        culated value of the effective ballistic coefficient (as well  as
        the  coefficient at standard conditions for the function  chosen)
        will be displayed on the screen (Fig. 2). Having found the  coef-
        ficient, BALLISTIC can now calculate the table. Press the <ENTER>
        key  to  redisplay the main menu then <1> to bring up  the  input
        section.

        D. The Ballistic Table
             Figure  3 shows the input data for main menu choice 1,  cal-
        culating  the ballistic table. Since the initial velocity,  range
        and  ballistic coefficient have been entered or calculated  on  a
        prior  screen, these values needn't be re-entered unless  a  dif-
        ferent value is required. In this case, entering a range value of
        500  will  create a table to 500 yards based on  the  performance
        noted over the first 100. Entering a value of zero for the  range
        will cause the program to switch to metallic silhouette mode. The
        user will then be prompted for his choice of standard  silhouette
        rifle  or pistol ranges rounded to the nearest yard. As  long  as
        the  input  value for range remains zero these  alternate  ranges
        will  be  used. The final necessary data item is  the  number  of
        intervals  into  which  the total range should  be  divided.  The
        maximum  number allowed is the smaller of 50 or the total  range.
        Data entry is concluded with an optional table title.
             Figure 4 shows the table itself and the program's prompt for
        generation  of a sight table. At this point, should it be  desir-
        able to get a printed copy, press <1>. The program will  redirect
        ballistic table output to the system's LST: device and return  to
        the  prompt. A form feed (page eject) can be sent to the  printer
        by pressing <2>.
             The "New Data" choice, <4>, will return the user to the data
        entry  screen to calculate another ballistic table,  while  "Main
        Menu"  (<5>  or <ESC>) will jump directly back to  the  program's
        initial screen.

        E. Sight (Trajectory) Tables.
             Sight (trajectory) tables can be produced by pushing <3>  in
        response to the prompt at the bottom of the ballistic table.  The
        program  will  require  that distance for  which  the  weapon  is
        "sighted  in"  (this value need NOT have appeared  in  the  range
        column  of  the original ballistic table) and the height  of  the
        front sight above the centerline of the bore. In silhouette mode,
        entering  a value of zero for the targeted range will  cause  the
        prompt to take the form of which silhouette (chicken, pig, turkey
        or  ram) the weapon is zeroed for. The user should  respond  with
        the first letter of the appropriate target. Output of this  table
        can  be  diverted  in exactly the same manner  as  the  ballistic
        table. Pressing <3> allows the user to enter new data for another
        sight  table  (using the current ballistic conditions),  and  <5>
        (or <ESC>) returns to the ballistic table and prompt.

        F. Plotting the Trajectory.
             Pressing <4> at the sight table prompt will present the user
        with a graphic representation of the bullet's trajectory on  sys-
        tems  with an appropriate graphics card. Range, in yards will  be


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 5




        indicated along the bottom, with tic marks appearing at distances
        corresponding to the entries in the ballistic table. Dotted lines
        will  appear vertically at the distance for which the  weapon  is
        zeroed and horizontally at the line of sight. The trajectory  (in
        inches above or below the line of sight) is indicated on the left
        scale.  Pressing  <A>  (for axes) will allow the user  to  set  a
        "viewport".  The  program  will prompt for  starting  and  ending
        range,  and  the maximum and minimum trajectory, then  plot  only
        that portion of the trajectory that falls in the described  "win-
        dow". Pressing <S> (for start) will reset the plot to the initial
        (program chosen) limits. <G> will toggle the appearance of a grid
        on  the plot and <H> will provide a short help screen. If <W>  is
        pressed, trajectory data (for the current viewport ONLY) will  be
        written  to  a file. This data may be "merged" with  the  current
        trajectory plot at any time by pressing <R>. Hardcopy of the plot
        (actually,  a screen dump) may be obtained by pressing <P> if  an
        appropriate graphics printer is present. (Supported printers  are
        discussed  in  the configuration file section under  PTYPE.)  De-
        pending  on  the display adapter and printer,  this  may  require
        several  minutes.  (A typical EGA graphics screen dump  is  about
        30k,  roughly the size of a ten page document, and takes just  as
        long to print.) Printing may be abandoned at any time by pressing
        a key. Users with a printer not listed may want to try using  the
        <PRINT  SCREEN> key which will usually require that  the  program
        GRAPHICS.COM (from the DOS system diskette) be run before BALLIS-
        TIC  is  started. Neither method will work with all  display  and
        printer  combinations. (Registered users may, of course,  contact
        the  author  and request support for their  particular  printer.)
        Pressing  <X> or the <ESC> key will return the user to the  sight
        table prompt.
             From  the sight table press <5> (or <ESC>) to return to  the
        ballistic table, (Figure 4 again) then a <5> (or <ESC>) to return
        to the main menu.

        G. Modifying the Ballistic Coefficient
             Those  living at high altitude or in areas of extreme  temp-
        erature  will want to adjust published (sea level) values of  the
        ballistic  coefficient to more accurate local values.  Main  menu
        choice  3 may be used to accomplish this (Figure 5). The  program
        will  need to know the altitude, barometric pressure and  temper-
        ature  in addition to the value of the ballistic  coefficient  at
        STP (Standard Temperature and Pressure, the published value).
             Bear  in mind that these meteorological  values  (especially
        temperature)  ALSO affect the initial velocity of a  given  load.
        This  effect is beyond the ability of this program  to  calculate
        but descriptions of it may be found in many reloading manuals.

        H. Changing the Cross Wind Value and Angle
             Menu choice 3 also allows for adjustment of the speed of the
        cross  wind  used to calculate wind deflection. By  default,  the
        program  sets this value to 10 miles per hour,  blowing  directly
        across  the  path of the bullet (0 degrees). It should  be  noted
        that  deflection  is a linear function, i.e., a 5 mph  wind  will
        deflect a bullet by exactly half the amount of a 10 mph wind. The
        angle  of the cross wind may be changed here as well. In  program
        coordinates,  0 degrees (the default) is blowing directly  across


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 6




        the  bullet's  path, either left to right or right  to  left.  90
        degrees  would be either a head or tail wind with no  cross  wind
        component. These values are used ONLY for calculating deflection.
        Their  effect  on other aspects of the  trajectory  is  currently
        ignored.

        I. Changing the Input Function Table
             Starting  with version 2.00, it is possible to switch  input
        function tables without restarting the program. Pressing <4> from
        the  main menu will cause a prompt for the new file name.   If  a
        filename containing wildcard characters ("*" or "?") is  entered,
        the  directory  of all matching filenames will be  displayed.  As
        noted  in section A, the default table type is ".TAB" which  need
        not  be entered. Simply press <ENTER> to abort and return to  the
        main menu.
             This  option doesn't affect the fact that  BALISTIC.TAB  (or
        the filename supplied with the "-F" command line option) will  be
        searched  for (and loaded if present) when the program  is  first
        started.  It  is provided only for users who routinely  use  more
        than one function table. Even so, program startup will be simpli-
        fied if the table most commonly used is copied to BALISTIC.TAB.
             It  should  be noted here that loading a new  function  file
        will  not reset the temperature and pressure to the defaults  for
        the  new table. Thus, some care should be taken if switching  be-
        tween two tables that use different standard conditions.

        J. Miscellaneous Functions Menu
             Pressing  <5> at the main menu prompt will present the  user
        with  the miscellaneous functions menu. From this menu  the  user
        may  elect to calculate recoil, the minimum necessary  twist  for
        bullet stabilization, or the point blank range for a given target
        size.

        K. Calculating Recoil
             The recoil energy and velocity of a weapon can be calculated
        using  miscellaneous menu choice 1, provided its weight  and  the
        weight of the powder charge are known (Figure 6). This number can
        be deceptive as the perception of recoil by different shooters is
        VERY subjective. In addition to the physics involved, there  must
        be some consideration given to the fit of the gun to the individ-
        ual,  shape  and  material  of the  stock  or  grips,  etc.  Many
        shooters,  for  instance, fear the recoil of a 12  gauge  shotgun
        even with target loads while thinking nothing of using a  6 pound
        30-06 despite the fact that the "calculated" recoil can be  quite
        similar.  Such  recoil is often in the eye (or shoulder)  of  the
        beholder.
             This  section also calculates whether a "muzzle brake"  type
        device  will  be useful in reducing felt recoil by  allowing  the
        user  to determine the rough percentage of recoil caused  by  the
        bullet  itself  (which a muzzle brake cannot affect).  The  value
        indicated is the level to which recoil energy would be reduced if
        there  were no powder at all. This is a crude estimate of what  a
        shooter  might achieve with a perfect brake. (Bear in mind,  how-
        ever,  that  NO  muzzle brake is 100% effective  and  the  actual
        amount of reduction will be less.)
             The  recoil  calculation used by BALLISTIC is a  very  rough


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 7




        approximation, similar to that discussed in the March 1988  Amer-
        ican Rifleman. It would be extremely challenging to write a  com-
        pletely accurate description of the recoil process. It would also
        be  very  difficult  to use as many variables  are  involved  in-
        cluding, but not limited to bore cross sectional area, length  of
        barrel,  atmospheric  pressure and temperature, type  of  powder,
        loading  density, etc. The values calculated here should  not  be
        considered  accurate to more than 10-15%. Barrel/powder  combina-
        tions that produce excessive muzzle flash will be even less accu-
        rate.

        L. Calculating Minimum Twist
             The slowest twist that will stabilize a bullet in flight may
        be calculated using miscellaneous menu choice 2. The formula used
        here is the approximation credited to Sir Alfred George Greenhill
        in 1879. Necessary input data includes the bullet's  diameter and
        length  in  inches and specific gravity. The  default  value  for
        specific  gravity  is the average density of a  typical  jacketed
        bullet.  Also listed on the input screen (for reference)  is  the
        specific gravity of pure lead. Specific gravities (or  densities)
        of  other  bullet  alloys seem difficult to find.  It  should  be
        pointed out that these specific gravities can NOT be added algeb-
        raically. That is, an alloy containing 50% lead and 50% tin  will
        NOT  have a specific gravity that is the average of the two  pure
        metals.  Appendix  D of this document contains  specific  gravity
        data for a small selection of common alloys.
             It has been pointed out to the author, that this  approxima-
        tion was originally intended for use with artillery  projectiles.
        More  recent findings indicate that, for typical small  arms  am-
        munition,  a Greenhill number smaller than the default  of  150.0
        (100  has  been suggested)  may be appropriate  especially  under
        adverse  atmospheric conditions such as rain and snow. A  discus-
        sion may be found in the June 1988 issue of Rifle. ("Shooting the
        Kalashnikov",  pp.  28 - 31.) This number  may  be  "permanently"
        changed using the configuration file.

        M. Calculating the Point Blank Range
             Given the velocity, sight height and ballistic  coefficient,
        a  point blank range may be determined for any target  size.  The
        point blank range is the maximum range for which a bullet can  be
        counted upon to strike a target by simply aiming the weapon  dir-
        ectly  at it. For example, given a 6 inch target, a  point  blank
        range may be calculated so that the bullet is always less than  6
        inches  from  the line of sight. BALLISTIC  will  calculate  this
        distance for a given target size and tell the user for what range
        the weapon should be sighted and what trajectory the bullet  will
        have at 100 yards. (If the targeted range is less than 100 yards,
        the  trajectory at 25 yards will be given instead.)  This  figure
        may be used to sight the weapon when the targeted range is either
        unrealistically  far  away, or an unusual number  of  yards.  For
        instance,  in the example screen, sighting the weapon 5.0  inches
        high  at 100 yards will allow the shooter to hit a 6 inch  target
        out to 337 yards, without allowing for any holdover. However, the
        bullet will only strike the CENTER of the target at 287 yards.




        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 8




        N. DOS Shell (Escape to DOS)
             Users operating under MS/PC-DOS version 3.00 or higher  have
        the option of shelling out to DOS from either the main or miscel-
        laneous menus. The only other requirement for this option is that
        there  be  a copy of COMMAND.COM in the place  indicated  by  the
        COMSPEC path variable.




















































        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 9






        3.  THE CONFIGURATION FILE

             Version  3.10  of BALLISTIC will allow certain  program  de-
        faults  to be overridden with the aid of the  configuration  file
        BALISTIC.CFG.  This option was originally provided for  users  in
        the  CP/M environment. The file is searched for only in the  cur-
        rent directory when BALLISTIC is first started and is NOT  neces-
        sary for the operation of the program.

        A. Using the configuration file
             The  configuration file is an ascii text file each  line  of
        which  contains the name of the parameter to be changed,  one  or
        more  spaces,  and the new value. Parameters listed as  "must  be
        integer" may NOT contain a decimal point or exponential notation.
        Certain parameters may only accept ON and OFF (or similar  string
        choices) as values. Entries are NOT case specific.
              The following file would turn off the bell, set the default
        altitude to 2000 feet and set the video write mode to BIOS:

        BELL OFF
        Altitude 2000
        video bios


        B. Allowable parameters
             The following parameters are allowable for BALLISTIC v3.10:

          ALTITUDE - The  altitude to be used in the ballistic  table
              and  ballistic coefficient calculations. May  be  REAL.
              The default value is zero.

          BELL - Controls whether the console bell is rung for errors
              detected  by the program. Allowable values are  ON  and
              OFF. The default is BELL ON.

          BKG - Determines  the background text screen color.  Allow-
              able  values are 0 through 7. Must be INTEGER. The  de-
              fault value is 0. This parameter is illegal for systems
              having only a monochrome text/graphics card.  Following
              are the colors corresponding to each value:
                      0 - Black         4 - Red
                      1 - Blue          5 - Magenta
                      2 - Green         6 - Brown
                      3 - Cyan          7 - Lt. Gray

          COLOR - The  text color. Default is 7. See BKG for  a  des-
              cription of allowable values and restrictions.

          GREENHILL - This  option specifies a new  Greenhill  number
              for  use in the minimum twist  calculation.  Acceptable
              values range from 75.0 to 200.0. The default is 150.0.

          GRID - This  option  informs the program whether  the  grid
              should initially appear in the Plot function. This  may


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 10




              also  be toggled from the Plot function itself.  Allow-
              able values are ON and OFF.

          PRESSURE - The atmospheric pressure used for the  ballistic
              table  and ballistic coefficient calculations.  May  be
              REAL.  The default value is dependent on  the  function
              file chosen.

          PRINTER - Line  width in characters of the system  printer.
              Must be an INTEGER value from 80 to 200. Default is 80.

          PTYPE - Type of graphics printer connected to system.  This
              option is only used by the graphic screen dump routine.
              Default is 1, for the HP Laserjet. Currently  supported
              values are:
                      1 - Hewlett Packard Laserjet
                      2 - Star SG-10 (in IBM mode)
                      3 - IBM Proprinter
                      4 - IBM Graphics Printer

          SCREEN - The  output screen width. This is for  future  re-
              visions of BALLISTIC. Currently, only 80 is  supported.
              Must be an INTEGER value.

          TEMPERATURE - The  temperature  to be  used  for  ballistic
              table  and ballistic coefficient calculations.  May  be
              REAL.  The default value is dependent on  the  function
              file chosen.

          VIDEO - Determines the method used to write to the  screen.
              Allowable  values are BIOS and DIRECT. BIOS causes  all
              output to be done through the use of system BIOS calls.
              This mode may be useful for computers/graphics adapters
              that are not 100% compatible with the IBM PC family. It
              does,  however,  significantly slow output.  Using  the
              DIRECT  option causes all screen output to  be  written
              directly to video memory. Default is DIRECT.





















        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 11






        4.  SOURCES OF DATA

             Much  of  the data necessary for ballistic  calculations  is
        readily available. Even the ballistic coefficient can usually  be
        calculated from the information at hand. Following are  suggested
        sources for specific input data to the program.

        A. Altitude
             The  calculation  doesn't depend on altitude  directly,  but
        rather  on the way air temperature and pressure vary  with  alti-
        tude.  The program uses this value to determine what  the  "stan-
        dard"  temperature and pressure are for a given  ballistic  func-
        tion. Users can look up the actual altitude of their location  in
        an  almanac or one of the U.S. Department of the Interior  "Quad-
        rangle Maps" available at many sporting goods or camping  stores.
        Either  jot it down near the computer so it can be  entered  when
        the  program  is run or add it to the configuration file  as  de-
        scribed in section 3.

        B. Ballistic Coefficient
             This  will  probably be the most difficult number  to  find.
        Those who reload will usually be able to get this value from  the
        manufacturer  of their bullets. (Speer and Sierra, for  instance,
        print this data in their reloading manuals.) The value for  other
        bullets  may sometimes be estimated by comparing  bullet  shapes,
        provided the bullet is of the same caliber. Comparing the  bullet
        in question to a specially prepared chart of shapes is often more
        accurate.  The  DuPont Company at one time produced a  series  of
        these  and  other useful charts, called "A Short Cut  To  Ballis-
        tics".  The complete set is supplied with Ackley's  handbook  and
        the  specific chart for estimating ballistic coefficients is  re-
        printed in HATCHER'S NOTEBOOK.
             The program itself will calculate the ballistic  coefficient
        in  certain cases. Both the initial and remaining velocity  at  a
        given  range  must be known. This data is available  for  factory
        loaded  ammunition in manufacturers' literature and sources  such
        as  SHOOTERS BIBLE. (A short section of coefficients for  several
        factory loadings calculated using this program and Ingalls' table
        may be found in Appendix C.)

        C. Bullet Weight, Length, and Caliber
             These are easy. On factory-loaded ammunition or  components,
        bullet weight (in grains) and caliber will be written on the box.
        Those who cast their own bullets will need to weigh several  sam-
        ples  prepared  with the actual alloy used. Take the  average  of
        half  a dozen or so and use that value. A  sufficiently  accurate
        value for bullet length may be found with a ruler.

        D. Gun, Powder Weights
             These two are needed only to calculate the amount of  recoil
        generated  by a given load. The weight of a rifle can usually  be
        found accurately enough on a bathroom-type scale. Actual  weights
        of  most  firearms can be found in manufacturers'  literature  as
        well as in such sources as SHOOTER'S BIBLE, GUN DIGEST, and  pro-


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 12




        duct reviews in many magazines. Don't forget to add in the weight
        of scopes, slings, custom stocks or any other accessories.
             Powder weights will be known if performing calculations  for
        handloads. If using factory loads, try estimating by comparing to
        available  reloading  data. Find a load that moves  a  bullet  of
        similar  construction  (jacketed, soft lead, etc.) to  about  the
        same muzzle velocity.

        E. Specific Gravity
             This  value  is only required for  calculating  the  minimum
        necessary  twist  for stabilization. Two more  or  less  standard
        values are 11.34 for pure lead, and 10.90 for a typical  jacketed
        bullet.  Other values are very difficult to find in  the  litera-
        ture.  Hatcher,  describes a fairly simple way  to  measure  this
        quantity,  but the two values above should be sufficiently  accu-
        rate for most practical purposes.
             Appendix D of this document contains a short compilation  of
        specific  gravity data for some common Lead/Tin/Antimony  alloys.
        These were taken primarily from volume one of the American  Soci-
        ety of Metals METALS HANDBOOK.

        F. Temperature, Atmospheric Pressure, Wind Speed and Direction
             Suitably accurate values for temperature and pressure can be
        obtained  from a weather report or newspaper. As  with  altitude,
        the  calculation  isn't terribly sensitive to these  factors,  so
        unless  the range is in the Sahara Desert or Antarctica they  can
        probably be ignored. (It CAN be interesting to set up a ballistic
        table and vary them just to see what happens... Experiment!)  The
        same  suggestion applies; try the program with and  without  cor-
        recting and see if the difference is big enough to  realistically
        notice.  Bear  in mind that this program examines the  effect  of
        these  variables only on the ballistic coefficient.  Temperature,
        for instance, will also change the initial velocity of a load,  a
        factor  beyond the ability of this program to calculate.  (Tables
        describing  this effect can be found in both the Speer  reloading
        manual and Ackley's handbook.) Temperature and pressure are  also
        valid parameters for use in the configuration file. (Section 3)
             Wind direction can only be estimated at the actual  shooting
        site.  Zero degrees indicates a wind blowing across the  bullet's
        path to either the right or left. Ninety degrees indicates a wind
        blowing  either  directly behind or directly  into  the  bullet's
        path. As this value is only used for calculating wind deflection,
        a signed value isn't necessary. Also, since deflection is  linear
        with  wind  speed, leaving the value set for the default  10  mph
        allows for easy interpolation at the range.

        G. Velocities
             Muzzle velocities of most factory ammunition can be found in
        periodicals  such  as the SHOOTER'S BIBLE. Those who  reload  are
        aware  that estimated or reported velocities are  usually  listed
        with the loading data for a particular cartridge.
             The most effective way to find the velocity for a completely
        unknown  load is, of course, the chronograph. Unfortunately,  few
        people  have access to one and their price puts them  beyond  the
        reach of the casual buyer. (The author once built an  inexpensive
        attachment  that allowed a Commodore-64 home computer to be  used


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 13




        as  a simple chronograph, but its usefulness was limited since  a
        source of house current was still needed nearby... also, the C-64
        isn't exactly portable. The technique SHOULD be adaptable to many
        other home computers and the author would be happy to discuss the
        project with registered users.) Ackley, in his book HANDBOOK  FOR
        SHOOTERS  AND RELOADERS, describes a simple "ballistic  pendulum"
        that  can be used to estimate projectile velocities. No  external
        power is necessary; it relies on the kinetic energy of the bullet
        to swing a heavy mass.

















































        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 14






        5.  USING GENTABLE AND READTABLE

        A. Using the pre-programmed functions
             Before  running  BALLISTIC for the first time  a  file  con-
        taining  the chosen set of function values the program  will  use
        during  its calculations must be produced. GENTABLE Version  3.00
        makes the following functions available:

                 FUNCTION           VELOCITY         ATMOSPHERIC
                                   max.   min.     temp.  pressure
             British 1909          4000    0        59      29.53
             "G1"                  4094   300       59      29.53
             Ingalls'              3600    0        60      30.00
             Ingalls' (extended)   4094    0        60      30.00

             The  British  1909 and Ingalls'  functions  are  practically
        identical until low velocities are reached. Both are well  suited
        to  calculations  involving typical hunting  or  pistol  bullets,
        i.e.,  rounded or slightly pointed (roughly two  caliber  radius)
        spitzers. Results for sharply pointed spitzers and boattails will
        not  be  as accurate with these functions as they might  be  with
        some others. Less accurate results will also be obtained if  bal-
        listic coefficients calculated with one set of functions are used
        with  another, i.e., using the coefficients listed in Appendix  C
        (calculated with Ingalls' table) with the British 1909 tables.
             The  extended  Ingalls' table is simply the  standard  table
        continued to the maximum allowable program velocity following the
        method  used in Hatcher. As values above 3600  are  extrapolated,
        they may not be as accurate as those below.
             Many  of the companies producing reloading  components  feel
        that the G1 table is the best choice for all around use.  Indeed,
        most  of  the major ammunition manufacturers seem to use  the  G1
        drag function for calculating their own "factory" ballistics  and
        duplication  of  these tables is most easily  accomplished  using
        this selection. This function is used by SAAMI in calculating the
        tables they supply to the manufacturers as well.
             GENTABLE is started by typing its name (BAL-GEN) at the  DOS
        prompt, optionally following it with a command line argument. The
        user will be presented with a short menu to which he should  res-
        pond with the number of the function he desires. The program will
        next  prompt for a filename to contain the new data, then  create
        the  table, overwriting any previous file with that  name.  Users
        that  plan to routinely use more than one table  should  probably
        create  them all ahead of time, renaming them to  something  more
        descriptive. Copy the one used most often to BALISTIC.TAB.
             GENTABLE will accept only one argument on the command  line.
        If the flag "-BIOS" is used all video output will be sent to  the
        screen via BIOS calls. The default is to write directly to screen
        memory.

        B. Creating custom function tables
             The  user is not limited to using the functions produced  by
        GENTABLE. Tables may be produced by any program or language  that
        stores  numbers  in IEEE format, including Microsoft  C  v5.0  or


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 15




        Quick  C.  (There will be a problem  calculating  checksums  when
        using  Microsoft  5.0 unless the -Op optimization is  used.)  The
        file format and data types used are as follows:

          1.  Truncated  revision number for version of  GENTABLE  used
              multiplied by -1. (int)
          2.  The table name. (char[32])
          3.  Standard temperature for table data. (double)
          4.  Standard pressure for table data. (double)
          5.  Maximum velocity in table (<=4094). (unsigned)
          6.  Minimum velocity in table. (unsigned)
          7.  S_table, T_table pairs as described in HATCHER'S NOTEBOOK
              for velocities (max >= v >= 0). (float)
          8.  Checksum  calculated  as the sum of (S_table  -  T_table)
              values. (float)

        C. Checking the function file
             After  creating  the  function file  it  may  be  optionally
        checked  with  READTABLE. READTABLE was originally written  as  a
        debugging aid and is included only to satisfy user's curiosity as
        to what is contained in a ballistic function table. It might also
        be of some use to those contemplating creation of their own func-
        tion files. Once started, it prompts the user for the name of the
        function  file to be examined, displays the  header  information,
        then  prints the values to the screen. The speed of  the  display
        may  be altered by pressing either the <-> or <+> keys.  Pressing
        any other key will cause the display to pause at the next  value.
        Once paused, pressing <ESC> causes execution to abort. Any  other
        key will cause the program to resume.
             As  with GENTABLE, READTABLE is started by typing  its  name
        (BAL-READ)  at the DOS prompt, optionally followed by any of  the
        following flags:

            -BIOS - Causes  the program to perform all writes using  BIOS
                 calls. This will significantly slow output.
            -F - (From) - Start listing the table to the screen with  the
                 value  immediately following the argument, i.e.,  -F2000
                 will start the listing at 2000 fps.
            -T - (To) - End the listing at the value following this argu-
                 ment.
            -N - (Noprint) - Don't print the table, calculate the  check-
                 sum only.
            -G - (Graphics) - Don't  use the IBM graphic  character  set.
                 (Use ASCII characters instead.)

             Flags  requiring numeric arguments should NOT have  a  space
        between the flag and input value.











        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 16






                      --==<  B A L L I S T I C  v3.10  >==--
                        (C) Copyright 1988 by W.R. Frenchu




                                  - MAIN MENU -


                    1 ........... Calculate Ballistic Table.
                    2 ..... Calculate Ballistic Coefficient.
                    3 ....... Adjust Atmospheric Conditions.
                    4 ........... Select New Function Table.
                    5 ............. Miscellaneous Functions.
                    6 ........................... DOS Shell.
                    7 .................... Return to System.


                                 Your Choice ? 1



        ---------------------( Fig. 1 - MAIN MENU )----------------------





                      --==<  B A L L I S T I C  v3.10  >==--
                        (C) Copyright 1988 by W.R. Frenchu




                       - CALCULATE BALLISTIC COEFFICIENT -


                                  Please input:
                         Initial velocity ....(fps)  2820
                         Final velocity ......(fps)  2507
                         Range .............(yards)  100
                         Altitude ............(Ft.)  0
                         Temperature ......(Deg. F)  59.0
                         Atmos. Pressure ..(In. Hg)  29.53

                          Effective Bal. Coeff. =  0.288
                           (Bal. Coeff. at STP = 0.288




        -------( Fig 2. - Calculating the Ballistic Coefficient )-------




        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 17






                      --==<  B A L L I S T I C  v3.10  >==--
                        (C) Copyright 1988 by W.R. Frenchu




                          - CALCULATE BALLISTIC TABLE -

                                  Please input:
                      Initial velocity ........(fps)  2820
                      Bullet weight ........(grains)  165
                      Effective Bal. Coeff. ........  0.288
                      Range .................(yards)  500
                      Number of intervals .(10 max.)  10


                                  Chart title ?
         .308 Winchester - 165 gr. Spire pt.



        -----------------( Fig. 3 - MAIN MENU choice 1 )-----------------




                     .308 Winchester - 165 gr. Spire pt.
                          (Calculated using G1 table)

     Bullet weight ......... 165 grains   IPSC Power Factor ..... 465.3
     Cross wind ............ 10.0 m.p.h.  Altitude .............. 0    Ft.
     Atmospheric pressure .. 29.53 in.    Temperature ........... 59.0 F
     Effective Bal. Coeff... 0.288        Bal. Coeff. at STP .... 0.288

    Range  Velocity  Energy   Momentum  Mx. Ht.  Defl.   Drop   Lead   Time
    yards   f.p.s.   ft-lbs   lb.-secs    in.     in.     in.  in/mph  secs
       0     2820    2913.2    2.0661     0.0     0.0     0.0    0.0   0.000
      50     2661    2593.5    1.9494     0.1     0.3     0.6    1.0   0.055
     100     2507    2302.4    1.8368     0.6     1.1     2.4    2.0   0.113
     150     2358    2037.4    1.7278     1.5     2.6     5.5    3.1   0.175
     200     2215    1797.1    1.6228     2.8     4.8    10.3    4.2   0.240
     250     2076    1579.4    1.5213     4.7     7.8    16.8    5.5   0.310
     300     1942    1382.2    1.4231     7.2    11.6    25.3    6.8   0.385
     350     1814    1205.8    1.3292    10.5    16.3    36.2    8.2   0.465
     400     1693    1050.3    1.2406    14.7    22.0    49.7    9.7   0.550
     450     1578     912.5    1.1563    20.0    28.8    66.2   11.3   0.642
     500     1470     791.2    1.0767    26.7    36.7    86.2   13.0   0.741

      1=Print  2=Form Feed  3=Sight table  4=New data  5=Main menu  ? 3

        ------------( Fig. 4 - The completed ballistic table )-----------





        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 18






                      --==<  B A L L I S T I C  v3.10  >==--
                        (C) Copyright 1988 by W.R. Frenchu




                        - ADJUST ATMOSPHERIC CONDITIONS -
                         (Modify ballistic coefficient)

                                  Please input:
                        Bal. Coeff. at STP ........ 0.288
                        Altitude .............(Ft.) 5000
                        Temperature .......(Deg. F) 41.2
                        Atmos. Pressure ...(In. Hg) 25.44
                        Wind Speed ........(M.P.H.) 10.0
                        Angle from Broadside (deg.) 0

                     Effective Ballistic Coefficient = 0.323




        --------( Fig. 5 - Modifying the ballistic coefficient )--------






                      --==<  B A L L I S T I C  v3.10  >==--
                        (C) Copyright 1988 by W.R. Frenchu



                              - CALCULATE RECOIL -

                                  Please input:
                        Initial velocity .....(fps) 2820
                        Weight of gun ........(lbs) 9.50
                        Weight of bullet ..(grains) 165
                        Weight of powder ..(grains) 42.0


                           Recoil Velocity =  9.5 fps
                          Recoil Energy   = 13.4 ft-lbs
                   (Recoil due to bullet =  7.2 ft-lbs or 54%)





        -----------------( Fig. 6 - Recoil calculation )----------------




        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 19






                      --==<  B A L L I S T I C  v3.10  >==--
                        (C) Copyright 1988 by W.R. Frenchu





                         - CALCULATE POINT BLANK RANGE -

                                  Please input:
                     Initial Velocity ............(fps)  2820
                     Sight Height .............(inches)  0.90
                     Max. Dist. from Sight Line ..(in.)  6.00
                     Effective Bal. Coeff. ............  0.288

                  Targeted range for +/-6.00 inch path is 287 yds.
                           Point-blank range is 337 yds.
                          (100 yd. trajectory = +5.0 in.)




        -----------( Fig. 7 - Calculating Point Blank Range )-----------







                      --==<  B A L L I S T I C  v3.10  >==--
                        (C) Copyright 1988 by W.R. Frenchu



                               - CALCULATE TWIST -

                                  Please input:
                        Bullet Diameter ......(in.)  0.308
                        Bullet Length ........(in.)  1.20
                        Greenhill Number ..........  150.0
                        Spec. Gravity of Bullet ...  10.90


                   Slowest twist allowing for stabilization is
                              1 turn in 11.9 inches.






        ------------------( Fig. 8 - Calculating twist )----------------



        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 20




                                   Appendix A
                                    Glossary

        BALLISTICS - The  study of moving projectiles. Commonly, what  is
             meant is "exterior" ballistics, that portion of the bullet's
             flight  between  muzzle and  target.  "Interior"  ballistics
             refers  to  the  portion between primer  ignition  and  free
             flight  and "terminal" ballistics to what happens  when  the
             bullet strikes its target.

        BALLISTIC COEFFICIENT - The  ratio of the sectional density of  a
             projectile to its coefficient of form. A measure of how well
             a  bullet  retains its velocity. Commonly  supplied  by  re-
             loading manufacturers, or it may be derived from their  bal-
             listic tables.

        BULLET - The actual projectile in small arms ammunition. Commonly
             corrupted to mean the entire cartridge.

        BULLET WEIGHT - Weight of the actual projectile. Usually given in
             grains.

        CALIBER - Technically, the diameter of the barrel measured across
             the lands. In practice, the diameter of the bullet.

        CARTRIDGE - Fixed ammunition, including case, powder, primer, and
             bullet, for small arms.

        COEFFICIENT OF FORM - A number relating the ballistic  efficiency
             of  a  given shape to the shape of the  projectile  used  to
             calculate the ballistic table.

        CROSS WIND ANGLE - The  angle  between the wind and line  of  de-
             parture.

        DRIFT - Technically,  the distance a bullet will travel  horizon-
             tally  due to its spin. This effect is usually quite  small,
             amounting to about 7 inches at 1000 yards for a military  M2
             (30-06) cartridge. Often confused with wind deflection.

        DEFLECTION - See wind deflection.

        DROP - The  distance a bullet will fall due to the  influence  of
             gravity.  Measured from the line of departure, not the  line
             of sight.

        ENERGY - Here,  the  kinetic energy of a moving  bullet,  usually
             given  in ft-lbs. Equal to one half the mass of  the  bullet
             multiplied by the square of the velocity.

        F.P.S. - Feet per second. A unit of velocity.

        FT.-LBS. - Foot  pounds.  A unit of energy equal  to  the  effort
             required to raise one pound to a height of one foot.

        GRAINS - A unit of weight equal to 1/7000 of a pound.


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 21





        INGALLS' TABLES - A  set of ballistic tables first calculated  by
             Col.  J. M. Ingalls in 1918. Probably the most  widely  used
             tables  for small arms calculations. Other  tables  commonly
             used include the British tables of 1909, 1929,  Winchester's
             G tables and the Ordnance Department's J table.

        I.H.M.S.A. - International  Handgun  Metallic  Silhouette  Assoc-
             iation.

        I.P.S.C - International Practical Shooting Confederation.

        LEAD - How far ahead of a moving target a shooter must aim to  be
             assured  of hitting it. In BALLISTIC, the lead is  given  in
             inches/m.p.h. of target speed. If the entry in the table  is
             "1.2",  the lead for a target moving at 5  m.p.h.,  (perpen-
             dicular to the bullet's path) would be (5 * 1.2) 6.0 inches.
             Wind speed is NOT taken into account in this calculation.

        LINE OF DEPARTURE - An  imaginary  line formed by  extending  the
             muzzle  of the weapon. It coincides with the  bullet's  path
             only while the bullet is actually in the barrel.

        LINE OF SIGHT - An  imaginary line from the center of the  sights
             to the point of aim. The bullet typically crosses this  line
             only twice; once, a few yards from the muzzle, and again  at
             the targeted distance.

        MAXIMUM HEIGHT - The highest vertical distance above the line  of
             sight attained by a bullet. Sometimes confused with the mid-
             range  trajectory due to the fact that it  typically  occurs
             about  halfway between muzzle and target. Maximum height  is
             usually somewhat higher and later than the MRT.

        M.O.A. - Minute of Angle. Equal to 1/60 of an angular degree.  At
             100 yards, 1 M.O.A. is approximately 1.047 inches.

        MOMENTUM - Equal to the mass of a bullet multiplied by its  velo-
             city.  Indicative  of the striking or knockdown power  of  a
             projectile.

        N.R.A - National  Rifle  Association. If you  shoot,  you  SHOULD
             belong to this organization.

        POINT-BLANK  RANGE - That  range  for  which  the  bullet's  path
             doesn't  vary  from the line of sight by more than  a  given
             amount.

        POWER FACTOR - A  number  used in IPSC competition  to  determine
             whether  a handgun cartridge may be scored as a  "major"  or
             "minor"  caliber. Defined as the bullet weight  (in  grains)
             divided  by 1000 and multiplied by the velocity.  Cartridges
             with  a power factor equal to or greater than 175  are  con-
             sidered "major". Cartridges ranking between 125 and 175  are
             "minor"  and those below 125 are not legal for  IPSC  compe-
             tition.


        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 22





        S.A.A.M.I - Sporting Arms Ammunition Manufacturers Institute.

        SECTIONAL DENSITY - The  weight of a projectile (in  pounds)  di-
             vided by the square of its diameter (in inches).

        SIGHT HEIGHT - The  measured distance between the centerlines  of
             the sights and muzzle of a gun.

        SPECIFIC GRAVITY - The ratio of the mass of a material to that of
             an equal volume of water.

        TARGETED RANGE - That  distance  where  the path  of  the  bullet
             crosses the line of sight. (The "sighting in" distance.)

        TIME OF FLIGHT - The  time necessary for a bullet to travel  from
             the muzzle of a gun to a given range.

        TRAJECTORY - The path of a moving projectile. Here, the number of
             inches above or below the line of sight.

        TWIST - Here,  the rate of twist in the rifling of a gun  barrel.
             The minimum amount of twist necessary to stabilize a  bullet
             in  flight can be determined from its length,  density,  and
             caliber. Usually expressed as "1 turn in xx inches" where xx
             may range from about 8 inches up to over 30. "Faster"  twist
             translates  to  a  smaller  number.  Minimum  twist  is  the
             "slowest" twist that will stabilize a given bullet.

        WIND DEFLECTION - The amount of horizontal motion attributable to
             the action of the wind. Often mistakenly called drift.



























        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 23




                                   Appendix B
                               Information Sources


        BALLISTICS:

             Any intermediate physics (mechanics) text.
             BALLISTICS ON THE HOME COMPUTER. American Rifleman, June
               1983
             BALLISTICS ON YOUR POCKET CALCULATOR. American Rifleman,
               June 1987
             BALLISTIC TABLES AND HOW TO USE THEM. American Rifleman,
               December 1963
             CALCULATING RECOIL. American Rifleman, March 1988
             EXPLORING BALLISTICS WITH YOUR COMPUTER, Byte Magazine
               September 1980
             EXTERIOR BALLISTICS, McShane, Kelly and Reno, University of
               Denver Press, 1953
             HATCHER'S NOTEBOOK, Julian S. Hatcher, Harrisburg: Stackpole
               Books, 1962
             TRAJECTORY COMPUTATION SYSTEM FOR DIGITAL COMPUTER, SAAMI
               publications, 1976


        RELOADING:

             CARTRIDGES OF THE WORLD, J.T. Amber, Northfield: Digest
               Books, 1972
             COMPLETE GUIDE TO HANDLOADING, Philip B. Sharpe, New York:
               Funk & Wagnells Co., 1953
             HORNADY HANDBOOK OF CARTRIDGE RELOADING, RIFLE-PISTOL, Grand
               Island: Hornady Manufacturing Co., 1973
             HANDBOOK FOR SHOOTERS AND RELOADERS, VOL I & II, P.O. Ackley,
               Salt Lake City: Publisher's Press, 1965
             LYMAN RELOADING HANDBOOK #46, Middlefield: Lyman Products
               for Shooters, 1970
             NRA HANDLOADER'S GUIDE, Wash. D.C.: The National Rifle
               Association of America, 1969
             PRINCIPLES AND PRACTICE OF HANDLOADING, Georgetown: Small
               Arms Technical Publishing Co., 1954
             SIERRA BULLETS RELOADING MANUAL, Santa Fe Springs: Sierra
               Bullets, 1971
             SPEER RELOADING MANUAL #10, Lewiston: Speer, Inc., 1979


        ASSOCIATIONS:

             THE NATIONAL RIFLE ASSOCIATION - 1600 Rhode Island Ave. NW,
               Washington, D.C. 20036
             S. A. A. M. I. (SPORTING ARMS AMMUNITION MANUFACTURERS
               INSTITUTE) - PO Box 838, Branford, Conn. 06405







        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 24




                                   Appendix C
                   Ballistic Coefficients for Factory Bullets

             The  coefficients  listed here were calculated  from  tables
        found  in  SHOOTER'S BIBLE No. 75 (1984) using  the  program  and
        Ingalls'  function.  No attempt was made to include  every  load,
        instead, representative loads for each caliber were chosen.


                     Part 1 - Centerfire Pistol and Revolver

             Cartridge      Bullet       Coefficient    Manufacturer
        ================================================================
             .25 ACP        50 FMC          .174            F
             .25 ACP        50 FMC          .097            R,W
             .380 ACP       85 STHP         .105            W
             .380 ACP       90 JHP          .073            F
             .380 ACP       95 FMC          .082            F,R,W
              9 mm          95 JHP          .101            F,R,W
              9 mm         115 FMC          .128            W
              9 mm         115 JHP          .131            R,F
              9 mm         115 STHP         .131            W
              9 mm         123 FMC          .140            F
             .38 SPEC.     110 STHP         .147            W
             .38 SPEC.     148 WC           .062            F,R,W
             .38 SPEC.     158 LRN          .162            F,R,W
             .357 MAG.     110 JHP          .093            F,R,W
             .357 MAG.     125 JHP          .122            F,R,W
             .357 MAG.     158 JSP          .135            F,R,W
             .44 MAG.      180 JHP          .120            F,R
             .44 MAG.      210 STHP         .125            W
             .44 MAG.      220 MCP          .193            F
             .44 MAG.      240 JHP          .156            R
             .44 MAG.      240 LGC          .139            R
             .45 ACP       185 MCWC         .082            R,W
             .45 ACP       185 JHP          .152            F
             .45 ACP       185 STHP         .137            W
             .45 ACP       230 FMC          .165            R,W
             .45 COLT      225 STHP         .167            W
             .45 COLT      225 SWCHP        .172            F
             .45 COLT      250 LRN          .157            R

        ---------------
        ABBREVIATIONS
        Manufacturers: F=Federal, R=Remington, W=Winchester
        Bullets:  FMC=Full  Metal  Case, STHP=Silver  Tip  Hollow  Point,
          JHP=Jacketed  Hollow Point, MCWC=Metal Case Wadcutter,  WC=Wad-
          cutter,  LRN=Lead Round Nose, LGC=Lead Gas Check,  JSP=Jacketed
          Soft Point, MCP=Metal Case Profile, SWCHP=Semiwadcutter  Hollow
          Point








        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 25








                            Part 2 - Centerfire Rifle

             Cartridge      Bullet       Coefficient    Manufacturer
        =================================================================
           .22-250 REM.     55 PSP          .231            F,W
           .22-250 REM.     55 PSP          .253            R
           .223 REM.        55 FMC          .207            R
           .223 REM.        55 FMC          .278            W
           .223 REM.        55 MCBT         .350            F
           .243 WIN.        80 SP           .259            F,R,W
           .243 WIN.       100 PSP          .371            F,R,W
           .270 WIN.       130 PSP          .378            F,W
           .270 WIN.       130 PSP          .345            R
           .270 WIN.       150 SP           .267            F,R
           .270 WIN.       150 PSP          .356            W
            7mm MAUSER     140 PSP          .433            F,R
            7mm MAUSER     175 SP           .280            F,W
            7mm REM.MAG.   150 PSP          .354            F,R,W
            7mm REM.MAG.   175 PSP          .453            F,R,W
           .30 CARBINE     110 FMC          .180            F,W
           .30 CARBINE     110 FMC          .164            R
            30-30 WIN.     150 SP           .221            F,W
            30-30 WIN.     150 SP           .195            R
            30-30 WIN.     170 SP           .259            F,R,W
            30-06          150 PSP          .329            F,R,W
            30-06          180 PSP          .398            F,R,W
            30-06          200 BTSP         .592            F
            30-06          220 SP           .299            R,W
           .300 WIN.MAG.   180 PSP          .462            F,R,W
           .308 WIN.       150 PSP          .323            F,R,W
           .308 WIN.       180 PSP          .390            F,R,W
           .35 REM         200 SP           .193            F,R,W
           .45-70          300 JHP          .302            F,W
           .45-70          405 SP           .269            R

        ---------------
        ABBREVIATIONS
        Manufacturers: F=Federal, R=Remington, W=Winchester
        Bullets:  FMC=Full  Metal Case, PSP=Pointed Soft  Point,  SP=Soft
          Point, BTSP=Boat Tail Soft Point, MCBT=Metal Case Boat Tail














        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 26








                                Part 3 - Rimfire

             Cartridge              Bullet   Coefficient  Manufacturer
        ==================================================================
           .22 LR "VIPER"           36 TC       .110           R
           .22 LR "YELLOW JACKET"   33 TCHP     .101           R
           .22 LR HV                40 LRN      .128           R
           .22 LR HV                36 LHP      .115           R
           .22 LR TARGET            40 LRN      .136           R
           .22 LONG                 29 LRN      .095           R
           .22 SHORT                29 LRN      .098           R
           .22 SHORT                27 LHP      .091           R
           .22 SHORT TARGET         29 LRN      .097           R

           .22 WIN. MAG.            40 JHP      .108           W
           .22 WIN. MAG.            40 FMC      .108           W
           .22 LR "XPEDITER"        29 LHP      .079           W
           .22 LR "H.P."            37 LRN      .117           W
           .22 LR "DYNAPOINT"       40 LDP      .127           W
           .22 LR "T22"             40 LRN      .135           W
           .22 LR                   40 LRN      .127           W
           .22 LONG                 29 LRN      .095           W
           .22 SHORT "H.P."         27 LRN      .091           W
           .22 SHORT "T22"          29 LRN      .097           W
           .22 SHORT                29 LRN      .098           W

           .22 LR "HI POWER"        40 LRN      .126           F
           .22 LR "HI POWER"        38 LHP      .122           F
           .22 LR "CHAMPION"        40 LRN      .135           F
           .22 LONG "HI POWER"      29 LRN      .094           F
           .22 SHORT                29 LRN      .100           F
           .22 SHORT                29 LHP      .092           F

        ---------------
        ABBREVIATIONS
        Manufacturers: F=Federal, R=Remington, W=Winchester
        Bullets:  LRN=Lead  Round Nose, LHP=Lead Hollow  Point,  LDP=Lead
          Dynapoint, FMC=Full Metal Case, TC=Truncated Cone, TCHP=  Trun-
          cated Cone Hollow Point















        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 27




                                   Appendix D
                       Specific Gravities of Bullet Alloys


                        Part 1 - Lead/Tin/Antimony Alloys

           Percent Composition      Specific Gravity      Trade or
           Pb      Sn       Sb         of alloy          Common Name
        =================================================================
          100                           11.340        pure lead
                  100                    7.298        pure tin
                           100           6.62         pure antimony
           30      70                    8.32         soft solder
           37      63                    8.42         eutectic solder
           50      50                    8.89         50-50 solder
           75      10       15           9.73         lead babbit-SAE 14
           80      20                   10.20         20-80 solder
           80       5       15          10.04         alloy 8
           83       2       15          10.09         alloy 10
           85               15          10.28         alloy 11
           85       5       10          10.24         lead babbit-SAE 13
           91                9          10.66         9% antimonial lead
           92                8          10.74         8% antimonial lead
           94                6          10.88         hard lead (bullets)
           95       5                   11.00         5-95 solder
           96                4          11.04         hard lead
           99                1          11.27         1% antimonial lead
                   92        8           7.28         white metal



                             Part 2 -  Other Alloys

                Composition         Specific Gravity      Trade or
                                       of alloy          Common Name
        =================================================================
          100 Cu                         8.96         pure copper
          100 Fe                         7.87         pure iron
           95 Cu, 5 Zn                   8.86         gilding
           90 Cu, 10 Zn                  8.80         commercial bronze
           70 Cu, 30 Zn                  8.53         cartridge brass
           98.75 Cu, 1.25 Sn             8.89         1.25% phos. bronze
           90 Cu, 10 Sn                  8.78         10% phosphor bronze
           97 Cu, 3 Si                   8.53         silicon bronze (A)
           98.5 Cu, 1.5 Si               8.75         silicon bronze (B)
           99.5 Fe,.06 C,.38 Mn,.01 Si   7.87         .06% carbon steel
           99.0 Fe,.23 C,.64 Mn,.11 Si   7.86         .23% carbon steel
           98.7 Fe,.44 C,.69 Mn,.20 Si   7.84         .435% carbon steel


        ---------------
        SOURCES:
        Metals Handbook, Vol. 1, "Properties and Selection of Metals"
          (8th ed.), American Society for Metals
        Metal and Alloys Data Book, Samuel L. Hoyt



        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 28




                                   Appendix E
                             User Supported Software


             User  Supported Software is based on the premise that  if  a
        someone  gets a chance to try out a program, likes it, and  finds
        he uses it on a regular basis, he will voluntarily contribute  to
        the  support of that program. (Where else do you get  the  oppor-
        tunity  to check out a product BEFORE you buy it?) Users are  en-
        couraged to copy and distribute User Supported Software for  non-
        commercial  purposes. Commercial users should be aware  that  the
        author of the program often retains commercial rights.
             BALLISTIC  is being distributed as User Supported  Software.
        If after an initial trial period you find you're using  BALLISTIC
        and  you like it, please send the registration form,  check  (and
        diskette if indicated) to:

                               William R. Frenchu
                               79 Taylor Terrace
                               Hopewell, NJ  08525

             (Please label the diskette with your name and address.)

             Contributors  will receive a copy of the latest revision  of
        the  program,  as well as the TURBO C source code.  In  addition,
        they  will be informed by mail of any major updates  or  improve-
        ments. Major revisions will probably not be undertaken without  a
        positive  user response. If you have any questions,  problems  or
        suggestions  about  the program, (or need support for  a  special
        printer, etc.) please contact the author.
             All  commercial  rights  to BALLISTIC are  reserved  by  the
        author. Anyone wishing to make any commercial use of this program
        (or the tables it produces) is urged to contact the author at the
        above  address. This includes people who use the program  in  any
        commercial  environment. Site and commercial licenses are  avail-
        able at very reasonable rates.
             Non-commercial  users are encouraged to make and  distribute
        as  many UNMODIFIED copies as they like, provided  the  following
        files are included:

                                  BAL-GEN.EXE
                                  BAL-READ.EXE
                                  BAL-READ.ME!
                                  BALISTIC.EXE
                                  BALISTIC.DOC
                                  BALISTIC.REV

             Comments  or  suggestions may be left for the  author  (Bill
        Frenchu) at any of the following places:

                    Bullet 'n Board BBS    (703)-971-4491
                    Road To Utopia BBS     (609)-799-5418 (CoSysop)
                    CompuServe                   74575,61





        BALLISTIC v3.10 - (C) Copyright 1988  W.R. Frenchu         Page 29




                     REGISTRATION FORM FOR BALLISTIC v3.10


        Name _____________________________________   Date _______________

        Mailing Address:

         Street __________________________________   Phone ______________

         City  ________________________  State ___   Zip ________________



        Computer type (& BIOS)________________________ Printer __________

        Display and adapter type ________________________________________


        Where did you get your copy of BALLISTIC? _______________________



        Please register my copy of BALLISTIC and send the latest version
        (as well as the TURBO-C source code) to the above address. (If
        the version being registered IS the latest, the next upgrade will
        be sent at half price.) Check:

         _____ I've enclosed $15.00 and a 5 1/4" DSDD (360k) or 3.5"
               (720k) diskette. (No 1.2 or 1.44 Meg diskettes please!)

         _____ I've enclosed $20.00. Please send  5 1/4"  3.5" (circle)


        The author is always trying to improve BALLISTIC. You can help!

        Comments about BALLISTIC v3.10:




        Comments about the documentation:




        Suggestions for future versions of BALLISTIC:




        Types of shooting you do:







        Mail to: William Frenchu, 79 Taylor Terrace, Hopewell, NJ  08525