Sydex Diskette RPM Test

                                   March 18, 1990

                                Copyright 1990, Sydex
                                153 North Murphy Ave.
                                 Sunnyvale, CA 94086
                               (408) 739-4866 (voice)
                                (408) 738-2860 (FAX)

          This test determines the rotational speed of any  diskette  drive
          connected to the primary,  or only, diskette adapter.  It is non-
          destructive in operation and requires only a  formatted  diskette
          to operate.

          For most DOS applications,  diskette rotation speed is not criti-
          cal, as there is usually plenty of tolerance in the diskette for-
          mat to take up small variations in speed.  However,  when format-
          ting diskettes for use in special applications where the data is-
          more densely packed, a too-fast drive will cause some of the for-
          matting information to be lost.

          Lately,  we've  encountered  a  few  instances  of these too-fast
          drives,  which seem to  be  more  common  among  the  Korean  and
          Taiwanese brands.   If you possess the technical knowledge to ad-
          just the speed of your drive,  then this may be  used  to  verify
          that  you've  done your work correctly.   If not,  this test will
          serve as a tool for selecting a drive that meets your needs.

          Well-adjusted 5.25" 360K and all 3.5"  720K  and  1.44M  diskette
          drives spin at 300 revolutions per minute (RPM).   A high-density
          1.2Mb 5.25" drive and all 8" drives spin at 360 RPM.   It's  much
          preferable  to have a drive that is spinning slightly slow (e.g.,
          296 RPM instead of 300) than to have one which is  slightly  fast
          (e.g. 305 RPM).

          To  verify the speed of a diskette drive,  simply enter this com-
          mand as:

                                       RPM d:

          Where d: is the letter of the drive to be tested.  A running dis-
          play of the current drive speed,  updated approximately twice per
          second will be shown.  To exit, simply press ESCape or remove the
          diskette.


          This program is released for non-commercial general use by Sydex.
          No fee may be charged for it, although a distribution fee, not to
          exceed  $5.00  may be requested to cover the costs of duplication
          and distribution.


                                          1







          Sydex  has  an  expanding  line  of  shareware  storage-managment
          software.  If you're not familiar with our offerings, please take
          the time to investigate them!

               AnaDisk  -- The compleat diskette utility.   Nothing like it
               anywhere else;  scan,  edit,  repair and copy just about any
               kind of diskette.  $25.00 ($150.00 site)  registration fee.

               Con>Format  --  Concurrent  "background" diskette formatter.
               Features  "pop-up"  operation  and  "hot  key"   activation.
               You've  got to see it to believe.   Supports all current DOS
               formats. $15.00 ($50.00 site) registration fee.

               22DISK -- Transfer files, format, examine and erase files on
               "foreign" CP/M diskettes on your PC.   Includes tips on sup-
               porting  8"  and  5.25" single-density diskettes.   Contains
               definitions for over 200 different formats.  $25.00 ($100.00
               site) registration fee.

               22NICE -- A CP/M 2.2 emulation package.   Supports  the  NEC
               V-series  chips  or  performs emulation by software for both
               the 8080 and Z80 processors.   Includes  terminal  emulation
               and  diskette  handling  for common CP/M systems.   Includes
               22DISK.  $40.00 ($150.00 site) registration fee.

               TeleDisk -- Turn any diskette into a  compressed  data  file
               and vice-versa.   Allows you to send and receive entire dis-
               kettes via modem.  Even works with some "copy-protected" dis-
               kettes.  $20.00 ($65.00 site) registration fee.

               COPYQM -- Mass diskette duplicator.  Format, copy and verify
               multiple diskettes from a single  master.    Implements  "no
               keyboard"  interaction  mode and drive "round robin" servic-
               ing.   Supports all standard DOS formats.    $15.00  ($50.00
               site) registration fee.

               FORMATQM  --  Mass diskette formatter - format a box of dis-
               kettes at a single sitting.  Implements "no keyboard" inter-
               action mode and drive "round robin" servicing.  Supports all
               standard DOS formats.   $10.00  ($40.00  site)  registration
               fee.

          Sydex  also offers a line of DOS device drivers to enable a PC to
          read, write and format MS-DOS diskettes from the DEC Rainbow, HP-
          150, Eagle 1600 and Sharp 5641.

          Information on any of these products can be obtained  from  Sydex
          by  calling (408) 739-4866 (voice) or by leaving a request on our
          Bulletin Board System (408) 738-2860 (1200-9600 bps, N81).




                                          2