THE LAST BYTE (tm)


           A DOS Memory Manager for Chips & Technologies Motherboards




                                  Version 1.14

                            Revised: October 24, 1990





                               Copyright (C) 1990
                               All Rights Reserved




                                       by


                              KEY SOFTWARE PRODUCTS
                                440 Ninth Avenue
                          Menlo Park, California 94025
                                 (415) 364-9847













                         Prodigy E-Mail Address: VGDC59A
               E-Mail on Internet, Bitnet, etc: DLEWIS@SCU.BITNET
             CompuServe E-Mail Address: >Internet:DLEWIS@SCU.BITNET




        



        Oct 24, 1990           The LAST BYTE (tm)                       1


        _1_.__I_n_t_r_o_d_u_c_t_i_o_n________ 

        LASTBYTE  is  a  collection  of software that can make up to 384k
        more  memory  available  to  your  286,  386, or 386SX machine by
        taking  advantage  of  those  motherboards  that  use  one of the
        following  memory  controller  chips  manufactured  by  Chips and
        Technologies: 

                82C302 - Used with 386 Systems without a Cache 
                82C307 - Used with 386 Systems with a Cache 
                82C212 - Part of the NEAT Chipset for 286 and 386 
                82C812 - Part of the NEAT Chipset for 386SX 

        LASTBYTE  does  this  by  using  the  384k of high memory (in the
        640k-1MB  range)  that  is  on  your  motherboard  but  which  is
        normally only used for Shadow RAM.  

        With  LASTBYTE,  this  memory  can  also  be  used for TSR's, TSR
        markers   (to   facilitate  TSR  removal),  device  drivers,  DOS
        Buffers,  RAM  disks,  and  Emulated  Expanded Memory rather than
        loading  all  of  these  into  conventional memory (0-640k) where
        they  use  precious  DOS  memory space needed by your application
        programs.   If  you don't have an EGA or VGA, or if you don't use
        graphics,  then  conventional  memory  (available  to application
        programs) can be extended from 640k to as much as 736k.  

        Other  system  requirements:  DOS  3.0  or  higher, 1M or more of
        (physical) memory.  

                              Important Differences

        LASTBYTE  has  five  significant advantages over other DOS Memory
        Managers: 

             o  LASTBYTE  doesn't  require  a  386.   Most other DOS
                memory  managers  won't  work  on  286 systems.  The
                only  hardware required by LASTBYTE is the Chips and
                Technology chipset and 1MB of hardware.  

             o  LASTBYTE   doesn't   use   any  386  protected  mode
                software.   This  means  that  unlike some other DOS
                memory  managers, LASTBYTE works well with Microsoft
                Windows/386 and Windows 3.0.  

             o  LASTBYTE  doesn't require any extended memory (above
                1MB).   Other  DOS memory managers depend on the 386
                processor's  ability  to  remap physical memory from
                above  1MB  into  high  memory,  but  of course that
                memory  is  no  longer available as extended memory.
                LASTBYTE  uses  the  memory you already have sitting
                between 640k and 1Meg.  



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                       2


             o  LASTBYTE,  unlike all other DOS memory managers, can
                use  the  high  memory  addresses that coincide with
                the  Display  Buffer,  Bios  ROM or any adapter that
                you     have    installed.     LASTBYTE    uses    a
                "Bank-Switching"  technique  to use this memory as a
                Ram  Disk,  as  Expanded  Memory,  and  to  hold TSR
                "markers"  to  facilitate  TSR  removal.  This gives
                LASTBYTE  the  unique  ability  to use *ALL* 384k of
                high memory! 

             o  LASTBYTE  does not slow down the performance of your
                computer,   both  because  it  does  not  incur  the
                instruction  execution  inherent  in  386  protected
                mode,  and  because  it  uses  regular  (full-speed)
                memory.    (Some  memory  managers  use  the  actual
                EGA/VGA  graphics  buffer  as  DOS  memory,  but the
                display  buffer memory of some EGA/VGA adapter cards
                can  be  as  much  as  six times slower than regular
                memory.)  


        _2_.__I_n_s_t_a_l_l_a_t_i_o_n________ 

        You  should first install LASTBYTE on a floppy to verify that you
        can boot and operate your PC reliably with LASTBYTE installed: 

             Step 1:  Use  the  FORMAT command with the /S option to
                      prepare a bootable floppy disk.  

             Step 2:  Copy  all  (it's easier) of the LASTBYTE files
                      onto  the  diskette.   (Actually, all you need
                      are  LASTBYTE.SYS,  HIGHDRVR.SYS, HIGHTSR.EXE,
                      HIGHMEM.EXE,    HIGHMARK.EXE,    HIGHUNDO.EXE,
                      CLOCK.EXE, COLS.40, and COLS.80.) 

             Step 3:  Copy  the DOS device driver file ANSI.SYS onto
                      the diskette.  

             Step 4:  Create  a  CONFIG.SYS  file on the floppy that
                      contains the lines: 

                              DEVICE=LASTBYTE.SYS ? 
                              DEVICE=HIGHDRVR.SYS ANSI.SYS 

                      The  "?" in the first line is intentional - it
                      directs  LASTBYTE  to display what it finds in
                      the high memory address space.  







         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                       3



             Step 5:  Create an AUTOEXEC.BAT file on the floppy that
                      contains the lines: 

                              HIGHMARK 
                              HIGHTSR CLOCK 

             Step 6:  Boot from the floppy.  (Note: NEAT chipsets on
                      286  and 386sx motherboards with only 1 Meg of
                      physical  memory provide a setup option to use
                      the  384k  as Extended Memory by relocating it
                      just  above  the  1 Meg boundary.  This option
                      is  incompatible  with  LASTBYTE  and  must be
                      disabled   in  the  CMOS  Setup  Configuration
                      Menu.) 


        If  everything  goes  ok,  you'll  see  a  sign-on box that looks
        something like the following: 

        ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
        º        The Last Byte v1.14f - Licensed for EVALUATION ONLY        º
        º   Copyright (C) 1990, Key Software Products, All Rights Reserved  º
        ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
        º      Memory locations A0000-BFFFF (128k) are VGA Display RAM.     º
        º      Memory locations C0000-C7FFF ( 32k) are ROM Bios Code.       º
        º      Memory locations C8000-CB7FF ( 14k) are Adapter Rom.         º
        º      Memory locations CB800-CBFFF (  2k) are Adapter Ram.         º
        º      Memory locations F0000-FFFFF ( 64k) are ROM Bios Code.       º
        ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
        º Conventional  High-DOS     Bank-Switch   Shadow-Ram     Excluded  º
        º     640k        32k            32k          96k           224k    º
        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        If  your  PC  stops before displaying the entire box shown above,
        or  if  it  fails  to  operate  properly  after  booting, this is
        because  LASTBYTE  failed  to  identify  one  of  your  installed
        adapters  that  uses  some  portion  of  the  high-memory address
        space.   If  this  happens,  you'll  probably  need  to  use  the
        "EXCLUDE="  command  line  option  (discussed  below) to manually
        disable  the  corresponding  region(s) where conflict occurs.  To
        temporarily  get  around this problem, you can manually abort all
        LASTBYTE  device drivers and TSR's by simultaneously holding down
        the  <left  shift>,  <alt>,  and  <ctrl>  keys  during  the  boot
        sequence.  

        After  AUTOEXEC.BAT  is  finished,  you'll  see  the current time
        displayed  in inverse video in the upper left-hand corner of your
        screen.   This  verifies  that HIGHTSR has succesfully loaded the
        CLOCK.EXE  into  high  memory.   You  can verify that ANSI.SYS is
        installed and operating by using the commands: 



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                       4



                TYPE COLS.40 

                        {switches display to 25 rows by 40 columns}, or 

                TYPE COLS.80 

                        {switches display to 25 rows by 80 columns}.  

        (These  commands  will  display garbage on the screen if ANSI.SYS
        has not been installed.) 

        Now  run  HIGHMEM to get a map of high memory.  Depending on what
        adapter  cards  you  have installed, HIGHMEM's output should look
        something like this: 

        HIGHMEM v1.14e (C) Key Software Products 1990.  All Rights Reserved.

        MCB    Address Range   Description     High-DOS Bnk-Swtch  Total  Mark
        ÄÄÄÄ   ÄÄÄÄÄÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄÄÄ ÄÄÄÄÄÄÄ ÄÄÄÄ
        C400 Ú A0000-C3FFF  <Wrap Block>                                
        C402 ÃÄ A0000-A7FFF  VGA Display Ram            [ 32,768]  32,768
        C404 ÃÄ A8000-BFFFF  VGA Display Ram                       98,304
        C406 ÀÄ C0000-C3FFF  Shadow Ram                   16,384   16,384
        C408    C4090-C467F  LASTBYTE.SYS         1,520             1,520
        C468    C4690-C46CF  CLOCK.EXE [Env]         64                64
        C46D    C46E0-C488F  CLOCK.EXE              432               432
        C489    C48A0-C7FDF  ....DOS Free      [ 14,144]           14,144
        C7FE Ú C8000-CBFFF  <Wrap Block>                                
        CC00 ÃÄ C8000-C97FF  Adapter Rom                            6,144
        CC02 ÃÄ C9800-C9FFF  Adapter Ram                            2,048
        CC04 ÀÄ CA000-CBFFF  DOS Unusable                           8,192
        CC06    CC070-CD1EF  ANSI.SYS             4,480             4,480
        CD1F    CD200-CFF9F  ....DOS Free      [ 11,680]           11,680
        CFFE Ú D0000-FFFFF  <Wrap Block>                                
        CFFA ÃÄ D0000-EFFFF  Excluded Block                       131,072
        CFFC ÀÄ F0000-FFFFF  Shadow Ram                   65,536   65,536
                                                ÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄ
                            High Memory In Use:   6,496   81,920  334,176
                            [Free High Memory]:  25,824   32,768   58,592
                                  MCB Overhead:     192      256      448
                                                ÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄ  ÄÄÄÄÄÄÄ
                             Total High Memory:  32,512  114,944  393,216


                         Paging the output of HIGHMEM   

             You  may  use  the  "/Page"  (or simply "/P") option of
             HIGHMEM  to force the output to pause after each screen
             full.  




         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                       5



        This  listing  is  for a PC that has an EGA display adapter and a
        SCSI  hard  disk adapter.  The "Shadow Ram" at C0000-C3FFF is the
        EGA  Bios and the "Adapter Rom" and "Adapter Ram" are on the SCSI
        adapter  card.   The  "DOS Unusable" region exists because of the
        16k  resolution  of the Chips and Technologies memory controller.
        On  a more typical machine (without a SCSI hard disk), the entire
        16k  region  from  C8000-CBFFF  would  be  available  for  device
        drivers and TSR's.  

        The  column  labelled "Bnk-Swtch" shows which entries can be used
        as  Bank-Switch  memory  for Ramdisk, emulated EMS memory, or TSR
        markers.  

        Numbers  enclosed in brackets (e.g., "[ 14,144]") refer to memory
        that  is  available for use.  Once you have licensed your copy of
        LASTBYTE,  the "Excluded Block" shown above would be added to the
        free  High-DOS  memory  pool,  and the second entry labelled "EGA
        Display  Ram"  would  be  added  to  the  free Bank-Switch memory
        pool.   That  means  a  total  of  approximately  160k  of memory
        available  for  device drivers and TSR's and another 128k for Ram
        Disks,  TSR  markers,  or emulated EMS memory.  (Sections 11, 12,
        and  14  explain  how  you  may even be able to increase the 160k
        figure to 224k or even 288k.) 

        The  column  labelled "Mark" is used in conjunction with HIGHMARK
        and  HIGHUNDO.   In  particular,  you  may  have wondered why the
        command  HIGHMARK  was  included in the AUTOEXEC.BAT file.  Since
        it  was  executed  before running HIGHTSR CLOCK, you are now able
        to  remove the clock from memory by simply running HIGHUNDO.  Try
        it! 


        _3_.__C_o_m_m_a_n_d__L_i_n_e__O_p_t_i_o_n_s__F_o_r__L_A_S_T_B_Y_T_E_._S_Y_S____ 

        During  initialization,  LASTBYTE.SYS  scans  high memory looking
        for  Bios  ROMs,  Display  Ram, and Adapter Cards that occupy the
        640k-1M  address  space.   The  unoccupied portion of high memory
        defaults  to  High-DOS  memory  (for  device  drivers and TSR's),
        while  the  occupied  portion defaults to Bank-Switch memory that
        can be made accessible for Ram disks, emulated EMS memory, etc.  

        These  defaults  can  be  modified  by  the  use  of command line
        options.   There  are  four command line options for LASTBYTE.SYS
        (you  may  abbreviate  any  of  these  by  using  only  the first
        letter): 

             DOS (Abbreviated "D") 

                  Forces   a   region  of  high  memory  that  would
                  normally  be used as Bank-Switch memory to be made



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                       6


                  available as High-DOS memory.  

             BSW (Abbreviated "B") 

                  Forces   a   region  of  high  memory  that  would
                  normally  be  used  as  High-DOS memory to be made
                  available as Bank-Switch memory.  

             EXCLUDE (Abbreviated "E") 

                  Forces   a   region  of  high  memory  to  not  be
                  available  either  as  High-DOS  or as Bank-Switch
                  memory.  

             APPEND (Abbreviated "A") 

                  Reserves  a region of high memory for appending to
                  the  end  of  DOS  low (conventional) memory, thus
                  increasing  it  beyond  640k.   The  memory is NOT
                  added   until   it   is   enabled  with  HIGHAPND.
                  Requires  setting  "<base>"  (see  below) to A000,
                  and   "<size>"  to  a  multiple  of  16k.   (Note:
                  "<size>"  is  limited  to  16k  in  the unlicensed
                  version  so  that  some High DOS memory will still
                  be available.) 

             ? (A question mark) 

                  Causes  LASTBYTE.SYS  to display a summary of what
                  it finds in the High Memory address space.  

        The format of the APPEND, DOS, BSW, and EXCLUDE options is: 

                             <keyword>=<base>:<size>

        where  "<base>"  is  a base paragraph (segment) address expressed
        as  four  hexadecimal digits, and "<size>" is kilobytes expressed
        in  decimal.   For  example,  to  force  the  64k  address  range
        starting  at  segment  A000 to be used as Bank-Switch memory, the
        proper option syntax would be: 

                                   BSW=A000:64

        (Examples  of  why this option can be useful are found in Section
        12, "Video Display RAM above 640k".) 

        In  a  similar  manner,  to  force LASTBYTE to use the 32k region
        starting  at  segment  F000 as High-DOS Memory, the proper option
        syntax would be: 

                                   DOS=F000:32



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                       7



        (Examples  of  why this option can be useful are found in Section
        11, "Using the DOS=F000:32 Option with AMI Bios Chips".) 

        There are two restrictions on these options: 

             o  The  base must be exactly 4 hexadecimal digits, must
                lie  at  or  above  A000,  and must be a multiple of
                0080  (2k).   (For  APPEND,  the base must always be
                A000.) 

             o  The  size must be in the range 2-384 kb, and must be
                a multiple of 2.  


        The  reason  for  the  "multiple  of  2 (kb)" requirement is that
        LASTBYTE   tries   to   allocate   memory   in   2k   increments,
        corresponding  to  the  IBM  spec  that  Bios  ROM's are sized in
        multiples  of  2kb.  However, this is somewhat complicated by the
        coarse   16k  resolution  of  the  Chips  and  Technology  memory
        controllers: 

        The  Chips  and  Technologies  memory controller chips divide the
        640k-1M  area into 24 blocks of 16k each.  Each 16k block must be
        either  totally  enabled or disabled.  I.e., if any part of a 16k
        address  space  is  occupied  by  an adapter card, the entire 16k
        block  of memory must be disabled and cannot be made available as
        High  DOS  Memory.   Thus the "DOS=" option restricts "<size>" to
        multiples  of  16,  and  "<base>"  to addresses that begin on 16k
        boundaries.  

        Once  you  are convinced that LASTBYTE is working satisfactorily,
        you  may  copy it to your hard disk and modify the CONFIG.SYS and
        AUTOEXEC.BAT files there accordingly.  


        _4_.__H_I_G_H_M_A_R_K__a_n_d__H_I_G_H_U_N_D_O_:__U_n_l_o_a_d_i_n_g__T_S_R_s__f_r_o_m__M_e_m_o_r_y__ 

        Sometimes  it  can  be  useful  to  remove one or more TSR's from
        memory,  either  because  you  no longer want to use the features
        that  they  provide  or perhaps in order to make room for another
        set of TSR's.  

        In  order to be able to remove a group of TSR's from high memory,
        they  must  be be marked.  To mark them, run HIGHMARK once before
        you  use  HIGHTSR  to  load  the  TSR's.   Then later, simply run
        HIGHUNDO  -  the  mark  and  all  of its assoicated TSR's will be
        removed.  

        HIGHMARK  may  be  executed more than once to establish levels of
        TSR's  to  be removed.  Each execution of HIGHMARK places another



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                       8


        mark  in  memory  with a unique mark number.  Every TSR loaded by
        HIGHTSR   is   automatically  associated  with  the  most  recent
        execution  of  HIGHMARK.   You  can use HIGHMEM to see the marks,
        their  mark  number,  and  the  set  of TSR's associated with the
        mark.   Every  execution  of HIGHUNDO will then remove the set of
        TSR's associated with the most recent HIGHMARK.  

        You  may  specify  a  mark level on the command line of HIGHMARK.
        This  will  cause it to remove all the TSR's and marks whose mark
        number  is  greater  than  or  equal to the number on the command
        line.  


        _5_.__H_I_G_H_I_N_S_T_:__L_o_a_d_i_n_g__S_H_A_R_E_._E_X_E__i_n_t_o__H_i_g_h__M_e_m_o_r_y___ 

        DOS  4 now installs the SHARE program automatically if you have a
        hard  disk which is greater than 32 MB in a single partition.  It
        does  this  without  asking  because  otherwise it is possible to
        corrupt  the  data on the disk when running programs that use the
        old File Control Block (FCB) approach to access files.  

        Unfortunately,  some  internal  parts of DOS still use FCB's!  So
        don't  try to prevent SHARE from being loaded by removing it from
        your  system!  If DOS can't find it, you'll get a warning message
        during  the  boot  saying  that "SHARE should be loaded for large
        media".   You  could  load it during AUTOEXEC.BAT processing, but
        you'll  still  get  the  warning  because the check occurs during
        CONFIG.SYS processing.  

        So  how  can  you  load this TSR into High Memory without getting
        the  warning?   DOS  recently introduced the "INSTALL=" directive
        that  allows  TSR's to be installed during CONFIG.SYS processing.
        Programs  that  Microsoft  suggests  be  loaded  in  this  manner
        include FASTOPEN, KEYB, NLSFUNC, and SHARE.  For example: 

                            INSTALL=C:\DOS\SHARE.EXE

        However,  the  above  command  causes  SHARE to be loaded down in
        Conventional Memory.  To get it into High Memory, use: 

                      INSTALL=HIGHINST.EXE C:\DOS\SHARE.EXE

        HIGHTSR  works  too, but you get an error message about the above
        line  in  CONFIG.SYS.   This  is because the DOS expects the name
        that  immediately  follows  the  equals  sign  to  be  a TSR, and
        anything else (e.g., HIGHTSR) will cause the error message.  

        HIGHINST  is a copy of HIGHTSR that has been modified to be a TSR
        so  that  this  error  message  can  be  avoided.  Since HIGHINST
        itself  is a TSR, a small part of it will remain resident down in
        Conventional Memory, but only 96 bytes.  



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                       9




        _6_.__T_h_e__/_S_I_Z_E__o_p_t_i_o_n__o_f__H_I_G_H_D_R_V_R__H_I_G_H_T_S_R__a_n_d__H_I_G_H_I_N_S_T_ 

        The  amount  of  High-DOS memory required to load a device driver
        or  TSR  (hereafter  called the "load requirement") is the larger
        of  two  amounts:  (1)  the amount required during initialization
        (greater  than  or  equal  to  the  size of the file) and (2) the
        amount required when finally resident.  

        Although  the  final  resident  requirement  of  any  high-loaded
        software  may  be obtained from the HIGHMEM output, remember that
        the  initialization  (and  thus  the  load)  requirement  may  be
        greater than EITHER the file size or the HIGHMEM listing! 

        Most   device   drivers   and   TSR's  require  more  memory  for
        initialization  than  when  resident,  although  there  are a few
        (such   as   SMARTDRV.SYS  and  NANSI.SYS)  which  require  extra
        resident  memory  for  buffers,  etc.  And then there's the weird
        behavior  of  FASTOPEN and MODE that require even more than this!
        (See   section   8,  "Installing  FASTOPEN  and  MODE  into  High
        Memory".)  Thus  the  normal  operation of HIGHDRVR, HIGHTSR, and
        HIGHINST  is  to  use  the  largest free High-DOS memory block to
        load  the  driver since the resident memory requirement cannot be
        determined   until   after  the  software  has  been  loaded  and
        initialized.  

        Unfortunately,  this  can  lead  to  a  less  than optimum use of
        memory.   If  the  memory  requirements were known, then a memory
        block  could  be  selected using a "best fit" strategy; i.e., the
        smallest  free  High-DOS  memory  block  which  is larger than or
        equal  to  the  load  requirement.   This usually results in much
        better utilization of memory.  

        HIGHDRVR,  HIGHTSR, and HIGHINST have a special option /SIZE that
        can be used to report the load requirement: 

                        DEVICE=HIGHDRVR.SYS /SIZE SMARTDRV.SYS 2048 512
                or:     INSTALL=HIGHINST.EXE /SIZE SHARE.EXE
                or:     HIGHTSR /SIZE PRINT.COM /D:PRN

        The  load requirement will then be displayed on the console after
        the  software  has been loaded and initialized.  This information
        can  then be used to specify the value (expressed in bytes) to be
        used  with  the  /SIZE  option  to force a "best fit" allocation.
        For example: 

                        DEVICE=HIGHDRVR.SYS /SIZE:16240 SMARTDRV.SYS 2048 512
                or:     INSTALL=HIGHINST.EXE /SIZE:13616 SHARE.EXE
                or:     HIGHTSR /SIZE:17120 PRINT.COM /D:PRN




         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      10



        _7_.__T_h_e__/_N_O_E_N_V__o_p_t_i_o_n__o_f__H_I_G_H_T_S_R__a_n_d__H_I_G_H_I_N_S_T__ 

        All  programs,  including  TSR's,  are  allocated  two regions of
        memory  when  they  are  loaded:  One is the area for the program
        itself,  and  the  other  is for a copy of the environment.  Most
        TSR's  don't  make  use  of  their environment, and some actually
        release it to the operating system rather than hanging onto it.  

        If  HIGHMEM  finds  an environment block, the corresponding entry
        in  the  "Description"  column will have the name of the TSR that
        it  belongs  to  (such as "CLOCK.EXE") followed by the indication
        "[Env]".    Occassionally,  you  may  see  a  similar  indication
        "[Dat]";  this  is  a  data block explicitly allocated by the TSR
        for some unknown purpose.  


                        TSRs that eliminate their PSP   

             The  authors  of  some  TSR's  attempt to save a little
             extra  memory  by  having  the  TSR  eliminate  its own
             Program  Segment  Prefix  (PSP)  during initialization.
             Doing  so makes it impossible for HIGHTSR, HIGHINST, or
             HIGHMEM   to  identify  the  TSR's  environment  block.
             However,  this  byte-saving mentality will usually mean
             that  the TSR's initialization code also eliminates its
             environment block, so this is rarely a problem.  


        If  you  see  a  block labelled "[Env]" in the output of HIGHMEM,
        then  you can use the following command line option of HIGHTSR or
        HIGHINST to release this memory, even if the TSR didn't: 

                        INSTALL=HIGHINST.EXE /NOENV CLOCK.EXE 
                or:     HIGHTSR /NOENV CLOCK 

        The  /NOENV  (and /SIZE) options must PRECEDE the name of the TSR
        that  is  to  be loaded high by HIGHTSR or HIGHINST.  Case of the
        option is insignificant.  


        _8_.__I_n_s_t_a_l_l_i_n_g__F_A_S_T_O_P_E_N__a_n_d__M_O_D_E__i_n_t_o__H_i_g_h__M_e_m_o_r_y__ 

        The  FASTOPEN and MODE programs that comes with DOS are TSR's and
        as  such  may  be  loaded into high memory with either HIGHTSR or
        HIGHINST.   Once  installed,  each  requires  very little memory,
        something  on  the  order  of 10k or less.  However, neither will
        install  unless  a  LOT  of  memory  is  available,  like  around
        50-90k.   (The  actual requirement depends partly on command line
        options;  you  can  determine  the  requirement  using  the /SIZE
        option of HIGHTSR or HIGHINST.) 



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      11



        The  worst  part  is  that  if  FASTOPEN  fails to install itself
        successfully,  it  doesn't  issue  any  error message - it simply
        doesn't   display   the   normal   "FASTOPEN  installed"  sign-on
        message.   Moral:  Let  FASTOPEN and MODE be the first TSR's that
        are  installed into High Memory in your AUTOEXEC.BAT file so that
        they get access to the maximum amount of memory.  

        The  second  hassle  with  these two TSR's is that they cannot be
        removed  by  using  HIGHMARK and HIGHUNDO.  Evidently they modify
        memory  other  than  that  tracked by the LASTBYTE utilities: the
        interrupt vector table and that memory allocated to them.  


        _9_.__H_I_G_H_D_I_S_K_:__A__R_a_m__D_i_s_k__i_n__B_a_n_k_-_S_w_i_t_c_h__M_e_m_o_r_y__ 

        HIGHDISK.SYS  is  a  device  driver  that  uses  high  memory  to
        implement  a  Ram  Disk.   Bank-Switch Memory is allocated first,
        and  if  that  isn't enough, then High-DOS Memory is allocated to
        satisfy  the total page request.  The device driver itself may be
        loaded   into   high   memory   by  using  HIGHDRVR.SYS  to  load
        HIGHDISK.SYS.  


                            Minimum Requirement      

             The  amount  of  available  Bank-Switch  memory must be
             sufficient  to  hold  the  Ram  Disk's boot sector, one
             copy  of  the FAT, and the directory.  Normally this is
             not  a problem, but may require that HIGHDISK be loaded
             before HIGHEMS3 (or HIGHEMS4).  


        A typical command in CONFIG.SYS might be: 

                        DEVICE=HIGHDRVR.SYS HIGHDISK.SYS

        This  creates  a  RAM  disk  that uses all available High Memory,
        with 32 directory entries and sectors of 128 bytes each.  

        A  command  line option may be used to change the size of the RAM
        disk as in: 

                      DEVICE=HIGHDRVR.SYS HIGHDISK.SYS 100

        This creates a 100k byte RAM disk.  

        Other  command  line  options may be used to change the number of
        bytes per sector and directory entries, as in: 

                   DEVICE=HIGHDRVR.SYS HIGHDISK.SYS 100 256 64



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      12



        This  creates  a  100k  RAM disk with 256 bytes per sector and 64
        root directory entries.  


        _1_0_.__W_i_n_d_o_w_s__3_._0__C_o_m_p_a_t_i_b_i_l_i_t_y______ 

        In  general,  LASTBYTE  has  a  high degree of compatibility with
        Windows  3.0.   However,  if  you  use  the  386 Enhanced Mode of
        Windows 3.0, there are some fine points that need clarification: 


        10.1 Modifying the Windows SYSTEM.INI File     

        On  a 386 or 386sx with Windows 3.0 running in 386 enhanced mode,
        LASTBYTE  and  WINDOWS  will both try to use the high memory area
        between   640k-1M,  thus  creating  a  conflict.   To  avoid  the
        conflict,  you must ask WINDOWS not to use this region.  This can
        be  done  with  a configuration option in the [386Enh] section of
        the Windows SYSTEM.INI file: 

                              EMMExclude=A000-FFFF

        If  you have used the "EXCLUDE" option of LASTBYTE.SYS to disable
        any  region of the high memory, then Windows may be told it is ok
        to  use  that area.  For example, if LASTBYTE is loaded using the
        line: 

                       DEVICE=LASTBYTE.SYS EXCLUDE=D000:64

        then  you may use the following configuration option (in addition
        to the EMMExclude option above) in your SYSTEM.INI file: 

                              EMMInclude=D000-DFFF

        The  EMMInclude  option  will take precedence over the EMMExclude
        option when the two overlap, as above.  


        10.2 HIGHMEM and Windows 386 Enhanced Mode    

        DOS  applications  (such  as HIGHMEM) run from inside Windows 3.0
        are  given  their  own  "virtual" address space of 640k.  Windows
        tells  the  386  processor to map memory references in this space
        to  the  particular  640k  of  physical  memory  which  has  been
        allocated  to the application.  References outside this range are
        considered  invalid  and thus return garbage.  Since HIGHMEM is a
        program  that  inspects memory between 640k-1M, there's no way it
        can  execute  properly  in this context.  Outside of Windows, and
        in  any  mode  other  than 386 Enhanced Mode, HIGHMEM will behave
        normally.  



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      13




        10.3 HIGHDISK and Windows 386 Enhanced Mode    

        HIGHDISK.SYS  also  uses  memory  in  the 640k-1M range and so is
        susceptible  to  the  same  problems  that HIGHMEM experiences as
        discussed  above in Section 10.2.  Outside of Windows, and in any
        mode   other   than  386  Enhanced  Mode,  HIGHDISK  will  behave
        normally.  


        _1_1_.__U_s_i_n_g__t_h_e__D_O_S_=_F_0_0_0_:_3_2__O_p_t_i_o_n__w_i_t_h__A_M_I__B_i_o_s__C_h_i_p_s_ 

        The  64k  region  starting  at paragraph address F000 is the Bios
        ROM.   Many  of the popular 286, 386, and 386sx clones use a Bios
        ROM  developed  by  AMI.   The more recent versions of these ROMs
        devote  the  first  32k  to initialization code that is only used
        during  the  boot  sequence,  and  use  the  second  32k for that
        portion that must remain available at all times.  

        By  the time your PC gets to the point in its boot sequence where
        it  is setting up the device drivers (e.g., when it is installing
        LASTBYTE.SYS),   the   Bios  initialization  code  is  no  longer
        needed.   If  you  have  one  of  these  AMI  Bios chips, you can
        capture  another 32k of high memory by using a DOS=F000:32 option
        (see Section 3, "Command Line Options For LASTBYTE.SYS").  

        Of  course,  whenever  you  press Ctrl-Alt-Del to do a warm boot,
        the  ROM  Bios  initialization  code  needs to be executed again!
        And  that could be a problem since you've effectively disabled it
        with   the   DOS=F000:32   option!    Fortunately,   LASTBYTE.SYS
        intercepts   all   keyboard  input  and  keeps  an  eye  out  for
        Ctrl-Alt-Del.   When it sees the warm boot request, it will force
        a  COLD  BOOT  if  you've  used  the  DOS=F000:32  option.   This
        re-enables  the  entire  64k  Bios ROM so that the initialization
        code  is  reactivated  before  the processor tries to execute it.
        Otherwise a normal warm boot is used.  


                               Keyboard TSRs      

             Some  TSRs intercept the keyboard hardware interrupt 9,
             and  will  jump  directly  into a fixed location in the
             Bios   ROM   where   the   Warm   Boot   code   begins.
             Unfortunately,  this  will bypass LASTBYTE's attempt to
             turn the ROM back on.  








         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      14


        _1_2_.__V_i_d_e_o__D_i_s_p_l_a_y__R_A_M__a_b_o_v_e__6_4_0_k____ 

        In  general,  the  region A0000-BFFFF is the video display buffer
        area.   Various  display  adapters  (MDA, Hercules, CGA, EGA, and
        VGA)  typically  use only a small subset of this space.  LASTBYTE
        automatically  senses  what  kind  of  video  display  adapter is
        installed  and  reserves  that portion of this address space that
        might  POTENTIALLY  be  used  by  the adapter.  You can determine
        where  these  areas  are with the HIGHMEM command or with the "?"
        option on the command line of LASTBYTE.SYS.  

        Theoretically,  neither  the  EGA  or  VGA  should  use  the  32k
        monochrome  region  (B0000-B7FFF),  and only use the 64k graphics
        buffer   (A0000-AFFFF)   in   high-resolution   graphics   modes.
        However,  the  ROM  Bios  of  a few EGA or VGA adapters have been
        known  to  write  into  one  or  more of these areas even if they
        aren't  in  monochrome  or  graphics  mode.   Thus  when LASTBYTE
        detects  an  EGA  or  VGA  adapter,  it  reserves the entire 128k
        display buffer between A0000-BFFFF.  

        If  a Hercules adapter is found, LASTBYTE reserves the entire 64k
        range   B0000-BFFFF   as  Bank-Switch  memory  in  case  Hercules
        graphics  modes are used although only the first 4k of this space
        is used for text modes.  

        Like  the  text-only  mode  of  a  Hercules  card, an MDA adapter
        should  use  only  the  4k  range  B0000-B0FFF,  and clearing the
        screen  with  a  DOS  "CLS"  command  should  erase the screen by
        writing  (only)  in  this  region.  However, the ROM BIOS on some
        clones  assumes  that the MDA display buffer fills a larger (16k)
        region  between  B0000-B3FFF and may write into memory beyond the
        first 4k.  

        Similarly,  the  four  video  text pages of the CGA, EGA, and VGA
        adapters   occupy  only  the  16k  range  B8000-BBFFF,  but  some
        software will write to the second 16k between BC000-BFFFF.  

        Therefore,  if  any  (monochrome)  Display Buffer RAM is found at
        B0000,  LASTBYTE  reserves  the entire 32k range B0000-B7FFF.  If
        any  (CGA,  EGA  or  VGA)  Display  Buffer RAM is found at B8000,
        LASTBYTE reserves the entire 32k range B8000-BFFFF.  

        You  may  choose  to  override these rather conservative defaults
        with  the  "DOS="  command  line  option  as described below.  In
        addition  to  the  constraints  imposed  by your particular video
        display   adapter,   the   16k   resolution   of  the  Chips  and
        Technologies  memory  controller limit what you can do.  For more
        information,  review  the  discussion in Section 3, "Command Line
        Options For LASTBYTE.SYS".  

        The  following  chart  summarizes the conservative approach taken



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      15


        by  LASTBYTE  as  well  as what "DOS=" options you may be able to
        use: 

        Display         Reserved        "DOS="                  "APPEND="
        Adapter         by default      Options                 Options
        -------         -----------     --------                ---------
        Monochrome      B0000-B7FFF     A000:64         or      A000:64
                                        B400:16         and     A000:64

        Hercules        B0000-BFFFF     A000:64         or      A000:64
                                        B400:48 (1)     and     A000:64

        CGA             B8000-BFFFF     A000:96         or      A000:96
                                        BC00:16 (2)     and     A000:96

        EGA and VGA     A0000-BFFFF     A000:64 (1)     or      A000:96
                                        B000:32         and     A000:64
                                        BC00:16 (2,3)   and     A000:96

        VGA Bios Rom    C0000-C7FFF     C600:8 (4)

                  Notes:  (1) Cannot be used with graphics modes.
                          (2) WINDOWS 3.0 may write in this area!
                          (3) May be combined with DOS=B000:32.
                          (4) See section 13, "Video Adapter Bios ROMs"

        _1_3_.__V_i_d_e_o__A_d_a_p_t_e_r__B_i_o_s__R_O_M_s_____ 

        MDA  and CGA use the standard ROM Bios; they have no ROM of their
        own.   Hercules,  EGA,  and  VGA  adapters,  however, incorporate
        their  own  ROM  Bios  chip  right on the adapter card.  LASTBYTE
        successfully  recognizes  these  ROMs,  but has to treat VGA in a
        special manner: 

        The  VGA  adapter  made  by  IBM  has  a  24k  ROM  installed  at
        C0000-C5FFF,  which  means  that  the 8k at C6000-C7FFF should be
        usable.   Although  almost  all  VGA  clones have a ROM signature
        that  indicates  24k,  many of them use the C6000-C7FFF space for
        ROM  Bios  or  RAM  extensions  that  provide  their  "Super VGA"
        features.    In   particular,   the  Video7  and  Paradise  VGA's
        incorporate  their  own  RAM  from C6000-C7FFF.  For this reason,
        when  LASTBYTE  finds  anybody's  VGA  adapter,  it automatically
        assumes that there is a 32k ROM at C0000-C7FFF.  


        _1_4_.__H_I_G_H_A_P_N_D_:__S_t_r_e_t_c_h_i_n_g__C_o_n_v_e_n_t_i_o_n_a_l__M_e_m_o_r_y__b_e_y_o_n_d__6_4_0_k___ 

        HIGHAPND.EXE  is  a  program that can only be used in conjunction
        with  the  "APPEND="  option  of LASTBYTE.SYS.  HIGHAPND.SYS is a
        device  driver  version  of  HIGHAPND.EXE.  Either can be used to
        append  some  of  the  memory that begins at 640k onto the end of



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      16


        DOS  Conventional  (low)  memory  (and  also  to  return later to
        640k).  

        Monochrome  (MDA),  Hercules,  and CGA display adapters don't use
        the  64k  region starting at A000, and so this memory can be used
        to  extend  conventional  memory  from 640k to 704k.  CGA display
        adapters  also  don't  use  the next 32k either, and so CGA users
        may extend conventional memory all the way to 736k.  

        EGA  and  VGA  display adapters have a 64k hi-resolution graphics
        display  buffer  that  is  located  at A000.  This buffer is only
        needed  when you are using only hi-resolution graphics.  When the
        display  is  in either text or low-resolution CGA graphics modes,
        this  memory  is not used, and may be used to extend conventional
        memory.   Since  most  EGA and VGA adapters usually don't use the
        32k  region  at B000, you may even be able to extend conventional
        memory up to 736k.  

        HIGHAPND  will automatically disable any EGA or VGA hi-resolution
        graphics   capability   whenever  conventional  memory  has  been
        extended  beyond  640k.   This  makes  software  that attempts to
        sense  what  type  of display adapter is installed think that you
        have  only  a  CGA  adapter.   Later,  when you need the graphics
        capability,   you   can   disable   the   memory   extension  and
        hi-resolution graphics will be automatically re-enabled.  

        HIGHAPND.SYS can be used during CONFIG.SYS processing: 

                DEVICE=HIGHAPND.SYS ON  {Extends conv. memory beyond 640k}

                DEVICE=HIGHAPND.SYS OFF {Resets conv. memory to 640k}

                Note:   HIGHAPND.SYS may not work properly with some versions
                        of DOS; in such cases, use HIGHAPND.EXE instead.

        or  HIGHAPND.EXE can be used during AUTOEXEC.BAT processing or at
        any time after the computer is booted: 

                A>HIGHAPND ON   {Extends conv. memory beyond 640k}

                A>HIGHAPND OFF  {Resets conv. memory to 640k}

                Note:   HIGHAPND.EXE may not work properly with DR DOS;
                        in such cases, use HIGHAPND.SYS instead.

        HIGHAPND  (or  HIGHMEM)  can  be  used  without  any command line
        options  to determine the current size of conventional memory and
        the state of EGA/VGA hi-resolution graphics: 

                A>HIGHAPND 




         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      17


        You  can  put  these  commands  into  a  batch  file  to simplify
        switching  back  and  forth.   For example, if you want the extra
        memory  all  the  time  except  when you need hi-res graphics for
        WINDOWS, create a batch file like the following to run windows: 

                @ECHO OFF 
                HIGHAPND OFF 
                WIN %1 %2 
                HIGHAPND ON 

        If  you  have  hi-res  graphics  disabled  and run a program that
        tries  to use hi-res graphics without first sensing for an EGA or
        VGA  adapter,  LASTBYTE  will notice the conflict, issue an error
        message,  and  terminate  the  program.  Some programs redirect a
        few  interrupts during their initialization and then restore them
        before  termination.  LASTBYTE's termination of graphics programs
        doesn't  know  how  to restore these interrupts, so in some cases
        you  may  have  to  reboot  the computer.  In other words, if you
        experience  this  kind of program termination with an application
        program,  it's  best  to prepare a batch file (as shown above) to
        run the program.  

                                      Notes

             o  The  use  of  HIGHAPND.EXE  requires  the  use of an
                APPEND=A000:??   option   on  the  LASTBYTE  command
                line.  

             o  There  is  no  benefit to using HIGHDRVR.SYS to load
                HIGHAPND.SYS  into  high  memory  because  it  never
                stays resident.  


        _1_5_.__U_s_i_n_g__T_h_e__L_a_s_t__B_y_t_e__w_i_t_h__E_x_p_a_n_d_e_d__M_e_m_o_r_y__ 

        Expanded  memory always has an associated device driver.  If that
        driver  is loaded before LASTBYTE.SYS in the CONFIG.SYS file (and
        if  the  hardware is enabled) LASTBYTE will recognize the 64k EMM
        Page  Frame  of  the  expanded  memory and do the right thing: It
        will  treat the Page Frame like any other Adapter Ram and disable
        the  motherboard RAM that falls in the same address space so that
        it  doesn't  interfere  with the Page Frame.  For example, if the
        EMM  driver  is  loaded first (as described above), LASTBYTE will
        report the 64k EMM Page Frame as "EMS Page Frame".  

        This  works  fine,  of  course,  but loading the EMM driver first
        precludes  the  possibility  of  loading it into High Memory.  To
        get  the  EMM  driver  in  to  High  Memory means that it must be
        loaded after LASTBYTE.SYS, but you must be careful! 

        If   LASTBYTE.SYS  is  loaded  first,  the  Page  Frame  will  be



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      18


        recognized  only  in  two  cases:  (1) The Page Frame used by the
        Expanded  Memory controller built into the Chips and Technologies
        NEAT  chipsets  will  be  recognized  and  reported  as "EMS Page
        Frame".   (2)  The  Page Frame of a REAL expanded memory board is
        (if  enabled)  recognized  and  reported  as  "Adapter  RAM".  In
        either case, LASTBYTE will not use that memory space.  


                           Recognizing EMS Boards     

             Some  EMS boards must be enabled by their device driver
             before   they   respond  as  read/write  memory.   This
             prevents  LASTBYTE  from recognizing them, and you will
             have  to  use  a  "BSW="  option  to keep LASTBYTE from
             using the Page Frame memory space.  


        If  you  don't  have  an  expanded  memory board, but have used a
        device  driver  (like  EMM386.SYS)  that EMULATES expanded memory
        using  extended memory, then LASTBYTE.SYS will not know about the
        page  frame unless the emulator is loaded first.  If LASTBYTE.SYS
        is  loaded  first,  then  you must use a "EXCLUDE=" (not "BSW="!)
        command  line  option  of  LASTBYTE.SYS  to  reserve a 64k region
        where  the  emulated  Page  Frame  can  be placed.  (Do NOT use a
        corresponding  EMMInclude  option  in  the SYSTEM.INI file.)  For
        EMM386.SYS,  this  64k region must lie at C000, C400, C800, CC00,
        D000, D400, D800, DC00, or E000.  


        _1_6_.__H_I_G_H_E_M_S_:__E_m_u_l_a_t_i_n_g__E_x_p_a_n_d_e_d__M_e_m_o_r_y__w_/_B_a_n_k_-_S_w_i_t_c_h__M_e_m_o_r_y___ 

        Two  Expanded  Memory Emulators are provided with LASTBYTE.  Both
        use  high  memory  as Expanded Memory.  HIGHEMS3.SYS is compliant
        with  the older LIM 3.2 spec, and HIGHEMS4.SYS with the newer LIM
        4.0  spec.   Both  are  included  since the HIGHEMS3.SYS requires
        much   less   memory   for   the   device   driver   itself  than
        HIGHEMS4.SYS.   In  many  applications,  you may find that 3.2 is
        all you need.  

        These  device  drivers  EMULATE Expanded Memory!  That means that
        they  use  software  to  copy  data  back  and  forth between the
        logical  EMS  memory (pages) and the Page Frame.  Obviously, this
        is  MUCH  slower  than  the  performance  you  would realize with
        hardware  support,  or  even  with  EMM386.SYS.  Therefore, these
        device  drivers  are  provided for those who have no other way of
        providing  EMS  memory  to their applications, such as users with
        only 1Meg of memory.  

        Both  HIGHEMS3.SYS and HIGHEMS4.SYS have an optional command line
        parameter  which  is the number of 16k EMS pages to allocate.  If
        omitted,  the  maximum  allocation  will  be  used.   Bank-Switch



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      19


        Memory  is  allocated first, and if that isn't enough, then other
        High Memory is allocated to satisfy the total page request.  

        Use  only  one  of  these  device  drivers,  and  load  it  AFTER
        LASTBYTE.SYS.   The  driver itself may be loaded into high memory
        using HIGHDRVR.SYS.  


                                Suggestion       

             On  a  machine  with no expanded memory, you might want
             to  use  HIGHEMS3  to  provide some Expanded Memory for
             Charles  Lazo's scroll-back TSR, WAS.COM.  This utility
             saves  lines  of  text  that have been scrolled off the
             top  of  the  screen  and  allows you to pull them back
             down  for  review.   WAS  is available from a number of
             BBS's,   usually   under  the  filename  WAS050.ZIP  or
             WAS050.ARC.  


        _1_7_.__F_i_n_e_-_T_u_n_i_n_g__y_o_u_r__A_d_a_p_t_e_r__H_a_r_d_w_a_r_e__C_o_n_f_i_g_u_r_a_t_i_o_n____ 

        Many  adapter  cards occupy some portion of the 640k-1Meg address
        space.   Some  of  these  cards,  such  as SCSI Disk Controllers,
        often  have  DIP  switches or jumpers that can be used to set the
        address space they occupy to one of a few chioces.  

        If  the memory map displayed by HIGHMEM is fragmented because one
        of  these adapters sits between two "....DOS Free" areas, you may
        want  to  try  to  reposition  the address space occupied by that
        adapter  by  modifying  the  DIP switch or jumper settings on the
        card.  

        Having  one  large  free  memory block is better than two smaller
        ones  because TSR's and device drivers almost always require more
        memory  during  initialization  than  once  installed.   In other
        words,  neither of the two smaller blocks may be large enough for
        the installation, but might if they were combined.  


        _1_8_.__U_s_i_n_g__H_I_G_H_U_M_M_._S_Y_S__w_i_t_h__4_D_O_S_____ 

        4DOS  is  a  shareware  replacement for COMMAND.COM.  HIGHUMM.SYS
        may  be  used in conjunction with the DOS device driver HIMEM.SYS
        to  move  the  4DOS  command processor and its master environment
        into  "Upper  Memory  Blocks"  (UMB's)  between 640k and 1M, thus
        reducing  the  amount  of  conventional memory below 640k used by
        4DOS from 3.4k bytes to 256 bytes.  

        First  you  must  be  sure that your CONFIG.SYS file contains the
        following three lines: 



         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      20



                DEVICE=LASTBYTE.SYS {and any LASTBYTE options}
                DEVICE=HIGHDRVR.SYS HIMEM.SYS {and any HIMEM options}
                DEVICE=HIGHDRVR.SYS HIGHUMM.SYS

        Then  you  must  add  a  "SHELL="  line  to  CONFIG.SYS for 4DOS,
        including  the options "/U" (to place the command processor in an
        UMB)  and  "/E:512U" (to place the master environment in an UMB).
        The  value "512" is of course only an example - other environment
        sizes  may  be  specified.   You  may  also want to specify these
        options   for   secondary   shells  in  the  4DSHELL  environment
        variable.  Consult the 4DOS documentation for further details.  

        4DOS  may  be  downloaded from The Future Technology BBS at (617)
        720-3600.  


        _1_9_.__H_I_G_H_B_F_R_S_:__L_o_a_d_i_n_g__D_O_S__B_u_f_f_e_r_s__i_n_t_o__H_i_g_h__M_e_m_o_r_y__ 

        NOTE:  HIGHBFRS  *ONLY*  works  for DOS 3.xx.  It does *NOT* work
        for DOS 4.  

                ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º WARNING!  PLACING DOS BUFFERS IN HIGH MEMORY    º
                º CAN RESULT IN THE LOSS OF DATA.  I.E., IT CAN   º
                º DAMAGE THE DIRECTORY AND FILE ALLOCATION TABLES º
                º OF YOUR DISK.  READ EVERYTHING IN THIS SECTION  º
                º BEFORE CONSIDERING THE USE OF THIS UTILITY.     º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Some  16-bit  adapter  cards  do  not properly decode the address
        lines  within  the narrow time constraints imposed by the Address
        Latch  Enable  (ALE)  signal.   As  a  result,  such  cards  will
        occassionally  respond  to  a  memory  access that is directed at
        some  other  portion  of  the address space.  Thinking that it is
        for  them,  they  force the transfer into 16-bit mode even though
        the  intended  recipient  requires  8-bit  mode,  and  thus cause
        erroneous   data   to   be   transferred  to  the  bytes  in  the
        odd-numbered  addresses.   The most common and damaging occurence
        occurs  during  the  8-bit  DMA  transfers  between a floppy disk
        drive  and  high  memory  near  the  address space occupied by an
        offending  16-bit  adapter  card.   Due  to  organization  of the
        address  signals  on  the AT bus, this phenomena only occurs when
        the  two  address  areas  are within the same 128k region.  There
        are  three  such  regions  in  the high memory area: A0000-BFFFF,
        C0000-DFFFF, and E0000-FFFFF.  

        Evidence  of  this  hardware  problem has been exhibited by other
        memory  managers  that  also offer software to locate DOS buffers
        in high memory.  The problem is NOT unique to LASTBYTE.  




         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      21


        HIGHBFRS  offers  two  solutions to this problem.  The first (and
        preferred  solution)  is to restrict the placement of DOS buffers
        to  particular  128k regions in high memory.  For example, if you
        have  an  offending  16-bit VGA card, you would want to place the
        DOS  buffers  in  only the last 128k region since the VGA display
        buffer  occupies  A0000-AFFFF and B8000-BFFFF and because the VGA
        Bios  Rom  occupies  C0000-C7FFF.  The corresponding command line
        options (explained in more detail later) would be: 

                   HIGHBFRS A000-BFFF=0 C000-DFFF=0 BUFFERS=20

        If  you  have  16-bit  adapter  cards in all three 128k segments,
        then  a  second  (different)  solution  may be both necessary and
        sufficient.   It  intercepts transfers between floppy disk drives
        (an  8-bit  DMA  interface)  and  high  memory, and redirects the
        transfer  through  an  intermediate sector buffer in conventional
        (low)  memory.   Almost  all hard disk controllers use 16-bit CPU
        instructions   to  transfer  data  and  thus  do  not  incur  the
        problem.  The corresponding command line options would be: 

                          HIGHBFRS FLOPPY=1 BUFFERS=20

        To  use  HIGHBFRS,  you  MUST  set "BUFFERS=1" in your CONFIG.SYS
        file.   This  one buffer in Conventional (low) memory is required
        by  the  FLOPPY  option  as the intermediate buffer for transfers
        between floppy disk drives and high memory.  

        The command line options of HIGHBFRS are as follows: 


             BUFFERS=<number> (Abbreviated "B=<number>") 

                  Changes  the  number  of  DOS buffers to the value
                  specified.  (Note:  "<number>"  is  a  number from
                  1-99.) 

             BUFFERS=MAXIMUM (Abbreviated "B=M") 

                  Changes  the  number of DOS buffers to the maximum
                  permitted  by the amount of available unrestricted
                  memory, but no more than the DOS limit of 99.  

             FLOPPY=<switch> (Abbreviated "F=<switch>") 

                  Enables  (1)  or  disables (0) redirection of Bios
                  INT  13h  calls  that  attempt  to  transfer  data
                  between  a  floppy disk drive and high memory.  If
                  redirected,   such   transfers   go   through   an
                  intermediate  buffer located in Conventional (low)
                  memory.  (Note: "<switch>" is either 0 or 1.) 




         Copyright (C) 1990, Key Software Products.  All Rights Reserved



        Oct 24, 1990           The LAST BYTE (tm)                      22


             A000-BFFF=<switch> (Abbreviated "A=<switch>") 
             C000-DFFF=<switch> (Abbreviated "C=<switch>") 
             E000-FFFF=<switch> (Abbreviated "E=<switch>") 

                  where  "<switch>"  is  0  or  1.   Enables  (1) or
                  disables  (0)  the placement of DOS buffers in the
                  corresponding  128k  region  of  the  high  memory
                  address space.  

        All  of these are optional, may be combined at random, and may be
        abbreviated  by  their  first letter (e.g., A=<switch> instead of
        A000-BFFF=<switch>).   The  first  time you run HIGHBFRS, all the
        options   default   to   1  unless  overridden  by  command  line
        arguments.   Each  successive  time HIGHBFRS is run, the defaults
        are whatever the last setting of each option happens to be.  

        When  HIGHBFRS  is  invoked  with  no  command line arguments, it
        simply  reports  the  number  of DOS buffers presently located in
        High  Memory  and  whether  or  not transfers between floppy disk
        drives  and  high memory are redirected.  You may use the HIGHMEM
        program  to  determine where the buffers have been placed in high
        memory.  

        MicroSoft  recommends setting the "BUFFERS=" option in CONFIG.SYS
        according  to  the  type  of  application  most  frequently used.
        Implicit  within  this  recommendation is the assumption that you
        won't  change  the  value  very  often  since it requires editing
        CONFIG.SYS and rebooting.  

        However,  since  HIGHBFRS  allows you to increase or decrease the
        number  of buffers dynamically, you could create some batch files
        to invoke your applications with the optimum number.  

        In  general, more buffers help when running programs that perform
        random  access on a relatively small number of disk records (such
        as  the  index  for a database program), or if your disk has many
        subdirectories organized on several levels.  

















         Copyright (C) 1990, Key Software Products.  All Rights Reserved



                               The LAST BYTE (tm)


                                Table of Contents


        1. Introduction        ....................................    1

        2. Installation        ....................................    2

        3. Command Line Options For LASTBYTE.SYS    ...............    5

        4. HIGHMARK and HIGHUNDO: Unloading TSRs from Memory  .....    7

        5. HIGHINST: Loading SHARE.EXE into High Memory   .........    8

        6. The /SIZE option of HIGHDRVR HIGHTSR and HIGHINST ......    9

        7. The /NOENV option of HIGHTSR and HIGHINST  .............   10

        8. Installing FASTOPEN and MODE into High Memory  .........   10

        9. HIGHDISK: A Ram Disk in Bank-Switch Memory  ............   11

        10. Windows 3.0 Compatibility      ........................   12
           10.1  Modifying the Windows SYSTEM.INI File    .........   12
           10.2  HIGHMEM and Windows 386 Enhanced Mode   ..........   12
           10.3  HIGHDISK and Windows 386 Enhanced Mode   .........   13

        11. Using the DOS=F000:32 Option with AMI Bios Chips ......   13

        12. Video Display RAM above 640k    .......................   13

        13. Video Adapter Bios ROMs     ...........................   15

        14. HIGHAPND: Stretching Conventional Memory beyond 640k      15

        15. Using The Last Byte with Expanded Memory  .............   17

        16. HIGHEMS: Emulating Expanded Memory w/Bank-Switch Memory   18

        17. Fine-Tuning your Adapter Hardware Configuration    ....   19

        18. Using HIGHUMM.SYS with 4DOS     .......................   19

        19. HIGHBFRS: Loading DOS Buffers into High Memory  .......   20











         Copyright (C) 1990, Key Software Products.  All Rights Reserved