ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ Designations claimed as trademark appear in initial capitals or all capitals ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
      (c) Copyright 1989-1990 by F.M. de Monasterio.  All rights reserved.

                                VIz version 3.63
                                ----------------

   SUMMARY

   VIz is a small resident program that accelerates BIOS (and DOS) video input
   and output in text mode; it can be used with IBM-compatible MDA, EGA or VGA
   adapter cards and Hercules HGC and HGC+ cards.  In its present version, VIz
   produces video interference ("snow") in old CGA cards; for such systems you
   can use VIz-CGA, a snow-free, 8088 oriented version.

   In addition, VIz includes an independent, resident component for displaying
   a block cursor, either continously or alternating with a line cursor (at an
   adjustable rate of alternation). The latter display is well suited for easy
   localization of the cursor in some laptop screens.

   Finally, VIz also contains an independent, resident ANSI-filter driver that
   mediates a subset of the ANSI escape sequences to control the console. This
   driver can be used, instead of ANSI.SYS, to implement ANSI escape sequences
   to control video display, with the advantage that can be turned off and on,
   and removed from memory without rebooting.

   All 3 resident modules occupy a total of less than about 1600 bytes of RAM.
   Depending on system configuration and BIOS version, video acceleration by a
   factor of 2 or higher may be expected.

                                ----------------

   GENERAL INFORMATION

   There are 3 basic ways of producing character-oriented, text video displays
   in DOS computers: (1) using direct video memory mapping, which is extremely
   fast but dependent on the video hardware and has a limited portability; (2)
   via BIOS services, provided by the first "hidden" DOS boot file and usually
   augmented by the video adapter, which are not as fast as direct mapping but
   more portable; and (3) via DOS services, provided by the other "hidden" DOS
   boot file and sometimes augmented via installable device drivers, which are
   much slower than the other two approaches, but have greater portability and
   permit additional operations such as redirection.

   Many of the DOS and BIOS video services can be accelerated using a resident
   program that intercepts the calls made to such services, and implements the
   video operation with faster instructions.  Because of the nature of DOS and
   of BIOS services, the interception must occur at the input site of the BIOS
   services (interrupt 10h), whereas it can occur at the input site (interrupt
   21h) or output site (interrupt 29h), or both, of the DOS services.

   VIz is a utility that accelerates many of the basic text video functions and
   permits changing the video mode, page and font of the display as well as the
   raw or cooked mode of DOS video operations; average accelerations are listed
   below for 3 video benchmarks.  When used in EGA/VGA systems, VIz also allows
   to control the red, green and blue mixture that determines the color of each
   of the 16 registers of the EGA/VGA color palette.



   1.  VIDEO ACCELERATION

   VIz installs itself as a resident program that can be invoked repeatedly for
   modification of its parameters, without producing multiple copies on memory;
   the resident accelerator uses less than 900 bytes. To maximize speed of code
   and to minimize resident size, acceleration only occurs for video page 0 (in
   other video pages VIz becomes quiescent and is automatically reawakened by a
   subsequent change to page 0).  The 286 release of VIz is faster than the 086
   release by taking advantage of cpu-specific code that also makes it smaller.
   Both versions require DOS 2.1 or higher.

   The acceleration of VIz can be turned off either by deallocating the program
   with the switch /U (if no other resident has been installed after VIz) or by
   making it quiescent with switch /Q (i.e. it remains resident but not active)
   until reactivation (any switch but /QU) or deallocation by a further call to
   VIz.

   The relative acceleration depends on several factors, including BIOS version
   and date, 80x86 Intel CPU model and speed, and whether or not ROM video BIOS
   is shadowed or remapped to faster RAM. Another factor, often disregarded, is
   the use of other residents also intercepting the interrupt 10h. In addition,
   some memory managers, even when RAM-shadowing video BIOS, have been observed
   to yield non-trivial degradations of video speed. While smaller acceleration
   values may be expected in machines performing a faster BIOS operation (i.e.,
   tighter ROM code, faster CPU, shadowed or remapped ROM), the relative weight
   of the individual factors sometimes results in unexpected results.

   VIz updates relevant parameters in the BIOS data area (segment 40h), such as
   cursor position (page 0 only) and type, video mode, page, and font, that are
   also processed by VIz; while the updating decreases video acceleration time,
   it also decreases the possibility of conflict with foreground utilities that
   use BIOS data but bypass BIOS calls.

   A 16-bit CRC calculation is performed each time VIz is invoked. If it fails,
   the program will abort to DOS; CRC failures indicate corruptions of the code
   and the program therefore should not be used.



   2.  BLOCK-AND-LINE CURSOR ALTERNATION

   To help cursor visualization in screens where the cursor is not easily seen,
   as in some laptop displays, VIz provides a small resident module that allows
   for the display of a (full-)block cursor, either continuously or alternating
   with a line cursor. The alternation rate can be adjusted in steps of 54.9 ms
   between about 0.055 s (/V1) and 5.5 s (/V99).  A zero alternation rate (/V0)
   produces a continously present block cursor. For this module to be loaded in
   memory, VIz must be installed with any /V switch (see below), and it adds an
   additional 100 bytes to the resident size of VIz.

   Very short or very long alternation rates are distracting or hard to follow.
   When selecting a rate for laptop displays, start with a value of n=9 (.50 s)
   or so.

   Block cursor alternation can be turned off by making this resident quiescent
   with the switch /Vd (until its reactivation with /Vn). All cursor operations
   use direct commands to the hardware, and assume register-level compatibility
   with the Motorola 6845 CRT controller. This chip is present in MDA, CGA, and
   HGC cards, while a 6845-compatible CRTC is a custom LSI chip in the IBM-EGA,
   part of the Memory Controller Gate Array on the MCGA, or a part of the Video
   Graphics Array on the VGA.

   Notice that the hardware-controlled blinking of the cursor is not eliminated
   by this service. Hence, depending on the alternation rate selected, a 2-beat
   frequency may be noticeable. For applications requiring complete elimination
   of the hardware-controlled blinking, you can use a utility such as NOBS.EXE,
   which is fully compatible with VIz, and permits controlling cursor shape and
   blinking.



   3.  ANSI-COMPATIBLE VIDEO FILTER

   MS-DOS and IBM PC-DOS files include ANSI.SYS, a console device driver that
   mediates a subset of American National Standards Institute (ANSI) standard
   escape sequences for video functions as well as a supplementary subset for
   keyboard functions (such as key reprogramming).

   VIz has a second, independently installable resident module that implements
   standard ANSI escape sequences to control the console video functions. This
   ANSI-compatible filter uses less than some 700 additional bytes of RAM when
   installed. It can be turned off either by deallocating both of VIz resident
   modules (accelerator and driver) or by making the driver quiescent with the
   switch /A- (until its reactivation with /A+). All video operations use BIOS
   calls.

   This filter does not provide by itself any acceleration of DOS video I/O as
   far as ANSI instructions are concerned.  Its advantages are small size, the
   capability of being switched on or off, and its harmonious working with the
   acceleration module of VIz.


   The ANSI-compatible filter implements the following subset of ANSI 3.64-1979
   standard escape sequences to control console video functions (see your MS/PC
   DOS documentation of ANSI commands):

     A. Selection of the foreground and background colors on a color display or
        the text attributes on a monochrome display system. The sequence syntax
        is <Esc>[#;...;#m, where # is 30-37 to select a foreground color, 40-47
        47 to select a background color, and 0-1, 4-5 or 7-8 to select the text
        attributes.

     B. Selection of the video mode (similar to using the MODE command of DOS).
        The sequence syntax is <Esc>[=#h or <Esc>[=#l, where # is 0-6 or higher
        (depending on the adapter card in use).

     C. Selection of word wrapping, i.e. whether lines longer than the width of
        the screen are truncated. The sequence syntax is <Esc>[?7h or <Esc>[?7l
        to turn word wrapping ON or OFF, respectively.

     D. Cursor positioning for the following sequences:

               <Esc>[r#;c#H  -  Move to specified row (r#) and column (c#)
               <Esc>[r#;c#f  -  Same a previous sequence
               <Esc>[r#A     -  Move cursor up by specified number of rows
               <Esc>[r#B     -  Move cursor down by specified number of rows
               <Esc>[c#C     -  Move forward the specified number of columns
               <Esc>[c#D     -  Move backward the specified number of columns

               <Esc>[s       -  Store current position of the cursor
               <Esc>[u       -  Restore to the position stored by <Esc>[s

               <Esc>[K       -  Erase from the cursor to end of the line
               <Esc>[2J      -  Clear all rows and home cursor (this sequence
                                preserves current color attribute)

   Not supported by the driver are the cursor-position-reporting ANSI sequence
   (<Esc>[r#;c#R), and the supplementary set of sequences used by DOS ANSI.SYS
   that permit keyboard reprogramming (i.e., <Esc>[#;'string';3p) and that are
   not part of the ANSI standard. Thus, you should consider using this driver,
   instead of ANSI.SYS, when interested in using video escape sequences alone,
   without any keyboard remapping.

   To avoid conflicts, VIz will not install its ANSI-compatible driver if DOS'
   ANSI.SYS or another driver with the CON: name is already loaded.  In such a
   case a notice will be displayed in the DOS command line when installing VIz
   and, after its installation, in the status/usage panel that is displayed by
   the command 'VIZ ?Ù'

                                ----------------

   4.  INTERCEPTED INTERRUPTS

   VIz versions 2.40 and higher do not monitor interrupt 1Ah any longer before
   attempting to uninstall the residents.  The following hardware and software
   interrupts are intercepted according to the loading configuration:


   A. Interrupt 8h (system timer):

   Channel 0 of the 8253/8254 timer chip produces a hardware interrupt (IRQ0),
   interrupt 8h, about 18.2 times a second that is used by the system time-of-
   day clock. When the cursor module is installed, switch /Vn (n=0 or 1 to 99)
   forces the display of the block cursor, either in continuous or alternating
   manner. Depending on the VIz version (cf. 4.2), cursor shape is implemented
   via *word* (VIZW.EXE) or *byte* (VIZB.EXE) OUT values.


   B. Interrupt 10h (video BIOS):

   The accelerator module of VIz intercepts the ROM BIOS video interrupt, 10h.
   When the system is in page 0 and a text mode, video acceleration occurs for
   subfunctions 0h through Eh, except for subfunctions 4h, 7h, Bh, and Ch.


   C. Interrupt 21h (DOS services):

   Starting with version 2.0, DOS allows the redirection of the Standard Input
   (StdIn) and Standard Output (StdOut) console device, permitting programs to
   send input to or to receive output from other programs.  Unless redirected,
   the StdIn comes from the keyboard and the StdOut goes to the screen.  These
   and some other devices can be addressed by predefined DOS 'file handles' as
   if they were disk files.  A common DOS-mediated technique to send output to
   the screen is to write to the handle 1 (StdOut) via interrupt 21h, function
   40h; in fact, this is the preferred method of DOS-mediated video output for
   DOS version 2.0 or higher.

   The accelerator module of VIz also intercepts interrupt 21h.  When the ANSI
   filter of VIz is not resident, switch /Z+ redirects to the teletype service
   of VIz the 21h/40h-stream to the console (StdOut), resulting in significant
   video acceleration of internal and external DOS services. This acceleration
   is as fast as or faster than that achieved jointly by switches /R+ and /X+.
   In contrast, switch /Z- (or default installation) does not redirect the 21h
   40h/1 video output.  Switch Z requests are ignored when the ANSI filter has
   been installed, since the DOS output must be filtered by this driver.

   Unlike the effects of switch /X+, the redirection of StdOut to VIz does not
   conflict with the CLS command as this redirection does not affect interrupt
   29h (see section 4.1).  Selection of switch /Z+, however, voids redirection
   of StdOut, including that to the NUL device (e.g., to avoid some messages),
   because the 21h/40h/1-stream is intercepted by VIz before the output can be
   redirected by DOS.


   D. Interrupt 29h (FastTTY):

   The ANSI-compatible driver of VIz intercepts the undocumented interrupt 29h
   (which mediates all the screen output of DOS). Int 29h is normally provided
   by the CONsole device driver installed by DOS and consists of a call to the
   BIOS 'teletype' service of interrupt 10h (subfunction 0Eh).  When a request
   to inactivate the installed ANSI driver is detected (switch /A-), VIz first
   checks if int 29h can be revectored to its original memory address. If this
   revectoring is not possible (i.e. when another resident has also hooked int
   29h), the driver remains partially active in order to handle an ANSI escape
   sequence generated by COMMAND.COM to clear the screen when a CLS command is
   encountered (see below); other ANSI sequences are ignored by the driver and
   passed to the screen via BIOS calls. Hence, if revectoring is possible, /A-
   has the same effect as loading VIz without switch A, except that the memory
   occupied by the ANSI driver is not released; the driver is reactivated by a
   subsequent call to execute VIz with switch /A+.

   When the ANSI filter has not been installed, switch /X+ redirects the video
   stream along int 29h to the 'teletype' function of VIz. In contrast, switch
   /X- (or default installation) does not redirect the stream to VIz, which is
   then processed by the console driver or by any utility revectoring int 29h.
   Switch /X requests are ignored if the ANSI filter has been installed, since
   DOS output must be filtered by this driver. When redirection of int 29h has
   occurred, it can be restored with switch /X- as long as further revectoring
   of this interrupt has not taken place.  Switch /X- is ignored if the vector
   of int 29h does not point to VIz.

   When the int-29h output stream has been redirected to VIz, the CLS command
   will not clear the screen unless a patch is made to COMMAND.COM (see below)
   or the switch /X- is implemented successfully. The reason for this conflict
   is explained below.



   4.1  THE CLS COMMAND AND INTERRUPT 29h

   The internal console device driver installed during booting handles the CLS
   as well as int 29h service. The CLS procedure of COMMAND.COM first tests to
   see if (1) the standard-output handle is associated with a character device
   driver (bit 7=1), and (2) the driver services int 29h (bit 4=1).  If one or
   both tests fail, or if both tests are successful but the vector for int 29h
   does not point to the memory segment of the DOS kernel, COMMAND.COM outputs
   the ANSI escape sequence <Esc>[2J to int 29h; otherwise, it makes a call to
   int 10h, subfunction 6 of the BIOS to clear the screen.

   When int 29h cannot be revectored on /A-, the partial driver activity slows
   down slightly the DOS video output whenever the ASCII character 27 (Esc) is
   found in the character stream. This partial activity is needed, however, as
   DOS issues an ANSI escape sequence to clear the screen whenever int 29h has
   been revectored.  Thus, if VIz were not to retain its ANSI driver partially
   active when revectoring of int 29h is not possible, the DOS escape sequence
   would be displayed (without clearing the screen) whenever a CLS command was
   issued.

   Also, selection of the switch /X+ will produce a failure of the CLS command
   of COMMAND.COM since the accelerator module, which is hooking int 29h, does
   not implement ANSI escape sequences but passes them to the screen (the ANSI
   sequence '[2J' is displayed when CLS is requested).

   If you wish to run VIz with switch /X+ enabled, several alternatives can be
   used to handle the CLS conflict. The first is to use an external utility to
   clear the screen, such as CLR.COM (enclosed in the distribution diskette of
   VIz). The second is to toggle between /X- and /X+ (if possible).  The third
   is to patch COMMAND.COM to make a direct BIOS call to erase the screen; the
   patching only changes 3 bytes and can be easily done with DEBUG as shown in
   the file VIZ.PAT. Keep in mind, however, that /Z+ yields an acceleration of
   DOS output much greater than that of /X+ alone and equal to or greater than
   than of /X+ together with /R+ ('raw' mode--see below).



   4.2  CURSOR POSITIONING

   Cursor position is updated via direct hardware commands.  In release 3.00+,
   these commands can be sent as *word* OUT values (VIZW.COM) or as successive
   *byte* OUT values (VIZB.COM).  The word OUT method of addressing, also used
   by other programs (e.g., Microsoft Windows), yields faster operation but it
   may not work with some clone systems.

   To test which method of addressing you can use, run the program TESTOUT.COM
   and see if the cursor appears at the indicated position. If so, your system
   can handle word OUTs, and you should rename VIZW.COM to VIZ.COM; otherwise,
   rename VIZB.COM to VIZ.COM.

                                ----------------

   5.  USAGE
                       Syntax:  VIZ [/Switches] [;Comments]

   Switches can be given in any order.  (Although shown here as preceded by a
   slash [/] any character between space and slash can be used as a separator
   between switches.)  Switches are not case sensitive.

   Switches /A, /B, /C. /D, /I, /M, /P, /R, and /S are "sticky" parameters in
   the sense that the video change they produce will remain in effect even if
   VIz is made quiescent or is uninstalled.

                                    --------

    [/?]  Syntax/Status.  Switch /? displays the video status and syntax when
     VIz is resident, or syntax only when it is not resident.

     When VIz is resident, the display lists the status of the accelerator (ON
     or OFF), the status of the ANSI-compatible resident (ON, OFF, Not Loaded,
     or ANSI.SYS installed), the status of the DOS 'raw' mode (ON or OFF), the
     redirection of int 29h to VIz by switch /X+, current video mode and video
     page numbers.

     When video modes higher than n+128 (which do not clear the display buffer
     when selected [AT and PS/2]) are detected, the mode number is followed by
     an asterisk.

     When switch /? is requested and a EGA or VGA adapter is present, VIz will
     attempt to read (and save) the contents of the palette registers prior to
     asserting its own attribute palette for the display. For the EGA, this is
     attempted by setting up a 'Parameter Save Area' that the EGA BIOS can use
     to store the contents of the palette registers, and the border (overscan)
     register, so that these contents can be restored upon exiting the Syntax/
     Status panel. If the EGA BIOS fails to store the data, VIz then loads the
     default palette described below in switch /C; the original palette can be
     restored by clearing the screen (if VIz had been installed with switch /C
     enabled) or by resetting the video mode.

                                    --------

    [/Nñ]   Messages dealing with nonfatal operations are either not displayed
     (/N+), as if they were sent to the NUL device, or displayed via the StdOut
     device (/N-), which can be redirected if switch /Z+ has not been selected.
     However, the installing, uninstalling, and fatal-operation messages of VIz
     cannot be redirected and are always displayed. The status of operation can
     be monitored in batch files with ERRORLEVEL commands.  Defaults: /N = /N+.

                                    --------

    [/Q]   Quiescent.  Switch /Q forces VIz to a 'quiet' mode; although still
     resident, VIz will not provide video acceleration.  The overhead time for
     having VIz in quiescent mode is 2% or less of that without VIz. Note that
     even when quiescent or during graphics video mode, VIz still monitors the
     BIOS video interrupt to check for video page or mode change requests.

                                    --------

    [/U]   Uninstall.  Switch /U uninstalls the resident components of VIz if
     the original interrupt vector 10h (and 29h, if the ANSI resident has also
     been installed) has not been changed.  As with any other resident, do not
     uninstall VIz after another resident has been installed since the machine
     is likely to crash.

     Starting with version 2.20, VIz can be identified by its name in memory-
     usage maps. Although VIz removes its own copy of the DOS' environment at
     at loading time (to minimize resident size), 'VIzxxx' will appear in the
     in the listings of these maps irrespective of the actual contents of the
     DOS command line at the time of VIz installation.  For instance, the 286
     version of VIz (accelerator only) will be listed by MAPMEM.COM (of Turbo
     Power Software) as:

            PSP  blks bytes owner    command line        hooked vectors
           ----- ---- ----- -------- ------------------- ---------------
           xxxx   1     880 N/A      VIz363              10 21


   ----------------------------------------------------------------------------
    The following switches are available only in registered 086 & 286 releases
   ----------------------------------------------------------------------------


   * [/Añ]  Installs a resident driver for the video subset of ANSI commands of
     escape sequences.  Installation is aborted if presence of the DOS ANSI.SYS
     is detected. The ANSI resident component, although taking advantage of VIz
     acceleration, is independent of the accelerator resident component and its
     activity can be controlled independently with this switch:

               /A+    Reactivates the resident if installed and inactivated, or
                      installs the ANSI resident.
               /A-    Inactivates the ANSI-driver resident if installed.

     Defaults: /A = /A+

                                    --------

   * [/Bn]  Selects the color for the screen border in text mode and the back-
     ground and border color for graphic modes. This color is specified by the
     Red-Green-Blue mixture value given as 1 or 2-digit number in octal format
     in the range from 0 to 77o (see Switch C below).

     Since the border is notoriously poor in most EGA systems (due to overscan
     properties), switch /B is not likely to produce an acceptable border with
     such systems.  No defaults.

                                    --------

   * [/C]   Allows changes in the EGA/VGA color palette.  This palette, which
     consists of 16 registers, is used map the video memory data into colors.
     In EGA-compatible modes of the VGA and in the EGA, where 16 simultaneous
     colors can be displayed out of a possible 64-color palette, the value in
     each one of such registers determines the amount of Red, Green, and Blue
     mixture in the displayed color.

     This amount can be represented by the data bits <RGBrgb>, where <000rgb>
     shows the color at 33%, <RGB000> at 66%, and <RGBrgb> at 100% intensity.
     These bits (and their resultant color) are shown below using both binary
     (base 1) and octal (base 8) number formats:

      ÚÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ binary  ³ octal ³    Color    ³    Since the binary format takes up a
      ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄ´    lot of space it is more convenient
     ø³ 000 000 ³  00   ³ 100% black  ³    to use the 2-digit octal format to
      ³ 000 001 ³  01   ³  33% blue   ³    represent an RGB value. The binary
      ³ 000 010 ³  02   ³  33% green  ³    equivalence of octal numbers is:
      ³ 000 011 ³  03   ³  33% cyan   ³
      ³ 000 100 ³  04   ³  33% red    ³
      ³ 000 101 ³  05   ³  33% magenta³              0o = 000000b
      ³ 000 110 ³  06   ³  33% yellow ³              1o = 000001b
      ³ 000 111 ³  07   ³  33% white  ³              2o = 000010b
      ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄ´              3o = 000011b
     ø³ 001 000 ³  10   ³  66% blue   ³              4o = 000100b
     ø³ 010 000 ³  20   ³  66% green  ³              5o = 000101b
     ø³ 011 000 ³  30   ³  66% cyan   ³              6o = 000110b
     ø³ 100 000 ³  40   ³  66% red    ³              7o = 000111b
     ø³ 101 000 ³  50   ³  66% magenta³             10o = 001000b
     ø³ 110 000 ³  60   ³  66% yellow ³             11o = 001001b
     ø³ 111 000 ³  70   ³  66% white  ³             12o = 001010b
      ÃÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄ´             13o = 001011b
     ø³ 001 001 ³  11   ³ 100% blue   ³             14o = 001100b
     ø³ 010 010 ³  22   ³ 100% green  ³             15o = 001101b
     ø³ 011 011 ³  33   ³ 100% cyan   ³             16o = 001110b
     ø³ 100 100 ³  44   ³ 100% red    ³             17o = 001111b
     ø³ 101 101 ³  55   ³ 100% magenta³             20o = 010000b
     ø³ 110 110 ³  66   ³ 100% yellow ³                etc
     ø³ 111 111 ³  77   ³ 100% white  ³
      ÀÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
      (ø) IBM-EGA default color palette

     Of course, other colors can also be generated when using a different RGB
     mixture value.  For instance, a desaturated (i.e., whitish) RGB sequence
     is obtained in the octal range 71o through 76o.  Those using the utility
     SPECTRUM.COM (Copyright 1987 Ziff-Davis Publishing Corp.) will recognize
     this <RGBrgb> octal format as the so-called "SPECTRUM code."

     This palette control is also enabled (VIz 2.42+) for VGA monochrome mode
     to remap color codes into 3 monochrome levels.


     The following services are available:

               /Cn:n  To modify the EGA/VGA color palette from the DOS command
                      line, type a 16-number sequence, in which numbers *must*
                      be separated by colons (:) as in the following example:

                         /C07:00:20:30:40:50:01:77:70:11:22:33:44:55:66:76

                      that represents the default palette colors loaded by VIz
                      when switch /C? is used.  When an incomplete sequence is
                      provided, the RGB values are written into the respective
                      palette registers starting from register 0.  When a non-
                      numeric value is provided, the palette is not changed.

                      If you are using a VGA adapter in native monochrome mode
                      (as opposed to MDA or HGC emulation mode) you should use
                      the following /Cn:n call prior to issuing any /C? call:

                         /C00:00:06:06:06:06:06:07:06:07:07:07:07:07:07:07


               /C?    This service provides a display of the palette registers
                      and the corresponding RGB mixture in octal format. It is
                      possible to alter the RGB mixture of any register simply
                      by pressing <R>, <G>, or <B> and then <> or <>.  These
                      arrows cycle through 0%, 33%, 66%, and 100% intensity of
                      the respective RGB component.  The actual RGB mixture of
                      the selection is also shown on a graph.  Press the right
                      or left arrow to cycle through the registers, and <HOME>
                      to go to register 0 or <END> to go to register 15.

                      Press <ENTER> to save the current palette, <ESC> to quit
                      the service without any palette changes, <DEL> to reject
                      any change and to restart the service, and the indicated
                      function keys to load several available palettes.

               /C-    Use to inactivate the implementation of EGA/VGA palette
                      changes via VIz.  The video attributes remain unchanged
                      until the a video operation reloads the palette (e.g. a
                      video mode change).

               /C+    Use to reactivate the implementation of EGA/VGA palette
                      changes via VIz.  It reloads the last color palette that
                      was selected via VIz.

     Defaults: /C = /C+.

     The selected EGA/VGA palette changes are asserted (i.e. the palette is re-
     loaded with the selected RGB values) each time that a video mode change or
     a video font change (int 10h functions 5h and 11h) is requested and VIz is
     active (i.e., no /Q switch, graphics mode, or video page other than 0).

     To preserve the small size of Viz, there is no hotkey pop-up service. If a
     program changes the palette when executed, the RGB mix values selected via
     VIz cannot be asserted except by shelling to DOS and invoking VIz with the
     switch /C+ to reload the palette or triggering a video mode/font change.

                                    --------

   * [/Dn]  Adjusts brightness of screen (VGA card only); the brightness change
     step is specified by the sign and value of number (n) between -63 and +63.
     Use of a high negative or positive number results in an unreadable screen.

     Requesting /D0 results in restoration of the screen to its default setting
     (as dictated by the manual controls of the video monitor).  Defaults: /D =
     = /D+1; /D1 = /D+1.

                                    --------

   * [/F]   If VIZ detects an EGA or VGA adapter, switch /F toggles between 25-
     row (EGA/VGA) and 43-row (EGA) or 50-row (VGA) displays.  (When an EGA/VGA
     adapter is found, VIz also selects the alternate BIOS print-screen service
     to avoid the default ROM-BIOS print-screen routine that works with 25 rows
     only.) In 25-row displays, VIz uses a 8x14 font for EGA or a 9x16 font for
     VGA.  Fonts with more than 25 rows can be loaded only if the current video
     page is between page 0 and 3.  No defaults.

                                    --------

   * [/Iñ]  Toggles blinking (/I-) and intense (/I+) background colors whenever
     the background attribute corresponds to a value between 8 and F (bit 7 on)
     in the selection of screen foreground/background color.  No defaults.

                                    --------

   * [/Mn]   Selects the video mode specified by a number (n) in the range of 0
     through 19; note that there is no checking that the selected mode is valid
     for the adapter.  No defaults.

                                    --------

   * [/Pn]   Selects the video page specified by a number (n) in the range of 0
     to 7 for EGA/VGA with 25-row font, or 0 to 3 for CGA and 43/50-row EGA/VGA
     adapter.  No defaults.

                                    --------

   * [/Rñ]  Force character device to 'raw' mode [R+] or normal ('cooked') mode
     [R-].  In 'raw' mode, DOS does not filter the character stream for control
     codes; tab characters (ASCII 9) present in the stream are not expanded. In
     normal mode DOS inspects each character for special or control codes, such
     as Ctrl-C.  (DOS-mediated video output is faster in 'raw' mode by a factor
     of about 1.40, depending on the DOS version.)  No defaults.

     NOTE:   When using 'raw' DOS mode as the default condition, be sure to set
             BREAK=ON in the CONFIG.SYS file to facilitate Ctrl-Break detection
             by DOS in IBM-compatible machines.

     Some utilities set the DOS mode to 'raw' when executed and then change the
     mode to 'cooked' when they finish, irrespective of the setting encountered
     when they were loaded. Thus, repeated use of switch /R may be necessary to
     maintain the 'raw' mode.

                                    --------

   * [/Sñ]  Inactivates [S-] or reactivates [S+] the BIOS Print Screen function
     triggered by pressing the <PrtSc> key. This is useful when the keys of the
     number pad are used often, and the chance of triggering an unwanted screen
     printing is commensurably high.  No defaults.


                                    --------

   * [/V]   Forces a cursor display of an alternating full block and thin line
     [Vn, n=1 to 99], a continuous full block [Vn, n=0], or the default cursor
     shape [Vd], or makes the cursor invisible [V-]. The switch /Vn produces a
     permanent but reversible change in cursor shape, while the effects of /V-
     remain in effect only during the operation of a batch file.  Defaults: /V
     = /Vd.

     NOTE: The cursor resident component is not loaded unless VIz is installed
           with the switch /Vd or /Vn, and cannot be loaded after installation
           of the resident.

                                    --------

   * [/Xñ]  Directs the DOS video output to the "fast" CON display service (the
     undocumented interrupt 29h supported by the console driver) [X-] or to VIz
     accelerator module [X+] when the ANSI driver is not installed. If the ANSI
     driver is installed, this switch is ignored.

     Selection of "/X+" also selects "/Z-" to insure a DOS-mediated processing
     for the StdOut device (to use both switches, use the sequence "/X+ /Z+").
     See above for conflict with the CLS command.  Defaults: Null or /X = /X-.

                                    --------

   * [/Zñ]  Directs video output mediated via interrupt 21h, fn. 40h (write to
     device [StdOut]) to the console driver [Z-], or to the accelerator module
     of VIz [Z+] if the ANSI driver is not installed; when this ANSI driver is
     installed, switch /Z status is ignored. Switch /Z+ provides a significant
     acceleration of video output for DOS-2+ services and many other utilities
     using this function.

     See above for conflicts with StdOut redirection. /Z+ processing uses an 8
     spaces tab expansion (which is the standard expansion used by DOS). This,
     however, conflicts with the 4-spaces expansion used for the DIR/W command
     of DOS.  Defaults: Null or /Z = /Z-.

                                    --------

   Comments may be added in the DOS command line invoking VIz after the desired
   switches.  The comments, which may be useful in clarifying batch files, must
   be preceded by a semicolon (;), and are ignored by VIz.

   NOTE:   Do not use the DOS redirection (<>) and pipe (|) characters in these
           comments as DOS will attempt to implement the implied redirection or
           pipe request.

                                ----------------

   5.1  EXECUTION

|  Starting with VIz version 3.63, the configuration switches can be specified
|  from the DOS command line or, when VIz is executed without any arguments in
|  this command line, via a DOS environment string named VIZ having the format

|                       VIZ=/SWITCH1/SWITCH2..../SWITCHn

|  A maximum of 80 characters after the equal sign is allowed. There cannot be
|  spaces between switches; use slash as a separator. The string can be placed
|  in the DOS environment via the SET command in your AUTOEXEC.BAT file.

|  A recommended use of the environment string is to specify the default /Cn:n
|  configuration (e.g. /C03:00:20:30:40:50:01:77:70:11:22:33:44:55:66:76) that
|  can be restored simply by executing VIz without any arguments after the RBG
|  EGA/VGA palette has been changed.

                                ----------------

   5.2  DOS ERRORLEVEL

   Starting with version 3.10, VIz uses the following operation codes that can
   be tested in a batch file with the ERRORLEVEL command:

                     0 - Successful operation
                     1 - Unknown/bad switch request
                     2 - Invalid Ansi (switch /A) request
                     3 - Invalid video adapter for the request
                     4 - Bad FastDos (switch /X) request
                     5 - Invalid video mode request
                     6 - Invalid video font for adapter and/or page
                     7 - Incomplete color palette list
                     8 - Invalid color palette datum
                     9 - Invalid window fill parameter(s)
                    10 - Invalid video page for adapter and/or font
                    11 - Cannot uninstall resident(s)
                    12 - Invalid cursor (switch /Vn) request
                    13 - Not enough memory for screen displays
                   255 - 286-VIz executed in a non-286/386+ machine
                   255 - CRC failure

                                ----------------

   6.0  INSTALLATION

   It is recommended that VIz be installed before other resident programs also
   using the BIOS video interrupt 10h.  Due to the nature of some of the video
   functions served, VIz often will not daisy chain the interrupt-10h requests
   to residents located down the intercepted interrupt-10h chain. In order for
   these residents to receive interrupt-10h data, they must be installed after
   VIz has been installed; thus, it is convenient to install VIz early in your
   AUTOEXEC.BAT file.

   Keep in mind that the larger the number of additional residents, the slower
   the absolute video acceleration times provided by VIz.  This is because the
   int-10h request has to be processed by each element in the interrupt chain.
   One way to minimize the problem is to install a minimum number of residents
   via the AUTOEXEC.BAT, and only install those residents deemed needed with a
   given task via a batch file that also executes the task program and removes
   the residents upon the completion of the task. (VIz itself may fall in this
   resident category.)

   If you intend to make occasional use of the ANSI-compatible driver, without
   removing the resident ANSI component from memory, VIz may be installed just
   as decribed above.  However, if you want to remove the ANSI component after
   a given ANSI-oriented task, then VIz must be the last resident to have been
   installed prior to such a removal.

   ANSI.SYS should not be installed via the CONFIG.SYS file if you want to use
   the ANSI driver of VIz. Notice that if both ANSI.SYS and VIz are installed,
   and if VIz is switched to a 'fast DOS' mode, /X+ and/or /Z+, ANSI.SYS would
   be unable to process the ANSI escape sequences since most or all DOS output
   would be sent to the accelerator module of VIz.


   6.1  HIGH-DOS MEMORY LOADING

   Registered copies of VIz can be loaded successfully in high memory with a
   286+ memory manager provided there is enough high-DOS memory for the size
|  of VIz plus the additional bytes required by the loading utility. When /?
|  or /C? has been selected, VIz requires an additional 4300 bytes of RAM.

   Note, however, that the unregistered, BBS-downloaded copy is a compressed
   COM file that expands upon loading by a factor of ca. 1.2. The difference
   between the loaded and the directory size may produce conflicts with high
   memory loading utilities that fail to measure the actual size of the file
   being loaded: If there is not enough high-DOS memory to permit expansion,
   but there is enough memory for the nominal directory size, such utilities
   will load the compressed program, whose subsequent expansion is likely to
   overwrite adjacent code and crash the computer.

|  In addition, when the correct size is specified, some high-memory loading
|  programs for 386 systems have been found to become corrupted when loading
|  into high memory compressed files of the type of the unregistered copy of
|  VIz.


   6.2  HIGH-DOS MEMORY UPDATING

   Starting with version 3.40, a high-memory loading utility is not required
   to update the resident component of VIz, when this resident was installed
   in the first megabyte of memory (286+ CPU).  Such updates can be made via
   normal calls from the DOS command line or batch-file calls. This obviates
   a major restriction in using high memory installation, namely the need to
   keep enough free high memory to load an entire program only to update its
   small resident component.


   6.3  HIGH-DOS MEMORY REMOVAL

   When VIz  version 3.50+ has been loaded in high-DOS memory, and switch /U
   is requested from the normal DOS command line (as opposed to requests via
   a high-memory loading utility), confirmation of of the request is needed,
   as some high-memory loading utilities may become corrupted if they do not
   mediate the uninstall request as well.

   Also, when uninstalling VIz via a high-DOS memory utility, some utilities
   warn that the resident installation has failed (on the assumption that a
   resident execution always implies in its installation). Such warnings are
   harmless and may be ignored.

                                ----------------

   7.  BENCHMARKS

   The data were obtained with the utilities HLTEXT.EXE and HLWINDOW.EXE of the
   PC TECH JOURNAL benchmarks 1.0, (c)1988 Ziff Communications Co., BENCH24.EXE
   of the PC MAGAZINE benchmarks 5.0, (c)1989 Ziff-Davis Corp., and VIZMARK.COM
   version 2.00, (c)1990 F.M. de Monasterio. These data represent the mean of 5
   sequential runs of each utility, after the initial run (that was discarded),
   expressed as the factor in accelerating operations relative to the benchmark
   results obtained without a video accelerator.

   The accelerator being tested was installed as the only resident program that
   intercepted the BIOS' video interrupt 10h in a 16-Mhz, 80386 computer with a
   16-bit, nonplanar VGA adapter in its native mode, and a 1984-IBM BIOS, or in
   a 10-Mhz, 8088 computer with an EGA and a 1988-EPSON BIOS. VIz was installed
   in (normal) low-DOS memory. Both machines were run under COMPAQ MS-DOS 3.31,
   the 286- and 086-VIz versions being tested used word OUT addressing, and the
   ROM video BIOS was not remapped to faster RAM in the 80386 machine.

                                    --------

   7.1 RELATIVE ACCELERATION:
                                  16 Mhz-80386 cpu      10 Mhz-8088 cpu
                               ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                               ³    286-VIz 3.63    ³³    086-VIz 3.63    ³
          ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
          ³  Load switches    ³³  Z-X-   X+    Z+   ³³  Z-X-   X+    Z+   ³
          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
          ³- HLTEXT.EXE       ³³                    ³³                    ³
          ³   BIOS scrolling  ³³  2.78  2.78  2.78  ³³  2.69  2.69  2.69  ³
          ³   DOS  scrolling  ³³  2.09  2.38  4.75  ³³  2.23  2.35  3.93  ³
          ³   Misc scrolling  ³³  3.21  3.21  3.21  ³³  1.84  1.84  1.84  ³
          ³   Wind scrolling  ³³  3.55  3.55  3.55  ³³  2.34  2.34  2.34  ³
          ³                   ³³                    ³³                    ³
          ³- HLWINDOW.EXE     ³³  3.56  3.56  3.56  ³³  2.15  2.15  2.15  ³
          ³                   ³³                    ³³                    ³
          ³- BENCH24.EXE      ³³                    ³³                    ³
          ³   TTY no scroll   ³³  5.01  5.01  5.01  ³³ 11.98 11.98 11.98  ³
          ³   TTY scrolling   ³³  3.39  3.39  3.39  ³³  3.97  3.97  3.97  ³
          ³   Direct write    ³³  1.00  1.00  1.00  ³³  1.00  1.00  1.00  ³
          ³                   ³³                    ³³                    ³
          ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
          ³- VIZMARK.COM      ³³                    ³³                    ³
          ³   DOS             ³³  1.90  2.19  9.94  ³³  2.73  2.90 10.15  ³
          ³   CON fast        ³³  3.10  4.41  3.10  ³³  5.45  6.73  5.48  ³
          ³       ANSI        ³³   NA    NA    NA   ³³   NA    NA    NA   ³
          ³                   ³³                    ³³                    ³
          ³   BIOS miscell    ³³  3.65  3.65  3.65  ³³  4.09  4.09  4.09  ³
          ³      no scroll    ³³  5.09  5.09  5.09  ³³ 11.44 11.44 11.44  ³
          ³      w/ scroll    ³³  3.51  3.51  3.51  ³³  4.34  4.34  4.34  ³
          ³   Direct write    ³³  1.00  1.00  1.00  ³³  1.00  1.00  1.00  ³
          ³                   ³³                    ³³                    ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

                                    --------

   7.2  BENCHMARK COMPARISONS (1):

                            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          16 Mhz-80386 cpu  ³  286-VIz  QUICKCRT  PCKSCRN  VSCREEN  THEFAST  ³
                            ³   3.63      (2)       (3)      (4)      (5)    ³
       ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
       ³  Resident size    ³³   880       1456      4592     1040     912    ³
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
       ³  Load switches    ³³    Z+        /F      /A+/Q+    none     none   ³
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
       ³- HLTEXT.EXE       ³³                                                ³
       ³   BIOS scrolling  ³³   2.78      2.65      2.41     1.52     0.96   ³
       ³   DOS  scrolling  ³³   4.75      2.03      1.92     1.38     0.97   ³
       ³   Misc scrolling  ³³   3.21      1.95      2.83     1.91     2.01   ³
       ³   Wind scrolling  ³³   3.55      2.66      2.43     2.52     2.81   ³
       ³                   ³³                                                ³
       ³- HLWINDOW.EXE     ³³   3.56      2.49      2.29     2.38     2.58   ³
       ³                   ³³                                                ³
       ³- BENCH24.EXE      ³³                                                ³
       ³   TTY no scroll   ³³   5.01      4.17      3.33     3.49     0.94   ³
       ³   TTY scrolling   ³³   3.39      3.16      2.74     1.77     0.95   ³
       ³   Direct write    ³³   1.00      1.00      1.00     1.00     1.00   ³
       ³                   ³³                                                ³
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
       ³- VIZMARK.COM      ³³                                                ³
       ³   DOS             ³³   9.94      1.84      1.73     1.57     0.95   ³
       ³   CON fast        ³³   3.10      2.87      2.53     2.07     0.94   ³
       ³       ANSI        ³³    NA        NA        NA       NA       NA    ³
       ³                   ³³                                                ³
       ³   BIOS miscell    ³³   3.65      3.23      2.60     1.70     2.48   ³
       ³      no scroll    ³³   5.09      4.21      3.24     3.65     0.91   ³
       ³      scrolling    ³³   3.51      3.19      2.79     1.87     0.94   ³
       ³   Direct write    ³³   1.00      1.00      1.00     1.00     1.00   ³
       ³                   ³³                                                ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
       ³ Average factor (6)³³   4.29      2.87      2.57     1.98     1.45   ³
       ³ Factor/kbyte   (7)³³   4.99      2.02      0.57     1.95     1.63   ³
       ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

   NOTES:
   (1) Unable to include ZENO.COM version 2.20 in the comparisons because
       its resident teletype service garbled the DOS prompt/command line.
   (2) Copyright 1986 T. Overfield (version 1.00).
   (3) Copyright 1987-89 MultiSoft Corp. (version 1.05).
   (4) Copyright 1985-87 Golden Bow Systems (version 1.06).
   (5) Copyright 1986-87 Soft Programming Service (version 1.04).
   (6) Sum of the relative acceleration factors divided by the 12 tasks.
   (7) Mean video acceleration factor divided by resident size in kbytes
       (1 kbyte = 1024 bytes).  This is an index of the effectiveness of
       the resident code in implementing video acceleration.

                                    --------

   7.3  ANSI FILTER COMPARISONS (asterisks indicate reference values):

                            ÚÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄ¿ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         16 Mhz-80386 cpu   ³DOS CON:³ANSI.SYS³³  286-VIz      ANSI.COM     ³
                            ³   (1)  ³  (2)   ³³   3.63          (3)        ³
       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ÃÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
       ³  Resident size    ³³   NA   ³  1600  ³³ 1648 (4)        2336       ³
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
       ³  Load switches    ³³  none  ³  none  ³³    A+     SLOW/B0  FAST/B0 ³
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
       ³- HLTEXT.EXE       ³³        ³        ³³                            ³
       ³   BIOS scrolling  ³³   **   ³  1.00  ³³   2.78      1.00    1.00   ³
       ³   DOS  scrolling  ³³   **   ³  0.72  ³³   1.83      0.67    1.40   ³
       ³   Misc scrolling  ³³   **   ³  1.00  ³³   3.21      1.00    1.00   ³
       ³   Wind scrolling  ³³   **   ³  1.00  ³³   3.55      1.00    1.00   ³
       ³                   ³³        ³        ³³                            ³
       ³- HLWINDOW.EXE     ³³   **   ³  1.00  ³³   3.56      1.00    1.00   ³
       ³                   ³³        ³        ³³                            ³
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
       ³- VIZMARK.COM      ³³        ³        ³³                            ³
       ³   DOS             ³³   **   ³  0.68  ³³   1.61      0.61    1.22   ³
       ³   CON fast        ³³   **   ³  0.60  ³³   2.18      0.53    1.38   ³
       ³       ANSI        ³³   NA   ³   **   ³³   3.01      0.86    1.87   ³
       ³                   ³³        ³        ³³                            ³
       ³   BIOS miscellan  ³³   **   ³  1.00  ³³   3.65      1.00    1.00   ³
       ³        no scroll  ³³   **   ³  1.00  ³³   5.09      1.00    1.00   ³
       ³        scrolling  ³³   **   ³  1.00  ³³   3.51      1.00    1.00   ³
       ³   Direct write    ³³   **   ³  1.00  ³³   1.00      1.00    1.00   ³
       ³                   ³³        ³        ³³                            ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÙÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

   NOTES:
   (1) ANSI.SYS not installed (DOS video output being handled by the internal
       console device driver 'CON:' of COMPAQ MS-DOS [version 3.31]).
   (2) COMPAQ MS-DOS (version 3.31).
   (3) Copyright 1989 Ziff-Davis Corp., Author: M.J. Mefford (version 1.20).
       Switch /B0 yields the smallest resident size; part of such a resident
       process keyboard reassignment, invalidating size comparisons.
   (4) Includes 880 bytes of the resident accelerator; ANSI resident size is
       768 bytes only.


--------------------------------------------------------------------------------

   REGISTRATION

   These programs and the documentations (the "software") are the copyrighted
   property of FM de Monasterio (the "author"), who provides the software and
   licenses its use.  Neither the title to nor ownership of this software are
   transferred to you by such a license, and both are retained by the author.
   All rights are reserved.

   The software is user-supported; the enclosed release, although lacking the
   options marked by asterisks, is a fully usable program.  You may test this
   release for (in)compatibilities with your system, but after the testing is
   completed you are requested to order a registered release of this software
   from the address below.

   Alternatively, to continue use of this unregistered copy, send to the same
   address a US$5.00 check marked "For Deposit Only," and payable to "Patient
   Care Fund, Children's Hospital" of Washington, DC. Unregistered users that
   donate to the fund will be allowed to register at half fee, if so desired.

   A form to be used to register or upgrade the software is found in the file
   VIZ.REG. Refer all inquiries about the software to:

                                                   FM de Monasterio
                                                   P.O. Box 219
                                                   Cabin John, MD 20818-0219
   LICENSE

   Upon registration you receive a non-exclusive, non-transferable license to
   use the software. Two types of license are available:

   Single User License:
   Upon registration/upgrade you are granted a nontransferable license to use
   the software in a single computer at a time. You may transfer the software
   physically to another computer provided that the software is then not used
   on more than one computer at any time.

   Site/10-Computer License:
   Upon registration/upgrade you are granted a nontransferable license to use
   the software in a single site or a set of sites provided that the software
   is not used in more than ten computers at any time and that such computers
   are located exclusively within the registered site(s).


   UPGRADES

   Within the same major version - Registered software users can upgrade free
   of charge within the same major version (e.g., 2.00 through 2.99)

   Outside the same major version - Registered users can upgrade for half the
   the license fee for a different version of the software.

   To upgrade send a self-addressed stamped diskette mailer with the original
   360 kb diskette to the address above, along with the upgrade form.


   SUPPORT

   Limited technical support is provided to registered users. If you discover
   a problem, please try to replicate it under the same conditions and, then,
   in the absence of other resident programs. (Changes in the order residents
   are installed sometimes solve conflicts.) If the problem can be replicated
   please write at the address above providing:

                - Your name and address.
                - Program version number (see the Syntax/Help panel).
                - Computer model and configuration, and hardware used.
                - A sufficiently detailed description of the problem.
                - A list of resident and nonresident programs in use,
                  and their sequence of loading into memory.

   Messages may also be left at:    The DC Information Exchange BBS (PCBoard)
   ----------------------------     (202) 433-6639 (Sysop: Bill Walsh), 2400+


   INJUNCTIONS

   You may distribute this software via magnetic and/or electronic means, but
   you are specifically prohibited from:

                - Charging fees or asking donations in exchange of or payment
                  for copies of the software.
                - Distributing this software with commercial products without
                  the written permission from the author.
                - Distributing this software via a for-profit organization or
                  group, either alone or with other software.

   The unauthorized copying, decompiling or disassembling of this software is
   prohibited; any other use of this software is prohibited without a written
   permission in advance from the author.


   LIMITED WARRANTY

   The author-copyright owner warrants for a period of thirty (30) days from
   the date of delivery that, under normal use and without any modification,
   the programs substantially conform to the accompanying specifications and
   that the documentation is substantially complete and contains information
   the author deems necessary to use the programs. If, during the thirty-day
   period, a demonstrable defect in the programs, magnetic medium upon which
   they are distributed, or documentation should appear, you may return this
   software for repair or replacement, at the author's option. If the defect
   cannot be repaired, or the software replaced with functionally equivalent
   software, within sixty (60) days of the author's receipt of the defective
   software, then you shall be entitled to a full refund of the license fee,
   but not of the mailing/handling costs described in the registration form.

   All other warranties of any kind, either express or implied,including but
   not limited to the implied warranties of  merchantability and fitness for
   for as a particular purpose, are expressly excluded.

   The author cannot and does not warrant that any function contained in the
   programs will meet your requirements, or that the operation will be error
   free. The entire risk as to the software performance or quality, or both,
   is solely with the user, and not with the author.


   LIMITATIONS OF REMEDIES

   You assume responsibility for the selection of the program to achieve your
   intended results, and for the installation, use, and results obtained from
   the software.

   The author makes no warranty, either implied or expressed, including with-
   out limitation any warranty with respect to this software documented here,
   its quality, performance, or fitness for a particular purpose. In no event
   shall the author be liable to you for damages, whether direct or indirect,
   incidental, special, or consequential arising out the use of or any defect
   in the software, even if the author has been advised of the possibility of
   such damages, or for any claim by any other party.

   The author's entire liability, and your exclusive remedy shall be: (1) the
   replacement of an original software diskette not meeting the above Limited
   Warranty and which is returned to the author along with proof of purchase,
   or (2), if the author is unable to deliver a replacement diskette which is
   free of defects, you may terminate the License Agreement by returning this
   software and the corresponding license fee will be returned.


   GENERAL

   By using the software, you acknowledge (1) to have read and understood all
   parts of this document and (2) to have agreed with and accepted all of its
   provisions without any reservation.

--------------------------------------------------------------------------------
[END]