WHATPORT.COM 
 
                           Version 3.8 
                         December 8, 1990 
 
                For detecting installed serial ports, 
             type of mouse, and potential IRQ conflicts
 
            Copyright 1989, 1990 Life Sciences Software 
                         812 Vista Drive 
                     Camano, Washington 98292 
 
 
AUTHOR:  Pete Petrakis (CIS 76555,1175)

 
IMPROVEMENTS IN THIS VERSION:

    Version 3.8 of WhatPort is essentially identical to version 3.7.
    It's just smaller and the screen and document reflect my change
    of address.  This version and its predecessor correct a flaw in
    version 3.6 that prevented detection of COM4 on a PS/2 system.
    Versions prior to 3.7 should therefore be discarded.  I thank
    Jim Luhman for testing the corrected program on a PS/2 with four
    COM ports installed and verifying that it can detect them all.

 
DESCRIPTION: 
 
    This program detects what serial ports (COM1-COM4) are installed 
    in a standard (PC, XT, AT) or PS/2 system.  The type of mouse, if
    present, is also shown (serial, bus, InPort, PS/2, HP) together with
    the interrupt request (IRQ) line it's using (unless it's a PS/2).
    The program warns of potential IRQ line conflicts between the
    mouse and serial ports.  In the case of PS/2 computers, where
    there should be no possibility of conflict between a PS/2 mouse
    and a serial port, WHATPORT only reports the presence of the
    PS/2 mouse and the serial ports that it finds installed (up to
    COM4).


PRINCIPLE:

    Because standard PCs have only two IRQ lines for serial ports,
    COM3 must share COM1's IRQ line and COM4 must share COM2's 
    IRQ line.  Unfortunately, two devices using the same IRQ 
    line can't be active at the same time.  COM3 can't be used for 
    a printer or modem if a serial mouse is active on COM1, for 
    example.  Likewise, COM4 can't be used if a serial mouse is 
    active on COM2.  In other words, if you have four COM 
    ports and a mouse is attached to one of them, you do not 
    have three COM ports available for other devices, you only 
    have two.  The COM port that shares the IRQ line being 
    used by the mouse is not usable.  WHATPORT detects and
    reports such conflicts.
 
    The following table shows what ports are available for other 
    devices in a PC, XT, or AT when a serial port mouse is present
    on a multiple-port system:

       Serial port mouse on     Ports available for other devices 
       _____________________    _________________________________
        COM1 or COM3 (IRQ4)          COM2 or COM4 (IRQ3) 
        COM2 or COM4 (IRQ3)          COM1 or COM3 (IRQ4) 

    Conflicts with serial ports are also possible in the case of a
    bus mouse.  For example, if a bus mouse is configured to use
    IRQ3, there will be a conflict with both COM2 and COM4.  If it
    is configured to use IRQ4, there will be a conflict with both
    COM1 and COM3.  WHATPORT also detects and reports these conditions
    so a different IRQ can be selected for the bus mouse.

    The PS/2 has a different arrangement.  COM1 in a PS/2 uses IRQ4,
    and COM2, COM3, and COM4 share IRQ3.  There should not be any IRQ
    conflicts with a PS/2 mouse in a PS/2 system since the PS/2 mouse
    has its own port and does not use either IRQ3 or IRQ4.  However, it
    seems theoretically possible that someone could attach an ordinary 
    (non-PS/2) serial or bus mouse to a PS/2 machine, in which case
    there could be IRQ conflicts.  With that kind of setup, a bus mouse
    using IRQ3 could make three serial ports (COM2, COM3, and COM4)
    unusable on a PS/2.
    
 
HOW TO USE THE PROGRAM:

    Just run it and read the results.  Adjustment for color or
    monochrome display is automatic, but monochrome can be forced
    by putting M on the command line.
    
    Some special considerations apply in the case of PS/2 systems, 
    because the port addresses they use for COM3 and COM4 are different
    from those in PCs, XTs, and ATs.  Version 3.8 of WHATPORT should
    automatically detect the presence of an IBM PS/2 system and check
    the right port addresses since it uses a standard interrupt for
    testing the system type (INT 15h, function C0h).  It is not certain,
    however, that this testing feature will work the same way with clones
    of the IBM PS/2.  For this reason the program also allows you to
    declare the presence of a PS/2 system by means of a command line
    switch.  To declare a PS/2 simply type WHATPORT PS2 (or WHATPORT PS/2)
    at the DOS prompt.  You probably won't need to do that, however.
 
    The good news is that if a PS/2 mouse is installed you'll never need a
    command line switch to tell the program you have that kind of system.
    The program knows a PS/2 mouse when it sees one, and the detection
    of that mouse is itself an adequate test for a PS/2 system (no other
    type of system could have such a mouse).  Thus you'll need to be
    concerned (mildly) about ability to detect a PS/2 system only if there
    is no PS/2 mouse installed.

 
DISTRIBUTION: 
 
    WHATPORT.COM and this document are provided free by Life Sciences
    Editorial Services, Annapolis, Maryland.  They may be copied and
    distributed promiscuously provided no money is charged for them,
    they are not modified, and they are not separated.  Although the
    program has been extensively tested, Pete Petrakis makes no warranty
    concerning its usefulness on all systems and he accepts no
    responsibility or liability for any mishap resulting from its use.

                                             Pete Petrakis
                                             Annapolis, Maryland